## Slide 1: Processor
CS 3410, Spring 2014
Computer Science
Cornell University
See P&H Chapter: 4.1-4.4, 1.4, Appendix A

## Slide 2: Full Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB

## Slide 3: Iclicker
How many stages of a datapath are there in our single cycle MIPS design?
A) 1
B) 2
C) 3
D) 4
E) 5

## Slide 4: Stages of datapath (1/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 5: Stages of datapath (2/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 6: Stages of datapath (3/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 7: Stages of datapath (4/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 8: Stages of datapath (5/5)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB

## Slide 9: Takeaway
The datapath for a MIPS processor has five stages:
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
This five stage datapath is used to execute all MIPS instructions

## Slide 10: Iclicker
There are how many types of instructions in the MIPS ISA?
A) 1
B) 3
C) 5
D) 200
E) 1000s

## Slide 11: MIPS instructions
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 12: MIPS Instruction Functions
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 13: Arithmetic Instructions: Shift
op | - | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rt, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rt, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rt, shamt | R[rd] = R[rt] >> shamt (sign ext.)
00000000000001000100000110000000
ex: r8 = r4 * 64 # SLL r8, r4, 6
r8 = r4 << 6
R-Type

## Slide 14: Shift
5
ALU
5
5
Reg. File
PC
Prog.
Mem
inst
+4
shamt
control
r4
shamt = 6
r8
sll
sll

## Slide 15: Arithmetic Instructions: Immediates
 | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + sign_extend(imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)
op | mnemonic | description
0x8 | ADDI rd, rs, imm | R[rd] = R[rs] + imm
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & imm
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ imm
op | rs | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00100000101001010000000000000101
I-Type
ex: r5 += -1
ex: r5 = r5 + 5 # ADDI r5, r5, 5
r5 += 5
What if immediate is negative?
Notes: For addi, sign extension and can do positive and negative. Will signal overflow.
For addiu, still use sign extension, but no overflow
Add vs. addu: no overflow for addu

## Slide 16: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
control
r5
r5
addi
addi

## Slide 17: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
control
r5
r5
addi
addi

## Slide 18: Arithmetic Instructions: Immediates
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00111100000001010000000000000101
I-Type
ex: LUI r5, 0xdead
ORI r5, r5 0xbeef
What does r5 = ?
r5 = 0xdeadbeef
ex: r5 = 0x50000 # LUI r5, 5

## Slide 19: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
16
control
r5
lui
lui
5
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 20: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  How fast can we make it?
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency

## Slide 21: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 22: Memory Instructions
op | mnemonic | description
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10101100101000010000000000000100
base + offset addressing
I-Type
signed offsets
ex: = Mem[4+r5] = r1 # SW r1, 4(r5)

## Slide 23: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
inst
sw
r5+4
4
Write Enable
r5
r1
ex: = Mem[4+r5] = r1 # SW r1, 4(r5)

## Slide 24: Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10101100101000010000000000000100
Notes: sw r1 4(r5)
sb r1, 3(r5)
If you don’t make sure half word accesses are half word aligned, or word accesses are word aligned, there will be an error signaled. We will talk about traps and exceptions later.

## Slide 25: Endianness
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word
0x78
0x56
0x34
0x12
0x5678
0x1234
0x12
0x34
0x56
0x78
0x1234
0x5678
Notes: Comes from Gulliver travels

## Slide 26: Memory Layout
Examples (big/little endian):
# r5 contains 5 (0x00000005)
SB r5, 2(r0)
LB r6, 2(r0)
# R[r6] = 0x05
SW r5, 8(r0)
LB r7, 8(r0)
LB r8, 11(r0)
# R[r7] = 0x00
# R[r8] = 0x05
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff
0x05
0x00
0x00
0x00
0x05
Notes: Big Endian means store MSB (most significant byte) first

## Slide 27: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 28: Control Flow: Absolute Jump
op | immediate
6 bits | 26 bits
00001010100001001000011000000011
J-Type
ex: j 0x1000000
PC = ((PC+4) & 0xf0000000) | 0x04000000
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28  target  00
(PC+4)31..28 target 00
4 bits | 26 bits | 2 bits
(PC+4)31..28 01000000000000000000000000 00
Notes: Where  is used to concatenate
Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 29: Control Flow: Absolute Jump
Absolute addressing for jumps
  Jump from 0x30000000 to 0x20000000? NO Reverse? NO
    But: Jumps from 0x2FFFFFFF to 0x3xxxxxxx are possible, but not reverse
  Trade-off: out-of-region jumps vs. 32-bit instruction encoding
MIPS Quirk:
  jump targets computed using already incremented PC
op | immediate
6 bits | 26 bits
00001010100001001000011000000011
J-Type
(PC+4)31..28 will be the same
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28  target  00
Notes: Where  is used to concatenate

## Slide 30: Absolute Jump
long jump? computed jump?
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
J
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28  target  00

## Slide 31: Control Flow: Jump Register
op | rs | - | - | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R-Type
ex: JR r3

## Slide 32: Jump Register
+4

tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R[r3]
JR

## Slide 33: Examples
E.g. Use Jump or Jump Register instruction to
jump to 0xabcd1234
But, what about a jump based on a condition?
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe00
else jump to 0xabcd1234

## Slide 34: Control Flow: Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
00010000101000010000000000000011
signed offsets
I-Type
ex: BEQ r5, r1, 3
If(R[r5]==R[r1]) then PC = PC+4 + 12 (i.e. 12 == 3<<2)
Notes: Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 35: Control Flow: Branches
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
R[r5]
BEQ
R[r1]
Notes: In the book, the ALU is used to determine the branch comparison. We are choosing to do it separately.
Anyway, can’t use ALU for both branc comparison and PC determination. At most, we can use it once. The book uses it for branch

## Slide 36: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
Conditional Jumps (cont.)
ex: BGEZ r5, 2
If(R[r5] ≥ 0) then PC = PC+4 + 8 (i.e. 8 == 2<<2)

## Slide 37: Control Flow: More Branches
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp
R[r5]
BEQZ

## Slide 38: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28  target  00
op | immediate
6 bits | 26 bits
00001100000001001000011000000010
J-Type
Why? Function/procedure calls
op | mnemonic | description
0x2 | J target | PC = (PC+4)31..28  target  00
Discuss later
ex: JAL 0x1000000
r31 = PC+8
PC = (PC+4)31..28 0x4000000
Notes: 0x0121808 == 1185800

## Slide 39: Jump and Link
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28 ¦¦ (target << 2)
R[r31]
PC+8

## Slide 40: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  How to get it?
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency
Pipelining
  Latency vs throughput

## Slide 41: Questions
How do we measure performance?
What is the performance of a single cycle CPU?
How do I get performance?
See: P&H 1.4

## Slide 42: What instruction has the longest path
A) LW
B) SW
C) ADD/SUB/AND/OR/etc
D) BEQ
E) J

## Slide 43: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
inst
lw
r5+4
4
Write Enable
r5
ex: = r1 = Mem[4+r5] # LW r1, 4(r5)
Mem[4+r5]
Mem[4+r5]
r1

## Slide 44: Performance
How do I get it?
Parallelism
Pipelining
Both!

## Slide 45: Performance: Aside
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
combinatorial
Logic
tcombinatorial
inputs arrive
outputs expected

## Slide 46: 4-bit Ripple Carry Adder
A3
B3
S3
C4
A1
B1
S1
A2
B2
S2
A0
B0
C0
S0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb

## Slide 47: Adding
Main ALU, slows us down
Does it need to be this slow?
Observations
Have to wait for Cin
Can we compute in parallel in some way?
CLA carry look-ahead adder

## Slide 48: Carry Look Ahead Logic
Can we reason independent of Cin?
  Just based on (A,B) only
When is Cout == 1, irrespective of Cin
If Cin == 1, when is Cout also == 1

## Slide 49: 1-bit Adder with Carry
A
B
S
Cin
Cout
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded

## Slide 50: 1-bit CLA adder
A
B
Cin
R
p
g
Create two terms: propagator, generator
g = 1, generates Cout: g = AB
  Irrespective of Cin
p = 1, propagates Cin to Cout: p = A + B
p and g generated in 1 cycle delay
R is 2 cycle delay after we get Cin

## Slide 51: 1-bit Adder with Carry
A
B
S
Cin
Cout
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded

## Slide 52: 4-bit CLA
A
B
C0
p
g
A
B
p
g
A
B
p
g
A
B
p
g
CLA (carry look-ahead logic)
CLA takes p,g from all 4 bits, C0 and generates all Cs: 2 gate delay
C1
C2
C3
C4
S
Ci = Function (C0, p and g values)

## Slide 53: 4-bit CLA
A0
B0
C0
A1
B1
A2
B2
A3
B3
CLA (carry look-ahead logic)
p0
g0
p1
g1
p2
g2
p3
g3
Given A,B’s, all p,g’s are generated in 1 gate delay in parallel
C1
C2
C3
Given all p,g’s, all C’s are generated in 2 gate delay in parallel
S3
S2
S1
S0
Given all C’s, all S’s are generated in 2 gate delay in parallel
Sequential operation is made into parallel operation!!

## Slide 54: Performance
Ripple carry adder vs carry lookahead adder for 8 bits
  2 x 8 vs. 5

## Slide 55: Performance
How do I get it?
Parallelism
Pipelining
Both!