## Slide 1: Caches 2
CS 3410, Spring 2014
Computer Science
Cornell University
See P&H Chapter: 5.1-5.4, 5.8, 5.15

## Slide 2: Memory Hierarchy
Memory closer to processor
  small & fast
  stores active data
Memory farther from processor
  big & slow
  stores inactive data
L1 Cache
SRAM-on-chip
L2/L3 Cache
SRAM
Memory
DRAM

## Slide 3: Memory Hierarchy
Memory closer to processor is fast but small
  usually stores subset of memory farther
    “strictly inclusive”
  Transfer whole blocks (cache lines):
  4kb: disk ↔ RAM
  256b: RAM ↔ L2
  64b: L2 ↔ L1

## Slide 4: Cache Questions
What structure to use?
  Where to place a block (book)?
  How to find a block (book)?
When miss, which block to replace?
What happens on write?

## Slide 5: Today
Cache organization
  Direct Mapped
  Fully Associative
  N-way set associative
Cache Tradeoffs
Next time: cache writing

## Slide 6: Cache Lookups (Read)
Processor tries to access Mem[x]
Check: is block containing Mem[x] in the cache?
  Yes: cache hit
    return requested data from cache line
  No: cache miss
    read block from memory (or lower level cache)
    (evict an existing cache line to make room)
    place new block in cache
    return requested data
     and stall the pipeline while all of this happens
Notes: Out of order execution

## Slide 7: Questions
How to organize cache
What are tradeoffs in performance and cost?

## Slide 8: Three common designs
A given data block can be placed…
  … in exactly one cache line  Direct Mapped
  … in any cache line  Fully Associative
    This is most like my desk with books
  … in a small set of cache lines  Set Associative

## Slide 9: Direct Mapped Cache
  Each block number maps to a single cache line index
  Where?
  address mod #blocks in cache
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Memory
Notes: Think of data accesses. Not instruction cache. Though that too applies.

## Slide 10: Direct Mapped Cache
line 0 | 
line 1 | 
0x00 | 
0x01 | 
0x02 | 
0x03 | 
0x04 | 
Memory (bytes)
Cache
2 cachelines
1-byte per cacheline
  index = address mod 2
  index = 0
Cache size = 2 bytes
index
1

## Slide 11: Direct Mapped Cache
line 0 | 
line 1 | 
Memory (bytes)
Cache
2 cachelines
1-byte per cacheline
  index = address mod 2
  index = 1
Cache size = 2 bytes
0x00 | 
0x01 | 
0x02 | 
0x03 | 
0x04 | 
index
1

## Slide 12: Direct Mapped Cache
line 0 | 
line 1 | 
line 2 | 
line 3 | 
Memory (bytes)
Cache
4 cachelines
1-byte per cacheline
  index = address mod 4
Cache size = 4 bytes
0x00 | 
0x01 | 
0x02 | 
0x03 | 
0x04 | 
0x05 | 
index
2

## Slide 13: Direct Mapped Cache
line 0 | ABCD
line 1 | 
line 2 | 
line 3 | 
0x00 | ABCD
0x04 | 
0x08 | 
0x0c | 
0x010 | 
0x014 | 
Cache
4 cachelines
1-word per cacheline
  index = address mod 4
  offset = which byte in each line
Cache size = 16 bytes
Memory (word)
index
offset
32-addr
2-bits
2-bits
28-bits

## Slide 14: Direct Mapped Cache: 2
0x000000 | ABCD
0x000004 | EFGH
0x000008 | IJKL
0x00000c | MNOP
0x000010 | QRST
0x000014 | UVWX
0x000018 | YZ12
0x00001c | 3456
0x000020 | abcd
0x000024 | efgh
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Memory
index
offset
32-addr
Cache
4 cachelines
2-words (8 bytes) per cacheline
line 0
line 1
line 0 | ABCD | EFGH
line 1 | IJKL | MNOP
line 2 | QRST | UVWX
line 3 | YZ12 | 3456
3-bits
2-bits
27-bits
line 2
line 3
line 0
line 1
line 2
line 3
  offset 3 bits: A, B, C, D, E, F, G, H
  index = address mod 4
  offset = which byte in each line
Notes: 4 bytes each, 8 bytes per line, show tags
Which of the two designs should you prefer? Depends on assumptions of spatial locality. More locality, larger blocks.

## Slide 15: Direct Mapped Cache: 2
0x000000 | ABCD
0x000004 | EFGH
0x000008 | IJKL
0x00000c | MNOP
0x000010 | QRST
0x000014 | UVWX
0x000018 | YZ12
0x00001c | 3456
0x000020 | abcd
0x000024 | efgh
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Memory
index
offset
32-addr
Cache
4 cachelines
2-words (8 bytes) per cacheline
line 0
line 1
line 0 | Tag & valid bits | ABCD | EFGH
line 1 |  | IJKL | MNOP
line 2 |  | QRST | UVWX
line 3 |  | YZ12 | 3456
3-bits
2-bits
27-bits
line 2
line 3
line 0
line 1
line 2
line 3
tag
  tag = which memory element is it?
  0x00, 0x20, 0x40?
Notes: 4 bytes each, 8 bytes per line, show tags
Which of the two designs should you prefer? Depends on assumptions of spatial locality. More locality, larger blocks.

## Slide 16: Direct Mapped Cache
Every address maps to one location
Pros: Very simple hardware
Cons: many different addresses land on same location and may compete with each other

## Slide 17: Direct Mapped Cache (Hardware)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
=
hit?
data
Word/byte select
32/8 bits
0…001000
offset
index
tag
3 bits

## Slide 18: Example: Direct Mapped Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 byte block
0
0
0
0
V
Using byte addresses in this example. Addr Bus = 5 bits

## Slide 19: Example: Direct Mapped Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 byte block
2 bit tag field
2 bit index field
1 bit block offset
0
0
0
0
V
Using byte addresses in this example. Addr Bus = 5 bits
Notes: 00 00 1
00 10 1
00 00 1
00 10 0
00 00 0

## Slide 20: Direct Mapped Example: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 3
140
100
140
Cache
00
tag data
2
100
110
150
140
1
1
0
0
0
00
150
140
1
0
V
M
M
H
H
H
Pathological example
Notes: 00001
00101
00001
00100
00000
So cache has entries in 00 and 10 i.e. 0 and 2
Then comes 12
01100 and overwrites the 2nd cache value
Then comes 5
0101 and overwrites the 2nd cache value

## Slide 21: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Addr: 01100
Cache
00
tag data
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
100
110
01
230
220

## Slide 22: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Cache
00
tag data
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
100
110
01
230
220
Notes: 00 10 1

## Slide 23: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
180
Misses: 4
Hits: 3
150
140
Addr: 00101
Cache
tag data
2
100
110
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
M
00
150
140
00
Notes: 01 10 0
00 10 1

## Slide 24: 8th and 9th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4+2
Hits: 3
Cache
00
tag data
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
M
M
M
100
110
01
230
220

## Slide 25: 10th and 11th, 12th and 13th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4+2+2+2
Hits: 3
Cache
00
tag data
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
M
M
M
M
M
M
M
100
110
01
230
220

## Slide 26: Problem
Working set is not too big for cache
Yet, we are not getting any hits?!

## Slide 27: Misses
Three types of misses
  Cold (aka Compulsory)
    The line is being referenced for the first time
  Capacity
    The line was evicted because the cache was not large enough
  Conflict
    The line was evicted because of another access whose index conflicted

## Slide 28: Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Capacity Misses
  Buy more cache
Conflict Misses
  Use a more flexible cache design

## Slide 29: Cache Organization
How to avoid Conflict Misses
Three common designs
  Direct mapped: Block can only be in one line in the cache
  Fully associative: Block can be anywhere in the cache
  Set-associative: Block can be in a few (2 to 8) places in the cache

## Slide 30: Fully Associative Cache
Block can be anywhere in the cache
  Most like our desk with library books
Have to search in all entries to check for match
  More expensive to implement in hardware
But as long as there is capacity, can store in cache
  So least misses

## Slide 31: Fully Associative Cache (Reading)
V
Tag
Block
word/byte select
hit?
data
line select
=
=
=
=
32 or 8 bits
Tag Offset
No index
Notes: “way” = line

## Slide 32: Fully Associative Cache (Reading)
V
Tag
Block
Tag Offset
m bit offset
Q: How big is cache (data only)?
Cache of size 2n blocks
Block size of 2m bytes
Cache Size: number-of-blocks x block size
= 2n x 2m bytes
= 2n+m bytes
, 2n blocks (cache lines)
Notes: “way” = line

## Slide 33: Fully Associative Cache (Reading)
V
Tag
Block
Tag Offset
m bit offset
Q: How much SRAM needed (data + overhead)?
Cache of size 2n blocks
Block size of 2m bytes
Tag field: 32 – m
Valid bit: 1
SRAM size: 2n x (block size + tag size + valid bit size)
= 2nx (2m bytes x 8 bits-per-byte + (32-m) + 1)
, 2n blocks (cache lines)
Notes: “way” = line

## Slide 34: Example: Simple Fully Associative Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 byte block
4 bit tag field
1 bit block offset
V
V
V
V
V
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 35: 1st Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
0
0
0
0
V

## Slide 36: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    random: select one of the lines at random
    round-robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 37: 1st Access
0
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 1
Hits: 0
LRU
Addr: 00001
block offset
1
0
0
M

## Slide 38: 2nd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 1
Hits: 0
lru
1
0
0
0
M

## Slide 39: 2nd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 0
150
140
150
Addr: 00101
block offset
1
1
0
0
M
M

## Slide 40: 3rd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 0
150
140
150
1
1
0
0
M
M

## Slide 41: 3rd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 1
150
140
150
110
1
1
0
0
Addr: 00001
block offset
M
M
H

## Slide 42: 4th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 1
150
140
150
110
1
1
0
0
M
M
H

## Slide 43: 4th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 2
150
140
150
140
1
1
0
0
Addr: 00100
block offset
M
M
H
H

## Slide 44: 5th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 2
150
140
150
140
1
1
0
0
M
M
H
H

## Slide 45: 5th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0
tag data
$0
$1
$2
$3
Memory
2
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 3
150
140
140
100
140
1
1
0
0
Addr: 00000
block offset
M
M
H
H
H

## Slide 46: 6th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Cache
Processor
0
tag data
$0
$1
$2
$3
Memory
2
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 3
150
140
140
100
140
1
1
0
0
M
M
H
H
H

## Slide 47: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Addr: 01100
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
M
M
H
H
H
M

## Slide 48: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3+1
150
140
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
M
M
H
H
H
M
H

## Slide 49: 8th and 9th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3+1+2
150
140
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
M
M
H
H
H
M
H
H
H

## Slide 50: 10th and 11th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 3
Hits: 3+1+2+2
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
M
M
H
H
H
M
H
H
H
H
H

## Slide 51: Cache Tradeoffs
Direct Mapped
+ Smaller
+ Less
+ Less
+ Faster
+ Less
+ Very
– Lots
– Low
– Common
Fully Associative
Larger –
More –
More –
Slower –
More –
Not Very –
Zero +
High +
?
Tag Size
SRAM Overhead
Controller Logic
Speed
Price
Scalability
# of conflict misses
Hit rate
Pathological Cases?

## Slide 52: Compromise
Set-associative cache
Like a direct-mapped cache
  Index into a location
  Fast
Like a fully-associative cache
  Can store multiple entries
    decreases conflicts
  Search in each element
n-way set assoc means n possible locations

## Slide 53: 2-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
Tag Index Offset

## Slide 54: 3-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
=
Tag Index Offset

## Slide 55: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4+2+2
Hits: 3
Cache
00
tag data
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
M
M
M
M
M
100
110
01
230
220

## Slide 56: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 3
Hits: 4+2+2
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
M
M
H
H
H
M
H
H
H
H
H
4 cache lines
2 word block
4 bit tag field
1 bit block offset field

## Slide 57: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3
0100
0000 /01/45/00/00
Evict 4,5
1100 M: 3, H: 3 12,13/0,1/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 58: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4
Hits: 7
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
M
M
H
H
H
M
M
H
H
H
H
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Notes: 0001 M: 1, H: 0 index = 0,
0101 M: 2, H: 0 index = 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 59: Summary on Cache Organization
Direct Mapped  simpler, low hit rate
Fully Associative  higher hit cost, higher hit rate
N-way Set Associative  middleground

## Slide 60: Misses
Cache misses: classification
Cold (aka Compulsory)
  The line is being referenced for the first time
    Block size can help
Capacity
  The line was evicted because the cache was too small
  i.e. the working set of program is larger than the cache
Conflict
  The line was evicted because of another access whose index conflicted
    Not an issue with fully associative
Notes: conflict can’t happen with fully associative
block size influences cold misses

## Slide 61: Cache Performance
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle plus 3 cycle per word
Performance depends on:
Access time for hit, hit rate, miss penalty
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average
.95 * 5 + .05 (100) = 4.75+5 = 9.75

## Slide 62: Basic Cache Organization
Q: How to decide block size?

## Slide 63: Experimental Results
Notes: Top to bottom: bigger cache means fewer misses.
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and miss penalty (time to fetch block) is larger

## Slide 64: Tradeoffs
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags, less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 65: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  big & fast memory built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty