## Slide 1: Lecture 1: Images and image filtering
CS5670: Intro to Computer Vision
Noah Snavely
Hybrid Images, Oliva et al., http://olivalab.mit.edu/hybridimage.htm
Notes: What expression are these people wearing?

## Slide 2: Lecture 1: Images and image filtering
Hybrid Images, Oliva et al., http://olivalab.mit.edu/hybridimage.htm
CS5670: Intro to Computer Vision
Noah Snavely
Notes: Now what expression?

## Slide 3
Lecture 1: Images and image filtering
Hybrid Images, Oliva et al., http://olivalab.mit.edu/hybridimage.htm
CS5670: Intro to Computer Vision
Noah Snavely
Notes: How about now?

## Slide 4: Reading
Szeliski, Chapter 3.1-3.3

## Slide 5: Announcements
Project 1 (Hybrid Images) will be released early next week
  Code due Friday, Feb 10
  This project will be done solo
  Other projects planned to be done in groups of 2
Project is in Python – we will provide skeleton code and instructions for setting up a Python environment for the project

## Slide 6: What is an image?
Notes: First, we should talk about what an image is.

## Slide 7: What is an image?
Digital Camera
The Eye
Source: A. Efros
We’ll focus on these in this class
(More on this process later)
Notes: One way to think of an image is as a record of a set of light rays that bounce through space and hit a piece of light-sensitive film or a digital sensor.
Another way is to think of an image as just a grid of pixel values.
Another way is to think of an image as a response of our retinas to a light stimulus. In this class, we’ll focus on digital images. Later, we’ll come back to talk about how images are formed via the transmission of light through a scene.

## Slide 8: What is an image?
A grid (matrix) of intensity values
(common to use one byte per value: 0 = black, 255 = white)
=
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 20 | 0 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 75 | 75 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 75 | 95 | 95 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 96 | 127 | 145 | 175 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 175 | 175 | 175 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 47 | 255 | 255
255 | 255 | 127 | 145 | 145 | 175 | 127 | 127 | 95 | 47 | 255 | 255
255 | 255 | 74 | 127 | 127 | 127 | 95 | 95 | 95 | 47 | 255 | 255
255 | 255 | 255 | 74 | 74 | 74 | 74 | 74 | 74 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255

## Slide 9: What is an image?
Can think of a (grayscale) image as a function f from R2 to R:
  f (x,y) gives the intensity at position (x,y)
  A digital image is a discrete (sampled, quantized) version of this function
x
y
f (x, y)
snoop
3D view
Notes: [Instructors note.] Here I show two demos.
One is “snoop” (https://www.csie.ntu.edu.tw/~cyy/projects/snoop/index.html), which is a Windows utility for zooming into the screen and showing the pixel values as numbers. So you can see brighter pixels have values close to 255, and darker pixels have values closer to 0. (Probably there exists some similar tool for Mac.)
The second demo is using Meshlab to open up a mesh that I’ve created to replicate an image, but where the “z” axis corresponds to intensity – really, just a visualization of the image as a function z = f(x,y). That mesh is here:
https://drive.google.com/open?id=1uJXcpQcWgRYlorrH_ctYn-yncEDvcxwV
If you look at it “head-on” it looks like the image of T100 above. If you move the viewpoint to the side, you see the image turn into hills and valleys. Bright regions are plateaus, dark regions are valleys, and “cliffs” represent edges in the image.

## Slide 10: Image transformations
As with any function, we can apply operators to an image
Today we’ll talk about a special kind of operator, convolution (linear filtering)
  g (x,y) = f (x,y) + 20
  g (x,y) = f (-x,y)

## Slide 11: Filters
Filtering
  Form a new image whose pixel values are a combination of the original pixel values
Why?
  To get useful information from images
    E.g., extract edges or contours (to understand shape)
  To enhance the image
    E.g., to remove noise
    E.g., to sharpen and “enhance image” a la CSI
  A key operator in Convolutional Neural Networks

## Slide 12: Canonical Image Processing problems
Image Restoration
  denoising
  deblurring
Image Compression
  JPEG, HEIF, MPEG, …
Locating Structural Features
  corners
  edges

## Slide 13: Question: Noise reduction
Given a camera and a still scene, how can you reduce noise?
Take lots of images and average them!
What’s the next best thing?
Source: S. Seitz
Notes: Answer: take lots of images, average them

## Slide 14: Image filtering
Modify the pixels in an image based on some function of a local neighborhood of each pixel
5
1
4
1
7
1
5
3
10
Local image data
7
Modified image data
Some function
Source: L. Zhang

## Slide 15: Linear filtering
One simple version of filtering: linear filtering (cross-correlation, convolution)
  Replace each pixel by a linear combination (a weighted sum) of its neighbors
The prescription for the linear combination is called the “kernel” (or “mask”, “filter”)
0.5
0.5
0
0
1
0
0
0
0
kernel
8
Modified image data
Source: L. Zhang
Local image data
6
1
4
1
8
1
5
3
10

## Slide 16: Cross-correlation
This is called a cross-correlation operation:
Let be the image, be the kernel (of size 2k+1 x 2k+1), and be the output image
Can think of as a “dot product” between local neighborhood and kernel for each pixel

## Slide 17: Convolution
Same as cross-correlation, except that the kernel is “flipped” (horizontally and vertically)
Convolution is commutative and associative
This is called a convolution operation:

## Slide 18: Convolution
Adapted from F. Durand

## Slide 19: Mean filtering
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1
1 | 1 | 1
1 | 1 | 1
*
=
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 

## Slide 20: Mean filtering/Moving average

## Slide 21: Mean filtering/Moving average

## Slide 22: Mean filtering/Moving average

## Slide 23: Mean filtering/Moving average

## Slide 24: Mean filtering/Moving average

## Slide 25: Mean filtering/Moving average

## Slide 26: Linear filters: examples
0
0
0
0
1
0
0
0
0
Original
Source: D. Lowe
*

## Slide 27
What image operation does filtering with this kernel perform? ([0 0 0; 0 1 0; 0 0 0])
ⓘ Start presenting to display the poll results on this slide.

## Slide 28: Linear filters: examples
0
0
0
0
1
0
0
0
0
Original
Identical image
Source: D. Lowe
*
=

## Slide 29: Linear filters: examples
0
0
0
0
0
1
0
0
0
Original
Source: D. Lowe
*

## Slide 30
What image operation does filtering with this kernel perform? ([0 0 0; 1 0 0; 0 0 0])
ⓘ Start presenting to display the poll results on this slide.

## Slide 31: Linear filters: examples
0
0
0
0
0
1
0
0
0
Original
Shifted left by 1 pixel
Source: D. Lowe
*
=

## Slide 32: Linear filters: examples
Original
1
1
1
1
1
1
1
1
1
Blur (with a mean filter)
Source: D. Lowe
*
=

## Slide 33: Linear filters: examples
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter (accentuates edges)
Source: D. Lowe
=
*

## Slide 34: Sharpening
Source: D. Lowe

## Slide 35: Smoothing with box filter revisited
Source: D. Forsyth
Notes: I always walk through the argument on the left rather carefully; it gives some insight into the
significance of impulse responses or point spread functions.

## Slide 36: Gaussian kernel
Source: C. Rasmussen

## Slide 37: Gaussian filters
= 30 pixels
= 1 pixel
= 5 pixels
= 10 pixels

## Slide 38: Mean vs. Gaussian filtering

## Slide 39: Gaussian filter
Removes “high-frequency” components from the image (low-pass filter)
Convolution with self is another Gaussian
  Convolving twice with Gaussian kernel of width = convolving once with kernel of width
Source: K. Grauman
*
=
Notes: Linear vs. quadratic in mask size

## Slide 40: Sharpening revisited
What does blurring take away?
original
smoothed (5x5)
–
detail
=
sharpened
=
Let’s add it back:
original
detail
+ α
(This “detail extraction” operation is also called a high-pass filter)
Photo credit: https://www.flickr.com/photos/geezaweezer/16089096376/

## Slide 41: Sharpen filter
Gaussian
scaled impulse
Sharpen filter
image
blurred image
unit impulse (identity kernel with single 1 in center, zeros elsewhere)
+
Notes: This slide derives a sharpen filter from the intuition in the previous slide – i.e., “sharpening is taking an image I, blurring it, subtracting the blurred image from I to get high-frequency edges, then scaling and adding those edges back to I to yield an image with emphasized edges).
f + a(f - f * g) = (1+a)f-af*g = f*((1+a)e-ag)

## Slide 42: Sharpen filter
unfiltered
filtered
Notes: Note how in sharpened region of the image (also known as “unsharp mask filtered” image), the edges are transformed so that the image gets darker on one side and brighter on the other – in this way, the edge is emphasized. The sharpened image “anticipates” the edges.

## Slide 43: “Optical” convolution
Source: https://www.diyphotography.net/diy_create_your_own_bokeh/
Bokeh: Blur in out-of-focus regions of an image.
Camera shake
*
=
Source: Fergus, et al. “Removing Camera Shake from a Single Photograph”, SIGGRAPH 2006

## Slide 44: Filters: Thresholding

## Slide 45: Linear filters
Can thresholding be implemented with a linear filter?
Notes: Answer: No.

## Slide 46
Can thresholding be implemented with a linear filter?
ⓘ Start presenting to display the poll results on this slide.

## Slide 47: Questions?