## Slide 1: Reconstruction

## Slide 2: Reconstruction
The forward process:
  Given
    3D shapes
    Their locations+orientations
    Their material+paint
    Light directions+intensity
    The Camera parameters
  Produce the image
Reconstruction: Reverse this process
Next two/three classes: reconstructing geometry

## Slide 3: Final perspective projection
Camera intrinsics: how your camera handles pixel. Changes if you change your camera
Camera extrinsics: where your camera is relative to the world. Changes if you move the camera

## Slide 4: Final perspective projection
Camera parameters

## Slide 5: Camera calibration
Goal: find the parameters of the camera
Why?
  Tells you where the camera is relative to the world/particular objects
  Equivalently, tells you where objects are relative to the camera
  Can allow you to ”render” new objects into the scene

## Slide 6: Camera calibration
Need to estimate P
How many parameters does P have?
  Size of P : 3 x 4
  But:
  P can only be known upto a scale
  3*4 - 1 = 11 parameters

## Slide 7: Camera calibration
Suppose we know that (X,Y,Z) in the world projects to (x,y) in the image.
How many equations does this provide?
Need to convert equivalence into equality.

## Slide 8: Camera calibration
Suppose we know that (X,Y,Z) in the world projects to (x,y) in the image.
How many equations does this provide?
Note: is unknown

## Slide 9: Camera calibration
Suppose we know that (X,Y,Z) in the world projects to (x,y) in the image.
How many equations does this provide?

## Slide 10: Camera calibration
Suppose we know that (X,Y,Z) in the world projects to (x,y) in the image.
How many equations does this provide?

## Slide 11: Camera calibration
Suppose we know that (X,Y,Z) in the world projects to (x,y) in the image.
How many equations does this provide?
2 equations!
Are the equations linear in the parameters?
How many equations do we need?

## Slide 12: Camera calibration
In matrix vector form: Ap = 0
6 points give 12 equations, 12 variables to solve for
But can only solve upto scale

## Slide 13: Camera calibration
In matrix vector form: Ap = 0
We want non-trivial solutions
If p is a solution, p is a solution too
Let’s just search for a solution with unit norm
s.t

## Slide 14: Camera calibration
In matrix vector form: Ap = 0
We want non-trivial solutions
If p is a solution, p is a solution too
Alternative form to deal with noisy inputs
How do you solve this?
  Eigenvector of ATA with smallest eigenvalue!
s.t

## Slide 15: Camera calibration
We need 6 world points for which we know image locations
Would any 6 points work?
  What if all 6 points are the same?
Need at least 6 non-coplanar points!

## Slide 16: Camera calibration
How do we get K, R and t from P?
Need to make some assumptions about K
What if K is upper triangular?
Added skew if image x and y axes are not perpendicular

## Slide 17: Camera calibration
How do we get K, R and t from P?
Need to make some assumptions about K
What if K is upper triangular?
P = K [ R t]
First 3 x 3 matrix of P is KR
“RQ” decomposition: decomposes an n x n matrix into product of upper triangular and rotation matrix

## Slide 18: Camera calibration
How do we get K, R and t from P?
Need to make some assumptions about K
What if K is upper triangular?
P = K [ R t]
First 3 x 3 matrix of P is KR
“RQ” decomposition: decomposes an n x n matrix into product of upper triangular and rotation matrix
t = K-1P[:,2]  last column of P

## Slide 19: Camera calibration and pose estimation
Where camera is relative to car equivalent to where car is relative to camera

## Slide 20: Reconstructing world points given camera
Can we recover this from just a single equation?

## Slide 21: Ambiguity
A pixel corresponds to an entire ray
  2 linear equations in 3D space
Need additional constraints!

## Slide 22: Triangulation
A pixel corresponds to an entire ray
  2 linear equations in 3D space
If we have corresponding pixel from another view, can intersect rays!
  4 equations

## Slide 23: Binocular stereo
Single
If we know where cameras are, we can shoot rays from corresponding pixels and intersect

## Slide 24: Triangulation
Suppose we have two cameras
  Calibrated: parameters known
And a pair of corresponding pixels
Find 3D location of point!

## Slide 25: Triangulation
Suppose we have two cameras
  Calibrated: parameters known
And a pair of corresponding pixels
Find 3D location of point!
(x1,y1)
(x2,y2)

## Slide 26: Triangulation

## Slide 27: Triangulation

## Slide 28: Triangulation
1 image gives 2 equations
Need 2 images!
Solve linear equations to get 3D point location

## Slide 29: Linear vs non-linear optimization

## Slide 30: Linear vs non-linear optimization
Reprojection error

## Slide 31: Linear vs non-linear optimization
Reprojection error is the squared error between the true image coordinates of a point and the projected coordinates of hypothesized 3D point
Actual error we care about
Minimize total sum of reprojection error across all images
Non-linear optimization
Reprojection error

## Slide 32: Binocular stereo
Given two calibrated cameras
  Find pairs of corresponding pixels
  Use corresponding image locations to set up equations on world coordinates
  Solve!

## Slide 33: Binocular stereo
General case: cameras can be arbitrary locations and orientations

## Slide 34: Binocular stereo
Special case: cameras are parallel to each other and translated along X axis
Z axis
X axis

## Slide 35: Stereo with rectified cameras
Special case: cameras are parallel to each other and translated along X axis
Z axis
X axis

## Slide 36
Stereo head
Kinect / depth cameras

## Slide 37: Stereo with “rectified cameras”

## Slide 38: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 39: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 40: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 41: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 42: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 43: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 44: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera

## Slide 45: Perspective projection in rectified cameras
Without loss of generality, assume origin is at pinhole of 1st camera
Y coordinate is the same!
X coordinate differs by tx/Z

## Slide 46: Perspective projection in rectified cameras
X coordinate differs by tx/Z
That is, difference in X coordinate is inversely proportional to depth
Difference in X coordinate is called disparity
Translation between cameras (tx) is called baseline
disparity = baseline / depth

## Slide 47: The disparity image
For pixel (x,y) in one image, only need to know disparity to get correspondence
Create an image with color at (x,y) = disparity
right image
left image
disparity

## Slide 48: Perspective projection in rectified cameras
For rectified cameras, correspondence problem is easier
Only requires searching along a particular row.

## Slide 49: NCC - Normalized Cross Correlation
Lighting and color change pixel intensities
Example: increase brightness / contrast
Subtract patch mean: invariance to
Divide by norm of vector: invariance to
similarity =

## Slide 50: Cross-correlation of neighborhood
translate so that mean is zero

## Slide 51
left image band
right image band
cross correlation
1
0
0.5
x

## Slide 52
left image band
right image band
cross correlation
1
0
x
0.5
target region

## Slide 53: The NCC cost volume
Consider M x N image
Suppose there are D possible disparities.
For every pixel, D possible scores
Can be written as an M x N x D array
To get disparity, take max along 3rd axis

## Slide 54: Computing the NCC volume
For every pixel (x, y)
  For every disparity d
    Get normalized patch from image 1 at (x, y)
    Get normalized patch from image 2 at (x + d, y)
    Compute NCC

## Slide 55: Computing the NCC volume
For every disparity d
  For every pixel (x, y)
    Get normalized patch from image 1 at (x, y)
    Get normalized patch from image 2 at (x + d, y)
    Compute NCC
Assume all pixels lie at same disparity d (i.e., lie on same plane) and compute cost for each
Plane sweep stereo

## Slide 57: Rectifying cameras
Given two images from two cameras with known relationship, can we rectify them?

## Slide 58: Rectifying cameras
Can we rotate / translate cameras?
  Do we need to know the 3D structure of the world to do this?

## Slide 59: Rotating cameras
Assume K is identity
Assume coordinate system at camera pinhole

## Slide 60: Rotating cameras
Assume K is identity
Assume coordinate system at camera pinhole

## Slide 61: Rotating cameras
What happens if the camera is rotated?

## Slide 62: Rotating cameras
What happens if the camera is rotated?
No need to know the 3D structure
Rotation matrix
Homogenous coordinates of original pixel
Homogenous coordinates of mapped pixel

## Slide 63: Rotating cameras

## Slide 64: Rectifying cameras

## Slide 65: Rectifying cameras

## Slide 66: Rectifying cameras

## Slide 67: Rectifying cameras

## Slide 68: Perspective projection in rectified cameras
For rectified cameras, correspondence problem is easier
Only requires searching along a particular row.

## Slide 69: Perspective projection in rectified cameras
For rectified cameras, correspondence problem is easier
Only requires searching along a particular row.
What about non-rectified cameras?
Is there an equivalent?

## Slide 70: A similar special case
Fixating camera system
Eyes fixate on object
Angle at which they merge proportional to inverse depth
b
a
Z