## Slide 1: State and Finite State Machines
Prof. Kavita Bala and Prof. Hakim Weatherspoon
CS 3410, Spring 2014
Computer Science
Cornell University
See P&H Appendix B.7. B.8, B.10, B.11

## Slide 2: Big Picture: Building a Processor
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 3: Review
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
A0 B0
S0
A1 B1
S1
A2 B2
S2
A3 B3
S3
C0

## Slide 4: Review
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub

## Slide 5: Example: A Calculator
decoder
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 6: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 7: Review : Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub

## Slide 8: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
  A) 2 ns
  B) 2 gate delays
  C) 10 ns
  D) 10 gate delays
  E) 8 gate delays

## Slide 9: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub
t=10
t=8
t=6
t=4
t=2
t=0

## Slide 10: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
  Can we store the result?
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub
t=10
t=8
t=6
t=4
t=2
t=0

## Slide 11: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 12: 4-bit Ripple Carry Adder
A3
B3
S3
C4
A1
B1
S1
A2
B2
S2
A0
B0
C0
S0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb
Notes: Carry-lookahead adders would be more efficient performance wise (i.e. lower gate delay), but more expense hardware wise (i.e. more logic gates)

## Slide 13: Stateful Components
Until now is combinationial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 14: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 15: Goal
How do we store store one bit?

## Slide 16: First Attempt: Unstable Devices
B
A
C

## Slide 17: First Attempt: Unstable Devices
0
1
Does not work!
  Unstable
  Oscillates wildly!
B
A
C
1
0
0
1

## Slide 18: Second Attempt: Bistable Devices
In stable state, A = B
How do we change the state?
A
B
A
B
1
A
B
1
0
0
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 19: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Notes: Can you store a value (with this circuit)?
Can you change its value?
Q is comes from Latin language "quiscens" or "the present particle" or "what is present available" or "present output"
How to create state? Feedback.
Show how the signal works

## Slide 20: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 21: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 | ? | ?
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | ? | ?
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0
1
0
Q will be 0 if R is 1
1
will be 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 |  | 
1 | 1 |  | 

## Slide 22: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | ? | ?
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | ? | ?
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1
0
1
Q will be 1
0
will be 0 if S is 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
What are the values for Q and ?
0 and 0
0 and 1
1 and 0
1 and 1
Notes: Ask a clicker question about Q and !Q

## Slide 23: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0
0
1
If Q is 1, will stay 1
if Q is 0, will stay 0
0
If is 0 will stay 0
If is 1 will stay 1
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
1

Notes: Since the set and reset input are both 0, the Q and !Q determine the output, which will hold.

## Slide 24: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1
1
0
Q will be 0 since R is 1
0
will be 0 since S is 1
What happens when S,R changes from 1,1 to 0,0?
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 25: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
10
1 0
01
0 1
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
What happens when S,R changes from 1,1 to 0,0?
Q and become unstable and will oscillate wildly
between values 0,0 to 1,1 to 0,0 to 1,1 …
0 1 0
01 0
0 1 0 1
01 0 1
0
0
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 26: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
S
R
Q
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 27: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 28: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 29: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 30: Fourth Attempt: (Unclocked) D Latch
D
S
R
Q
Q
D
D | Q | 
0 | 0 | 1
1 | 1 | 0
D | Q | 
0 | 0 | 1
1 | 1 | 0
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Fill in the truth table?
Data (D) Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (…after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 31: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 32: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 33: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 34: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 35: Clock Methodology
Clock Methodology
Negative edge, synchronous
    Edge-Triggered: Signals must be stable near falling clock edge
Positive edge synchronous
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 36: Fifth Attempt: D Latch with Clock
S
R
D
Q
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 37: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 38: Fifth Attempt: D Latch with Clock
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
D
clk
Q
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 39: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 40: Sixth Attempt: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
L
L
clk
D
X
Q
c
X
c
Q
D
clk
0
0
1
0
1
Activity#1: Fill in timing graph and values for X and Q
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 41: Sixth Attempt: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
L
L
clk
D
X
Q
c
X
c
Q
D
clk
1
0
1
0
0
1
1
0
0
1
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 42: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 43: Next Goal
How do we store more than one bit, N bits?

## Slide 44: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 45: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is be created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 46: An Example: What will this circuit do?
4-bit
reg
Clk
Decoder
+1
4
4
4
16
4

## Slide 47: An Example: What will this circuit do?
4-bit
reg
Clk
Run
WE
R
Reset
Decoder
A[4]
1 = 0001 =B[4]
S[4]
Cout
+1
4
4
4
16
4

## Slide 48: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0
Notes: Previous slide would need to display up to 16, so would need a 16-segment LED decoder

## Slide 49: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0

## Slide 50: Decoder Example: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 51: 7 Segment LED Decoder Implementation
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 52: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 53: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 54: Encoders
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Log2(N) outputs wires
N Input wires
e.g. Voting:
Can only vote for one out of N
candidates, so N inputs.
But can encode vote efficiently
with binary encoding.
Notes: N possible inputs -> log2(N) wires to encode

## Slide 55: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  |  |  | 
0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 56: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  | o2 | o1 | o0
0 | 0 | 0 | 0 |  | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 0 | 0 | 1
0 | 1 | 0 | 0 |  | 0 | 1 | 0
0 | 0 | 1 | 0 |  | 0 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0
o0
o1
o2
o2 = abcd
o1 = abcd + abcd
o0 = abcd + abcd
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 57: Basic Building Blocks Example: Voting
Ballots
The 3410 optical scan
vote reader
machine
detect
enc
8
3
7
7LED decode

## Slide 58: Recap
We can now build interesting devices with sensors
  Using combinationial logic
We can also store data values (aka Sequential Logic)
  In state-holding elements
  Coupled with clocks

## Slide 59: Administrivia
Make sure to go to your Lab Section this week
Completed Lab1 due before winter break, Friday, Feb 14th
Note, a Design Document is due when you submit Lab1 final circuit
Work alone
Homework1 is out
Due a week before prelim1, Monday, February 24th
Work on problems incrementally, as we cover them in lecture
Office Hours for help
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 60: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2014sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, March 4th
  Thursday, May 1th
Schedule is subject to change

## Slide 61: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 62: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 63: Finite State Machines

## Slide 64: Next Goal
How do we design logic circuits with state?

## Slide 65: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 66: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 67: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic
Notes: Put sequential logic term on slide

## Slide 68: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 69: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: = up or = down
Output: = on or = off
States: = A, = B, = C, or = D
Notes: Say left of slash is input and right is output

## Slide 70: FSM Example
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 0=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 71: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 72: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 73: Moore Machine FSM Example
Legend
state out
input
startout
A off
B on
C off
D off
down
up
down
down
up
up
down
up
Input: up or down
Output: on or off
States: A, B, C, or D
Notes: Also show a mealy machine

## Slide 74: Mealy Machine FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 75: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Notes: Ask as a clicker question

## Slide 76: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-out
1
Notes: Ask as a clicker question

## Slide 77: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-in
1
Notes: Ask as a clicker question

## Slide 78: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Carry-out
1
1
Sum: output
Notes: Ask as a clicker question

## Slide 79: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
  How many states are needed to represent FSM?
  Draw and Fill in FSM diagram
…10110
…01111
…00101
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Sum: output
Notes: Ask as a clicker question

## Slide 80: FSM: State Diagram
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  .
…10110
…01111
…00101
a
b
z

## Slide 81: FSM: State Diagram
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
…10110
…01111
…00101
a
b
z
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 82: FSM: State Diagram
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z (Mealy Machine)
…10110
…01111
…00101
a
b
z

## Slide 83: Serial Adder: State Table
a | b | Current state | z | Next state
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
(2) Write down all input and state combinations

## Slide 84: Serial Adder: State Table
(2) Write down all input and state combinations
a | b | Current state | z | Next state
0 | 0 | S0 | 0 | S0
0 | 1 | S0 | 1 | S0
1 | 0 | S0 | 1 | S0
1 | 1 | S0 | 0 | S1
0 | 0 | S1 | 1 | S0
0 | 1 | S1 | 0 | S1
1 | 0 | S1 | 0 | S1
1 | 1 | S1 | 1 | S1
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1

## Slide 85: Serial Adder: State Assignment
(3) Encode states, inputs, and outputs as bits
Two states, so 1-bit is sufficient
  A single flip-flop will encode the state
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0
1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1

## Slide 86: Serial Adder: Circuit
(4) Determine logic equations for next state and outputs
Combinational Logic Equations
  z = b + a + s + abs
  s’ = ab + bs + as + abs
Next State
Current State
Input
Output
Comb. Logic
a
b
D
Q
s
z
s'
s'
Next State
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
Notes: Practice minimizing circuit w/a Karnaugh map

## Slide 87: Sequential Logic Circuits
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Next State
Current State
Input
Output
Comb. Logic
a
b
D
Q
s
z
s'
s'
Next State
  z = b + a + s + abs
  s’ = ab + bs + as + abs
  .
  .
  .

## Slide 88: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes
  State Machines or Ad-Hoc Circuits