## Slide 1: RISC, CISC, and ISA Variations
Prof. Kavita Bala and Prof. Hakim Weatherspoon
CS 3410, Spring 2014
Computer Science
Cornell University
See P&H Appendix 2.16 – 2.18, and 2.21

## Slide 2: Survey
Lectures
  Need to repeat student questions
  Slow down
  iClicker
    Will get you feedback
  Lecture slides not completed by end of lecture
Handouts
  Will make available online and in front and back
  Lecture slide formats, pdf and pptx

## Slide 3: Survey
Homeworks
  Really liked having fewer deadlines
  Liked modified problems
Labs
  Lots of good feedback
  Over-crowded labs. Can go to morning sessions
  Control the length of the lab sessions

## Slide 4: Administrivia
There is a Lab Section this week, C-Lab2
Project1 (PA1) is due next Tueday, March 11th
Prelim today week
Starts at 7:30pm sharp
Upson B17 [a-e]*, Olin 255[f-m]*, Philips 101 [n-z]*
Go based on netid

## Slide 5: Administrivia
Prelim1 today:
  Time: We will start at 7:30pm sharp, so come early
  Loc: Upson B17 [a-e]*, Olin 255[f-m]*, Philips 101 [n-z]*
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of last week
    Everything up to and including data hazards
    Appendix B (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, Lab0, Lab1, Lab2

## Slide 6: Big Picture: Where are we now?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 7: Big Picture: Where are we going?
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
op = addi r0 r5 10
op = addi r5 r5 15
op = r-type r5 r5 shamt=1 func=sll
r0 = 0
r5 = r0 + 10
r5 = r5<<1 #r5 = r5 * 2
r5 = r15 + 15
Notes: 32 bits, 4 bytes
Add a line to represent the instruction set architecture
Another line for assembly
Another line, high level language

## Slide 8: Big Picture: Where are we going?
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
Instruction Set
Architecture (ISA)
High Level Languages
Notes: 32 bits, 4 bytes
Add a line to represent the instruction set architecture
Another line for assembly
Another line, high level language

## Slide 9: Goals for Today
Instruction Set Architectures
  ISA Variations, and CISC vs RISC
Next Time
  Program Structure and Calling Conventions
Notes:   Time for Prelim1 Questions

## Slide 10: Next Goal
Is MIPS the only possible instruction set architecture (ISA)?
What are the alternatives?

## Slide 11: Instruction Set Architecture Variations
ISA defines the permissible instructions
  MIPS: load/store, arithmetic, control flow, …
  ARMv7: similar to MIPS, but more shift, memory, & conditional ops
  ARMv8 (64-bit): even closer to MIPS, no conditional ops
  VAX: arithmetic on memory or registers, strings, polynomial evaluation, stacks/queues, …
  Cray: vector operations, …
  x86: a little of everything
Notes: Bring out competing goals

## Slide 12: Brief Historical Perspective on ISAs
Accumulators
  Early stored-program computers had one register!
  One register is two registers short of a MIPS instruction!
  Requires a memory-based operand-addressing mode
    Example Instructions: add 200
      Add the accumulator to the word in memory at address 200
      Place the sum back in the accumulator
EDSAC (Electronic Delay Storage
Automatic Calculator) in 1949
Intel 8008 in 1972
was an accumulator
Notes: Accumulator: one register (http://en.wikipedia.org/wiki/Electronic_Delay_Storage_Automatic_Calculator )
The accumulator is bot the source operand and the destination for the operation. The second operand comes from memory.
EDSAC (Electronic Delay Storage Automatic Calculator) in 1949. EDSAC was the second electronic digital stored-program computer to go into regular service. The first being the EDVAC (Electronic Discrete Variable Automatic Computer), which, unlike its predecessor the ENIAC, it was binary rather than decimal, and was a stored program computer. The EDVAC had a memory capacity of 1000 44-byte words (i.e. 5.5 kB today). EDVAC's addition time was 864 microseconds (about 1.16 kHz) and its multiplication time was 2900 microseconds (about 0.38 kHz). The computer had almost 6,000 vacuum tubes and 12,000 diodes, and consumed 56 kW of power. It covered 490 ft² (45.5 m²) of floor space and weighed 17,300 lb (7,850 kg). The full complement of operating personnel was thirty people per eight-hour shift.
EDSAC details: The instructions available were: add, subtract, multiply, collate,[10] shift left, shift right, load multiplier register, store (and optionally clear) accumulator, conditional skip, read input tape, print character, round accumulator, no-op and stop. There was no division instruction (though a number of division subroutines were available) and no way to directly load a number into the accumulator (a “store and zero accumulator” instruction followed by an “add” instruction were necessary for this).

## Slide 13: Brief Historical Perspective on ISAs
Next step, more registers…
  Dedicated registers
    E.g. indices for array references in data transfer instructions, separate accumulators for multiply or divide instructions, top-of-stack pointer.
  Extended Accumulator
    One operand may be in memory (like previous accumulators).
    Or, all the operands may be registers (like MIPS).
Intel 8086
“extended accumulator”
Processor for IBM PCs
Notes: The next step in the evolution of instruction sets was the addition of registers dedicated to specific operations. Hence, registers might be included to act as indices for array references in data transfer instructions, to act as separate accumulators for multiply or divide instructions, and to serve as the top-of-stack pointer. Perhaps the best-known example of this style of instruction set is found in the Intel 8086, the computer at the core of the IBM Personal Computer. This style of instruction set is labeled extended accumulator, dedicated register, or special-purpose register. Like the single-register accumulator architectures, one operand may be in memory for arithmetic instructions. Like the MIPS architecture, however, there are also instructions where all the operands are registers.

## Slide 14: Brief Historical Perspective on ISAs
Next step, more registers…
  General-purpose registers
    Registers can be used for any purpose
    E.g. MIPS, ARM, x86
  Register-memory architectures
    One operand may be in memory (e.g. accumulators)
    E.g. x86 (i.e. 80386 processors
  Register-register architectures (aka load-store)
    All operands must be in registers
    E.g. MIPS, ARM
Notes: The generalization of the dedicated-register architectureallows all the registers to be used for any purpose, hence the name general-purpose register. MIPS is an example of a general-purpose register architecture. This style of instruction set may be further divided into those that allow one operand to be in memory (as found in accumulator architectures), called a register-memory architecture, and those that demand that operands always be in registers, called either a load-store or a register-register architecture.
The 80386 is Intel’s attempt to transform the 8086 into a general-purpose register-memory instruction set. Perhaps the best-known register-memory instruction set is the IBM 360 architecture, first announced in 1964. This instruction set is still at the core of IBM’s mainframe computers—responsible for a large part of the business of the largest computer company in the world. Register-memory architectures were the most popular in the 1960s and the first half of the 1970s.
Digital Equipment Corporation’s VAX architecture took memory operands one step further in 1977. It allowed an instruction to use any combination of registers and memory operands. A style of architecture in which all operands can be in memory is called memory-memory. (In truth the VAX instruction set, like almost all other instruction sets since the IBM 360, is a hybrid, since it also has general-purpose registers.)

## Slide 15: Takeaway
The number of available registers greatly influenced the instruction set architecture (ISA)
Machine | Num General Purpose Registers | Architectural Style | Year
EDSAC | 1 | Accumulator | 1949
IBM 701 | 1 | Accumulator | 1953
CDC 6600 | 8 | Load-Store | 1963
IBM 360 | 18 | Register-Memory | 1964
DEC PDP-8 | 1 | Accumulator | 1965
DEC PDP-11 | 8 | Register-Memory | 1970
Intel 8008 | 1 | Accumulator | 1972
Motorola 6800 | 2 | Accumulator | 1974
DEC VAX | 16 | Register-Memory, Memory-Memory | 1977
Intel 8086 | 1 | Extended Accumulator | 1978
Motorola 6800 | 16 | Register-Memory | 1980
Intel 80386 | 8 | Register-Memory | 1985
ARM | 16 | Load-Store | 1985
MIPS | 32 | Load-Store | 1985
HP PA-RISC | 32 | Load-Store | 1986
SPARC | 32 | Load-Store | 1987
PowerPC | 32 | Load-Store | 1992
DEC Alpha | 32 | Load-Store | 1992
HP/Intel IA-64 | 128 | Load-Store | 2001
AMD64 (EMT64) | 16 | Register-Memory | 2003
Notes: The generalization of the dedicated-register architectureallows all the registers to be used for any purpose, hence the name general-purpose register. MIPS is an example of a general-purpose register architecture. This style of instruction set may be further divided into those that allow one operand to be in memory (as found in accumulator architectures), called a register-memory architecture, and those that demand that operands always be in registers, called either a load-store or a register-register architecture.
The 80386 is Intel’s attempt to transform the 8086 into a general-purpose register-memory instruction set. Perhaps the best-known register-memory instruction set is the IBM 360 architecture, first announced in 1964. This instruction set is still at the core of IBM’s mainframe computers—responsible for a large part of the business of the largest computer company in the world. Register-memory architectures were the most popular in the 1960s and the first half of the 1970s.
Digital Equipment Corporation’s VAX architecture took memory operands one step further in 1977. It allowed an instruction to use any combination of registers and memory operands. A style of architecture in which all operands can be in memory is called memory-memory. (In truth the VAX instruction set, like almost all other instruction sets since the IBM 360, is a hybrid, since it also has general-purpose registers.)
Digital Equipment Corporation’s VAX architecture took memory operands one step further in 1977. It allowed an instruction to use any combination of registers and memory operands. A style of architecture in which all operands can be in memory is called memory-memory. (In truth the VAX instruction set, like almost all other instruction sets since the IBM 360, is a hybrid, since it also has general-purpose registers.)

## Slide 16: Takeaway
The number of available registers greatly influenced the instruction set architecture (ISA)
Notes: The generalization of the dedicated-register architectureallows all the registers to be used for any purpose, hence the name general-purpose register. MIPS is an example of a general-purpose register architecture. This style of instruction set may be further divided into those that allow one operand to be in memory (as found in accumulator architectures), called a register-memory architecture, and those that demand that operands always be in registers, called either a load-store or a register-register architecture.
The 80386 is Intel’s attempt to transform the 8086 into a general-purpose register-memory instruction set. Perhaps the best-known register-memory instruction set is the IBM 360 architecture, first announced in 1964. This instruction set is still at the core of IBM’s mainframe computers—responsible for a large part of the business of the largest computer company in the world. Register-memory architectures were the most popular in the 1960s and the first half of the 1970s.
Digital Equipment Corporation’s VAX architecture took memory operands one step further in 1977. It allowed an instruction to use any combination of registers and memory operands. A style of architecture in which all operands can be in memory is called memory-memory. (In truth the VAX instruction set, like almost all other instruction sets since the IBM 360, is a hybrid, since it also has general-purpose registers.)
Digital Equipment Corporation’s VAX architecture took memory operands one step further in 1977. It allowed an instruction to use any combination of registers and memory operands. A style of architecture in which all operands can be in memory is called memory-memory. (In truth the VAX instruction set, like almost all other instruction sets since the IBM 360, is a hybrid, since it also has general-purpose registers.)

## Slide 17: Next Goal
How to compute with limited resources?
i.e. how do you design your ISA if you have limited resources?

## Slide 18
People programmed in assembly and machine code!
  Needed as many addressing modes as possible
  Memory was (and still is) slow
CPUs had relatively few registers
  Register’s were more “expensive” than external mem
  Large number of registers requires many bits to index
Memories were small
  Encouraged highly encoded microcodes as instructions
  Variable length instructions, load/store, conditions, etc

## Slide 19
People programmed in assembly and machine code!
E.g. x86
  > 1000 instructions!
    1 to 15 bytes each
    E.g. dozens of add instructions
  operands in dedicated registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]
E.g. VAX
  Like x86, arithmetic on memory or registers, but also on strings, polynomial evaluation, stacks/queues, …

## Slide 20: Complex Instruction Set Computers (CISC)

## Slide 21: Takeaway
The number of available registers greatly influenced the instruction set architecture (ISA)
Complex Instruction Set Computers were very complex
  Necessary to reduce the number of instructions required to fit a program into memory.
  However, also greatly increased the complexity of the ISA as well.
Notes: can reduce the number of instructions required to execute a program and possibly increase performance by adding complexity to the ISA; however, they greatly increase the complexity of the ISA as well.

## Slide 22: Next Goal
How do we reduce the complexity of the ISA while maintaining or increasing performance?

## Slide 23: Reduced Instruction Set Computer (RISC)
John Cock
  IBM 801, 1980 (started in 1975)
  Name 801 came from the bldg that housed the project
  Idea: Possible to make a very small and very fast core
  Influences: Known as “the father of RISC Architecture”. Turing Award Recipient and National Medal of Science.

## Slide 24: Reduced Instruction Set Computer (RISC)
Dave Patterson
  RISC Project, 1982
  UC Berkeley
  RISC-I: ½ transistors & 3x faster
  Influences: Sun SPARC, namesake of industry
John L. Hennessy
  MIPS, 1981
  Stanford
  Simple pipelining, keep full
  Influences: MIPS computer system, PlayStation, Nintendo
Notes: Put picture of advisor and advisors advisor

## Slide 25: Reduced Instruction Set Computer (RISC)
Dave Patterson
  RISC Project, 1982
  UC Berkeley
  RISC-I: ½ transistors & 3x faster
  Influences: Sun SPARC, namesake of industry
John L. Hennessy
  MIPS, 1981
  Stanford
  Simple pipelining, keep full
  Influences: MIPS computer system, PlayStation, Nintendo
Notes: Put picture of advisor and advisors advisor

## Slide 26: Reduced Instruction Set Computer (RISC)
MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes
Notes: Need a segway
Make sure to define and discuss ISA and ARM
What happens when the common case is slow?
  Can we add some complexity in the ISA for a speedup?

## Slide 27: Reduced Instruction Set Computer
MIPS = Reduced Instruction Set Computer (RlSC)
  ≈ 200 instructions, 32 bits each, 3 formats
  all operands in registers
    almost all are 32 bits each
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in dedicated registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]
Notes: DEC PDP-8 has about 8 insructions

## Slide 28: RISC vs CISC
RISC Philosophy
Regularity & simplicity
Leaner means faster
Optimize the common case
Energy efficiency
Embedded Systems
Phones/Tablets
CISC Rebuttal
Compilers can be smart
Transistors are plentiful
Legacy is important
Code size counts
Micro-code!
Desktops/Servers
Notes: RISC:
regularity means no mem-to-mem, few addressing modes… thus load-store
regularity means uniform instruction size… sizeof(common) = sizeof(rare)
lean means fewer, more general instructions… thus bigger programs, more instructions
common case means measurement
CISC:
Compilers can be smart
Transistors are plentiful
Legacy is important
Code size counts
Micro-code!

## Slide 29: ARMDroid vs WinTel
  Android OS on ARM processor
  Windows OS on Intel (x86) processor
Notes:   In 2005, about 98% of the more than one billion mobile phones sold each year used at least one ARM processor.[5] As of 2009, ARM processors account for approximately 90% of all embedded 32-bit RISC processors[6] and are used extensively in consumer electronics, including personal digital assistants (PDAs), tablets, mobile phones, digital media and music players, hand-held game consoles, calculators and computer peripherals such as hard drives and routers.

## Slide 30: Takeaway
The number of available registers greatly influenced the instruction set architecture (ISA)
Complex Instruction Set Computers were very complex
- Necessary to reduce the number of instructions required to fit a program into memory.
- However, also greatly increased the complexity of the ISA as well.
Back in the day… CISC was necessary because everybody programmed in assembly and machine code! Today, CISC ISA’s are still dominant due to the prevalence of x86 ISA processors. However, RISC ISA’s today such as ARM have an ever increasing market share (of our everyday life!).
ARM borrows a bit from both RISC and CISC.
Notes: Grammar
Need an activity for the first part, iclicker or other activity. Same for second part.

## Slide 31: Next Goal
How does MIPS and ARM compare to each other?

## Slide 32: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 33: ARMv7 instruction formats
All ARMv7 instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
opx | op | rs | rd | opx | rt
4 bits | 8 bits | 4 bits | 4 bits | 8 bits | 4 bits
opx | op | rs | rd | immediate
4 bits | 8 bits | 4 bits | 4 bits | 12 bits
opx | op | immediate (target address)
4 bits | 4 bits | 24 bits
Notes: 9 addressing modes
Bring of of a contrast to MIPS and ARM
Make type of instruction same color
Add a Take away slide

## Slide 34: ARMv7 Conditional Instructions
  while(i != j) {
  if (i > j)
  i -= j;
  else
  j -= i;
  }
  Loop: BEQ Ri, Rj, End // if "NE" (not equal), then stay in loop
  SLT Rd, Rj, Ri // "GT" if (i > j),
  BNE Rd, R0, Else // …
  SUB Ri, Ri, Rj // if "GT" (greater than), i = i-j;
  J Loop
  Else: SUB Rj, Rj, Ri // or "LT" if (i < j)
  J Loop // if "LT" (less than), j = j-i;
End:
In MIPS, performance will be
slow if code has a lot of branches
Notes: At least one NOP (flush of pipeline) may follow a branch

## Slide 35: ARMv7 Conditional Instructions
  while(i != j) {
  if (i > j)
  i -= j;
  else
  j -= i;
  }
  LOOP: CMP Ri, Rj // set condition "NE" if (i != j)
  // "GT" if (i > j),
  // or "LT" if (i < j)
  SUBGT Ri, Ri, Rj // if "GT" (greater than), i = i-j;
  SUBLE Rj, Rj, Ri // if "LE" (less than or equal), j = j-i;
  BNE loop // if "NE" (not equal), then loop
=
≠
<
>
0
1
0
0
=
≠
<
>
0
0
0
1
=
≠
<
>
1
0
1
0
=
≠
<
>
0
1
0
0
In ARM, can avoid delay due to
Branches with conditional
instructions
Notes: In ARM assembly, the loop avoids the branches around the then and else clauses. Note that if Ri and Rj are equal then neither of the SUB instructions will be executed, optimizing out the need for a conditional branch to implement the while check at the top of the loop, for example had SUBLE (less than or equal) been used.

## Slide 36: ARMv7: Other Cool operations
Shift one register (e.g. Rc) any amount
Add to another register (e.g. Rb)
Store result in a different register (e.g. Ra)
ADD Ra, Rb, Rc LSL #4
Ra = Rb + Rc<<4
Ra = Rb + Rc x 16

## Slide 37: ARMv7 Instruction Set Architecture
All ARMv7 instructions are 32 bits long, has 3 formats
Reduced Instruction Set Computer (RISC) properties
  Only Load/Store instructions access memory
  Instructions operate on operands in processor registers
  16 registers
Complex Instruction Set Computer (CISC) properties
  Autoincrement, autodecrement, PC-relative addressing
  Conditional execution
  Multiple words can be accessed from memory with a single instruction (SIMD: single instr multiple data)
Notes: Quadrants? (e.g. x-axis is complexit and y-axis is speed)

## Slide 38: ARMv8 (64-bit) Instruction Set Architecture
All ARMv8 instructions are 64 bits long, has 3 formats
Reduced Instruction Set Computer (RISC) properties
  Only Load/Store instructions access memory
  Instructions operate on operands in processor registers
  16 registers
Complex Instruction Set Computer (CISC) properties
  Autoincrement, autodecrement, PC-relative addressing
  Conditional execution
  Multiple words can be accessed from memory with a single instruction (SIMD: single instr multiple data)
Notes: Quadrants? (e.g. x-axis is complexit and y-axis is speed)

## Slide 39: Instruction Set Architecture Variations
ISA defines the permissible instructions
  MIPS: load/store, arithmetic, control flow, …
  ARMv7: similar to MIPS, but more shift, memory, & conditional ops
  ARMv8 (64-bit): even closer to MIPS, no conditional ops
  VAX: arithmetic on memory or registers, strings, polynomial evaluation, stacks/queues, …
  Cray: vector operations, …
  x86: a little of everything
Notes: Bring out competing goals

## Slide 40: Next time
How do we coordinate use of registers?
Calling Conventions!
PA1 due next Tueday

## Slide 41: Prelim 1 Review Questions

## Slide 42: Prelim 1
  Time: We will start at 7:30pm sharp, so come early
  Loc: Upson B17 [a-e]*, Olin 255[f-m]*, Philips 101 [n-z]*
  Closed Book
  Cannot use electronic device or outside material
Material covered everything up to end of last week
    Everything up to and including data hazards
    Appendix B (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, Lab0, Lab1, Lab2

## Slide 43: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 44: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 45: Critical Path
How long does it take to compute a result?
S
A
B
Cin
S
A
B
S
A
B
S
A
B
Cout

## Slide 46: Critical Path
How long does it take to compute a result?
  Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
t=8
t=4
t=2
t=0
S
A
B
Cin
S
A
B
S
A
B
S
A
B
Cout
t=6

## Slide 47: Example: Mealy Machine
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Next State
Current State
Input
Output
Comb. Logic
a
b
D
Q
s
z
s'
s'
Next State
  z = b + a + s + abs
  s’ = ab + bs + as + abs
  .
  .
  .
Notes: Sequential Logic Circuits

## Slide 48: Endianness
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word
0x78
0x56
0x34
0x12
0x5678
0x1234
0x12
0x34
0x56
0x78
0x1234
0x5678
Notes: Comes from Gulliver travels

## Slide 49: Memory Layout
Examples (big/little endian):
# r5 contains 5 (0x00000005)
SB r5, 2(r0)
LB r6, 2(r0)
# R[r6] = 0x05
SW r5, 8(r0)
LB r7, 8(r0)
LB r8, 11(r0)
# R[r7] = 0x00
# R[r8] = 0x05
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff
0x05
0x00
0x00
0x00
0x05
Notes: Big Endian means store MSB (most significant byte) first

## Slide 50: Forwarding Datapath 1
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
M
W
IF
ID
Ex
IF
ID
Ex
M
W
Notes: Note that the arrow is not going backward in time.

## Slide 51: Forwarding Datapath 2
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M

## Slide 52: Register File Bypass
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W

## Slide 53: Memory Load Data Hazard
data mem
inst mem
D
B
A
NOP
sub r6,r4,r1
lw r4, 20(r8)
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
DELAY SLOT!
Notes: requires one bubble

## Slide 54: Quiz
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Notes: Find all hazards, and say how they are resolved

## Slide 55: Quiz
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Forwarding from Ex/MID/Ex (MEx)
Forwarding from M/WID/Ex (WEx)
RegisterFile (RF) Bypass
Forwarding from M/WID/Ex (WEx)
Stall
+ Forwarding from M/WID/Ex (WEx)
5 Hazards
Notes: Find all hazards, and say how they are resolved

## Slide 56: Questions?