## Slide 1: Assemblers, Linkers, and Loaders
Prof. Kavita Bala and Prof. Hakim Weatherspoon
CS 3410, Spring 2014
Computer Science
Cornell University
See: P&H Appendix A.1-2, A.3-4 and 2.12

## Slide 2: Administrivia
Upcoming agenda
  PA2 Work-in-Progress due yesterday, Monday, March 17th
  PA2 due next week, Thursday, March 27th
  HW2 available, due before Prelim2 in April
  Spring break: Saturday, March 29th to Sunday, April 6th

## Slide 3: Academic Integrity
All submitted work must be your own
  OK to study together, but do NOT share soln’s
  e.g. CANNOT email soln, look at screen, writ soln for others
  Cite your (online) sources
  “Crowd sourcing” your problem/soln same as copying
Project groups submit joint work
  Same rules apply to projects at the group level
  Cannot use of someone else’s soln
Closed-book exams, no calculators
  Stressed? Tempted? Lost?
    Come see me before due date!
Plagiarism in any form will not be tolerated

## Slide 4: Academic Integrity
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
Plagiarism in any form will not be tolerated

## Slide 5: Goal for Today: Putting it all Together
Compiler output is assembly files
Assembler output is obj files
Linker joins object files into one executable
Loader brings it into memory and starts execution
  .

## Slide 6: Goal for Today: Putting it all Together
Compiler output is assembly files
Assembler output is obj files
  How does the assembler resolve references/labels?
  How does the assembler resolve external references?
Linker joins object files into one executable
  How does the linker combine separately compiled files?
  How does linker resolve unresolved references?
  How does linker relocate data and code segments
Loader brings it into memory and starts execution
  How does the loader start executing a program?
  How does the loader handle shared libraries?

## Slide 7: Big Picture
calc.c
math.c
io.s
libc.o
libm.o
calc.s
math.s
io.o
calc.o
math.o
calc.exe
Compiler
Assembler
linker
C source
files
assembly
files
obj files
executable
program
Executing
in
Memory
loader
process
exists on
disk
Notes: C compiller produces assembly files (contain MIPS assembly, pseudo-instructions, directives, etc.)
MIPS assembler produces object files (contain MIPS machine code, missing symbols, some layout information, etc.)
MIPS linker produces executable file (contains MIPS machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 8: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 9: Example: Review of Program Layout
vector* v = malloc(8);
v->x = prompt(“enter x”);
v->y = prompt(“enter y”);
int c = pi + tnorm(v);
print(“result %d”, c);
calc.c
int tnorm(vector* v) {
return abs(v->x)+abs(v->y);
}
math.c
global variable: pi
entry point: prompt
entry point: print
entry point: malloc
lib3410.o
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
v
c
v
pi
“enter y”
“enter x”
abs
tnorm
main
“result %d”
Notes: What does memory look like when program is running?
OS reserved space
stack: function local vars and args
heap: vector object (8 bytes)
data: strings, pi
text: assembly

## Slide 10: Anatomy of an executing program
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)

## Slide 11: Big Picture: Assembling file separately
Output of assembler is a object files
  Binary machine code, but not executable
  How does assembler handle forward references?
math.c
math.s
math.o
.o = Linux
.obj Windows

## Slide 12: Next Goal
How does the assembler handle local references

## Slide 13: How does Assembler handle forward references
Two-pass assembly
  Do a pass through the whole program, allocate instructions and lay out data, thus determining addresses
  Do a second pass, emitting instructions and data, with the correct label offsets now determined
One-pass (or backpatch) assembly
  Do a pass through the whole program, emitting instructions, emit a 0 for jumps to labels not yet determined, keep track of where these instructions are
  Backpatch, fill in 0 offsets as labels are defined

## Slide 14: How does Assembler handle forward references
Example:
  bne $1, $2, L sll $0, $0, 0 L: addiu $2, $3, 0x2
The assembler will change this to
  bne $1, $2, +1 sll $0, $0, 0 addiu $2, $3, $0x2
Final machine code
  0X14220001 # bne 0x00000000 # sll 0x24620002 # addiu
Notes: 0X14220001 = 000101 00001 00010 0000 0000 0000 0001 # bne $1, $2, 0x1 0x00000000 = 000000 00000 00000 00000 00000 000000 # sll $0, $0, $0 0x24620002 = 001001 00011 00010 0000 0000 0000 0010 # addiu $2, $3, 0x2

## Slide 15: Big Picture: Assembling file separately
Output of assembler is a object files
  Binary machine code, but not executable
  How does assembler handle forward references?
  May refer to external symbols
  Each object file has illusion of its own address space
    Addresses will need to be fixed later
math.c
math.s
math.o
.o = Linux
.obj Windows
e.g. .text (code) starts at addr 0x00000000
.data starts @ addr 0x00000000
i.e. Need a “symbol table”

## Slide 16: Next Goal
How does the assembler handle external references

## Slide 17: Symbols and References
Global labels: Externally visible “exported” symbols
  Can be referenced from other object files
  Exported functions, global variables
Local labels: Internal visible only symbols
  Only used within this object file
  static functions, static variables, loop labels, …
e.g. pi
(from a couple of slides ago)
e.g.
static foo
static bar
static baz
e.g.
$str
$L0
$L2

## Slide 18: Object file
Header
  Size and position of pieces of file
Text Segment
  instructions
Data Segment
  static data (local/global vars, strings, constants)
Debugging Information
  line number  code address map, etc.
Symbol Table
  External (exported) references
  Unresolved (imported) references
Object File

## Slide 19: Example
int pi = 3;
int e = 2;
static int randomval = 7;
extern char *username;
extern int printf(char *str, …);
int square(int x) { … }
static int is_prime(int x) { … }
int pick_prime() { … }
int pick_random() {
return randomval;
}
math.c
gcc -S … math.c
gcc -c … math.s
objdump --disassemble math.o
objdump --syms math.o
Compiler
Assembler
global
local (to current file)
external (defined in another file)
global
local

## Slide 20: Objdump disassembly
csug01 ~$ mipsel-linux-objdump --disassemble math.o
math.o: file format elf32-tradlittlemips
Disassembly of section .text:
00000000 <pick_random>:
0: 27bdfff8 addiu sp,sp,-8
4: afbe0000 sw s8,0(sp)
8: 03a0f021 move s8,sp
c: 3c020000 lui v0,0x0
10: 8c420008 lw v0,8(v0)
14: 03c0e821 move sp,s8
18: 8fbe0000 lw s8,0(sp)
1c: 27bd0008 addiu sp,sp,8
20: 03e00008 jr ra
24: 00000000 nop
00000028 <square>:
28: 27bdfff8 addiu sp,sp,-8
2c: afbe0000 sw s8,0(sp)
30: 03a0f021 move s8,sp
34: afc40008 sw a0,8(s8)
…
Notes: something suspicious: a lot of zero constants in this code

## Slide 21: Objdump disassembly
csug01 ~$ mipsel-linux-objdump --disassemble math.o
math.o: file format elf32-tradlittlemips
Disassembly of section .text:
00000000 <pick_random>:
0: 27bdfff8 addiu sp,sp,-8
4: afbe0000 sw s8,0(sp)
8: 03a0f021 move s8,sp
c: 3c020000 lui v0,0x0
10: 8c420008 lw v0,8(v0)
14: 03c0e821 move sp,s8
18: 8fbe0000 lw s8,0(sp)
1c: 27bd0008 addiu sp,sp,8
20: 03e00008 jr ra
24: 00000000 nop
00000028 <square>:
28: 27bdfff8 addiu sp,sp,-8
2c: afbe0000 sw s8,0(sp)
30: 03a0f021 move s8,sp
34: afc40008 sw a0,8(s8)
…
Address
instruction
Mem[8] = instruction 0x03a0f021 (move s8,sp)
prologue
body
epilogue
symbol
resolved (fixed) later
Notes: something suspicious: a lot of zero constants in this code

## Slide 22: Objdump symbols
csug01 ~$ mipsel-linux-objdump --syms math.o
math.o: file format elf32-tradlittlemips
SYMBOL TABLE:
00000000 l df *ABS* 00000000 math.c
00000000 l d .text 00000000 .text
00000000 l d .data 00000000 .data
00000000 l d .bss 00000000 .bss
00000000 l d .mdebug.abi32 00000000 .mdebug.abi32
00000008 l O .data 00000004 randomval
00000060 l F .text 00000028 is_prime
00000000 l d .rodata 00000000 .rodata
00000000 l d .comment 00000000 .comment
00000000 g O .data 00000004 pi
00000004 g O .data 00000004 e
00000000 g F .text 00000028 pick_random
00000028 g F .text 00000038 square
00000088 g F .text 0000004c pick_prime
00000000 *UND* 00000000 username
00000000 *UND* 00000000 printf
Notes: notice: pick_random, square, other functions; pi, e, randomval; some undefined symbols

## Slide 23: Objdump symbols
csug01 ~$ mipsel-linux-objdump --syms math.o
math.o: file format elf32-tradlittlemips
SYMBOL TABLE:
00000000 l df *ABS* 00000000 math.c
00000000 l d .text 00000000 .text
00000000 l d .data 00000000 .data
00000000 l d .bss 00000000 .bss
00000000 l d .mdebug.abi32 00000000 .mdebug.abi32
00000008 l O .data 00000004 randomval
00000060 l F .text 00000028 is_prime
00000000 l d .rodata 00000000 .rodata
00000000 l d .comment 00000000 .comment
00000000 g O .data 00000004 pi
00000004 g O .data 00000004 e
00000000 g F .text 00000028 pick_random
00000028 g F .text 00000038 square
00000088 g F .text 0000004c pick_prime
00000000 *UND* 00000000 username
00000000 *UND* 00000000 printf
Address
l: local
g: global
segment
size
segment
Static local
func @
addr=0x60
size=0x28 bytes
f: func
O: obj
external
reference
Notes: notice: pick_random, square, other functions; pi, e, randomval; some undefined symbols

## Slide 24: Separate Compilation
Q: Why separate compile/assemble and linking steps?

## Slide 25
Linkers

## Slide 26: Next Goal
How do we link together separately compiled and assembled machine object files?

## Slide 27: Big Picture
calc.c
math.c
io.s
libc.o
libm.o
calc.s
math.s
io.o
calc.o
math.o
calc.exe
Executing
in
Memory
linker

## Slide 28: Linkers
Linker combines object files into an executable file
  Relocate each object’s text and data segments
  Resolve as-yet-unresolved symbols
  Record top-level entry point in executable file
End result: a program on disk, ready to execute
  E.g. ./calc Linux
  ./calc.exe Windows
  simulate calc Class MIPS simulator
  .

## Slide 29: Linker Example
main.o
...
0C000000
21035000
1b80050C
8C040000
21047002
0C000000
...
00 T main
00 D uname
*UND* printf
*UND* pi
40, JL, printf
4C, LW/gp, pi
50, JL, square
math.o
...
21032040
0C000000
1b301402
3C040000
34040000
...
20 T square
00 D pi
*UND* printf
*UND* uname
28, JL, printf
30, LUI, uname
34, LA, uname
printf.o
...
3C T printf
.text
Symbol tbl
Relocation info
External references need
to be resolved (fixed)
Steps
Find UND symbols in
symbol table
Relocate segments that
collide
e.g. uname @0x00
pi @ 0x00
square @ 0x00
main @ 0x00
Notes: main.o
0C000000 = 0000 1100 (JAL)
21035000 = 001000 01000 00011 0101 0000 0000 0000 (ADDI $3,$8, 0x5000)
1B80050C = 000110 11100 00000 0000 0101 0000 1100 (BLEZ $28, 0x050C)
3C040000 = 001111 00000 00100 0000 0000 0000 0000 (LUI, $4, 0)
21047002 = 001000 01000 00100 0111 0000 0000 0010 (ADDI $4, $8, 0x7002)
math.o
21032040 = 001000 01000 00011 0010 0000 0100 0000 (ADDI $3,$8, 0x2040)
0C000000 = 0000 1100 (JAL)
1B301402 = 000110 11001 10000 0001 0100 0000 0010 (BLEZ $23, 0x1402)
3C040000 = 001111 000000 0100 0000 0000 0000 0000 (LUI, $4, 0)
34040000 = 001101 000000 0100 0000 0000 0000 0000 (ORI, $4, 0)
1111 f
1110 e
1101 d
1100 c
1011 b
1010 a

## Slide 30: Linker Example
main.o
...
0C000000
21035000
1b80050C
8C040000
21047002
0C000000
...
00 T main
00 D uname
*UND* printf
*UND* pi
40, JL, printf
4C, LW/gp, pi
50, JL, square
math.o
...
21032040
0C000000
1b301402
3C040000
34040000
...
20 T square
00 D pi
*UND* printf
*UND* uname
28, JL, printf
30, LUI, uname
34, LA, uname
printf.o
...
3C T printf
...
21032040
0C40023C
1b301402
3C041000
34040004
...
0C40023C
21035000
1b80050c
8C048004
21047002
0C400020
...
10201000
21040330
22500102
...
Entry:0040 0100
text:0040 0000
data:1000 0000
calc.exe
00000003
0077616B
2
1
B
A
3
1
2
3
0040 0000
0040 0100
0040 0200
1000 0000
1000 0004
LUI 1000
ORI 0004
uname
pi
math
main
printf
.text
Symbol tbl
Relocation info
LW $4,-32764($gp)
$4 = pi
JAL square
JAL printf
LA uname
Notes: math
21032040 = 001000 01000 00011 0010 0000 0100 0000 (ADDI $3,$8, 0x2040)
0C40023C = 0000 1100 (JAL)
1B301402 = 000110 11001 10000 0001 0100 0000 0010 (BLEZ $23, 0x1402)
3C041000 = 001111 00000 00100 (LUI, $4, 0x1000)
34040004 = 001101 00000 00100 (ORI, $4, 0x0004)
main
0C40023C = 0000 1100 (JAL)
21035000 = 001000 01000 00011 0101 0000 0000 0000 (ADDI $3,$8, 0x5000)
1B80050C = 000110 11100 00000 0000 0101 0000 1100 (BLEZ $28, 0x050C)
8F048004 = 100011 11100 00100 1000 0000 0000 0100 (LW $4, 0x8004($28))
21047002 = 001000 01000 00100 0111 0000 0000 0010 (ADDI $4, $8, 0x7002)
printf
10201000 = 000100 00001 00000 0001 0000 0000 0000 (BEQ $1, 0x1000)
21040330 = 001000 01000 00100 0000 0011 0011 0000 (ADDI $4, $8, 0x0330)
22500102 = 001000 10010 10000 0000 0001 0000 0010 (ADDI $16, $18, 0x0102)
40023C = 0001 0000 0000 0000 1000 1111
10008f
Starting with msb, bit 31 on left
0C = 0000 1100 (J or JAL)
4C04 = 0100 1100 0000 0100 (?)
3C041000 = 0011 1100 0000 0100 (LUI, $4, 0x1000)
34040004 = 0011 0100 0000 0100 (ORI, $4, 0x0004)
1111 f
1110 e
1101 d
1100 c
1011 b
1010 a

## Slide 31: Object file
Header
  location of main entry point (if any)
Text Segment
  instructions
Data Segment
  static data (local/global vars, strings, constants)
Relocation Information
  Instructions and data that depend on actual addresses
  Linker patches these bits after relocating segments
Symbol Table
  Exported and imported references
Debugging Information
Object File

## Slide 32: Object File Formats
Unix
  a.out
  COFF: Common Object File Format
  ELF: Executable and Linking Format
  …
Windows
  PE: Portable Executable
All support both executable and object files

## Slide 33
Loaders and Libraries

## Slide 34: Big Picture
calc.c
math.c
io.s
libc.o
libm.o
calc.s
math.s
io.o
calc.o
math.o
calc.exe
Executing
in
Memory
executable
program
loader
process
exists on
disk

## Slide 35: Loaders
Loader reads executable from disk into memory
  Initializes registers, stack, arguments to first function
  Jumps to entry-point
Part of the Operating System (OS)

## Slide 36: Static Libraries
Static Library: Collection of object files (think: like a zip archive)
Q: But every program contains entire library!
A: Linker picks only object files needed to resolve undefined references at link time
e.g. libc.a contains many objects:
  printf.o, fprintf.o, vprintf.o, sprintf.o, snprintf.o, …
  read.o, write.o, open.o, close.o, mkdir.o, readdir.o, …
  rand.o, exit.o, sleep.o, time.o, ….

## Slide 37: Shared Libraries
Q: But every program still contains part of library!
A: shared libraries
  executable files all point to single shared library on disk
  final linking (and relocations) done by the loader
Optimizations:
  Library compiled at fixed non-zero address
  Jump table in each program instead of relocations
  Can even patch jumps on-the-fly
Notes: fixed address: drawbacks? advantages?
(makes linking trivial: few relocations needed)

## Slide 38: Direct Function Calls
Direct call:
00400010 <main>:
...
jal 0x00400330
...
jal 0x00400620
...
jal 0x00400330
...
00400330 <printf>:
...
00400620 <gets>:
...
Drawbacks:
Linker or loader must edit every use of a symbol (call site, global var use, …)
Idea:
Put all symbols in a single “global offset table”
Code does lookup as needed

## Slide 39: Indirect Function Calls
00400010 <main>:
...
jal 0x00400330
...
jal 0x00400620
...
jal 0x00400330
...
00400330 <printf>:
...
00400620 <gets>:
...
GOT: global offset table
0x00400330 # printf
0x00400620 # gets
0x00400010 # main
Indirect call:
Notes: .got = global offset table
filled in by linker (or loader)
all jumps go indirect via global offset table

## Slide 40: Indirect Function Calls
00400010 <main>:
...
jal 0x00400330
...
jal 0x00400620
...
jal 0x00400330
...
00400330 <printf>:
...
00400620 <gets>:
...
GOT: global offset table
0x00400330 # printf
0x00400620 # gets
0x00400010 # main
Indirect call:
# data segment
# global offset table
# to be loaded
# at -32712($gp)
# printf = 4+(-32712)+$gp
# gets = 8+(-32712)+$gp
0
4
8
lw $t9,-32708($gp)
jalr $t9
lw $t9,-32704($gp)
jalr $t9
lw $t9,-32708($gp)
jalr $t9
Notes: .got = global offset table
filled in by linker (or loader)
all jumps go indirect via global offset table

## Slide 41: Indirect Function Calls
00400010 <main>:
...
jal 0x00400330
...
jal 0x00400620
...
jal 0x00400330
...
00400330 <printf>:
...
00400620 <gets>:
...
.got
0x00400330 # printf
0x00400620 # gets
0x00400010 # main
Indirect call:
# data segment
# global offset table
# to be loaded
# at -32712($gp)
# printf = 4+(-32712)+$gp
# gets = 8+(-32712)+$gp
.word
.word
.word
lw $t9,-32708($gp)
jalr $t9
lw $t9,-32704($gp)
jalr $t9
lw $t9,-32708($gp)
jalr $t9
Notes: .got = global offset table
filled in by linker (or loader)
all jumps go indirect via global offset table

## Slide 42: Dynamic Linking
Indirect call with on-demand dynamic linking:
00400010 <main>:
...
# load address of prints # from .got[1]
lw t9, -32708(gp)
# now call it
jalr t9
...
.got
.word 00400888 # open
.word 00400888 # prints
.word 00400888 # gets
.word 00400888 # foo
Notes: dlresolve:
# t9 = 0x400888
# t8 = index of func that needs to be loaded/linked
... # t7 = loadfromdisk(t8)
... # got[t8] = t7
jr t7

## Slide 43: Dynamic Linking
Indirect call with on-demand dynamic linking:
00400010 <main>:
...
# load address of prints # from .got[1]
lw t9, -32708(gp)
# also load the index 1
li t8, 1
# now call it
jalr t9
...
.got
.word 00400888 # open
.word 00400888 # prints
.word 00400888 # gets
.word 00400888 # foo
...
00400888 <dlresolve>:
# t9 = 0x400888
# t8 = index of func that # needs to be loaded
# load that func
... # t7 = loadfromdisk(t8)
# save func’s address so # so next call goes direct
... # got[t8] = t7
# also jump to func
jr t7
# it will return directly # to main, not here
Notes: dlresolve:
# t9 = 0x400888
# t8 = index of func that needs to be loaded/linked
... # t7 = loadfromdisk(t8)
... # got[t8] = t7
jr t7

## Slide 44: Big Picture
calc.c
math.c
io.s
libc.o
libm.o
calc.s
math.s
io.o
calc.o
math.o
calc.exe
Executing
in
Memory

## Slide 45: Dynamic Shared Objects
Windows: dynamically loaded library (DLL)
  PE format
Unix: dynamic shared object (DSO)
  ELF format
Unix also supports Position Independent Code (PIC)
    Program determines its current address whenever needed (no absolute jumps!)
    Local data: access via offset from current PC, etc.
    External data: indirection through Global Offset Table (GOT)
    … which in turn is accessed via offset from current PC
Notes: .dll
.so
PIC: why?

## Slide 46: Static and Dynamic Linking
Static linking
  Big executable files (all/most of needed libraries inside)
  Don’t benefit from updates to library
  No load-time linking
Dynamic linking
  Small executable files (just point to shared library)
  Library update benefits all programs that use it
  Load-time cost to do final linking
    But dll code is probably already in memory
    And can do the linking incrementally, on-demand
Notes: cost of loading big executables
dll hell, versioning problems

## Slide 47: Recap
Compiler output is assembly files
Assembler output is obj files
Linker joins object files into one executable
Loader brings it into memory and starts execution