## Slide 1: Multicore and Parallelism
CS 3410, Spring 2014
Computer Science
Cornell University
See P&H Chapter: 4.10, 1.7, 1.8, 5.10, 6.4, 2.11

## Slide 2: Announcements
Notes: Register renaming
Hardware multithreading
Write serializability
Synchronization

## Slide 3: Dynamic Multiple Issue
Notes: In-order commit: A commit in which the results of pipelined execution are written to the programmer visible state in the same order that instructions are

## Slide 4: Limits of Static Scheduling
Compiler scheduling for dual-issue MIPS…
lw $t0, 0($s1) # load A
addi $t0, $t0, +1 # increment A
sw $t0, 0($s1) # store A
lw $t1, 0($s2) # load B
addi $t1, $t1, +1 # increment B
sw $t1, 0($s2) # store B
ALU/branch slot Load/store slot cycle
nop lw $t0, 0($s1) 1
nop nop 2
addi $t0, $t0, +1 nop 3
nop sw $t0, 0($s1) 4
nop lw $t1, 0($s2) 5
nop nop 6
addi $t1, $t1, +1 nop 7
nop sw $t1, 0($s2) 8
Notes: Rename registers, move load B up, eliminate delay slot
But! s1 and s2 might be equal => Aliasing!

## Slide 5: Does Multiple Issue Work?
Q: Does multiple issue / ILP work?
A: Kind of… but not as much as we’d like
Limiting factors?
  Programs dependencies
  Hard to detect dependencies  be conservative
    e.g. Pointer Aliasing: A[0] += 1; B[0] *= 2;
  Hard to expose parallelism
    Can only issue a few instructions ahead of PC
  Structural limits
    Memory delays and limited bandwidth
  Hard to keep pipelines full

## Slide 6: Administrivia
Next few weeks
  Week 12 (Apr 22): Lab4 release and Proj3 due Fri
    Note Lab 4 is now IN CLASS
  Week 13 (Apr 29): Proj4 release, Lab4 due Tue, Prelim2
  Week 14 (May 6): Proj3 tournament Mon, Proj4 design doc due
Final Project for class
  Week 15 (May 13): Proj4 due Wed

## Slide 7: Today
Many ways to improve performance
Multicore
Performance in multicore
Synchronization
Next 2 lectures: synchronization and GPUs

## Slide 8: How to improve performance?
We have looked at
  Pipelining
To speed up:
  Deeper pipelining
  Make the clock run faster
  Parallelism
    Not a luxury, a necessity

## Slide 9: Why Multicore?
Moore’s law
  A law about transistors
  Smaller means more transistors per die
  And smaller means faster too
But: need to worry about power too…

## Slide 10: Power Wall
Power = capacitance * voltage2 * frequency
approx. capacitance * voltage3
Reducing voltage helps (a lot)
Better cooling helps
The power wall
  We can’t reduce voltage further - leakage
  We can’t remove more heat
Notes: If frequency drops, voltage can be dropped. So sometimes use the

## Slide 11: Power Limits
Hot Plate
Rocket Nozzle
Nuclear Reactor
Surface of Sun
Xeon
180nm
32nm
Notes: Intel Westmere: 32 nm = 0.032u, 130W / 240mm^2 = 54 W/cm^2

## Slide 12: Why Multicore?
Power
1.0x
1.0x
Performance
Single-Core
Power
1.2x
1.7x
Performance
Single-Core Overclocked +20%
Power
0.8x
0.51x
Performance
Single-Core
Underclocked -20%
1.6x
1.02x
Dual-Core
Underclocked -20%
Undervolted -20%

## Slide 13: Inside the Processor
AMD Barcelona Quad-Core: 4 processor cores

## Slide 14: Inside the Processor
Intel Nehalem Hex-Core
Notes: 4 wide pipeline

## Slide 15: Hardware multithreading
Hardware multithreading
  Increase utilization with low overhead
Switch between hardware threads for stalls

## Slide 16: What is a thread?
Process includes multiple threads, code, data and OS state

## Slide 17: Hardware multithreading
Fine grained vs. Coarse grained hardware multithreading
Simultaneous multithreading (SMT)
Hyperthreads (Intel simultaneous multithreading)
  Need to hide latency

## Slide 18: Hardware multithreading
Fine grained vs. Coarse grained hardware multithreading
Fine grained multithreading
Switch on each cycle
Pros: Can hide very short stalls
Cons: Slows down every thread
Coarse grained multithreading
Switch only on quite long stalls
Pros: removes need for very fast switches
Cons: flush pipeline, short stalls not handled

## Slide 19: Simultaneous multithreading
SMT
Leverages multi-issue pipeline with dynamic instruction scheduling and ILP
Exploits functional unit parallelism better than single threads
Always running multiple instructions from multiple threads
  No cost of context switching
  Uses dynamic scheduling and register renaming through reservation stations
Can use all functional units very efficiently

## Slide 21: Hyperthreading
Multi-Core vs. Multi-Issue
Programs:
Num. Pipelines:
Pipeline Width:
Hyperthreads
  HT = MultiIssue + extra PCs and registers – dependency logic
  HT = MultiCore – redundant functional units + hazard avoidance
Hyperthreads (Intel)
  Illusion of multiple cores on a single core
  Easy to keep HT pipelines full + share functional units
vs. HT
N | 1 | N
N | 1 | 1
1 | N | N
Notes: HT = MultiIssue + extra PCs and registers – dependency logic
HT = MultiCore – redundant functional units + hazard avoidance

## Slide 22: Example: All of the above
8 multiprocessors
4 core per multiprocessor
2 HT per core
Dynamic multi-issue: 4 issue
Pipeline depth: 16
Note: each processor may
have multiple processing
cores, so this is an example
of a multiprocessor multicore
hyperthreaded system
Notes: MultiCore: 8 processors dies * 4 cores per processor die
Hyperthreading: 2 HT per core
Dynamic Multi-Issue: 4 issue
Pipeline: 16 stages

## Slide 23: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work, balancing load
  Coordination & synchronization
  Communication overhead
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
Notes: Or hyperthreads

## Slide 24: Work Partitioning
Partition work so all cores have something to do

## Slide 25: Load Balancing
Need to partition so all cores are actually working

## Slide 26: Amdahl’s Law
If tasks have a serial part and a parallel part…
Example:
step 1: divide input data into n pieces
step 2: do work on each piece
step 3: combine all results
Recall: Amdahl’s Law
As number of cores increases …
  time to execute parallel part?
  time to execute serial part?
  Serial part eventually dominates
goes to zero
Remains the same

## Slide 27: Amdahl’s Law
Notes: Underclocking messes up the ratios completely. Work through a 8x slowdown example.

## Slide 28: Pitfall: Amdahl’s Law
affected execution time
amount of improvement
+ execution time unaffected
Execution time after improvement =
Timproved = + Tunaffected
Notes: Amdahl’s Law

## Slide 29: Pitfall: Amdahl’s Law
Example: multiply accounts for 80s out of 100s
How much improvement do we need in the multiply performance to get 5× overall improvement?
20 = 80/n + 20
Improving an aspect of a computer and expecting a proportional improvement in overall performance
  Can’t be done!
Timproved = + Tunaffected
Notes: Clicker question

## Slide 30: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors?
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 100/10 × tadd + 10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5
100 processors
  Time = 100/100 × tadd + 10 × tadd = 11 × tadd
  Speedup = 110/11 = 10
Assumes load can be balanced across processors
Notes: Pair up question
10 processors
  Speedup = 110/20 = 5.5 (55% of potential)
  100 processors
  Speedup = 110/11 = 10 (10% of potential)

## Slide 31: Scaling Example
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91
Assuming load balanced
Notes: 10 processors
Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Speedup = 10010/110 = 91 (91% of potential)

## Slide 32: Scaling
Strong scaling vs. weak scaling
Strong scaling: scales with same problem size
Weak scaling: scales with increased problem size

## Slide 33: Parallelism is a necessity
Necessity, not luxury
Power wall
Not easy to get performance out of
Many solutions
Pipelining
Multi-issue
Hyperthreading
Multicore

## Slide 34: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  Balancing load over cores
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
HW
SW
Your
career…
Notes: Most is software, but hardware can help:
- communications (fast core-to-core interconnect)
- coordination and synchronization primitives (next time)

## Slide 35: Synchronization
P&H Chapter 2.11 and 5.10

## Slide 36: Parallelism and Synchronization
How do I take advantage of parallelism?
How do I write (correct) parallel programs?
What primitives do I need to implement correct parallel programs?

## Slide 37: Topics
Understand Cache Coherency
Synchronizing parallel programs
  Atomic Instructions
  HW support for synchronization
How to write parallel programs
  Threads and processes
  Critical sections, race conditions, and mutexes

## Slide 38: Parallelism and Synchronization
Cache Coherency Problem: What happens when two or more processors cache shared data?

## Slide 39: Parallelism and Synchronization
Cache Coherency Problem: What happens when two or more processors cache shared data?
i.e. the view of memory held by two different processors is through their individual caches
As a result, processors can see different (incoherent) values to the same memory location

## Slide 40: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 41: Parallelism and Synchronization
Each processor core has its own L1 cache
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache

## Slide 42: Shared Memory Multiprocessors
Core0
Core1
Core3
Core2
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 8 cores each
  HW provides single physical address space for all processors
  Assume uniform memory access (UMA) (ignore NUMA)
Cache
Memory
I/O
Interconnect
Cache
Cache
Cache
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 43: Shared Memory Multiprocessors
Core0
Core1
CoreN
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 8 cores each
  HW provides single physical address space for all processors
  Assume uniform memory access (ignore NUMA)
...
Cache
Memory
I/O
Interconnect
Cache
Cache
...
...
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 44: Cache Coherency Problem
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
What will the value of x be after both loops finish?
Start: x = 0
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 45: iClicker
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
Notes: How do they share data? How do they coordinate? How do they scale?
T0 1, T1 6, T0 simultaneously does its remaining 4 and writes 5 which is lost.
T0 3, T0 writes 4, T1 simultaneously does 3+5 = 8

## Slide 46: Cache Coherency Problem
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW $t0, addr(x) LW $t1, addr(x)
ADDIU $t0, $t0, 1 ADDIU $t1, $t1, 1
SW $t0, addr(x) SW $t1, addr(x) } }
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 47: iClicker
Thread A (on Core0) Thread B (on Core1) for(int i = 0; i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
What can the value of x be after both loops finish?
6
8
10
All of the above
None of the above
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 48: Cache Coherence Problem
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...

## Slide 49: Two issues
Coherence
What values can be returned by a read
Consistency
When a written value will be returned by a read

## Slide 50: Coherence Defined
Informal: Reads return most recently written value
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
  P1 writes X before P2 reads X  read returns written value
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
    Aka write serialization
Notes: second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 51: Coherence Defined
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
    (preserve program order)
  P1 writes X before P2 reads X  read returns written value
    (coherent memory view, can’t read old value forever)
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
    Aka write serialization
    (else X can see P2’s write before P1 and Y can see the opposite; their final understanding of state is wrong)
Notes: second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 52: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence and support shared memory
  Migration of data to local caches
    Reduces bandwidth for shared memory (performance)
  Replication of read-shared data
    Reduces contention for access (performance)
Snooping protocols
  Each cache monitors bus reads/writes (correctness)

## Slide 53: Snooping
Snooping for Hardware Cache Coherence
  All caches monitor bus and all other caches
Write invalidate protocol
  Bus read: respond if you have dirty data
  Bus write: update/invalidate your copy of data
Snoop
Snoop
Snoop
...
Core0
Cache
Memory
I/O
Interconnect
...
...
Snoop
Core1
Cache
Snoop
CoreN
Cache
Snoop
Notes: In reality: very complicated, lots of corner cases

## Slide 54: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read is another cache miss
    Owning cache supplies updated value
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
3 | CPU A writes 1 to X | Invalidate for X | 1 |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
3 | CPU A writes 1 to X | Invalidate for X | 1 |  | 0
4 | CPU B read X | Cache miss for X | 1 | 1 | 

## Slide 55: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read is another cache miss
    Owning cache supplies updated value
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
3 | CPU A writes 1 to X | Invalidate for X | 1 |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
3 | CPU A writes 1 to X | Invalidate for X | 1 |  | 0
4 | CPU B read X | Cache miss for X | 1 | 1 | 1

## Slide 56: Writing
Write-back policies for bandwidth
Write-invalidate coherence policy
  First invalidate all other copies of data
  Then write it in cache line
  Anybody else can read it
Works with one writer, multiple readers
In reality: many coherence protocols
  Snooping doesn’t scale
  Directory-based protocols
    Caches and memory record sharing status of blocks in a directory

## Slide 57: Summary of cache coherence
Informally, Cache Coherency requires that reads return most recently written value
Cache coherence hard problem
Snooping protocols are one approach

## Slide 59: Next Goal: Synchronization
Is cache coherency sufficient?
i.e. Is cache coherency (what values are read) sufficient to maintain consistency (when a written value will be returned to a read)
Need both coherency and consistency

## Slide 60: Is Cache Coherency Sufficient?
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW $t0, addr(x) LW $t0, addr(x)
ADDIU $t0, $t0, 1 ADDIU $t0, $t0, 1
SW $t0, addr(x) SW $t0, addr(x) } }
Very expensive and difficult to maintain consistency
Notes: Is cache coherence enough? Maybe?
read (1) 40 read (3) 40
Inc (2) 41 inc (4) 41
Write (5) 41 write (6) 41
second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 61: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory (e.g. ATS, BTS; x86)
  Or an atomic pair of instructions (e.g. LL and SC; MIPS)

## Slide 62: Synchronization in MIPS
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: MOVE $t0,$s4 ;copy exchange value
  LL $t1,0($s1) ;load linked
  SC $t0,0($s1) ;store conditional
  BEQZ $t0,try ;branch store fails
  MOVE $s4,$t1 ;put load value in $s4
Any time a processor intervenes and modifies the value in memory between the LL and SC instruction, SC returns 0 in $t0, causing the code to try again