Spring 2005 Newsletter

Welcome to Cornell RoboCup’s first annual Newsletter! This year has gotten off to a spectacular start with a new team that is thirsty for victory.  We are extremely excited to announce our recent qualification for the 2005 RoboCup tournament to be hosted this year in Osaka, Japan.

Our innovations this year have built on last year’s work with Windows CE and PC104 based robots.  We are aiming to design more robust, compact, and powerful robots. The team finished building the first prototype in mid- February and we are currently doing extensive testing on various parts including the dribbler, kicker, and drivetrain.  Furthermore, we are currently in the process of manufacturing 12 more robots constituting the remainder of the soccer club.

Following, you will find several brief summaries composed by this year’s team leaders.  It highlights some important features our robots will be featuring at this year’s competition.

Mechanical (The Brawn)

The structure of this year’s robot includes the best of the 2003 and 2004 designs accompanied by a few new twists. For example, Pat Conrad is using an internal gear arrangement to reduce the gear jamming experienced at last year’s competition while simultaneously increasing the gear ratio.

Mi Zhou's is working on a dribbler that uses a simpler motor mount and sports a multi-piece frame which simplifies machining – this should bring a smile to the face of the people who know what machining the dribbler frame is like.

Kicking has seen Tom Hanselman introduce linear bearings, guide rails, and possibly a curved face to improve passing and scoring accuracy. Look out; Ronaldo has just joined Cornell RoboCup.

We have given a position for chassis and hat design to Umang Khanna this year. As a key troubleshooter for the team she has laid out a highly serviceable electronic interface which has reduced our connectors by over 30 percent, and made it possible to troubleshoot boards without removing them.

This year’s robot is incredibly dense due to the 3 element PC104 stack (Digital board, PC104, 802.11a) plus an analog board. The PC104 stack pivots around the top dribbler bar so that we can have separate digital and analog boards, but be able to run and probe them while they are connected.

Helen Ng is the most recent team member.  She has been helping out with integration issues, parts manufacturing, and business activities.

~Mike Sherback

(Mech. Team Leader)

Front view:  shows dribbler, kicker, and drive.

Electrical (The Nervous System)

The basis of this year’s system will be a PC104-MCU-FPGA link. Previous technology to be carried over to this year includes an RF wireless link which sends vision data to the robots. This data will be processed by the PC104 onboard computer running local control.  The 802.11a will be used by the robots to communicate amongst themselves. The MCU will act as a hub between the PC104 and the rest of the system by forwarding commands and compiling sensor data. The FPGA will handle the brushless motor commutations. With a redesigned motor drive circuitry layout, we generate almost no heat on the analog board. Finally, to ensure that we do not overdraw and damage the Lithium Polymer batteries, we have implemented an auto-shutdown circuit which will kill power to the robot if the battery voltage drops too low.

The team members this year are Jeff Johnson (FPGA), Steven Keiper (PC104/Wireless), Chris Lehmann (MCU), Steve Lowe (Motors/Kicker), and Mike McCabe (Onboard Sensors).

~Mike McCabe

(Electrical Team Leader)

Computer Science (The Brain)

This year’s software architecture design focuses on implementing a universal system with reusable components for basic

learning which will help avoid rebuilding completely new systems in the future. Our primary goal is to gradually shift

centralized intelligence to distributed

Side view: Shows the compact yet dense design with the new electrical design.

intelligence.  This will enable the robots while in play to self-tune and adjust to changing field conditions.

Our global vision system will use two Basler A301fc cameras to provide 658x492 pixels in Bayer pattern at a maximum frame rate of 80Hz each. The vision system is designed to work under varying lighting conditions and in the presence of shadows on the field. It is also improved to mitigate the effects of latency in the system.

For local sensing, each robot is equipped with an IR sensor that triggers when the ball is in front of the dribbler. This year, we are investigating the use of a ball vision camera which would detect the exact position of the ball with respect to the dribbler.

~Gene Byrnes

(C.S. Team Leader)

Huge strides have been made with the completion of this year’s prototype.  From this point forward we are performing various testing and debugging procedures.  At the current rate Cornell RoboCup hopes to return this summer with another World Championship.