## Slide 1: Caches
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See P&H 5.2 (writes), 5.3, 5.5

## Slide 2: Announcements
HW3 available due next Tuesday
  HW3 has been updated. Use updated version.
  Work with alone
  Be responsible with new knowledge
Use your resources
  FAQ, class notes, book, Sections, office hours, newsgroup, CSUGLab
Next six weeks
  Two homeworks and two projects
  Optional prelim1 has been graded
  Prelim2 will be Thursday, April 28th
  PA4 will be final project (no final exam)

## Slide 3: Goals for Today: caches
Caches vs memory vs tertiary storage
  Tradeoffs: big & slow vs small & fast
    Best of both worlds
  working set: 90/10 rule
  How to predict future: temporal & spacial locality
Cache organization, parameters and tradeoffs associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty

## Slide 4: Cache Performance
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle per word, plus 3 cycle per consecutive word
Performance depends on:
Access time for hit, miss penalty, hit rate
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 5: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 6: Avoiding Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Other Misses
  Buy more SRAM
  Use a more flexible cache design
Notes: fix program, prefetching = special instructions, prediction in CPU, prediction in cache controller, …

## Slide 7
Bigger cache doesn’t always help…
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, …
Hit rate with four direct-mapped 2-byte cache lines?
With eight 2-byte cache lines?
With four 4-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
Notes: What program is this? Memcpy

## Slide 8: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted…
  … because some other access with the same index
  Conflict Miss
… because the cache is too small
  i.e. the working set of program is larger than the cache
  Capacity Miss
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 9: Avoiding Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Capacity Misses
  Buy more SRAM
Conflict Misses
  Use a more flexible cache design

## Slide 10: Three common designs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Asociative

## Slide 11: A Simple Fully Associative Cache
Memory
Fully Associative Cache
Processor
lb $1  M[ 1 ]
lb $2  M[ 13 ]
lb $3  M[ 0 ]
lb $3  M[ 6 ]
lb $2  M[ 5 ]
lb $2  M[ 6 ]
lb $2  M[ 10 ]
lb $2  M[ 12 ]
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
A =
Notes: 4 cache lines
line size = 2 words
offset is 1 bit
tag is 4 bits

## Slide 12: Fully Associative Cache (Reading)
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 13: Fully Associative Cache Size
m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Tag Offset
, 2n cache lines
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 26 bit tag  27*512 = 24*512+1536 = 1536bytes + 192 bytes = 1728bytes overhead

## Slide 14
Fully-associative reduces conflict misses...
… assuming good eviction strategy
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, 20, …
Hit rate with four fully-associative 2-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
Notes: No temporal locality, but lots of spacial locality  larger blocks would help

## Slide 15
… but large block size can still reduce hit rate
vector add trace: 0, 100, 200, 1, 101, 201, 2, 202, …
Hit rate with four fully-associative 2-byte cache lines?
With two fully-associative 4-byte cache lines?

## Slide 16: Misses
Cache misses: classification
Cold (aka Compulsory)
  The line is being referenced for the first time
Capacity
  The line was evicted because the cache was too small
  i.e. the working set of program is larger than the cache
Conflict
  The line was evicted because of another access whose index conflicted
Notes: conflict can’t happen with fully associative
block size influences cold misses

## Slide 17: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  big & fast memory built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty
Next up: other designs; writing to caches

## Slide 18: Cache Tradeoffs
Direct Mapped
+ Smaller
+ Less
+ Less
+ Faster
+ Less
+ Very
– Lots
– Low
– Common
Fully Associative
Larger –
More –
More –
Slower –
More –
Not Very –
Zero +
High +
?
Tag Size
SRAM Overhead
Controller Logic
Speed
Price
Scalability
# of conflict misses
Hit rate
Pathological Cases?

## Slide 19
Set Associative Caches

## Slide 20: Compromise
Set Associative Cache
  Each block number mapped to a single cache line set index
  Within the set, block can go in any line
set 0 | line 0 |  | 
 | line 1 |  | 
 | line 2 |  | 
set 1 | line 3 |  | 
 | line 4 |  | 
 | line 5 |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
0x00004c | 
Notes: Set Associative Cache
Like direct mapped cache
  Only need to check a few lines for each access… so: fast, scalable, low overhead
Like a fully associative cache
  Several places each block can go… so: fewer conflict misses, higher hit rate

## Slide 21: 2-Way Set Associative Cache
Set Associative Cache
Like direct mapped cache
  Only need to check a few lines for each access… so: fast, scalable, low overhead
Like a fully associative cache
  Several places each block can go… so: fewer conflict misses, higher hit rate

## Slide 22: 3-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 23: A Simple 2-Way Set Associative Cache
Memory
2-Way Set Associative Cache
Processor
lb $1  M[ 1 ]
lb $2  M[ 13 ]
lb $3  M[ 0 ]
lb $3  M[ 6 ]
lb $2  M[ 5 ]
lb $2  M[ 6 ]
lb $2  M[ 10 ]
lb $2  M[ 12 ]
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
A =
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Notes: 4 cache lines, but 2 sets
line size = 2 words
offset is 1 bit
index is 1 bits
tag is 3 bits

## Slide 24: Comparing Caches
Memory
Fully Associative
Processor
lb $1  M[ 1 ]
lb $2  M[ 8 ]
lb $3  M[ 1 ]
lb $3  M[ 8 ]
lb $2  M[ 1 ]
lb $2  M[ 16 ]
lb $2  M[ 1 ]
lb $2  M[ 8 ]
$1
$2
$3
$4
A Pathological Case
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Direct Mapped
2-Way Set Associative

## Slide 25: Remaining Issues
To Do:
  Evicting cache lines
  Picking cache parameters
  Writing using the cache

## Slide 26: Eviction
Q: Which line should we evict to make room?
For direct-mapped?
A: no choice, must evict the indexed line
For associative caches?
FIFO: oldest line (timestamp per line)
LRU: least recently used (ts per line)
LFU: (need a counter per line)
MRU: most recently used (?!) (ts per line)
RR: round-robin (need a finger per set)
RAND: random (free!)
Belady’s: optimal (need time travel)

## Slide 27
Cache Parameters

## Slide 28: Performance Comparison
cache size →
miss rate →
direct mapped, 2-way, 8-way, fully associative
direct mapped
Notes: Q: which one is which?
Q: where are cold misses? capacity misses? conflict misses?

## Slide 29: Cache Design
Need to determine parameters:
  Cache size
  Block size (aka line size)
  Number of ways of set-associativity (1, N, )
  Eviction policy
  Number of levels of caching, parameters for each
  Separate I-cache from D-cache, or Unified cache
  Prefetching policies / instructions
  Write policy

## Slide 30: A Real Example
> dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 31: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 32: Basic Cache Organization
Q: How to decide block size?
A: Try it and see
But: depends on cache size, workload, associativity, …
Experimental approach!

## Slide 33: Experimental Results
Notes: For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and miss penalty (time to fetch block) is larger

## Slide 34: Tradeoffs
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 35
Writing with Caches

## Slide 36: Cached Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 37: Write Allocation Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is not in the cache…
Write-Allocate
  allocate a cache line for new data (and maybe write-through)
No-Write-Allocate
  ignore cache, just go to main memory

## Slide 38: A Simple 2-Way Set Associative Cache
Memory
Direct Mapped Cache + Write-through + Write-allocate
Processor
lb $1  M[ 1 ]
lb $2  M[ 7 ]
sb $2  M[ 0 ]
sb $1  M[ 5 ]
lb $2  M[ 9 ]
sb $1  M[ 5 ]
sb $1  M[ 0 ]
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181

## Slide 39: How Many Memory References?
Write-through performance
Each miss (read or write) reads a block from mem
  5 misses  10 mem reads
Each store writes an item to mem
  4 mem writes
Evictions don’t need to write to mem
  no need for dirty bit

## Slide 40: A Simple 2-Way Set Associative Cache
Memory
Direct Mapped Cache + Write-back + Write-allocate
Processor
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
D
lb $1  M[ 1 ]
lb $2  M[ 7 ]
sb $2  M[ 0 ]
sb $1  M[ 5 ]
lb $2  M[ 9 ]
sb $1  M[ 5 ]
sb $1  M[ 0 ]

## Slide 41: How Many Memory References?
Write-back performance
Each miss (read or write) reads a block from mem
  5 misses  10 mem reads
Some evictions write a block to mem
  1 dirty eviction  2 mem writes
  (+ 2 dirty evictions later  +4 mem writes)
  need a dirty bit

## Slide 42: Write-Back Meta-Data
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 43: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 44: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 45: Performance Tradeoffs
Q: Hit time: write-through vs. write-back?
A: Write-through slower on writes.
Q: Miss penalty: write-through vs. write-back?
A: Write-back slower on evictions.

## Slide 46: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: What does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 47: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: What does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 48: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 49: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
May need to snoop on other CPU’s cache activity
Invalidate cache line when other CPU writes
Flush write-back caches before other CPU reads
Or the reverse: Before writing/reading…
Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net

## Slide 50
Cache Conscious Programming

## Slide 51: Cache Conscious Programming
Every access is a cache miss!
(unless entire matrix can fit in cache)
// H = 12, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];
1 | 11 | 21 |  |  |  |  |  |  | 
 |  | 2 | 12 | 22 |  |  |  |  | 
 |  |  |  | 3 | 13 | 23 |  |  | 
 |  |  |  |  |  | 4 | 14 | 24 | 
 |  |  |  |  |  |  |  | 5 | 15
25 |  |  |  |  |  |  |  |  | 
6 | 16 | 26 |  |  |  |  |  |  | 
 |  | 7 | 17 | … |  |  |  |  | 
 |  |  |  | 8 | 18 |  |  |  | 
 |  |  |  |  |  | 9 | 19 |  | 
 |  |  |  |  |  |  |  | 10 | 20

## Slide 52: Cache Conscious Programming
Block size = 4  75% hit rate
Block size = 8  87.5% hit rate
Block size = 16  93.75% hit rate
And you can easily prefetch to warm the cache.
// H = 12, W = 10
int A[H][W];
for(y=0; y < H; y++)
for(x=0; x < W; x++)
sum += A[y][x];
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
11 | 12 | 13 | … |  |  |  |  |  | 

## Slide 53: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  (big & fast) built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate

## Slide 54: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
Multi-core / Multi-Processor is complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right