## Slide 1: Arithmetic
See: P&H Chapter 3.1-3, C.5-6

## Slide 2: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Cin

## Slide 3: Arithmetic with Negative Numbers
Addition with negatives:
  pos + pos  add magnitudes, result positive
  neg + neg  add magnitudes, result negative
  pos + neg  subtract smaller magnitude, keep sign of bigger magnitude

## Slide 4: First Attempt: Sign/Magnitude Representation
First Attempt: Sign/Magnitude Representation
1 bit for sign (0=positive, 1=negative)
N-1 bits for magnitude
Notes: problems? two zeros, circuit still complicated

## Slide 5: Two’s Complement Representation
Better: Two’s Complement Representation
Leading 1’s for negative numbers
To negate any number:
    complement all the bits
    then add 1
Notes: add 1 and *discard carry*

## Slide 6: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives
(two’s complement: flip then add 1):
~0 = 1111 -0 = 0000
~1 = 1110 -1 = 1111
~2 = 1101 -2 = 1110
~3 = 1100 -3 = 1101
~4 = 1011 -4 = 1100
~5 = 1010 -5 = 1011
~3 = 1001 -6 = 1010
~7 = 1000 -7 = 1001
~8 = 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 7: Two’s Complement Facts
Signed two’s complement
  Negative numbers have leading 1’s
  zero is unique: +0 = - 0
  wraps from largest positive to largest negative
N bits can be used to represent
  unsigned:
    eg: 8 bits 
  signed (two’s complement):
    ex: 8 bits 

## Slide 8: Sign Extension & Truncation
Extending to larger size
Truncate to smaller size
  Copy the leftmost bit into new leading bits
    For positive number, put 0’s in new leading bits
    For negative number, put 1’s in new leading bits
  Drop leading bits so long as sign doesn’t change

## Slide 9: Two’s Complement Addition
Addition with two’s complement signed numbers
Perform addition as usual, regardless of sign (it just works)
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)

## Slide 10: Diversion: 10’s Complement
How does that work?
-154 +283

## Slide 11: Overflow
Overflow
  adding a negative and a positive?
  adding two positives?
  adding two negatives?
Rule of thumb:
Overflow happened iff carry into msb != carry out of msb

## Slide 12: Two’s Complement Adder
Two’s Complement Adder with overflow detection
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
over flow
0

## Slide 13: Binary Subtraction
Two’s Complement Subtraction
Lazy approach
A – B = A + (-B) = A + (B + 1)
R0
R1
R2
R3
over flow
1
A0
B0
A1
B1
A2
B2
A3
B3
Q: What if (-B) overflows?
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 14: A Calculator
decoder
8
8
S 0=add
1=sub
A
B
8

## Slide 15: A Calculator
0
1
adder
mux
mux
decoder
8
8
8
8
8
S
A
B
8
Notes: red herring? constants into mux

## Slide 16: Efficiency and Generality
  Is this design fast enough?
  Can we generalize to 32 bits? 64? more?
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
C0

## Slide 17: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 18: 4-bit Ripple Carry Adder
A3
B3
R3
C4
A1
B1
R1
A2
B2
R2
A0
B0
C0
R0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb