## Slide 1: CS 3410: Computer System Organization and Programming
Hakim Weatherspoon
Spring 2011
Computer Science
Cornell University
CS 3410: Systems Programming

## Slide 2: Information
Instructor: Hakim Weatherspoon
(hweather@cs.cornell.edu)
Tu/Th 1:25-2:40
Phillips 101

## Slide 3: Course Objective
Bridge the gap between hardware and software
  How a processor works
  How a computer is organized
Establish a foundation for building higher-level applications
  How to understand program performance
  How to understand where the world is going

## Slide 4: Who am I?
Prof. Hakim Weatherspoon
  (Hakim means Doctor, wise, or prof. in Arabic)
  Background in Education
    Undergraduate University of Washington
      Played Varsity Football
        Some teammates collectively make $100’s of millions
        I teach!!!
    Graduate University of California, Berkeley
      Some class mates collectively make $100’s of millions
      I teach!!!
  Background in Operating Systems
    Peer-to-Peer Storage
      Antiquity project - Secure wide-area distributed system
      OceanStore project – Store your data for 1000 years
    Network overlays
      Bamboo and Tapestry – Find your data around globe
    Tiny OS
      Early adopter in 1999, but ultimately chose P2P direction

## Slide 5: Who am I?
Cloud computing/storage
  Optimizing a global network of data centers
  Cornell Ntional λ-Rail Rings testbed
  Software Defined Network Adapter
  Energy: KyotoFS/SMFS
Antiquity: built a global-scale storage system

## Slide 6: Course Staff
cs3410-staff-l@cs.cornell.edu
TAs
  Han Wang (hwang@cs.cornell.edu)
  Bo Peng (bpeng@cs.cornell.edu)
  Jun Erh (je96@cornell.edu)
Undergraduate consultants
  Ansu Abraham (aaa98@cornell.edu)
  Ethan Kao (ek382@cornell.edu)
  Peter Tseng (pht24@cornell.edu)
  Jiaqi Zhai (jz392@cornell.edu)
  Administrative Assistant:
  Angela Downing (angela@cs.cornell.edu)

## Slide 7: Book
Computer Organization and Design
  The Hardware/Software Interface
David Patterson, John Hennessy
  Get the 4th Edition

## Slide 8: Grading
4 Programming Assignments (35-45%)
  Work in groups of two
4-5 Homeworks Assignments (20-25%)
  Work alone
2 prelims (30-40%)
Discretionary (5%)

## Slide 9: Grading
Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 10: Administrivia
http://www.cs.cornell.edu/courses/cs3410/2011sp
  Office Hours / Consulting Hours
  Lecture slides & schedule
  Logisim
  CSUG lab access (esp. second half of course)
Sections
T 2:55 – 4:10pm Hollister 372 W 3:35 – 4:50pm Upson 215 R 11:40 – 12:55pm Hollister 372 R 2:55 – 4:10pm Hollister 368
F 2:55 – 4:10pm Phillips 213 TBD
  Will cover new material
  Next week: intro to logisim

## Slide 11: Communication
Email
  cs3410-staff-l@cs.cornell.edu
  The email alias goes to me and the TAs, not to whole class
Assignments
  CMS: http://cms.csuglab.cornell.edu
Newsgroup
  cornell.class.cs3410
  For students

## Slide 12: Sections & Projects
Sections start next week
  But can go this week to find a project partner
Projects will be done in two-person teams
  We will pair you up if you don’t have a preferred partner
  Start early, time management is key
  Manage the team effort

## Slide 13: Academic Integrity
All submitted work must be your own
  OK to study together, but do not share soln’s
  Cite your sources
Project groups submit joint work
  Same rules apply to projects at the group level
  Cannot use of someone else’s soln
Closed-book exams, no calculators
  Stressed? Tempted? Lost?
    Come see me before due date!
Plagiarism in any form will not be tolerated

## Slide 14: Computer System Organization

## Slide 15: Compilers & Assemblers
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
language
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
MIPS
machine
language
assembler
Notes: 32 bits, 4 bytes

## Slide 16: Compilers
MIPS assembly language
C
compiler
sum3: lw r9, 0(r5) lw r10, 4(r5)
lw r11, 8(r5) add r3, r9, r10 add r3, r3, r11 jr r31
main: ... addi r5, r0, 1000 jal sum3 sw r3, 12(r5) ...
int sum3(int v[]) { return v[0] + v[1] + v[2]; } main() { ... int v[] = ...; int a = sum3(v); v[3] = a; ... }

## Slide 17: Assemblers
MIPS machine language
assembler
10001100101010010000000000000000 10001100101010100000000000000100 10001100101010110000000000001000
00000001001010100001100000100000
00000000011010110001100000100000
00000011111000000000000000001000
... ... ... 00100000000001010000001111101000
00001100000100000000000000000000
10101100101000110000000000001100 ...
MIPS assembly language
sum3: lw r9, 0(r5) lw r10, 4(r5)
lw r11, 8(r5) add r3, r9, r10 add r3, r3, r11 jr r31
main: ... addi r5, r0, 1000 jal sum3 sw r3, 12(r5) ...

## Slide 18: Computer System Organization
Computer System =
?
Input + Output + Memory + Datapath + Control
CPU
Registers
Network
Video
bus
Memory
bus
Disk
USB
Audio
Keyboard
Mouse
Serial

## Slide 19: Instruction Set Architecture
ISA
  abstract interface between hardware and the lowest level software
  user portion of the instruction set plus the operating system interfaces used by application programmers

## Slide 20: Transistors and Gates
in
out
+
gnd
In | Out
0 | 1
1 | 0
Truth table

## Slide 21: Logic and State
a
b
1
c
d
2
3
4
o1
o0
o1
o2
S
R
Q
Q

## Slide 22: A Calculator
0
1
adder
mux
mux
reg
reg
led-dec
8
8
8
8
8
add/sub select
…
…
doit

## Slide 23: Basic Computer System
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  von Neumann architecture: combined inst and data
A bus connects the two
regs
bus
processor
memory
01010000
10010100
…
addr, data,
r/w

## Slide 24: Simple Processor
memory
inst
32
pc
2
00
new pc
calculation
register file
control
5 5 5
alu
00: addi r5, r0, 10
04: muli r5, r5, 2
08: addi r5, r5, 15

## Slide 25: Inside the Processor
AMD Barcelona: 4 processor cores
Figure from Patterson & Hennesssy, Computer Organization and Design, 4th Edition

## Slide 26: Overview
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Firmware
Memory
system
Datapath & Control
Notes: For class handout

## Slide 27: MIPS R3000 ISA
Instruction Categories
  Load/Store
  Computational
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
Registers

## Slide 28: Calling Conventions
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
addiu sp,sp,-4
sw $31, 0(sp)
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
lw $31, 0(sp)
addiu sp,sp,4
jr $31

## Slide 29: Data Layout
sp
arguments
return address
local variables
saved regs
arguments
saved regs
return address
blue() {
pink(0,1,2,3,4,5);
}
pink() {
orange(10,11,12,13,14);
}
local variables

## Slide 30: Buffer Overflows
sp
arguments
return address
local variables
saved regs
arguments
saved regs
return address
blue() {
pink(0,1,2,3,4,5);
}
pink() {
orange(10,11,12,13,14);
}
orange() {
char buf[100];
gets(buf); // read string, no check!
}
local variables

## Slide 31: Parallel Processing
Spin Locks
Shared memory, multiple cores
Etc.

## Slide 32: Applications
Everything these days!
  Phones, cars, televisions, games, computers,…

## Slide 33: Why should you care?
Bridge the gap between hardware and software
  How a processor works
  How a computer is organized
Establish a foundation for building higher-level applications
  How to understand program performance
  How to understand where the world is going

## Slide 34: Example: Can answer the question…
A: for i = 0 to 99
  for j = 0 to 999
    A[i][j] = complexComputation ()
B: for j = 0 to 999
  for i = 0 to 99
    A[i][j] = complexComputation ()
Why is B 15 times slower than A?

## Slide 35: Example 2: Moore's Law
The number of transistors integrated on a single die will double every 24 months... – Gordon Moore, Intel co-founder, 1965
Amazingly Visionary
1971 – 2300 transistors – 1MHz – 4004
1990 – 1M transistors – 50MHz – i486
2001 – 42M transistors – 2GHz – Xeon
2004 – 55M transistors – 3GHz – P4
2007 – 290M transistors – 3GHz – Core 2 Duo
2009 – 731M transistors – 2GHz – Nehalem
Notes: Complexity is *the* issue.

## Slide 36: Example 3: New Devices
Berkeley mote
NVidia GPU
Xilinx FPGA
millions

## Slide 37: Covered in this course
I/O system
Instr. Set Proc.
Compiler
Operating
System
Application
Digital Design
Circuit Design
Instruction Set
Architecture
Firmware
Memory
system
Datapath & Control
Notes: For class handout

## Slide 38: Nuts and Bolts: Switches, Transistors, Gates

## Slide 39: A switch
A switch is a simple device that can act as a conductor or isolator
Can be used for amazing things…

## Slide 40: Switches
Either (OR)
Both (AND)
+
-
-
But requires mechanical force

## Slide 41: Transistors
Solid-state switch
  The most amazing invention of the 1900s
PNP and NPN
base
collector
emitter
N
P
P
collector
emitter
-
+
PNP
base
base
collector
P
N
N
emitter
+
-
NPN

## Slide 42: NPN Transistors
base
collector
P
N
N
emitter
+
-
NPN
Semi-conductor
Connect E to C when base = 1
E
C
B
Notes: Silicon doped with impurity makes it n-type or p-type (holes)
NPN is most common, since electrons move freely.

## Slide 43: P and N Transistors
NPN Transistor
Connect E to C when base = 1
PNP Transistor
Connect E to C when base = 0
E
C
E
C
B
B

## Slide 44: Then and Now
The first transistor
  on a workbench at AT&T Bell Labs in 1947
An Intel Nehalem
  731 million transistors

## Slide 45: Inverter
In | Out
0 | 1
1 | 0
Function: NOT
Called an inverter
Symbol:
Useful for taking the inverse of an input
CMOS: complementary-symmetry metal–oxide–semiconductor
in
out
Truth table
in
out

## Slide 46: NAND Gate
A | B | out
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
Function: NAND
Symbol:
b
a
out

## Slide 47: NOR Gate
a
out
+Vdd
Vss
b
A | B | out
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
Function: NOR
Symbol:
b
a
out

## Slide 48: Building Functions
NOT:
AND:
OR:
NAND and NOR are universal
  Can implement any function with NAND or just NOR gates
  useful for manufacturing

## Slide 49: Reflect
Why take this course?
  Basic knowledge needed for all other areas of CS:
    operating systems, compilers, ...
  Levels are not independent
    hardware design ↔ software design ↔ performance
  Crossing boundaries is hard but important
    device drivers
  Good design techniques
    abstraction, layering, pipelining, parallel vs. serial, ...
  Understand where the world is going