## Slide 1: Gates and Logic
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell Universty
See: P&H Appendix C.0, C.1, C.2

## Slide 2: Gates and Logic
See: P&H Appendix C.0, C.1, C.2
http://www.xkcd.com/74/

## Slide 3: Announcements
Class newsgroup created
  Posted on web-page
  Use it for partner finding
First assignment is to find partners
Sections start next week
  Use this weeks section to find a partner
Note about class
  No Verilog or VHDL
  Clickers not required, but will use them from time-to-time

## Slide 4: A switch
Acts as a conductor or insulator
Can be used to build amazing things…

## Slide 5: Better Switch
One current controls another (larger) current
Static Power:
  Keeps consuming power when in the ON state
Dynamic Power:
  Jump in power consumption when switching

## Slide 6: Atoms
e
N
P
N
P
N
P
N
P
N
P
N
P
N
P
e
e
e
e
e
e
e
e
e
e
e
e
e
hole

## Slide 7: Elements
B
e
e
e
e
Si
e
e
e
Silicon
Phosphorus
Boron
e
P
e
e
e
e

## Slide 8: Silicon Crystal
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
e
Si
e
e
e
Silicon

## Slide 9: Phosphorus Doping
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
N-Type: Silicon + Phosphorus
e
P
e
e
e
e
e
P
e
e
e
e
e
P
e
e
e
e
e
P
e
e
e
e
Notes: neutral -> conductor
high voltage -> insulator

## Slide 10: Boron Doping
B
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
P-Type: Silicon + Boron
B
e
e
e
B
e
e
e
B
e
e
e
Notes: neutral -> conductor
low voltage -> insulator

## Slide 11: Semiconductors
Insulator
n-type (Si+Phosphorus) has mobile electrons:
p-type (Si+Boron)
has mobile holes:
low voltage (mobile electrons) → conductor high voltage (depleted)
→ insulator
low voltage (depleted) → insulator high voltage (mobile holes) → conductor

## Slide 12: Bipolar Junction
P-Type
N-Type
e
e
e
e
e
e
e
e
e
e
e
e
e
e
low v → conductor high v → insulator
low v → insulator high v → conductor

## Slide 13: Reverse Bias
P-Type
N-Type
e
e
e
e
e
e
e
e
e
e
e
e
e
+
–
low v → conductor high v → insulator
low v → insulator high v → conductor
e

## Slide 14: Forward Bias
P-Type
N-Type
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
e
–
+
low v → conductor high v → insulator
low v → insulator high v → conductor

## Slide 15: Diodes
p-type
n-type
PN Junction “Diode”
Conventions: vdd = vcc = +1.2v = +5v = hi vss = vee = 0v = gnd

## Slide 16: PNP Junction
p-type
p-type
n-type

## Slide 17: Bipolar Junction Transistors
Solid-state switch: The most amazing invention of the 1900s
Emitter = “input”, Base = “switch”, Collector = “output”
p
n
p
C
E=vdd
B
E
C
B
vdd
p
n
vss=E
C
B
C
E
B
vss
n
PNP Transistor
NPN Transistor

## Slide 18: Field Effect Transistors
P-type FET
Connect Source to Drain when Gate = lo
Drain must be vdd, or connected to source of another P-type transistor
N-type FET
Connect Source to Drain when Gate = hi
Source must be vss, or connected to drain of another N-type transistor
Drain = vdd
Source
Gate
Drain
Source = vss
Gate

## Slide 19: Multiple Transistors
In | Out
voltage
Gate delay
transistor switching time
voltage, propagation, fanout, temperature, …
CMOS design (complementary-symmetry metal–oxide–semiconductor)
  Power consumption = dynamic + leakage
in
out
Vdd
Vss
t
0v
+5v

## Slide 20: Digital Logic
In | Out
+5v | 0v
0v | +5v
voltage
in
out
Vdd
Vss
t
0v
+5v
+2v
+0.5v
In | Out
truth table
Conventions: vdd = vcc = +1.2v = +5v = hi = true = 1 vss = vee = 0v = gnd = false = 0

## Slide 21: NOT Gate (Inverter)
In | Out
0 | 1
1 | 0
in
out
Truth table
Function: NOT
Symbol:
in
out
Vdd
Vss

## Slide 22: NAND Gate
A | B | out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
b
a
out
A
out
Vdd
Vss
B
B
A
Vdd
Function: NAND
Symbol:

## Slide 23: NOR Gate
b
a
out
A
out
Vss
Vdd
B
B
A
Vss
Function: NOR
Symbol:
A | B | out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 24: Building Functions
AND:
OR:
NOT:

## Slide 25: Universal Gates
NAND is universal (so is NOR)
  Can implement any function with just NAND gates
    De Morgan’s laws are helpful (pushing bubbles)
  useful for manufacturing
E.g.: XOR (A, B) = A or B but not both (“exclusive or”)
Proof: ?

## Slide 26: Logic Equations
Some notation:
constants: true = 1, false = 0
variables: a, b, out, …
operators:
  AND(a, b) = a b = a & b = a  b
OR(a, b) = a + b = a | b = a  b
NOT(a) = ā = !a = a

## Slide 27: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a 0 =
  a 1 =
  a ā =
  (a + b) =
  (a b) =
  a + a b =
  a(b+c) =
  a(b+c) =
  a
  1
  1
  0
  a
  0
  a b
  a + b
  a
  ab + ac
  a + bc

## Slide 28: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 29: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
 |  |  | a+b | a+c | LHS |  | 
 |  |  | 0 | 0 | 0 |  | 
 |  |  | 0 | 1 | 0 |  | 
 |  |  | 1 | 0 | 0 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  |  |  |  | bc | RHS
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 1 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 1 | 1
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 31: Logic Minimization
A common problem is how to implement a desired function most efficiently
One can derive the equation from the truth table
How does one find the most efficient equation?
  Manipulate algebraically until satisfied
  Use Karnaugh maps (or K maps)
a | b | c | minterm
0 | 0 | 0 | abc
0 | 0 | 1 | abc
0 | 1 | 0 | abc
0 | 1 | 1 | abc
1 | 0 | 0 | abc
1 | 0 | 1 | abc
1 | 1 | 0 | abc
1 | 1 | 1 | abc
for all outputs
that are 1,
take the corresponding minterm
Obtain the result in
“sum of products” form

## Slide 32: Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d
0

## Slide 33: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build a truth table
  = abd + abd + a bd + a b d
  = ad + bd
a
b
d
0

## Slide 34: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Draw the circuit
  out = ad + bd
a
b
d
0
d
out
b
a

## Slide 35: Logic Gates
One can buy gates separately
  ex. 74xxx series of integrated circuits
  cost ~$1 per chip, mostly for packaging and testing
Cumbersome, but possible to build devices using gates put together manually

## Slide 36: Integrated Circuits
Or one can manufacture a complete design using a custom mask
Intel Nehalem has approximately 731 million transistors

## Slide 37: Voting machine
Build something interesting
A voting machine
Assume:
  A vote is recorded on a piece of paper,
  by punching out a hole,
  there are at most 7 choices
  we will not worry about “hanging chads” or “invalids”

## Slide 38: Voting machine
For now, let’s just display the numerical identifier to the ballot supervisor
  we won’t do counting yet, just decoding
  we can use four photo-sensitive transistors to find out which hole is punched out
A photo-sensitive transistor detects the presence of light
Photo-sensitive material triggers the gate

## Slide 39: Ballot Reading
  Input: paper with a hole in it
  Out: number the ballot supervisor can record
Ballots
The 3410 vote recording
machine

## Slide 40: Encoders
N sensors in a row
Want to distinguish which of the N sensors has fired
Want to represent the firing sensor number in compact form
  N might be large
  Only one wire is on at any time
  Silly to route N wires everywhere, better to encode in log N wires
a
b
o0
1
c
d
2
3
4
o1
A 3-bit encoder
(7-to-3)
(5 inputs shown)
o2
e
5
.
.

## Slide 41: Number Representations
Decimal numbers are written in base 10
  3 x 101 + 7 x 100 = 37
Just as easily use other bases
  Base 2 - “Binary”
  Base 8 - “Octal”
  Base 16 – “Hexadecimal”
37
101 100

## Slide 42: Number Representations
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  Sanity check with 37 and base 10
3
101 100
7

## Slide 43: Binary Representation
Check 37 and base 2
37 = 32 + 4 + 1
64
20
21
22
23
24
25
26
32
16
8
4
2
1
1
0
1
0
0
1
0
Notes: 1 + 2 x (0 + 2 x 9)
= 1 + 2 x 0 + 4 x (1 + 2 x 4)
= 1 + 2 x 0 + 4 x 1 + 8 x (0 + 2 x 2)
= 1 + 2 x 0 + 4 x 1 + 8 x 0 + 16 x (0 + 2 x 1)
= 1 + 2 x 0 + 4 x 1 + 8 x 0 + 16 x 0 + 32 x 1

## Slide 44: Hexadecimal Representation
37 decimal = (25)16
Convention
  Base 16 is written with a leading 0x
  37 = 0x25
Need extra digits!
  0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
Binary to hexadecimal is easy
  Divide into groups of 4, translate groupwise into hex digits
25
161 160

## Slide 45: Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  | o2 | o1 | o0
0 | 0 | 0 | 0 |  | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 0 | 0 | 1
0 | 1 | 0 | 0 |  | 0 | 1 | 0
0 | 0 | 1 | 0 |  | 0 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0
o0
o1
o2
o2 = abcd
o1 = abcd + abcd
o0 = abcd + abcd

## Slide 46: Ballot Reading
Ok, we built first half of the machine
Need to display the result
Ballots
The 3410 voting
machine

## Slide 47: 7-Segment LED Decoder
4 inputs encoded in binary
8 outputs, each driving an independent, rectangular LED
Can display numbers
Just a simple logic circuit
Write the truth table

## Slide 48: 7-Segment LED Decoder
4 inputs encoded in binary
8 outputs, each driving an independent, rectangular LED
Can display numbers
0
1
0
0

## Slide 49: 7-Segment LED Decoder
4 inputs encoded in binary
8 outputs, each driving an independent, rectangular LED
Can display numbers
0
1
1
0

## Slide 50: 7-Segment Decoder Truth Table
i3 | i2 | i1 | i0 |  | o0 | o1 | o2 | o3 | o4 | o5 | o6
0 | 0 | 0 | 0 |  | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 |  | 1 | 1 | 0 | 1 | 1 | 1 | 0
0 | 0 | 1 | 1 |  | 1 | 1 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 |  | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 |  | 0 | 1 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 |  | 0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 |  | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 |  | 1 | 1 | 1 | 1 | 0 | 1 | 1
o0
o1
o2
o3
o4
o5
o6
Exercise: find the error(s) in this truth table

## Slide 51: 7-Segment Decoder Truth Table
i3 | i2 | i1 | i0 |  | o0 | o1 | o2 | o3 | o4 | o5 | o6
0 | 0 | 0 | 0 |  | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 |  | 1 | 1 | 0 | 1 | 1 | 1 | 0
0 | 0 | 1 | 1 |  | 1 | 1 | 0 | 1 | 0 | 1 | 1
0 | 1 | 0 | 0 |  | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 |  | 0 | 1 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 |  | 0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 |  | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 |  | 1 | 1 | 1 | 1 | 0 | 1 | 1
o0
o1
o2
o3
o4
o5
o6
Exercise: find the error(s) in this truth table

## Slide 52: Ballot Reading
Done!
Ballots
The 3410 voting
machine

## Slide 53: Summary
We can now implement any logic circuit
  Can do it efficiently, using Karnaugh maps to find the minimal terms required
  Can use either NAND or NOR gates to implement the logic circuit
  Can use P- and N-transistors to implement NAND or NOR gates