## Slide 1: Numbers & Arithmetic
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See: P&H Chapter 2.4 - 2.6, 3.2, C.5 – C.6

## Slide 2: Announcements
Make sure you are
Registered for class
Can access CMS
Have a Section you can go to
Have a project partner
Sections are on this week
HW 1 out later today
Due in one week, start early
Work alone
Use your resources
  Class notes, book, Sections, office hours, newsgroup, CSUGLab

## Slide 3: Announcements
Check online syllabus/schedule
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims: Thursday, March 11 and April 28th
Schedule is subject to change

## Slide 4: Goals for today
Review
  Circuit design (e.g. voting machine)
  Number representations
  Building blocks (encoders, decoders, multiplexors)
Binary Operations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Subtraction (two’s compliment)
  Performance

## Slide 5: Logic Minimization
How to implement a desired function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 6: Logic Minimization
How to implement a desired function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
sum of products:
OR of all minterms where out=1
corollary: any combinational circuit can be implemented in two levels of logic (ignoring inverters)
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c

## Slide 7: Karnaugh Maps
        How does one find the most efficient equation?
          Manipulate algebraically until…?
          Use Karnaugh maps (optimize visually)
          Use a software optimizer
          For large circuits
          Decomposition & reuse of building blocks

## Slide 8: Voting machine
Voting Machine!
  optical scan (thanks FL)
Assume:
  vote is recorded on paper by filling a circle
  fixed number of choices
  don’t worry about “invalids”
Al Franken
Bill Clinton
Condi Rice
Dick Cheney
Eliot Spitzer
Fred Upton
Write-in

## Slide 9: Voting Machine Components
Ballots
The 3410 optical scan
vote counter reader
machine
  Input: paper with at exactly one mark
  Datapath: process current ballot
  Output: a number the supervisor can record
  Memory & control: none for now
5 Essential Components?

## Slide 10: Input
Photo-sensitive transistor
  photons replenish gate depletion region
  can distinguish dark and light spots on paper
Use array of N sensors for voting machine input
i0
i1
i2
i3
i5
i4
i6
Vdd

## Slide 11: Output
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0

## Slide 12: Block Diagram
detect
8
N
Notes: could do big combinatorial circuit
truth table too large: 2^N rows
no possibility for re-use of components
routing N wires is expensive

## Slide 13: Encoders
N might be large
Routing wires is expensive
More efficient encoding?
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Notes: N possible inputs -> log2(N) wires to encode

## Slide 14: Number Representations
Base 10 - Decimal
Just as easily use other bases
  Base 2 - Binary
  Base 8 - Octal
  Base 16 - Hexadecimal
6 3 7
102 101 100

## Slide 15: Counting
Counting

## Slide 16: Base Conversion
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
Notes: 637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 17: Base Conversion
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
Notes: 637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 18: Base Conversion
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
Notes: 637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 19: Hexadecimal, Binary, Octal Conversions

## Slide 20: Encoder Implementation
Implementation . . .
    assume 8 choices, exactly one mark detected
i0
i1
b0
1
i2
i3
2
3
4
b1
3-bit encoder
(8-to-3)
b2
i4
5
i5
i6
i7
6
7
0
encoder
Notes: o0 = lsb
o2 = msb

## Slide 21: Ballot Reading
detect
enc
8
3
8

## Slide 22: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 23: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 

## Slide 24: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 25: Ballot Reading and Display
Ballots
The 3410 optical scan
vote counter reader
machine
detect
enc
8
3
7
7LED decode

## Slide 26: Building Blocks
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 27: Goals for today
Review
  Circuit design (e.g. voting machine)
  Number representations
  Building blocks (encoders, decoders, multiplexors)
Binary Operations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Subtraction (two’s compliment)
  Performance

## Slide 28: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
183 + 254
001110
+ 011100

## Slide 29: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
R
C

## Slide 30: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
A
B
R
Cout
Cin

## Slide 31: 4-bit Adder
4-Bit Full Adder
Adds two 4-bit numbers and carry in
Computes 4-bit result and carry out
Can be cascaded
A[4]
B[4]
R[4]
Cout
Cin

## Slide 32: 4-bit Adder
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Cin
Notes: carry-out = overflow indicates result does not fit in 4 bits

## Slide 33: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Cin

## Slide 34: Arithmetic with Negative Numbers
Addition with negatives:
  pos + pos  add magnitudes, result positive
  neg + neg  add magnitudes, result negative
  pos + neg  subtract smaller magnitude, keep sign of bigger magnitude

## Slide 35: First Attempt: Sign/Magnitude Representation
First Attempt: Sign/Magnitude Representation
1 bit for sign (0=positive, 1=negative)
N-1 bits for magnitude
Notes: problems? two zeros, circuit still complicated

## Slide 36: Two’s Complement Representation
Better: Two’s Complement Representation
Leading 1’s for negative numbers
To negate any number:
    complement all the bits
    then add 1
Notes: add 1 and *discard carry*

## Slide 37: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives
(two’s complement: flip then add 1):
~0 = 1111 -0 = 0000
~1 = 1110 -1 = 1111
~2 = 1101 -2 = 1110
~3 = 1100 -3 = 1101
~4 = 1011 -4 = 1100
~5 = 1010 -5 = 1011
~3 = 1001 -6 = 1010
~7 = 1000 -7 = 1001
~8 = 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 38: Two’s Complement Facts
Signed two’s complement
  Negative numbers have leading 1’s
  zero is unique: +0 = - 0
  wraps from largest positive to largest negative
N bits can be used to represent
  unsigned:
    eg: 8 bits 
  signed (two’s complement):
    ex: 8 bits 

## Slide 39: Sign Extension & Truncation
Extending to larger size
Truncate to smaller size
  Copy the leftmost bit into new leading bits
    For positive number, put 0’s in new leading bits
    For negative number, put 1’s in new leading bits
  Drop leading bits so long as sign doesn’t change

## Slide 40: Two’s Complement Addition
Addition with two’s complement signed numbers
Perform addition as usual, regardless of sign (it just works)
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)

## Slide 41: Diversion: 10’s Complement
How does that work?
-154 +283

## Slide 42: Overflow
Overflow
  adding a negative and a positive?
  adding two positives?
  adding two negatives?
Rule of thumb:
Overflow happened iff carry into msb != carry out of msb

## Slide 43: Two’s Complement Adder
Two’s Complement Adder with overflow detection
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
over flow
0

## Slide 44: Binary Subtraction
Two’s Complement Subtraction
Lazy approach
A – B = A + (-B) = A + (B + 1)
R0
R1
R2
R3
over flow
1
A0
B0
A1
B1
A2
B2
A3
B3
Q: What if (-B) overflows?
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 45: A Calculator
decoder
8
8
S 0=add
1=sub
A
B
8

## Slide 46: A Calculator
0
1
adder
mux
mux
decoder
8
8
8
8
8
S
A
B
8
Notes: red herring? constants into mux

## Slide 47: Efficiency and Generality
  Is this design fast enough?
  Can we generalize to 32 bits? 64? more?
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
C0

## Slide 48: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 49: 4-bit Ripple Carry Adder
A3
B3
R3
C4
A1
B1
R1
A2
B2
R2
A0
B0
C0
R0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb

## Slide 50: Summary
We can now implement any combinational (combinatorial) logic circuit
  Decompose large circuit into manageable blocks
    Encoders, Decoders, Multiplexors, Adders, ...
  Design each block
    Binary encoded numbers for compactness
  Can implement circuits using NAND or NOR gates
  Can implement gates using use P- and N-transistors
  And can add and subtract numbers (in two’s compliment)!
  Next time, state and finite state machines…