## Slide 1: State & Finite State Machines
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See P&H Appendix C.7. C.8, C.10, C.11

## Slide 2: Announcements
Make sure you are
Registered for class
Can access CMS
Have a Section you can go to
Have a project partner
Sections are on this week
HW 1 out later today
Due in one week, start early
Work alone
Use your resources
  Class notes, book, Sections, office hours, newsgroup, CSUGLab

## Slide 3: Announcements
Check online syllabus/schedule
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims: Evening of Thursday, March 10 and April 28th
Schedule is subject to change
HW1 Correction:
Hint 1: Your ALU should use your adder and left shifter as components. But, as in class, your ALU should only use a single adder component
to implement both addition and subtraction. Similarly, your ALU should use only a single left shifter component to implement all of the shift
operations. For instance, left right shifting can be accomplished by transforming the inputs and outputs to your left shifter. You
will be penalized if your final ALU circuit uses more than one adder or left shifter. Of course, always strive to make your implementation
clear, but do not duplicate components in an effort to do so.

## Slide 4: Goals for Today: Stateful Components
Until now is combinatorial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M

## Slide 5: Unstable Devices
B
A
C

## Slide 6: Bistable Devices
A
B
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 7: Bistable Devices
In stable state, A = B
How do we change the state?
A
B
A
B
1
A
B
1
0
0
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 8: SR Latch
Set-Reset (SR) Latch
Stores a value Q and its complement Q
S | R | Q | Q
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
Q
S
R
Q
Q
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire

## Slide 9: Unclocked D Latch
Data (D) Latch
D | Q | Q
0 |  | 
1 |  | 
S
R
D
Q
Q
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 10: Unclocked D Latch
Data (D) Latch
D | Q | Q
0 | 0 | 1
1 | 1 | 0
S
R
D
Q
Q
Data Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 11: D Latch with Clock
S
R
D
clk
Q
Q
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? no

## Slide 12: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge

## Slide 13: Edge-triggering
Can design circuits to change on the rising or falling edge
Trigger on rising edge = positive edge-triggered
Trigger on falling edge = negative edge-triggered
Inputs must be stable just before the triggering edge
input
clock

## Slide 14: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data is captured when clock is high
Outputs change only on falling edges
D
Q
Q
D
Q
Q
c
F
L
L
clk
D
F
Q
c
Q
Q
D
clk

## Slide 15: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 16: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg

## Slide 17: Metastability and Asynchronous Inputs
1-bit reg
Clk

## Slide 18: Metastability and Asynchronous Inputs
Q: What happens if input changes near clock edge?
A: Google “Buridan’s Principle” by Leslie Lamport
1-bit reg
Clk
0
1

## Slide 19: An Example
32-bit
reg
Clk
+1
Run
WE
R
Reset

## Slide 20: Clock Methodology
Clock Methodology
Negative edge, synchronous
    Signals must be stable near falling clock edge
Positive edge synchronous
Asynchronous, multiple clocks, . . .
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 21: Finite State Machines

## Slide 22: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 23: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 24: Voting Machine
mux
32
...
reg
detect
enc
3
decoder (3-to-8)
32
32
32
LED dec
3
WE
+1
reg
WE
reg
WE
reg
WE
mux
D
V

## Slide 25: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 26: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 27: FSM Example Details
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 1=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 28: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 29: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 30: Moore Machine Example
Legend
state out
input
startout
A off
B on
C off
D on
down
up
down
down
up
down
up
up
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 31: Digital Door Lock
Digital Door Lock
Inputs:
keycodes from keypad
clock
Outputs:
“unlock” signal
display how many keys pressed so far

## Slide 32: Door Lock: Inputs
Assumptions:
signals are synchronized to clock
Password is B-A-B
K
A
B
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed

## Slide 33: Door Lock: Outputs
Assumptions:
High pulse on U unlocks door
U
D3D2D1D0
4
LED dec
8

## Slide 34: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
any
else
else
B3
”3”
else

## Slide 35: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else

## Slide 36: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Output
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”

## Slide 37: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Input | Next State
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle

## Slide 38: State Table Encoding
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”
U
D3D2D1D0
4
dec
8
D3 | D2 | D1 | D0 | U
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
R
P
Q
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed
K | A | B
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
x | x | x
0 | 0 | 0
1 | x | x
0 | 0 | 0
1 | x | x
S2 | S1 | S0
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
State | S2 | S1 | S0
Idle | 0 | 0 | 0
G1 | 0 | 0 | 1
G2 | 0 | 1 | 0
G3 | 0 | 1 | 1
B1 | 1 | 0 | 0
B2 | 1 | 0 | 1
S2 | S1 | S0 |  | S’2 | S’1 | S’0
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 0 |  | 0 | 0 | 1
0 | 0 | 0 |  | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 1
0 | 0 | 1 |  | 0 | 1 | 0
0 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 0 | 1 |  | 0 | 0 | 0

## Slide 39: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
A
B
C
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 40: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes
  But be wary of asynchronous (un-clocked) inputs
  State Machines or Ad-Hoc Circuits