## Slide 1: A Processor
See: P&H Chapter 2.16-20, 4.1-3

## Slide 2: Announcements
HW2 available later today
HW2 due in one week and a half
Work alone
Use your resources
  FAQ, class notes, book, Sections, office hours, newsgroup, CSUGLab
Make sure you
  Registered for class, can access CMS, have a Section, and have a project partner
  Check online syllabus/schedule, review slides and lecture notes, Office Hours, early homework and programming assignments

## Slide 3: Announcements
Prelims: Evening of Thursday, March 10 and April 28th
Late Policy
1) Each person has a total of four “slip days”
2) For projects, slip days are deducted from all partners
3) 10% deducted per day late after slip days are exhausted
Notes: Late Policy:
1) Each individual person gets a total of **4 "slip" days**.
Use them whenever you want without penalty. Further, no excuse is necessary. Make sure to email the head TA to enable CMS to accept your assignment when you are ready.
*caution: use slip days wisely, do not use all slip days on HW1, there are more homeworks and programming assignments!
2) For projects/programming assignments, slip days are deducted from all partners. Thus, all partners need a slip day available to use.
3) 10% deducted per day late after slip days are exhausted.

## Slide 4: Basic Computer System
Let’s build a MIPS CPU
  …but using (modified) Harvard architecture
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 5: Instructions
High Level Language
  C, Java, Python, Ruby, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Assembly Language
  No symbols (except labels)
  One operation per statement
Machine Langauge
  Binary-encoded assembly
  Labels become addresses

## Slide 6: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  unconditional jumps
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 7: Complexity
MIPS
  ≈ 200 instructions, 32 bits each, 3 formats
    mostly orthogonal
  all operands in registers
    almost all are 32 bits each, can be used interchangeably
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in special registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]
= Reduced Instruction Set Computer (RlSC)

## Slide 8: MIPS Register file
MIPS register file
  32 registers, 32-bits each (with r0 wired to zero)
  Write port indexed via RW
    Writes occur on falling edge but only if WE is high
  Read ports indexed via RA, RB
clk
W
32
A
B
r1
r2
…
r31
5
5
5
WE
RW
RA
RB
32
32

## Slide 9: MIPS Memory
MIPS Memory
  Up to 32-bit address
  32-bit data (but byte addressed)
  Enable + 2 bit memory control
    00: read word (4 byte aligned)
    01: write byte
    10: write halfword (2 byte aligned)
    11: write word (4 byte aligned)
memory
≤ 32
addr
2
mc
32
32
E

## Slide 10: Instruction Usage
Basic CPU execution loop
  fetch one instruction
  increment PC
  decode
  execute

## Slide 11: Instruction Fetch
Instruction Fetch Circuit
  Fetch instruction from memory
  Calculate address of next instruction
  Repeat
Program Memory
inst
32
PC
2
00
32
+4

## Slide 12: Arithmetic Instructions
op | rs | rt | rd | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x21 | ADDU rd, rs, rt | R[rd] = R[rs] + R[rt]
0x0 | 0x23 | SUBU rd, rs, rt | R[rd] = R[rs] – R[rt]
0x0 | 0x25 | OR rd, rs, rt | R[rd] = R[rs] ¦ R[rt]
0x0 | 0x26 | XOR rd, rs, rt | R[rd] = R[rs]  R[rt]
0x0 | 0x27 | NOR rd, rs rt | R[rd] = ~ ( R[rs] ¦ R[rt] )
00000001000001100010000000100110
R-Type

## Slide 13: Arithmetic and Logic
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4

## Slide 14: Example Programs
r4 = (r1 + r2) | r3
r8 = 4*r3 + r4 – 1
r9 = 9
ADDU rd, rs, rt
SUBU rd, rs, rt
OR rd, rs, rt
XOR rd, rs, rt
NOR rd, rs rt
Notes: -1: NOR r1, r0, r0
1: SUB r1, r0, r1
2: ADDU r2, r2, r2
4: ADDU r2, r2, r2
8: ADDU r2, r2, r2
9: ADDU r9, r1, r2

## Slide 15
Instruction fetch + decode + ALU
= Babbage’s engine
+ speed
+ reliability
– hand crank
Notes: A Babbage engine allows the values of the polynomial to be produced without ever having to multiply. A babbage engine only needs to be able to add!
This is why a babbage engine is also called a difference engine
A Babbage Engine (Difference Engine) is an automatic, mechanical calculator designed to tabulate polynomial functions. Both logarithmic and trigonometric functions can be approximated by polynomials, so a difference engine can compute many useful sets of numbers. -- http://en.wikipedia.org/wiki/Difference_engine

## Slide 16: Arithmetic Instructions: Shift
op | - | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rs, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rs, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rs, shamt | R[rd] = R[rs] >> shamt (sign ext.)
00000000000001000100000110000011
ex: r5 = r3 * 8
R-Type

## Slide 17: Shift
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
shamt

## Slide 18: Arithmetic Instructions: Immediates
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + imm
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & imm
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ imm
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + sign_extend(imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)
op | rs | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00100100101001010000000000000101
I-Type
ex: r5 += 5
ex: r9 = -1
ex: r9 = 65535

## Slide 19: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 20: Arithmetic Instructions: Immediates
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00111100000001010000000000000101
I-Type
ex: r5 = 0xdeadbeef

## Slide 21: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst
16
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 22: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 23: Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10100100101000010000000000000010
base + offset addressing
I-Type
signed offsets

## Slide 24: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 25: Example
int h, A[];
A[12] = h + A[8];
Notes: lw, t0, 32(s3)
add t0, s2, t0
sw t0, 48(s3)

## Slide 26: Memory Layout
Examples:
# r5 contains 0x5 sb r5, 2(r0) lb r6, 2(r0) sw r5, 8(r0) lb r7, 8(r0) lb r8, 11(r0)
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff

## Slide 27: Endianness
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word

## Slide 28: Control Flow: Absolute Jump
Absolute addressing for jumps
  Jump from 0x30000000 to 0x20000000? NO Reverse? NO
    But: Jumps from 0x2FFFFFFF to 0x3xxxxxxx are possible, but not reverse
  Trade-off: out-of-region jumps vs. 32-bit instruction encoding
MIPS Quirk:
  jump targets computed using already incremented PC
op | mnemonic | description
0x2 | J target | PC = target
op | immediate
6 bits | 26 bits
00001010100001001000011000000011
J-Type
op | mnemonic | description
0x2 | J target | PC = target ¦¦ 00
op | mnemonic | description
0x2 | J target | PC = (PC+4)32..29 ¦¦ target ¦¦ 00

## Slide 29: Absolute Jump
long jump? computed jump?
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 30: Control Flow: Jump Register
op | rs | - | - | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R-Type

## Slide 31: Jump Register
+4
||
tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 32: Examples (2)
jump to 0xabcd1234

## Slide 33: Examples (2)
jump to 0xabcd1234
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe0
else jump to 0xabcd1234

## Slide 34: Examples (2)
jump to 0xabcd1234
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe0
else jump to 0xabcd1234

## Slide 35: Control Flow: Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
00010000101000010000000000000011
signed offsets
I-Type

## Slide 36: Examples (3)
if (i == j) { i = i * 4; }
else { j = i - j; }
s1
s0

## Slide 37: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp

## Slide 38: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp

## Slide 39: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)

## Slide 40: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp

## Slide 41: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 PC = (PC+4)32..29 ¦¦ target ¦¦ 00
op | immediate
6 bits | 26 bits
00001100000001001000011000000010
J-Type

## Slide 42: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4

## Slide 43: Next Time
CPU Performance
Pipelined CPU