## Slide 1
CS3410
Guest Lecture
A Simple CPU: remaining branch instructions
CPU Performance
Pipelined CPU
Tudor Marian

## Slide 2: Memory Layout
Examples (big/little endian):
# r5 contains 5 (0x00000005)
sb r5, 2(r0) lb r6, 2(r0)
sw r5, 8(r0) lb r7, 8(r0) lb r8, 11(r0)
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff

## Slide 3: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
Conditional Jumps (cont.)

## Slide 4: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)

## Slide 5: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28 ¦¦ (target << 2)
op | immediate
6 bits | 26 bits
00001100000001001000011000000010
J-Type
Function/procedure calls
op | mnemonic | description
0x2 | J target | PC = (PC+4)31..28 ¦¦ (target << 2)

## Slide 6: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28 ¦¦ (target << 2)

## Slide 7
Performance
See: P&H 1.4

## Slide 8: Design Goals
What to look for in a computer system?
  Correctness: negotiable?
  Cost
    purchase cost = f(silicon size = gate count, economics)
    operating cost = f(energy, cooling)
    operating cost >= purchase cost
  Efficiency
    power = f(transistor usage, voltage, wire size, clock rate, …)
    heat = f(power)
      Intel Core i7 Bloomfield: 130 Watts
      AMD Turion: 35 Watts
      Intel Core 2 Solo: 5.5 Watts
      Cortex-A9 Dual Core @800MHz: 0.4 Watts
  Performance
  Other: availability, size, greenness, features, …

## Slide 9: Performance
How to measure performance?
  GHz (billions of cycles per second)
  MIPS (millions of instructions per second)
  MFLOPS (millions of floating point operations per second)
  benchmarks (SPEC, TPC, …)
Metrics
  latency: how long to finish my program
  throughput: how much work finished per unit time

## Slide 10: How Fast?
ALU
PC
Prog. Mem
control
new pc
Reg. File
~ 3 gates
All signals are stable
80 gates => clock period of at least 160 ns, max frequency ~6MHz
Better:
21 gates => clock period of at least 42 ns, max frequency ~24MHz
Assumptions:
  alu: 32 bit ripple carry + some muxes
  next PC: 30 bit ripple carry
  control: minimized for delay (~3 gates)
  transistors: 2 ns per gate
  prog,. memory: 16 ns (as much as 8 gates)
  register file: 2 ns access
  ignore wires, register setup time
Better:
  alu: 32 bit carry lookahead + some muxes (~ 9 gates)
  next PC: 30 bit carry lookahead (~ 6 gates)
Better Still:
  next PC: cheapest adder faster than 21 gate delays

## Slide 11: Adder Performance
32 Bit Adder Design | Space | Time
Ripple Carry | ≈ 300 gates | ≈ 64 gate delays
2-Way Carry-Skip | ≈ 360 gates | ≈ 35 gate delays
3-Way Carry-Skip | ≈ 500 gates | ≈ 22 gate delays
4-Way Carry-Skip | ≈ 600 gates | ≈ 18 gate delays
2-Way Look-Ahead | ≈ 550 gates | ≈ 16 gate delays
Split Look-Ahead | ≈ 800 gates | ≈ 10 gate delays
Full Look-Ahead | ≈ 1200 gates | ≈ 5 gate delays

## Slide 12: Optimization: Summary
Critical Path
  Longest path from a register output to a register input
  Determines minimum cycle, maximum clock frequency
Strategy 1 (we just employed)
  Optimize for delay on the critical path
  Optimize for size / power / simplicity elsewhere
    next PC

## Slide 13: Processor Clock Cycle
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
extend
new pc
register file
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]

## Slide 14: Processor Clock Cycle
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
extend
new pc
register file
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
op | mnemonic | description
0x2 | J target | PC = (PC+4)31..28 ¦¦ (target << 2)

## Slide 15: Multi-Cycle Instructions
Strategy 2
  Multiple cycles to complete a single instruction
E.g: Assume:
  load/store: 100 ns
  arithmetic: 50 ns
  branches: 33 ns
  Multi-Cycle CPU
  30 MHz (33 ns cycle) with
    3 cycles per load/store
    2 cycles per arithmetic
    1 cycle per branch
  Faster than Single-Cycle CPU?
  10 MHz (100 ns cycle) with
    1 cycle per instruction
Notes: 100ns = 10MHz; 50ns = 20MHz; 33ns = 30 MHz

## Slide 16: CPI
Instruction mix for some program P, assume:
  25% load/store ( 3 cycles / instruction)
  60% arithmetic ( 2 cycles / instruction)
  15% branches ( 1 cycle / instruction)
Multi-Cycle performance for program P:
3 * .25 + 2 * .60 + 1 * .15 = 2.1
average cycles per instruction (CPI) = 2.1
Multi-Cycle @ 30 MHz
Single-Cycle @ 10 MHz
Single-Cycle @ 15 MHz
800 MHz PIII “faster” than 1 GHz P4

## Slide 17: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2
  15% branches, CPI = 1

## Slide 18: Amdahl’s Law
Amdahl’s Law
Execution time after improvement =
Or:
Speedup is limited by popularity of improved feature
Corollary:
Make the common case fast
Caveat:
Law of diminishing returns
execution time affected by improvement
amount of improvement
+ execution time unaffected
contribution to execution time

## Slide 19
Pipelining
See: P&H Chapter 4.5

## Slide 20: The Kids
Alice
Bob
They don’t always get along…

## Slide 21: The Bicycle

## Slide 22: The Materials
Saw
Drill
Glue
Paint

## Slide 23: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 24: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 25: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:

## Slide 26: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
Alice
Bob
Carol
Dave

## Slide 27: Pipelined Performance
time 1 2 3 4 5 6 7…
What if some tasks don’t need drill?
Latency:
Throughput:
Concurrency:
Notes: Throughput: 1 task / cycle
Delay: 4 cycles / task
Parallelism: 4 concurrent tasks

## Slide 28: Unequal Pipeline Stages
0h 1h 2h 3h…
15 min
30 min
45 min
90 min
Latency:
Throughput:
Concurrency:
Notes: Add newaiting areas
Throughput: 1 task / 90 min
Delay:  min / task
Parallelism:  concurrent tasks

## Slide 29: Poorly-balanced Pipeline Stages
0h 1h 2h 3h…
15 min
30 min
45 min
90 min
Latency:
Throughput:
Concurrency:
Notes: Throughput: 1 task / 90 min
Delay: 360 min / task
Parallelism: 4 concurrent tasks

## Slide 30: Re-Balanced Pipeline Stages
0h 1h 2h 3h…
15 min
30 min
45 min
90 min
Latency:
Throughput:
Concurrency:
Notes: Throughput: 1 task / 90 min
Delay: 180 min / task
Parallelism: 2 concurrent tasks

## Slide 31: Splitting Pipeline Stages
0h 1h 2h 3h…
15 min
30 min
45 min
45+45 min
Latency:
Throughput:
Concurrency:
Notes: Throughput: 1 task / 45 min
Delay: 180 min / task
Parallelism: 4 concurrent tasks

## Slide 32: Pipeline Hazards
0h 1h 2h 3h…
Q: What if glue step of task 3 depends on output of task 1?
Latency:
Throughput:
Concurrency:
Notes: A: Insert stalls as needed in task 3… and delay task 4+
Q: What is executing in glue stage?
A: Nothing
Performance is harder to predict

## Slide 33: Lessons
Principle:
Throughput increased by parallel execution
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards

## Slide 34: A Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 35: A Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
register file
control
alu
imm
memory
din
dout
addr
inst
PC
memory
compute jump/branch targets
new pc
+4
extend

## Slide 36: Basic Pipeline
Five stage “RISC” load-store architecture
  Instruction fetch (IF)
    get instruction from memory, increment PC
  Instruction Decode (ID)
    translate opcode into control signals and read registers
  Execute (EX)
    perform ALU operation, compute jump/branch targets
  Memory (MEM)
    access memory if needed
  Writeback (WB)
    update register file
Notes: This is simpler than the MIPS, but we’re using it to get the concepts across – everything you see here applies to MIPS, but we have to deal w/ fewer bits in these examples (that’s why I like them)

## Slide 37: Pipelined Implementation
Break instructions across multiple clock cycles (five, in this case)
Design a separate stage for the execution performed during each clock cycle
Add pipeline registers (flip-flops) to isolate signals between different stages
Slides thanks to Kevin Walsh, Sally McKee, and Kavita Bala