## Slide 1: Pipeline Hazards
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See P&H Appendix 4.7

## Slide 2: Announcements
PA1 available: mini-MIPS processor
PA1 due next Friday
Work in pairs
Use your resources
  FAQ, class notes, book, Sections, office hours, newsgroup, CSUGLab
HW1 graded
  Max: 10; Median: 9; Mean: 8.3; Stddev: 1.8
  Great job!
  Regrade policy
    Submit written request to lead TA, lead TA will pick a different grader
    Submit another written request, lead TA will regrade directly
    Submit yet another written request for professor to regrade.

## Slide 3: Announcements
Prelims:
  Thursday, March 10th in class
  Thursday, April 28th Evening
Late Policy
1) Each person has a total of four “slip days”
2) For projects, slip days are deducted from all partners
3) 10% deducted per day late after slip days are exhausted
Notes: Late Policy:
1) Each individual person gets a total of **4 "slip" days**.
Use them whenever you want without penalty. Further, no excuse is necessary. Make sure to email the head TA to enable CMS to accept your assignment when you are ready.
*caution: use slip days wisely, do not use all slip days on HW1, there are more homeworks and programming assignments!
2) For projects/programming assignments, slip days are deducted from all partners. Thus, all partners need a slip day available to use.
3) 10% deducted per day late after slip days are exhausted.

## Slide 4: Goals for Today
Data Hazards
  Data dependencies
  Problem, detection, and solutions
    (delaying, stalling, forwarding, bypass, etc)
  Forwarding unit
  Hazard detection unit
Next time
  Control Hazards
  What is the next instruction to execute if
  a branch is taken? Not taken?

## Slide 5: Broken Example
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
sub r5, r3, r4
lw r6, 4(r3)
or r5, r3, r5
sw r6, 12(r3)
add r3, r1, r2

## Slide 6: What Can Go Wrong?
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (ID.rA != 0 && (ID.rA == EX.rD || ID.rA == M.rD || ID.rA == WB.rD))
|| (same for rB)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rAneeded, rBneeded (can ensure this in ID stage)

## Slide 7: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rd
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8

## Slide 8: Resolving Data Hazards
What to do if data hazard detected?
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 9: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
Notes: find hazards first, then draw

## Slide 10: Forwarding Datapath
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 11: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 12: Forwarding
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 

## Slide 13: Forwarding
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r4 |  |  |  |  |  |  |  |  | 
lw r6, 4(r3) |  |  |  |  |  |  |  |  | 
or r5, r3, r5 |  |  |  |  |  |  |  |  | 
sw r6, 12(r3) |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX D=55 | MEM D=55 | WB r5=55 |  |  | 
 |  | IF | ID 33=r3 | EX D=? | MEM D=66 | WB r6=66 |  | 
 |  |  | IF | ID 33=r3 55=r5 | EX | MEM | WB | 
 |  |  |  | IF | ID 33=r3 66=r6 | EX | MEM | 
Notes: identify hazards then draw; if “or” had used r6, would have needed to stall

## Slide 14: Forwarding
Forward correct value from?
  ALU output: too late in cycle?
  EX/MEM.D pipeline register (output from ALU)
  WB data value (output from ALU or memory)
  MEM output: too late in cycle, on critical path
to?
  ID (just after register file)
    maybe pointless?
  EX, just after ID/EX.A and ID/EX.B are read
  MEM, just after EX/MEM.B is read: on critical path
data mem
B
A
B
D
M
D
inst mem
D
B
A
1
2
3
b
c
4
a
Notes: Forward correct value from?
  ALU output: too late in cycle
  EX/MEM.D pipeline register (output from ALU)
  WB data value (output from ALU or memory)
  MEM output: too late in cycle
to?
  ID (just after register file): pointless?
  EX, just after ID/EX.A and ID/EX.B are read
  MEM, just after EX/MEM.B is read: on critical path

## Slide 15: Forwarding Path 1
add r4, r1, r2 |  |  |  |  |  |  |  |  | 
nop |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: bypass from WB to mux in EX

## Slide 16: WB to EX Bypass
WB to EX Bypass
  EX needs value being written by WB
Resolve:
Add bypass from WB final value to start of EX
Detect:
Notes: ((ID/EX.Ra == MEM/WB.Rd) or (ID/EX.Rb == MEM/WB.Rd)) and (EX needs A or B) and (WB is writing a register)

## Slide 17: Forwarding Path 2
add r4, r1, r2 |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: draw bypass from WB to mux in EX

## Slide 18: MEM to EX Bypass
MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
Resolve:
Add a bypass from EX/MEM.D to start of EX
Detect:
Notes: ((ID/EX.Ra == EX/MEM.Rd) or (ID/EX.Rb == EX/MEM.Rd)) and (MEM will be writing a register) and (MEM is not a load instruction)

## Slide 19: Forwarding Datapath
data mem
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
Notes: draw control signals

## Slide 20: Tricky Example
data mem
inst mem
D
B
A
add r1, r1, r2 |  |  |  |  |  |  |  |  | 
SUB r1, r1, r3 |  |  |  |  |  |  |  |  | 
OR r1, r4, r1 |  |  |  |  |  |  |  |  | 
Notes: which paths get used

## Slide 21: More Data Hazards
add r4, r1, r2 |  |  |  |  |  |  |  |  | 
nop |  |  |  |  |  |  |  |  | 
nop |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A

## Slide 22: Register File Bypass
Register File Bypass
  Reading a value that is currently being written
Detect:
((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
Resolve:
Add a bypass around register file (WB to ID)
Better: (Hack) just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle

## Slide 23: Quiz
Find all hazards, and say how they are resolved: add r3, r1, r2 sub r3, r2, r1 nand r4, r3, r1 or r0, r3, r4 xor r1, r4, r3 sb r4, 1(r0)
Notes: 6 hazards
be careful of store (no rD)
be careful or r0 (never a hazard)

## Slide 24: Memory Load Data Hazard
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: requires one bubble

## Slide 25: Resolving Memory Load Hazard
Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Resolution:
  MIPS 2000/3000: one delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 26: Quiz 2
add r3, r1, r2 nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Notes: Find all hazards, and say how they are resolved

## Slide 27: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 28: More Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 29: More Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 30: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 31: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
ori r2, r0, 1 |  |  |  |  |  |  |  |  | 
L: or r3, r1, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch

## Slide 32: Control Hazards: Speculative Execution
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC not known until 2 cycles after branch/jump
Stall
Delay Slot
Speculative Execution
  Guess direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 33: Loops

## Slide 34: Branch Prediction

## Slide 35: Pipelining: What Could Possibly Go Wrong?
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard