## Slide 1: Pipeline Control Hazards and Instruction Variations
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See P&H Appendix 4.8 & 2.16 and 2.17

## Slide 2: Announcements
PA1 available: mini-MIPS processor
PA1 due next Friday
Work in pairs
Use your resources
  FAQ, class notes, book, Sections, office hours, newsgroup, CSUGLab
Prelims:
  Thursday, March 10th in class
  Thursday, April 28th Evening

## Slide 3: Goals for Today
Recap: Data Hazards
Control Hazards
  What is the next instruction to execute if a branch is taken? Not taken?
  How to resolve control hazards
  Optimizations
Instruction Variations
  ARM
  x86

## Slide 4: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 5: More Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 6: More Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 7: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 8: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
ori r2, r0, 1 |  |  |  |  |  |  |  |  | 
L: or r3, r1, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch

## Slide 9: Control Hazards: Speculative Execution
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC not known until 2 cycles after branch/jump
Stall
Delay Slot
Speculative Execution
  “Guess” direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 10: Loops

## Slide 11: Branch Prediction

## Slide 12: Branch Prediction

## Slide 13: Pipelining: What Could Possibly Go Wrong?
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard

## Slide 14: Goals for Today
Recap: Data Hazards
Control Hazards
  What is the next instruction to execute if a branch is taken? Not taken?
  How to resolve control hazards
  Optimizations
Instruction Variations
  ARM
  x86

## Slide 15: Variations
More shifts
Notes: variable shift amount
rotate
(ARM)

## Slide 16: Variations
Condition flags
Notes: branch if a < b?
mips:
compute a - b; // might overflow
branch on (b-a) less than zero
better mips:
slt a b
bne (a<b), 0
cmp a, b  flags (gt, lt, eq, zero, …)
(ARM, X86, most ISAs)

## Slide 17: Variations
Condition flags
Notes: branch if a < b?
mips:
compute a - b; // might overflow
branch on (b-a) less than zero
better mips:
slt a b
bne (a<b), 0
cmp a, b  flags (gt, lt, eq, zero, …)
(ARM, X86, most ISAs)

## Slide 18: Variations
Condition flags
Notes: branch if a < b?
mips:
compute a - b; // might overflow
branch on (b-a) less than zero
better mips:
slt a b
bne (a<b), 0
cmp a, b  flags (gt, lt, eq, zero, …)
(ARM, X86, most ISAs)

## Slide 19: Variations
Conditional instructions
top: CMP r3, r4
SUBGT r3, r3, r4
SUBLT r4, r4, r3
BNE top
Notes: (ARM)

## Slide 20: Variations
Stack operations & multiple destinations
Notes: swap
push
pop
(X86)

## Slide 21: Variations
String instructions
MOV AX, FFh
MOV DI, 5000h
MOV CX, 2000h
REP STOSB
Notes: (X86)
STOSB = store byte (register AX into memory at DI)

## Slide 22: Variations
Vector instructions
vaddubs v3, v1, v2
Notes: SIMD: (PowerPC AltiVec, X86 MMX/SSE, Cray, …)

## Slide 23: Next time
Instruction Variations
  ARM/MIPS (RISC)
  Versus x86 (CISC)