## Slide 1: RISC, CISC, and Assemblers
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See P&H Appendix B.1-2, and Chapters 2.8 and 2.12

## Slide 2: Announcements
PA1 due this Friday
Work in pairs
Use your resources
  FAQ, class notes, book, Sections, office hours, newsgroup, CSUGLab
Prelims1: next Thursday, March 10th in class
  Material covered
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 and Appendix B (RISC/CISC, MIPS, and calling conventions)
    Chapter 1 (Performance)
    HW1, HW2, PA1, PA2
  Practice prelims are online in CMS
  Closed Book: cannot use electronic device or outside material
  We will start at 1:25pm sharp, so come early

## Slide 3: Goals for Today
Instruction Set Architetures
  Arguments: stack-based, accumulator, 2-arg, 3-arg
  Operand types: load-store, memory, mixed, stacks, …
  Complexity: CISC, RISC
Assemblers
  assembly instructions
  psuedo-instructions
  data and layout directives
  executable programs

## Slide 4: Instruction Set Architecture
ISA defines the permissible instructions
  MIPS: load/store, arithmetic, control flow, …
  ARM: similar to MIPS, but more shift, memory, & conditional ops
  VAX: arithmetic on memory or registers, strings, polynomial evaluation, stacks/queues, …
  Cray: vector operations, …
  x86: a little of everything

## Slide 5: One Instruction Set Architecture
Toy example: subleq a, b, target
Mem[b] = Mem[b] – Mem[a] then if (Mem[b] <= 0) goto target else continue with next instruction
clear a == subleq a, a, pc+4
jmp c == subleq Z, Z, c
add a, b == subleq a, Z, pc+4; subleq Z, b, pc+4; subleq Z, Z, pc+4

## Slide 6: PDP-8
Not-a-toy example: PDP-8
One register: AC
Eight basic instructions:
AND a # AC = AC & MEM[a]
TAD a # AC = AC + MEM[a]
ISZ a # if (!++MEM[a]) skip next
DCA a # MEM[a] = AC; AC = 0
JMS a # jump to subroutine (e.g. jump and link)
JMP a # jump to MEM[a]
IOT x # input/output transfer
OPR x # misc operations on AC

## Slide 7: Stack Based
Stack machine
  data stack in memory, stack pointer register
  Operands popped/pushed as needed add
[ Java Bytecode, PostScript, odd CPUs, some x86 ]
Tradeoffs:
Notes: Elegant/simple; dependent on memory performance; small instructions (no args!) / compact programs

## Slide 8: Accumulator Based
Accumulator machine
  Results usually put in dedicated accumulator register add b store b
[ Some x86 ]
Tradeoffs:
Notes:     EAX on x86 = “accumulator”; Historically useful, small instructions (1 arg)

## Slide 9: Load-Store
Load/store (register-register) architecture
  computation only between registers
[ MIPS, some x86 ]
Tradeoffs:
Notes: larger instructions (3 args); more instructions (load, compute, store); maybe higher clock rate (simpler instructions)

## Slide 10: Axes
Axes:
  Arguments: stack-based, accumulator, 2-arg, 3-arg
  Operand types: load-store, memory, mixed, stacks, …
  Complexity: CISC, RISC

## Slide 11: Complex Instruction Set Computers
People programmed in assembly and machine code!
  Needed as many addressing modes as possible
  Memory was (and still is) slow
CPUs had relatively few registers
  Register’s were more “expensive” than external mem
  Large number of registers requires many bits to index
Memories were small
  Encoraged highly encoded microcodes as instructions
  Variable length instructions, load/store, conditions, etc

## Slide 12: Reduced Instruction Set Computer
Dave Patterson
  RISC Project, 1982
  UC Berkeley
  RISC-I: ½ transtisters & 3x faster
  Influences: Sun SPARC, namesake of industry
John L. Hennessy
  MIPS, 1981
  Stanford
  Simple pipelining, keep full
  Influences: MIPS computer system, PlayStation, Nintendo

## Slide 13: Complexity
MIPS = Reduced Instruction Set Computer (RlSC)
  ≈ 200 instructions, 32 bits each, 3 formats
  all operands in registers
    almost all are 32 bits each
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in dedicated registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]
Notes: DEC PDP-8 has about 8 insructions

## Slide 14: RISC vs CISC
RISC Philosophy
Regularity & simplicity
Leaner means faster
Optimize the common case
CISC Rebuttal
Compilers can be smart
Transistors are plentiful
Legacy is important
Code size counts
Micro-code!
Notes: RISC:
regularity means no mem-to-mem, few addressing modes… thus load-store
regularity means uniform instruction size… sizeof(common) = sizeof(rare)
lean means fewer, more general instructions… thus bigger programs, more instructions
common case means measurement
CISC:
Compilers can be smart
Transistors are plentiful
Legacy is important
Code size counts
Micro-code!

## Slide 15: Goals for Today
Instruction Set Architetures
  Arguments: stack-based, accumulator, 2-arg, 3-arg
  Operand types: load-store, memory, mixed, stacks, …
  Complexity: CISC, RISC
Assemblers
  assembly instructions
  psuedo-instructions
  data and layout directives
  executable programs

## Slide 16: Examples
...
T: ADDI r4, r0, -1
BEQ r3, r0, B
ADDI r4, r4, 1
LW r3, 0(r3)
J T
NOP
B: ...
...
JAL L
nop
nop
L: LW r5, 0(r31)
ADDI r5, r5, 1
SW r5, 0(r31)
...

## Slide 17: cs3410 Recap/Quiz
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
Notes: 32 bits, 4 bytes

## Slide 18: Example 1
...
T: ADDI r4,r0,-1
BEQ r3, r0, B
ADDI r4,r4, 1
LW r3, 0(r3)
J T
NOP
B: ...
... | 
001000 | 
000100 | 
001000 | 
100011 | 
000010 | 
00000000000000000000000000000000 | 
... | 
Notes: length of linked list
Q: how is this assembled?
A: mostly, just encode in binary; but need 2 passes to resolve forward references

## Slide 19: References
Q: How to resolve labels into offsets and addresses?
A: Two-pass assembly
  1st pass: lay out instructions and data, and build a symbol table (mapping labels to addresses) as you go
  2nd pass: encode instructions and data in binary, using symbol table to resolve references

## Slide 20: Example 2
...
JAL L
nop
nop
L: LW r5, 0(r31)
ADDI r5,r5,1
SW r5, 0(r31)
...
...
00100000000100000000000000000100
00000000000000000000000000000000
00000000000000000000000000000000
10001111111001010000000000000000
00100000101001010000000000000001
00000000000000000000000000000000
...
Notes: Counts how many times it was executed
lessons:
data and instructions are mixed: von Neumann machine
-need better way to specify data: replace second nop with “.word 0”
-better to separate code and data: use .text and .data segments
-being careful of branch delay slot is painful

## Slide 21: Example 2 (better)
.text 0x00400000 # code segment
...
ORI r4, r0, counter
LW r5, 0(r4)
ADDI r5, r5, 1
SW r5, 0(r4)
...
.data 0x10000000 # data segment
counter:
.word 0
Notes: ORI is broken; need to do LUI then ORI
-better to use pseudoinstruction: LA (load 32-bit address) or LI (load 32-bit immediate)

## Slide 22: Lessons
Lessons:
  Mixed data and instructions (von Neumann)
  … but best kept in separate segments
  Specify layout and data using assembler directives
  Use pseudo-instructions

## Slide 23: Pseudo-Instructions
Pseudo-Instructions
NOP # do nothing
MOVE reg, reg # copy between regs
LI reg, imm # load immediate (up to 32 bits)
LA reg, label # load address (32 bits)
B label # unconditional branch
BLT reg, reg, label # branch less than
Notes: BLT rA, rB, label
becomes
SLT r1, rA, rB
BNE r1, r0, label

## Slide 24: Assembler
Assembler:
assembly instructions
+ psuedo-instructions
+ data and layout directives
= executable program
Slightly higher level than plain assembly
e.g: takes care of delay slots
(will reorder instructions or insert nops)

## Slide 25: Motivation
Q: Will I program in assembly?
A: I do...
  For kernel hacking, device drivers, GPU, etc.
  For performance (but compilers are getting better)
  For highly time critical sections
  For hardware without high level languages
  For new & advanced instructions: rdtsc, debug registers, performance counters, synchronization, ...

## Slide 26: Stages
calc.c
math.c
io.s
libc.o
libm.o
calc.s
math.s
io.o
calc.o
math.o
calc.exe
Notes: C compiller produces assembly files (contain MIPS assembly, pseudo-instructions, directives, etc.)
MIPS assembler produces object files (contain MIPS machine code, missing symbols, some layout information, etc.)
MIPS linker produces executable file (contains MIPS machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 27: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text

## Slide 28: Example program
vector v = malloc(8);
v->x = prompt(“enter x”);
v->y = prompt(“enter y”);
int c = pi + tnorm(v);
print(“result”, c);
calc.c
int tnorm(vector v) {
return abs(v->x)+abs(v->y);
}
math.c
global variable: pi
entry point: prompt
entry point: print
entry point: malloc
lib3410.o
Notes: OS
stack: function local vars and args
heap: vector object (8 bytes)
data: strings, pi
text: assembly

## Slide 29: math.s
int abs(x) {
return x < 0 ? –x : x;
}
int tnorm(vector v) {
return abs(v->x)+abs(v->y);
}
math.c
tnorm:
# arg in r4, return address in r31
# leaves result in r4
abs:
# arg in r3, return address in r31
# leaves result in r3
BLEZ r3, pos
SUB r3, r0, r3
pos:
JR r31
.global tnorm
MOVE r30, r31
LW r3, 0(r4)
JAL abs
MOVE r6, r3
LW r3, 4(r4)
JAL abs
ADD r4, r6, r3
JR r30
Notes: lessons:
need “.global” directive
starting to need conventions:
- where to put function arguments
- where to put return value

## Slide 30: calc.s
vector v = malloc(8);
v->x = prompt(“enter x”);
v->y = prompt(“enter y”);
int c = pi + tnorm(v);
print(“result”, c);
calc.c
dostuff:
# no args, no return value, return addr in r31
MOVE r30, r31
LI r3, 8 # call malloc: arg in r3, ret in r3
JAL malloc
MOVE r6, r3 # r6 holds v
LA r3, str1 # call prompt: arg in r3, ret in r3
JAL prompt
SW r3, 0(r6)
LA r3, str2 # call prompt: arg in r3, ret in r3
JAL prompt
SW r3, 4(r6)
MOVE r4, r6 # call tnorm: arg in r4, ret in r4
JAL tnorm
LA r5, pi
LW r5, 0(r5)
ADD r5, r4, r5
LA r3, str3 # call print: args in r3 and r4
MOVE r4, r5
JAL print
JR r30
.data
str1: .asciiz “enter x”
str2: .asciiz “enter y”
str3: .asciiz “result”
.text
.extern prompt
.extern print
.extern malloc
.extern tnorm
.global dostuff
# clobbered: need stack
# might clobber stuff
# might clobber stuff
# might clobber stuff
# clobbers r6, r31, r30 …
Notes: step through, then ask what is broken
lessons:
string data goes elsewhere
definitely need conventions:
- where to put function arguments
- where to put return value
- which functions modify which registers
- where to save registers?

## Slide 31: Next time
Calling Conventions!
PA1 due Friday
Prelim1 Next Thursday, in class