## Slide 1: Virtual Memory 1
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
P & H Chapter 5.4 (up to TLBs)

## Slide 2: Announcements
HW3 available due today Tuesday
  HW3 has been updated. Use updated version.
  Work with alone
  Be responsible with new knowledge
PA3 available later today or by tomorrow
  Work in pairs
Next five weeks
  One homeworks and two projects
  Prelim2 will be Thursday, April 28th
  PA4 will be final project (no final exam)

## Slide 3: Goals for Today
Title says Virtual Memory, but really finish caches: writes
Introduce idea of Virtual Memory

## Slide 4: Cache Design
Need to determine parameters:
  Cache size
  Block size (aka line size)
  Number of ways of set-associativity (1, N, )
  Eviction policy
  Number of levels of caching, parameters for each
  Separate I-cache from D-cache, or Unified cache
  Prefetching policies / instructions
  Write policy

## Slide 5: A Real Example
> dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 6: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 7: Basic Cache Organization
Q: How to decide block size?
A: Try it and see
But: depends on cache size, workload, associativity, …
Experimental approach!

## Slide 8: Experimental Results
Notes: For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and miss penalty (time to fetch block) is larger

## Slide 9: Tradeoffs
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 10
Writing with Caches

## Slide 11: Cached Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 12: Write Allocation Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is not in the cache…
Write-Allocate
  allocate a cache line for new data (and maybe write-through)
No-Write-Allocate
  ignore cache, just go to main memory

## Slide 13: A Simple Direct Mapped Cache
Memory
Direct Mapped Cache + Write-through + Write-allocate
Processor
lb $1  M[ 1 ]
lb $2  M[ 7 ]
sb $2  M[ 0 ]
sb $1  M[ 5 ]
lb $2  M[ 9 ]
sb $1  M[ 5 ]
sb $1  M[ 0 ]
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181

## Slide 14: How Many Memory References?
Write-through performance
Each miss (read or write) reads a block from mem
  5 misses  10 mem reads
Each store writes an item to mem
  4 mem writes
Evictions don’t need to write to mem
  no need for dirty bit

## Slide 15: A Simple Direct Mapped Cache
Memory
Direct Mapped Cache + Write-back + Write-allocate
Processor
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
D
lb $1  M[ 1 ]
lb $2  M[ 7 ]
sb $2  M[ 0 ]
sb $1  M[ 5 ]
lb $2  M[ 9 ]
sb $1  M[ 5 ]
sb $1  M[ 0 ]

## Slide 16: How Many Memory References?
Write-back performance
Each miss (read or write) reads a block from mem
  5 misses  10 mem reads
Some evictions write a block to mem
  1 dirty eviction  2 mem writes
  (+ 2 dirty evictions later  +4 mem writes)
  need a dirty bit

## Slide 17: Write-Back Meta-Data
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 18: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 19: Performance Tradeoffs
Q: Hit time: write-through vs. write-back?
A: Write-through slower on writes.
Q: Miss penalty: write-through vs. write-back?
A: Write-back slower on evictions.

## Slide 20: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: What does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 21: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 22: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
May need to snoop on other CPU’s cache activity
Invalidate cache line when other CPU writes
Flush write-back caches before other CPU reads
Or the reverse: Before writing/reading…
Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net

## Slide 23
Cache Conscious Programming

## Slide 24: Cache Conscious Programming
Every access is a cache miss!
(unless entire matrix can fit in cache)
// H = 12, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];
1 | 11 | 21 |  |  |  |  |  |  | 
 |  | 2 | 12 | 22 |  |  |  |  | 
 |  |  |  | 3 | 13 | 23 |  |  | 
 |  |  |  |  |  | 4 | 14 | 24 | 
 |  |  |  |  |  |  |  | 5 | 15
25 |  |  |  |  |  |  |  |  | 
6 | 16 | 26 |  |  |  |  |  |  | 
 |  | 7 | 17 | … |  |  |  |  | 
 |  |  |  | 8 | 18 |  |  |  | 
 |  |  |  |  |  | 9 | 19 |  | 
 |  |  |  |  |  |  |  | 10 | 20

## Slide 25: Cache Conscious Programming
Block size = 4  75% hit rate
Block size = 8  87.5% hit rate
Block size = 16  93.75% hit rate
And you can easily prefetch to warm the cache.
// H = 12, W = 10
int A[H][W];
for(y=0; y < H; y++)
for(x=0; x < W; x++)
sum += A[y][x];
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
11 | 12 | 13 | … |  |  |  |  |  | 

## Slide 26: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  (big & fast) built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate

## Slide 27: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
Multi-core / Multi-Processor is complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right

## Slide 28: Virtual Memory

## Slide 29: Processor & Memory
CPU address/data bus...
… routed through caches
… to main memory
  Simple, fast, but…
Q: What happens for LW/SW to an invalid location?
  0x000000000 (NULL)
  uninitialized pointer
CPU
Text
Data
Stack
Heap
Memory

## Slide 30: Multiple Processes
Running multiple processes…
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 31: Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
  Take turns using memory?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap

## Slide 32: Solution? Multiple processes/processors
Can we relocate second program?
  What if they don’t fit?
  What if not contiguous?
  Need to recompile/relink?
  …
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap

## Slide 33
All problems in computer science can be solved by another level of indirection.
– David Wheeler
– or, Butler Lampson
– or, Leslie Lamport
– or, Steve Bellovin

## Slide 34: Virtual Memory
Virtual Memory: A Solution for All Problems
Each process has its own virtual address space
  Programmer can code as if they own all of memory
On-the-fly at runtime, for each memory access
  all access is indirect through a virtual address
  translate fake virtual address to a real physical address
  redirect load/store to the physical address

## Slide 35: Address Spaces
wikipedia

## Slide 36: Address Space
Programs load/store to virtual addresses
Actual memory uses physical addresses
Memory Management Unit (MMU)
  Responsible for translating on the fly
  Essentially, just a big array of integers: paddr = PageTable[vaddr];
CPU
MMU
A
B
C
X
Y
Z
X
Y
Z
C
B
A
CPU
MMU
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 37: Virtual Memory Advantages
Advantages
Easy relocation
  Loader puts code anywhere in physical memory
  Creates virtual mappings to give illusion of correct layout
Higher memory utilization
  Provide illusion of contiguous memory
  Use all physical memory, even physical address 0x0
Easy sharing
  Different mappings for different programs / cores
And more to come…

## Slide 38
Address Translation
Pages, Page Tables, and
the Memory Management Unit (MMU)

## Slide 39: Address Translation
Attempt #1: How does MMU translate addresses?
paddr = PageTable[vaddr];
Granularity?
  Per word…
  Per block…
  Variable…
Typical:
  4KB – 16KB pages
  4MB – 256MB jumbo pages
Notes: per word … too expensive: 4GB PageTable arrray
per block… ?
Variable … complicated hardware
We will stick to 4kb pages

## Slide 40: Address Translation
Attempt #1: For any access to virtual address:
  Calculate virtual page number and page offset
  Lookup physical page number at PageTable[vpn]
  Calculate physical address as ppn:offset
vaddr
Page Offset
Virtual page number
Page offset
Physical page number
Lookup in PageTable
paddr
Notes: 4kb pages = 12 bits for page offset, 20 bits for VPN

## Slide 41: Simple PageTable
Q: Where to store page tables?
A: In memory, of course… Special page table base register (CR3:PTBR on x86) (Cop0:ContextRegister on MIPS)
CPU
MMU
Data
Read Mem[0x00201538]
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
* lies to children
Notes: VADDR = 0x00401538
PFN = VADDR/4kb = VADDR>>12 = 0x401
PageTableEntry at 0x90000804 contains 0x4123B000
Data at 0x4123B538

## Slide 42: Summary
vpn | pgoff
 | Physical Page Number
 | 0x10045
 | 0xC20A3
 | 0x4123B
 | 0x00000
 | 0x20340
vaddr
* lies to children
PTBR

## Slide 43: Page Size Example
Overhead for VM Attempt #1 (example)
Virtual address space (for each process):
  total memory: 232 bytes = 4GB
  page size: 212 bytes = 4KB
  entries in PageTable?
  size of PageTable?
Physical address space:
  total memory: 229 bytes = 512MB
  overhead for 10 processes?
* lies to children
Notes: 220 entries in pagetable, so 222 bytes = 4MB (w/ 4byte entries), so 40MB (25% of total!)
Q: Can we possibly have a “full” pagetable?
A: Not enough physical memory pages – some pagetable entries will be duplicates!

## Slide 44: Invalid Pages
Cool Trick #1: Don’t map all pages
Need valid bit for each page table entry
Q: Why?
V |  | Physical Page Number
0 |  | 
1 |  | 0x10045
0 |  | 
0 |  | 
1 |  | 0xC20A3
1 |  | 0x4123B
1 |  | 0x00000
0 |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
Notes: A: now access to NULL will fail
A: we might not have that much physical memory

## Slide 45: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses?
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
Multi-level PageTable
* x86 does exactly this
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 46: Page Permissions
Cool Trick #2: Page permissions!
Keep R, W, X permission bits for each page table entry
Q: Why?
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0x10045
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x00000
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 47: Aliasing
Cool Trick #3: Aliasing
Map the same physical page at several virtual addresses
Q: Why?
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x00000
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
Notes: A: can make different views of same data with different permissions

## Slide 48
Paging

## Slide 49: Paging
Can we run process larger than physical memory?
  The “virtual” in “virtual memory”
View memory as a “cache” for secondary storage
  Swap memory pages out to disk when not in use
  Page them back in when needed
Assumes Temporal/Spatial Locality
  Pages used recently most likely to be used again soon

## Slide 50: Paging
Cool Trick #4: Paging/Swapping
Need more bits:
Dirty, RecentlyUsed, …
V | R | W | X | D | Physical Page Number
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 0x10045
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
0 |  |  |  | 0 | disk sector 200
0 |  |  |  | 0 | disk sector 25
1 |  |  |  | 1 | 0x00000
0 |  |  |  |  | invalid
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
25
200
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 51
Role of the Operating System
Context switches, working set,
shared memory

## Slide 52: sbrk
Suppose Firefox needs a new page of memory
(1) Invoke the Operating System
  void *sbrk(int nbytes);
(2) OS finds a free page of physical memory
  clear the page (fill with zeros)
  add a new entry to Firefox’s PageTable

## Slide 53: Context Switch
Suppose Firefox is idle, but Skype wants to run
(1) Firefox invokes the Operating System
  int sleep(int nseconds);
(2) OS saves Firefox’s registers, load skype’s
  (more on this later)
(3) OS changes the CPU’s Page Table Base Register
  Cop0:ContextRegister / CR3:PDBR
(4) OS returns to Skype

## Slide 54: Shared Memory
Suppose Firefox and Skype want to share data
(1) OS finds a free page of physical memory
  clear the page (fill with zeros)
  add a new entry to Firefox’s PageTable
  add a new entry to Skype’s PageTable
    can be same or different vaddr
    can be same or different page permissions

## Slide 55: Multiplexing
Suppose Skype needs a new page of memory, but Firefox is hogging it all
(1) Invoke the Operating System
  void *sbrk(int nbytes);
(2) OS can’t find a free page of physical memory
  Pick a page from Firefox instead (or other process)
(3) If page table entry has dirty bit set…
  Copy the page contents to disk
(4) Mark Firefox’s page table entry as “on disk”
  Firefox will fault if it tries to access the page
(5) Give the newly freed physical page to Skype
  clear the page (fill with zeros)
  add a new entry to Skyps’s PageTable

## Slide 56: Paging Assumption 1
OS multiplexes physical memory among processes
  assumption # 1: processes use only a few pages at a time
  working set = set of process’s recently actively pages
# recent accesses
0x00000000
0x90000000

## Slide 57: Reasons for Thrashing
Q: What if working set is too large?
Case 1: Single process using too many pages
Case 2: Too many processes
working set
mem
disk
swapped
P1
working set
mem
disk
swapped
ws
mem
disk
ws
ws
ws
ws
ws

## Slide 58: Thrashing
Thrashing b/c working set of process (or processes) greater than physical memory available
    Firefox steals page from Skype
    Skype steals page from Firefox
  I/O (disk activity) at 100% utilization
    But no useful work is getting done
Ideal: Size of disk, speed of memory (or cache)
Non-ideal: Speed of disk

## Slide 59: Paging Assumption 2
OS multiplexes physical memory among processes
  assumption # 2: recent accesses predict future accesses
  working set usually changes slowly over time
working set
time 

## Slide 60: More Thrashing
Q: What if working set changes rapidly or unpredictably?
A: Thrashing b/c recent accesses don’t predict future accesses
working set
time 

## Slide 61: Preventing Thrashing
How to prevent thrashing?
  User: Don’t run too many apps
  Process: efficient and predictable mem usage
  OS: Don’t over-commit memory, memory-aware scheduling policies, etc.