## Slide 1: Traps, Exceptions, System Calls, & Privileged Mode
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
P&H Chapter 4.9, pages 509–515, appendix B.7

## Slide 2
Operating Systems

## Slide 3: Control Transfers
Control Transfers to OS
Case 1: Program invokes OS
  eg: sbrk(), mmap(), sleep()
  Like a function call: invoke, do stuff, return results
Attempt #1: OS as a library
  Just a function call: JAL sbrk
  Standard calling conventions

## Slide 4: VM Hardware/Software Boundary
Virtual to physical address translation
Hardware (typical):
  Traverse PageTables on TLB miss, install TLB entries
  Update dirty bit in PTE when evicting
  Flush when PTBR changes
Software (typical):
  Decide when to do context switches, update PTBR
  Decide when to add, remove, modify PTEs and PDEs
    and invoke MMU to invalidate TLB entries
  Handle page faults: swap to/from disk, kill processes
Hardware (minimal):
  Notify OS on TLB miss; software does everything else

## Slide 5: Control Transfers
Control Transfers to OS
Case 1: Program invokes OS
  eg: sbrk(), mmap(), sleep()
  Like a function call: invoke, do stuff, return results
Case 2: Hardware invokes OS on behalf of program
  Page fault, divide by zero, arithmetic overflow, …
  OS takes corrective action; then restarts/kills program
  Can CPU simply fake this: a0 = cause JAL exception_handler

## Slide 6: Attempt #2:
Attempt #2: OS as a library + Exception Handler
Program invokes OS: regular calling convention
HW invokes OS:
  New registers: EPC, Cause, Vector*, …
  On exception, CPU does… EPC PC Cause  error/reason code PC  Vector
  Code at Vector does… take corrective action based on Cause return to EPC
* x86: via IDTR register and IDT; MIPS used a constant
Notes: Q: What does OS do?

## Slide 7: Sketch of Exception Handler
# MIPS exception vector is 0x80000180
.ktext 0x80000180
# EPC has offending PC, Cause has errcode
# (step 1) save *everything* but $k0, $k1
lui $k0, 0xB000
sw $1, 0($k0)
sw $2, 4($k0)
sw $3, 8($k0)
sw $4, 12($k0)
…
sw $31, 120($k0)
mflo $1
sw $1, 124($k0)
mfhi $1
sw $1, 128($k0)
…
* approximate
Notes: Observation 1: this code lives in upper “kernel reserved” half of memory
Observation 2: this had better be mapped (in pagetables of the running process)
Observation 3: this had better not be swapped to disk
Observation 4: we need a place in kernel memory to save state, with same restrictions
Observation 5: this is why we have $k0 and $k1 – because we can’t store to arbitrary locations without at least one register

## Slide 8: Sketch of Exception Handler
# MIPS exception vector is 0x80000180
.ktext 0x80000180
# EPC has offending PC, Cause has errcode
# (step 1) save *everything* but $k0, $k1
# (step 2) set up a usable OS context
li $sp, 0xFFFFFF00
li $fp, 0xFFFFFFFF
li $gp, …
* approximate
Notes: Observation 6: Can’t use process’ $sp, $gp (they could be broken / non-standard / paged out / …)

## Slide 9: Sketch of Exception Handler
# MIPS exception vector is 0x80000180
.ktext 0x80000180
# EPC has offending PC, Cause has errcode
# (step 1) save *everything* but $k0, $k1
# (step 2) set up a usable OS context
# (step 3) examine Cause register, and take corrective action
mfc0 $t0, Cause # move-from-coprocessor-0
if ($t0 == PAGE_FAULT) {
mfc0 $a0, BadVAddr # another dedicated register
jal kernel_handle_pagefault
} else if ($t0 == PROTECTION_FAULT) {
…
} else if ($t0 == DIV_BY_ZERO) {
…
}
* approximate
Notes: Observation 6: Can’t use process’ $sp, $gp (they could be broken / non-standard / paged out / …)

## Slide 10: Sketch of Exception Handler
# MIPS exception vector is 0x80000180
.ktext 0x80000180
# EPC has offending PC, Cause has errcode
# (step 1) save *everything* but $k0, $k1
# (step 2) set up a usable OS context
# (step 3) examine Cause register, and take corrective action
# (step 4) restore registers and return to where program left off
lui $k0, 0xB000
lw $1, 0($k0)
lw $2, 4($k0)
lw $3, 8($k0)
…
lw $31, 120($k0)
…
mfc0 $k1, EPC
jr $k1
* approximate
Notes: Observation 6: Can’t use process’ $sp, $gp (they could be broken / non-standard / paged out / …)

## Slide 11: Hardware/Software Boundary
Hardware Support:
  registers: EPC, Cause, Vector, BadVAddr, …
  instructions: mfc0, TLB flush/invalidate, cache flush, …
Hardware guarantees for precise exceptions:
  EPC points at offending instruction
  Earlier instructions are finished
  EPC and later instructions have not started
  Returning to EPC will pick up where we left off

## Slide 12: Double Faults, Triple Faults
  EPC points at offending inst
  Earlier inst are finished; EPC and later inst not started
  Returning to EPC will pick up where we left off
What could possibly go wrong?
Exception happens during exception handler… original EPC and Cause are lost
  Disable exceptions until current exception is resolved?
    MIPS: Status register has a bit for enable/disable
    turn exceptions back on just when returning to EPC
    works for issues that can be (temporarily) ignored
  Use a “double fault” exception handler for rest
    BSOD
  And if that faults? Triple fault  instant shutdown
Notes: double / triple faults
just before? just after? in the jump delay slot!

## Slide 13: Precise Exceptions
  EPC points at offending inst
  Earlier inst are finished; EPC and later inst not started
  Returning to EPC will pick up where we left off
What could possibly go wrong?
Multiple simultaneous exceptions in pipeline
    lw $4, 0($0) # page fault
    xxx $4, $5, $5 # illegal instruction
    add $2, $2, $3 # overflow
  need stalls to let earlier inst raise exception first
  even worse with speculative / “out-of-order” execution
Notes: simultaneous exceptions

## Slide 14: Precise Exceptions
  EPC points at offending inst
  Earlier inst are finished; EPC and later inst not started
  Returning to EPC will pick up where we left off
What could possibly go wrong?
Exception happened in delay slot
    jal prints
    lw $4, 0($0) # page fault
    …
  need more than just EPC to identify “where we left off”
Notes: exception in delay slot

## Slide 15: Precise Exceptions
  EPC points at offending inst
  Earlier inst are finished; EPC and later inst not started
  Returning to EPC will pick up where we left off
What could possibly go wrong?
Instructions with multiple faults or side effects
    store-and-update-register
    memory-to-memory-copy
    memory-fill, x86 “string” prefix, x86 “loop” prefix
  need more than just EPC to identify “where we left off”
  or: try to undo effects that have already happened
  or: have software try to finish the partially finished EPC
  or: all of the above
Notes: side effects

## Slide 16
“The interaction between branch delay slots and exception handling is extremely unpleasant and you'll be happier if you don't think about it.”
– Matt Welch

## Slide 17: Attempt #2: Recap
Attempt #2: Recap
Program invokes OS
  regular calling convention
HW invokes OS:
  precise exceptions vector to OS exception handler
  Drawbacks?

## Slide 18: Attempt #2 is broken
Drawbacks:
  Any program can muck with TLB, PageTables, OS code…
  A program can intercept exceptions of other programs
  OS can crash if program messes up $sp, $fp, $gp, …
Wrong: Make these instructions and registers available only to “OS Code”
  “OS Code” == any code above 0x80000000
  Program can still JAL into middle of OS functions
  Program can still muck with OS memory, pagetables, …

## Slide 19
Privileged Mode
aka Kernel Mode

## Slide 20: Operating System
Some things not available to untrusted programs:
  Exception registers, HALT instruction, MMU instructions, talk to I/O devices, OS memory, ...
Need trusted mediator: Operating System (OS)
  Safe control transfer
  Data isolation
P1
P2
P3
P4
VM
filesystem
net
driver
driver
disk
eth
MMU
Notes: user/kernel/hardware

## Slide 21: Privilege Mode
CPU Mode Bit / Privilege Level Status Register
Mode 0 = untrusted = user domain
  “Privileged” instructions and registers are disabled by CPU
Mode 1 = trusted = kernel domain
  All instructions and registers are enabled
Boot sequence:
  load first sector of disk (containing OS code) to well known address in memory
  Mode  1; PC  well known address
OS takes over…
  initialize devices, MMU, timers, etc.
  loads programs from disk, sets up pagetables, etc.
  Mode  0; PC  program entry point
(note: x86 has 4 levels x 3 dimensions, but nobody uses any but the 2 extremes)
Notes: boot sequence

## Slide 22: Privilege Mode
CPU Mode Bit / Privilege Level Status Register
Mode 0 = untrusted = user domain
  “Privileged” instructions and registers are disabled by CPU
Mode 1 = trusted = kernel domain
  All instructions and registers are enabled
Boot sequence:
  load first sector of disk (containing OS code) to well known address in memory
  Mode  1; PC  well known address
OS takes over…
  initialize devices, MMU, timers, etc.
  loads programs from disk, sets up pagetables, etc.
  Mode  0; PC  program entry point
(note: x86 has 4 levels x 3 dimensions, but nobody uses any but the 2 extremes)
Notes: boot sequence

## Slide 23: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous (planned), program-to-kernel transfer
  SYSCALL instruction in MIPS (various on x86)
Exception: Asynchronous, program-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
* real mechanisms, but nobody agrees on these terms

## Slide 24: Sample System Calls
System call examples:
putc(): Print character to screen
  Need to multiplex screen between competing programs
send(): Send a packet on the network
  Need to manipulate the internals of a device
sbrk(): Allocate a page
  Needs to update page tables & MMU
sleep(): put current prog to sleep, wake other
  Need to update page table base register

## Slide 25: System Calls
System call: Not just a function call
  Don’t let program jump just anywhere in OS code
  OS can’t trust program’s registers (sp, fp, gp, etc.)
SYSCALL instruction: safe transfer of control to OS
  Mode  0; Cause  syscall; PC  exception vector
MIPS system call convention:
  user program mostly normal (save temps, save ra, …)
  but: $v0 = system call number

## Slide 26: Invoking System Calls
int getc() {
asm("addiu $2, $0, 4");
asm("syscall");
}
char *gets(char *buf) {
while (...) {
buf[i] = getc();
}
}

## Slide 27: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  Compiler doesn’t know OS interface
Libraries implement standard API from system API
libc (standard C library):
  getc()  syscall
  sbrk()  syscall
  write()  syscall
  gets()  getc()
  printf()  write()
  malloc()  sbrk()
  …

## Slide 28: Protection Boundaries
user
kernel
Notes: draw: program, libc, kernel dispatch, syscall handler

## Slide 29: Where does OS live?
Kernel code and data lives above 0x80000000
In same virtual address space as user process?
  but… user code can modify kernel code and data!

## Slide 30: Where does OS live?
Kernel code and data lives above 0x80000000
In its own address space?
  all traps switch to a different address space [expensive]
  prints(“hi”) syscall is tricky [why?]

## Slide 31: Where does OS live?
Kernel code and data lives above 0x80000000
Solution
  map kernel code/data into all processes at same vaddr
  but use supervisor=1 protection bit on PTEs
  VM hardware enforces user/kernel isolation

## Slide 32
Interrupts

## Slide 33: Recap: Traps
 Map kernel into every process using supervisor PTEs
 Switch to kernel mode on trap, user mode on return
Syscall: Synchronous, program-to-kernel transfer
  user does caller-saves, invokes kernel via syscall
  kernel handles request, puts result in v0, and returns
Exception: Asynchronous, program-to-kernel transfer
  user div/load/store/… faults, CPU invokes kernel
  kernel saves everything, handles fault, restores, and returns
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
  kernel saves everything, handles event, restores, and returns

## Slide 34: Example: Clock Interrupt
Example: Clock Interrupt*
  Every N cycles, CPU causes exception with Cause = CLOCK_TICK
  OS can select N to get e.g. 1000 TICKs per second
.ktext 0x80000180
# (step 1) save *everything* but $k0, $k1 to 0xB0000000
# (step 2) set up a usable OS context
# (step 3) examine Cause register, take action
if (Cause == PAGE_FAULT) handle_pfault(BadVaddr)
else if (Cause == SYSCALL) dispatch_syscall($v0)
else if (Cause == CLOCK_TICK) schedule()
# (step 4) restore registers and return to where program left off
* not the CPU clock, but a programmable timer clock

## Slide 35: Scheduler
struct regs context[];
int ptbr[];
schedule() {
i = current_process;
j = pick_some_process();
if (i != j) {
current_process = j;
memcpy(context[i], 0xB0000000);
memcpy(0xB0000000, context[j]);
asm(“mtc0 Context, ptbr[j]”);
}
}

## Slide 36: Syscall vs. Interrupt
Syscall vs. Exceptions vs. Interrupts
Same mechanisms, but…
Syscall saves and restores much less state
Others save and restore full processor state
Interrupt arrival is unrelated to user code
Notes: most state