## Slide 1: Virtual Memory 3
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
P & H Chapter 5.4-5

## Slide 2: Announcements
PA3 available. Due Tuesday, April 19th
  Work with pairs
  Be responsible with new knowledge
  Scheduling a games night, possibly Friday, April 22nd
Next four weeks
  Two projects and one homeworks
  Prelim2 will be Thursday, April 28th
  PA4 will be final project (no final exam)
    Will not be able to use slip days

## Slide 3: Goals for Today
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching

## Slide 4
Making Virtual Memory Fast
  The Translation Lookaside Buffer (TLB)

## Slide 5: Translation Lookaside Buffer (TLB)
Hardware Translation Lookaside Buffer (TLB)
A small, very fast cache of recent address mappings
  TLB hit: avoids PageTable lookup
  TLB miss: do PageTable lookup, cache result for later

## Slide 6: TLB Diagram
V | R | W | X | D | 
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  | 0 | 
1 |  |  |  | 1 | 
0 |  |  |  |  | invalid
V | R | W | X | D | tag | ppn
V |  | 
0 |  | invalid
0 |  | invalid
0 |  | invalid
1 |  | 
0 |  | invalid
1 |  | 
1 |  | 
0 |  | invalid

## Slide 7: A TLB in the Memory Hierarchy
(1) Check TLB for vaddr (~ 1 cycle)
(2) TLB Miss: traverse PageTables for vaddr
(3a) PageTable has valid entry for in-memory page
  Load PageTable entry into TLB; try again (tens of cycles)
(3b) PageTable has entry for swapped-out (on-disk) page
  Page Fault: load from disk, fix PageTable, try again (millions of cycles)
(3c) PageTable has invalid entry
  Page Fault: kill process
CPU
TLB
Lookup
Cache
Mem
Disk
PageTable
Lookup
(2) TLB Hit
  compute paddr, send to cache
Notes: TLB miss in hardware usually, but not always
PageTable stuff in software

## Slide 8: TLB Coherency
TLB Coherency: What can go wrong?
A: PageTable or PageDir contents change
  swapping/paging activity, new shared pages, …
A: Page Table Base Register changes
  context switch between processes
Notes: Fully transparent

## Slide 9: Translation Lookaside Buffers (TLBs)
When PTE changes, PDE changes, PTBR changes….
Full Transparency: TLB coherency in hardware
  Flush TLB whenever PTBR register changes [easy – why?]
  Invalidate entries whenever PTE or PDE changes [hard – why?]
TLB coherency in software
If TLB has a no-write policy…
  OS invalidates entry after OS modifies page tables
  OS flushes TLB whenever OS does context switch
Notes: process ID could just be the PTBR for the process

## Slide 10: TLB Parameters
TLB parameters (typical)
  very small (64 – 256 entries), so very fast
  fully associative, or at least set associative
  tiny block size: why?
Intel Nehalem TLB (example)
  128-entry L1 Instruction TLB, 4-way LRU
  64-entry L1 Data TLB, 4-way LRU
  512-entry L2 Unified TLB, 4-way LRU

## Slide 11
Virtual Memory meets Caching
  Virtually vs. physically addressed caches
  Virtually vs. physically tagged caches

## Slide 12: Virtually Addressed Caching
Q: Can we remove the TLB from the critical path?
A: Virtually-Addressed Caches
CPU
TLB
Lookup
Virtually
Addressed
Cache
Mem
Disk
PageTable
Lookup
Notes: A: have to flush entire cache on context switch
A:
Doing synonym updates requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits

## Slide 13: Virtual vs. Physical Caches
CPU
Cache
SRAM
Memory
DRAM
addr
data
MMU
Cache
SRAM
MMU
CPU
Memory
DRAM
addr
data
Cache works on physical addresses
Cache works on virtual addresses
Q: What happens on context switch?
Q: What about virtual memory aliasing?
Q: So what’s wrong with physically addressed caches?
Notes: A1: Physically-addressed: nothing; Virtually-addressed: need to flush cache
A2: Physically-addressed: nothing; Virtually-addressed: problems

## Slide 14: Indexing vs. Tagging
Physically-Addressed Cache
  slow: requires TLB (and maybe PageTable) lookup first
Virtually-Indexed, Virtually Tagged Cache
  fast: start TLB lookup before cache lookup finishes
  PageTable changes (paging, context switch, etc.)
     need to purge stale cache lines (how?)
  Synonyms (two virtual mappings for one physical page)
     could end up in cache twice (very bad!)
Virtually-Indexed, Physically Tagged Cache
  ~fast: TLB lookup in parallel with cache lookup
  PageTable changes  no problem: phys. tag mismatch
  Synonyms  search and evict lines with same phys. tag
Virtually-Addressed Cache

## Slide 15: Typical Cache Setup
CPU
L2 Cache
SRAM
Memory
DRAM
addr
data
MMU
Typical L1: On-chip virtually addressed, physically tagged
Typical L2: On-chip physically addressed
Typical L3: On-chip …
L1 Cache
SRAM
TLB SRAM

## Slide 16: Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Direct, n-way, fully associative
What block is replaced on miss?
  LRU, Random, LFU, …
How are writes handled?
  No-write (w/ or w/o automatic invalidation)
  Write-back (fast, block at time)
  Write-through (simple, reason about consistency)
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 17: Summary of Cache Design Parameters
 | L1 | Paged Memory | TLB
Size (blocks) | 1/4k to 4k | 16k to 1M | 64 to 4k
Size (kB) | 16 to 64 | 1M to 4G | 2 to 16
Block size (B) | 16-64 | 4k to 64k | 4-32
Miss rates | 2%-5% | 10-4 to 10-5% | 0.01% to 2%
Miss penalty | 10-25 | 10M-100M | 100-1000