## Slide 1: I/O
Hakim Weatherspoon
CS 3410, Spring 2011
Computer Science
Cornell University
See: P&H Chapter 6.5-6

## Slide 2: Goals for Today
Computer System Organization
How to talk to device?
  Programmed I/O or Memory-Mapped I/O
How to get events?
  Polling or Interrupts
How to transfer lots of data?
  Direct Memory Access (DMA)

## Slide 3: Computer System Organization
Computer System =
Input + Output + Memory + Datapath + Control
CPU
Registers
Network
Video
bus
Memory
bus
Disk
USB
Audio
Keyboard
Mouse
Serial

## Slide 4: Challenge
How do we interface to other devices
  Keyboard
  Mouse
  Disk
  Network
  Display
  Programmable Timer (for clock ticks)
  Audio
  Printer(s)
  Camera
  iPod
  Scanner
  …

## Slide 5: Interconnects
Bad Idea #1: Put all devices on one interconnect
  We would have to replace all devices as we improve/change the interconnect
  keyboard speed == main memory speed ?!
CPU
Network
Video
Memory
Disk
Audio
Keyboard
Serial
Cache
interconnect

## Slide 6: I/O Controllers
Decouple via I/O Controllers and “Bridges”
  fast/expensive busses when needed; slow/cheap elsewhere
  I/O controllers to connect end devices
Notes: Graphics card lives on PCIe
Network card lives on PICe or PCI-X

## Slide 7: I/O Controllers
Decouple via I/O Controllers and “Bridges”
  fast/expensive busses when needed; slow/cheap elsewhere
  I/O controllers to connect end devices
Notes: Graphics card lives on PCIe
Network card lives on PICe or PCI-X

## Slide 8: Interconnecting Components
Interconnects are (were?) busses
  parallel set of wires for data and control
  shared channel
    multiple senders/receivers
    everyone can see all bus transactions
  bus protocol: rules for using the bus wires
Alternative (and increasingly common):
  dedicated point-to-point channels
Notes:   CPU – North Bridge / Memory Controller
  North Bridge – South Bridge / SuperIO

## Slide 9: Bus Parameters
Width = number of wires
Transfer size = data words per bus transaction
Synchronous (with a bus clock) or asynchronous (no bus clock / “self clocking”)

## Slide 10: Bus Types
Processor – Memory (“Front Side Bus”. Also QPI)
  Short, fast, & wide
  Mostly fixed topology, designed as a “chipset”
    CPU + Caches + Interconnect + Memory Controller
I/O and Peripheral busses (PCI, SCSI, USB, LPC, …)
  Longer, slower, & narrower
  Flexible topology, multiple/varied connections
  Interoperability standards for devices
  Connect to processor-memory bus through a bridge
Notes: Note: USB is not really a bus, it is really a network.

## Slide 11: Typical x86 PC I/O System
Notes: FSB: > 10 bytes wide
LPC = 4 bits wide

## Slide 12: Typical x86 PC I/O System
Notes: FSB: > 10 bytes wide
LPC = 4 bits wide

## Slide 13: I/O Device API
Typical I/O Device API
  a set of read-only or read/write registers
Command registers
  writing causes device to do something
Status registers
  reading indicates what device is doing, error codes, …
Data registers
  Write: transfer data to a device
  Read: transfer data from a device

## Slide 14
Simple (old) example: AT Keyboard Device
8-bit Status:
8-bit Cmd: 0xAA = “self test” 0xAE = “enable kbd” 0xED = “set LEDs”
…
8-bit Data: scancode (when reading) LED state (when writing) or …
PE | TO | AUXB | LOCK | AL2 | SYSF | IBS | OBS
Notes: IBS = input buffer status: 0 = waiting for commands, 1 = busy
OBS = output buffer status: 0 = waiting for data, 1 = data is available

## Slide 15: Communication Interface
Q: How does program OS code talk to device?
A: special instructions to talk over special busses
Programmed I/O
  inb $a, 0x64
  outb $a, 0x60
  Specifies: device, data, direction
  Protection: only allowed in kernel mode
*x86: $a implicit; also inw, outw, inh, outh, …

## Slide 16: Communication Interface
Q: How does program OS code talk to device?
A: Map registers into virtual address space
Memory-mapped I/O
  Accesses to certain addresses redirected to I/O devices
  Data goes over the memory bus
  Protection: via bits in pagetable entries
  OS+MMU+devices configure mappings

## Slide 17: Memory-Mapped I/O
Keyboard Registers
Video Registers & Memory
Audio Registers
Physical
Address
Space
RAM
Virtual
Address
Space

## Slide 18: Device Drivers
Programmed I/O
char read_kbd()
{
do {
sleep();
status = inb(0x64);
} while (!(status & 1));
return inb(0x60);
}
Memory Mapped I/O
struct kbd {
char status, pad[3];
char data, pad[3];
};
kbd *k = mmap(...);
char read_kbd()
{
do {
sleep();
status = k->status;
} while (!(status & 1));
return k->data;
}

## Slide 19: Communication Method
Q: How does program learn device is ready/done?
A: Polling: Periodically check I/O status register
  If device ready, do operation
  If device done, …
  If error, take action
Pro? Con?
  Predictable timing & inexpensive
  But: wastes CPU cycles if nothing to do
  Efficient if there is always work to do
Common in small, cheap, or real-time embedded systems
Sometimes for very active devices too…

## Slide 20: Communication Method
Q: How does program learn device is ready/done?
A: Interrupts: Device sends interrupt to CPU
  Cause identifies the interrupting device
  interrupt handler examines device, decides what to do
Priority interrupts
  Urgent events can interrupt lower-priority interrupt handling
  OS can disable defer interrupts
Notes: Con: unpredictable b/c event arrival depends on other devices’ activity

## Slide 21: Typical x86 PC I/O System
Notes: Show interrupt lines

## Slide 22: I/O Data Transfer
How to talk to device? Programmed I/O or Memory-Mapped I/O
How to get events? Polling or Interrupts
How to transfer lots of data?
disk->cmd = READ_4K_SECTOR;
disk->data = 12;
while (!(disk->status & 1) { }
for (i = 0..4k)
buf[i] = disk->data;

## Slide 23: DMA: Direct Memory Access
Programmed I/O xfer: Device  CPU  RAM
  for (i = 1 .. n)
  CPU issues read request
  Device puts data on bus & CPU reads into registers
  CPU writes data to memory
CPU
RAM
DISK

## Slide 24: I/O Data Transfer
Q: How to transfer lots of data efficiently?
A: Have device access memory directly
Direct memory access (DMA)
  OS provides starting address, length
  controller (or device) transfers data autonomously
  Interrupt on completion / error

## Slide 25: DMA: Direct Memory Access
Programmed I/O xfer: Device  CPU  RAM
  for (i = 1 .. n)
  CPU issues read request
  Device puts data on bus & CPU reads into registers
  CPU writes data to memory
DMA xfer: Device  RAM
  CPU sets up DMA request
  for (i = 1 ... n) Device puts data on bus & RAM accepts it
CPU
RAM
DISK
CPU
RAM
DISK

## Slide 26: DMA Example
DMA example: reading from audio (mic) input
  DMA engine on audio device… or I/O controller … or …
int dma_size = 4*PAGE_SIZE;
int *buf = alloc_dma(dma_size);
...
dev->mic_dma_baseaddr = (int)buf;
dev->mic_dma_count = dma_len;
dev->cmd = DEV_MIC_INPUT | DEV_INTERRUPT_ENABLE | DEV_DMA_ENABLE;

## Slide 27: DMA Issues (1): Addressing
Issue #1: DMA meets Virtual Memory
RAM: physical addresses
Programs: virtual addresses
Solution: DMA uses physical addresses
  OS uses physical address when setting up DMA
  OS allocates contiguous physical pages for DMA
  Or: OS splits xfer into page-sized chunks
    (many devices support DMA “chains” for this reason)
CPU
RAM
DISK
MMU

## Slide 28: DMA Example
DMA example: reading from audio (mic) input
  DMA engine on audio device… or I/O controller … or …
int dma_size = 4*PAGE_SIZE;
void *buf = alloc_dma(dma_size);
...
dev->mic_dma_baseaddr = virt_to_phys(buf);
dev->mic_dma_count = dma_len;
dev->cmd = DEV_MIC_INPUT | DEV_INTERRUPT_ENABLE | DEV_DMA_ENABLE;

## Slide 29: DMA Issues (1): Addressing
Issue #1: DMA meets Virtual Memory
RAM: physical addresses
Programs: virtual addresses
Solution 2: DMA uses virtual addresses
  OS sets up mappings on a mini-TLB
CPU
RAM
DISK
MMU
uTLB

## Slide 30: DMA Issues (2): Virtual Mem
Issue #2: DMA meets Paged Virtual Memory
DMA destination page may get swapped out
Solution: Pin the page before initiating DMA
Alternate solution: Bounce Buffer
  DMA to a pinned kernel page, then memcpy elsewhere
CPU
RAM
DISK

## Slide 31: DMA Issues (4): Caches
Issue #4: DMA meets Caching
DMA-related data could be cached in L1/L2
  DMA to Mem: cache is now stale
  DMA from Mem: dev gets stale data
Solution: (software enforced coherence)
  OS flushes some/all cache before DMA begins
  Or: don't touch pages during DMA
  Or: mark pages as uncacheable in page table entries
    (needed for Memory Mapped I/O too!)
CPU
RAM
DISK
L2

## Slide 32: DMA Issues (4): Caches
Issue #4: DMA meets Caching
DMA-related data could be cached in L1/L2
  DMA to Mem: cache is now stale
  DMA from Mem: dev gets stale data
Solution 2: (hardware coherence aka snooping)
  cache listens on bus, and conspires with RAM
  Dma to Mem: invalidate/update data seen on bus
  DMA from mem: cache services request if possible, otherwise RAM services
CPU
RAM
DISK
L2

## Slide 33: I/O Summary
How to talk to device? Programmed I/O or Memory-Mapped I/O
How to get events? Polling or Interrupts
How to transfer lots of data?
DMA