## Slide 1: xkcd/619

## Slide 2: Multicore & Parallel Processing
Guest Lecture: Kevin Walsh
CS 3410, Spring 2011
Computer Science
Cornell University

## Slide 3: Review
affected execution time
amount of improvement
+ execution time unaffected
Execution time after improvement =
Notes: Amdahl’s Law

## Slide 4: Problem Statement
Q: How to improve system performance?
 Increase CPU clock rate?
 But I/O speeds are limited
Disk, Memory, Networks, etc.
Recall: Amdahl’s Law
Solution: Parallelism

## Slide 5: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
Q: How to get more instruction level parallelism?
A: Deeper pipeline
Pipeline depth limited by…
    max clock speed (less work per stage  shorter clock cycle)
    min unit of work
    dependencies, hazards / forwarding logic
Notes: Draw pictures: 250MHz 1-stage; 500Mhz 2-stage; 1GHz 4-stage; 4GHz 16-stage

## Slide 6: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
Q: How to get more instruction level parallelism?
A: Multiple issue pipeline
    Start multiple instructions per clock cycle in duplicate stages
Notes: Draw picture; 4 stage, 4-way * 4GHz = 16B inst/cycles Next: Static issue

## Slide 7: Static Multiple Issue
Static Multiple Issue
a.k.a. Very Long Instruction Word (VLIW)
Compiler groups instructions to be issued together
  Packages them into “issue slots”
Q: How does HW detect and resolve hazards?
A: It doesn’t.
 Simple HW, assumes compiler avoids hazards
Example: Static Dual-Issue 32-bit MIPS
  Instructions come in pairs (64-bit aligned)
    One ALU/branch instruction (or nop)
    One load/store instruction (or nop)
Notes: show program, decode stage
Ideal CPI = 0.5

## Slide 8: Scheduling Example
Compiler scheduling for dual-issue MIPS…
TOP: lw $t0, 0($s1) # $t0 = A[i]
lw $t1, 4($s1) # $t1 = A[i+1] addu $t0, $t0, $s2 # add $s2 addu $t1, $t1, $s2 # add $s2 sw $t0, 0($s1) # store A[i] sw $t1, 4($s1) # store A[i+1] addi $s1, $s1, +8 # increment pointer bne $s1, $s3, TOP # continue if $s1!=end
ALU/branch slot Load/store slot cycle
TOP: nop lw $t0, 0($s1) 1
nop lw $t1, 4($s1) 2
addu $t0, $t0, $s2 nop 3
addu $t1, $t1, $s2 sw $t0, 0($s1) 4
addi $s1, $s1, +8 sw $t1, 4($s1) 5
bne $s1, $s3, TOP nop 6
Notes:   assume 1 delay slot for loads
  can move addi earlier
  CPI = 6 cycles / 8 instructions = 0.75
  CPI = 5 cycles / 8 instructions = 0.625

## Slide 9: Limits of Static Scheduling
Compiler scheduling for dual-issue MIPS…
lw $t0, 0($s1) # load A
addi $t0, $t0, +1 # increment A
sw $t0, 0($s1) # store A
lw $t0, 0($s2) # load B
addi $t0, $t0, +1 # increment B
sw $t0, 0($s2) # store B
ALU/branch slot Load/store slot cycle
nop lw $t0, 0($s1) 1
nop nop 2
addi $t0, $t0, +1 nop 3
nop sw $t0, 0($s1) 4
nop lw $t0, 0($s2) 5
nop nop 6
addi $t0, $t0, +1 nop 7
nop sw $t0, 0($s2) 8
Notes: Rename registers, move load B up, eliminate delay slot
But! s1 and s2 might be equal => Aliasing!

## Slide 10: Dynamic Multiple Issue
Dynamic Multiple Issue
a.k.a. SuperScalar Processor (c.f. Intel)
  CPU examines instruction stream and chooses multiple instructions to issue each cycle
  Compiler can help by reordering instructions….
  … but CPU is responsible for resolving hazards
Even better: Speculation/Out-of-order Execution
  Execute instructions as early as possible
  Aggressive register renaming
  Guess results of branches, loads, etc.
  Roll back if guesses were wrong
  Don’t commit results until all previous insts. are retired

## Slide 11: Does Multiple Issue Work?
Q: Does multiple issue / ILP work?
A: Kind of… but not as much as we’d like
Limiting factors?
  Programs dependencies
  Hard to detect dependencies  be conservative
    e.g. Pointer Aliasing: A[0] += 1; B[0] *= 2;
  Hard to expose parallelism
    Can only issue a few instructions ahead of PC
  Structural limits
    Memory delays and limited bandwidth
  Hard to keep pipelines full

## Slide 12: Power Efficiency
Q: Does multiple issue / ILP cost much?
A: Yes.
 Dynamic issue and speculation requires power
CPU | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
 Multiple simpler cores may be better?
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 13: Moore’s Law
486
286
8088
8080
8008
4004
386
Pentium
Atom
P4
Itanium 2
K8
K10
Dual-core Itanium 2
Notes: NVIDIA GF100 has 3B transistors

## Slide 14: Why Multicore?
Moore’s law
  A law about transistors
  Smaller means more transistors per die
  And smaller means faster too
But: Power consumption growing too…

## Slide 15: Power Limits
Hot Plate
Rocket Nozzle
Nuclear Reactor
Surface of Sun
Xeon
Notes: Intel Westmere: 32 nm = 0.032u, 130W / 240mm^2 = 54 W/cm^2

## Slide 16: Power Wall
Power = capacitance * voltage2 * frequency
In practice: Power ~ voltage3
Reducing voltage helps (a lot)
... so does reducing clock speed
Better cooling helps
The power wall
  We can’t reduce voltage further
  We can’t remove more heat

## Slide 17: Why Multicore?
Power
1.0x
1.0x
Performance
Single-Core
Power
1.2x
1.7x
Performance
Single-Core Overclocked +20%
Power
0.8x
0.51x
Performance
Single-Core
Underclocked -20%
1.6x
1.02x
Dual-Core
Underclocked -20%

## Slide 18: Inside the Processor
AMD Barcelona Quad-Core: 4 processor cores

## Slide 19: Inside the Processor
Intel Nehalem Hex-Core

## Slide 20: Hyperthreading
Multi-Core vs. Multi-Issue
Programs:
Num. Pipelines:
Pipeline Width:
Hyperthreads (Intel)
  Illusion of multiple cores on a single core
  Easy to keep HT pipelines full + share functional units
vs. HT
Notes: HT = MultiIssue + extra PCs and registers – dependency logic
HT = MultiCore – redundant functional units + hazard avoidance

## Slide 21: Example: All of the above
Notes: MultiCore: 8 processors dies * 8 cores per processor die
Hyperthreading: 2 HT per core
Dynamic Multi-Issue: 4 issue
Pipeline: 16 stages

## Slide 22: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  Balancing load over cores
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
Notes: Or hyperthreads

## Slide 23: Work Partitioning
Partition work so all cores have something to do

## Slide 24: Load Balancing
Load Balancing
Need to partition so all cores are actually working

## Slide 25: Amdahl’s Law
If tasks have a serial part and a parallel part…
Example:
step 1: divide input data into n pieces
step 2: do work on each piece
step 3: combine all results
Recall: Amdahl’s Law
As number of cores increases …
  time to execute parallel part?
  time to execute serial part?

## Slide 26: Amdahl’s Law
Notes: Underclocking messes up the ratios completely. Work through a 8x slowdown example.

## Slide 27: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  Balancing load over cores
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
Notes: Most is software, but hardware can help:
- communications (fast core-to-core interconnect)
- coordination and synchronization primitives (next time)