## Slide 1: Fast Adders
See: P&H Chapter 3.1-3, C.5-6

## Slide 2
Goals:
serial to parallel conversion
time vs. space tradeoffs
design choices

## Slide 3: 4-bit Ripple Carry Adder
A3
B3
R3
C4
A1
B1
R1
A2
B2
R2
A0
B0
C0
R0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb

## Slide 4: Observations
Every bit needs to wait for carry in.
Q: Can we compute Cin earlier?
A: carry look-ahead adder (CLA)

## Slide 5: Reasoning About Carries
For each bit, analyze situation independent of Cin
  Just based on (A,B) only
Q: When is Cout == 1, irrespective of Cin?
A: When A == 1 and B == 1 (this bit generates a carry, irrespective of Cin)
Q: When else might Cout == 1?
A: When A == 1 or B == 1, and Cin == 1 (this bit propagates carry from Cin to Cout)

## Slide 6: Carry Logic
Ai
Bi
gi
pi
Invent two new terms: propagator, generator
  g == 1 means this bit generates carry, irrespective of Cin
    g = AB
  p == 1 means this bit propagates Cin to Cout, but doesn’t generate carry
    p = A xor B
Performance?
  p and g generated in 1 gate delay after A and B arrive
  R is 2 gate delay after Cin arrives
Ri
Cin

## Slide 7: Carry Look-Ahead Logic
CLL inputs: p,g from all 4 bits, C0 CLL outputs: all carry bits (using just 2 gate delays)
C1 = g0 + p0C0
C2 = g1 + p1C1 = g1 + p1(g0 + p0C0) = g1 + p1g0 + p1p0C0
C3 = g2 + p2C2 = g2 + p2g1 + p2p1g0 + p2p1p0C0
C4 = g3 + p3C3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0C0
C3
C2
C1
C0
CLL (carry look-ahead logic)
C4
g
p
A1
B1
g
p
A3
B3
g
p
A2
B2
g
p
A0
B0
C0
Notes: Given A,B’s, all p,g’s are generated in 1 gate delay in parallel.
Given all p,g’s, all C’s are generated in 2 gate delay in parallel.
Given all C’s, all R’s are generated in 2 gate delay in parallel.
Sequential operation in RCA is made into parallel operation!!

## Slide 8: 4-bit CLA
CLL (carry look-ahead logic)
C4
g
p
A1
B1
g
p
A3
B3
g
p
A2
B2
g
p
A0
B0
C0
R3
R2
R1
R0
Notes: Given A,B’s, all p,g’s are generated in 1 gate delay in parallel.
Given all p,g’s, all C’s are generated in 2 gate delay in parallel.
Given all C’s, all R’s are generated in 2 gate delay in parallel.
Sequential operation in RCA is made into parallel operation!!

## Slide 9: Space Time Tradeoff
 | Space | Time
4 Bit Ripple | 4 x 9 = 36 gates (4 input) | 4 x 2 = 8 gate delays
4 Bit Look-Ahead | 4 x 11 + 14 = 58 gates (5 input) | 5 gate delays
16 Bit Ripple |  | 
16 Bit Look-Ahead |  | 
64 Bit Ripple | 64 x 9 = 576 gates (4 input) | 64 x 2 = 128 gate delays
64 Bit Look-Ahead | 64 x 11 + 2144 = 2848 gates (65 input) | 5 gate delays
16 Bit Ripple | 16 x 9 = 144 gates (4 input) | 16 x 2 = 32 gate delays
 | 16 x 11 + 152 = 328 gates (17 input) | 5 gate delays

## Slide 10: Carry-Skip Adders
Only compute some fast carry signals
C0
C16

## Slide 11: Carry-Skip Adders
Carry-Skip Adder Only compute some fast carry signals
C0
C16
compute C8
Time: ~ 2x faster than ripple
Space: O(N) extra gates, O(N) gate inputs

## Slide 12: Hybrid Adders
Hybrid Approach
4-bit
CLA
4-bit
CLA
C16
4-bit CLA
4-bit
CLA
C0
C4
C8
C12
Carry ripples from lsb to msb
A7..4
B7..4
A15..8
B15..8
A11..8
B11..8
A3..0
B3..0
R15..8
R11..8
R7..4
R3..0

## Slide 13: Hierarchical
Hierarchical Approach
CLL (carry look-ahead logic)
C16
4-bit
g
p
A7..4
B7..4
4-bit
g
p
A15..8
B15..8
4-bit
g
p
A11..8
B11..8
4-bit
g
p
A3..0
B3..0
C0
4-bit CLA
R15..8
4-bit
CLA
R11..8
4-bit
CLA
R7..4
4-bit
CLA
R3..0

## Slide 14: Example Programs
r4 = (r1 + r2) | r3
r8 = 4*r3 + r4 – 1
r9 = 9
ADDU rd, rs, rt
SUBU rd, rs, rt
OR rd, rs, rt
XOR rd, rs, rt
NOR rd, rs rt
Notes: -1: NOR r1, r0, r0
1: SUB r1, r0, r1
2: ADDU r2, r2, r2
4: ADDU r2, r2, r2
8: ADDU r2, r2, r2
9: ADDU r9, r1, r2

## Slide 15: Arithmetic and Logic
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
R-type instruction

## Slide 16: Shift
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
shamt
R-type instruction

## Slide 17: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst
I-type instruction

## Slide 18: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst
16
I-type Instruction
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)