## Slide 1: Numbers & Arithmetic
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See: P&H Chapter 2.4 - 2.6, 3.2, C.5 – C.6

## Slide 2: Goals for today
Today
  Review Logic Minimization
  Build a circuit (e.g. voting machine)
  Number representations
  Building blocks (encoders, decoders, multiplexors)
Binary Operations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Subtraction (two’s compliment)
  Performance

## Slide 3: Logic Minimization
How to implement a desired function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 4: Logic Minimization
How to implement a desired function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
sum of products:
OR of all minterms where out=1
corollary: any combinational circuit can be implemented in two levels of logic (ignoring inverters)
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c

## Slide 5: Karnaugh Maps
        How does one find the most efficient equation?
          Manipulate algebraically until…?
          Use Karnaugh maps (optimize visually)
          Use a software optimizer
          For large circuits
          Decomposition & reuse of building blocks

## Slide 6: Minimization with Karnaugh maps (1)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  abc + abc + abc + abc

## Slide 7: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  abc + abc + abc + abc
Karnaugh maps identify which inputs are (ir)relevant to the output
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 8: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  abc + abc + abc + abc
Karnaugh map minimization
  Cover all 1’s
  Group adjacent blocks of 2n 1’s that yield a rectangular shape
  Encode the common features of the rectangle
    out = ab + ac
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 9: Karnaugh Minimization Tricks (1)
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 10: Karnaugh Minimization Tricks (1)
Minterms can overlap
  out = bc + ac + ab
Minterms can span 2, 4, 8 or more cells
  out = c + ab
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 11: Karnaugh Minimization Tricks (2)
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 12: Karnaugh Minimization Tricks (2)
The map wraps around
  out = bd
  out = bd
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 13: Karnaugh Minimization Tricks (3)
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 14: Karnaugh Minimization Tricks (3)
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out = d
  assume middle x’s = 0
  assume 4th column x = 1
  out = bd
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 15: Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d
Notes: What is the truth table

## Slide 16: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build a truth table
  = abd + abd + a bd + a b d
a
b
d

## Slide 17: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build the Karnaugh map
a
b
d
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab

## Slide 18: Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Derive Minimal Logic Equation
  out = ad + bd
a
b
d
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab

## Slide 19: Multiplexer Implementation
d
out
b
a
00 01 11 10
0
1
d
ab
Derive Minimal Logic Equation
  out = ad + bd
0 | 0 | 1 | 1
0 | 1 | 1 | 0
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d

## Slide 20: Logic Gates
One can buy gates separately
  ex. 74xxx series of integrated circuits
  cost ~$1 per chip, mostly for packaging and testing
Cumbersome, but possible to build devices using gates put together manually

## Slide 21: Integrated Circuits
Or one can manufacture a complete design using a custom mask
Intel Westmere has approximately 1.17 billion transistors

## Slide 22: Recap
We can now implement any logic circuit
  Can do it efficiently, using Karnaugh maps to find the minimal terms required
  Can use either NAND or NOR gates to implement the logic circuit
  Can use P- and N-transistors to implement NAND or NOR gates

## Slide 23: Voting machine
Lets build something interesting
A voting machine
Assume:
  A vote is recorded on a piece of paper,
  by punching out a hole,
  there are at most 7 choices
  we will not worry about “hanging chads” or “invalids”

## Slide 24: Voting machine
For now, let’s just display the numerical identifier to the ballot supervisor
  we won’t do counting yet, just decoding
  we can use four photo-sensitive transistors to find out which hole is punched out
A photo-sensitive transistor detects the presence of light
Photo-sensitive material triggers the gate

## Slide 25: Ballot Reading
  Input: paper with a hole in it
  Output: number the ballot supervisor can record
Ballots
The 3410 optical scan
vote counter reader
machine
Notes: Input: paper with at exactly one mark
Datapath: process current ballot
Output: a number the supervisor can record
Memory & control: none for now

## Slide 26: Input
Photo-sensitive transistor
  photons replenish gate depletion region
  can distinguish dark and light spots on paper
Use array of N sensors for voting machine input
i0
i1
i2
i3
i5
i4
i6
Vdd

## Slide 27: Output
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0

## Slide 28: Block Diagram
detect
8
N
Notes: could do big combinatorial circuit
truth table too large: 2^N rows
no possibility for re-use of components
routing N wires is expensive

## Slide 29: Encoders
N might be large
Routing wires is expensive
More efficient encoding?
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Notes: N possible inputs -> log2(N) wires to encode

## Slide 30: Number Representations
Base 10 - Decimal
Just as easily use other bases
  Base 2 - Binary
  Base 8 - Octal
  Base 16 - Hexadecimal
6 3 7
102 101 100

## Slide 31: Counting
Counting

## Slide 32: Base Conversion
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
Notes: 637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 33: Base Conversion
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
Notes: 637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 34: Base Conversion
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
Notes: 637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 35: Hexadecimal, Binary, Octal Conversions

## Slide 36: Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 37: Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  | o2 | o1 | o0
0 | 0 | 0 | 0 |  | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 0 | 0 | 1
0 | 1 | 0 | 0 |  | 0 | 1 | 0
0 | 0 | 1 | 0 |  | 0 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0
o0
o1
o2
o2 = abcd
o1 = abcd + abcd
o0 = abcd + abcd
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 38: Ballot Reading
detect
enc
8
3
8

## Slide 39: Ballot Reading
Ok, we built first half of the machine
Need to display the result
Ballots
The 3410 optical scan
vote counter reader machine

## Slide 40: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 41: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 

## Slide 42: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 43: Ballot Reading and Display
Ballots
The 3410 optical scan
vote counter reader
machine
detect
enc
8
3
7
7LED decode

## Slide 44: Building Blocks
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 45: Administrivia
Make sure you are
Registered for class, can access CMS
Have a Section you can go to
Have project partner in same Lab Section
Lab1 and HW1 are out
Both due in one week, next Monday, start early
Work alone
But, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab
Homework Help Session
Wednesday and Friday from 3:30-5:30pm
Location: 203 Thurston

## Slide 46: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2012sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 28th
  Thursday, March 29th
  April 26th
Schedule is subject to change

## Slide 47: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
183 + 254
001110
+ 011100

## Slide 48: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
R
C

## Slide 49: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
A
B
R
Cout
Cin

## Slide 50: 4-bit Adder
4-Bit Full Adder
Adds two 4-bit numbers and carry in
Computes 4-bit result and carry out
Can be cascaded
A[4]
B[4]
R[4]
Cout
Cin

## Slide 51: 4-bit Adder
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Cin
Notes: carry-out = overflow indicates result does not fit in 4 bits

## Slide 52: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Cin

## Slide 53: Arithmetic with Negative Numbers
Addition with negatives:
  pos + pos  add magnitudes, result positive
  neg + neg  add magnitudes, result negative
  pos + neg  subtract smaller magnitude, keep sign of bigger magnitude

## Slide 54: First Attempt: Sign/Magnitude Representation
First Attempt: Sign/Magnitude Representation
1 bit for sign (0=positive, 1=negative)
N-1 bits for magnitude
Notes: problems? two zeros, circuit still complicated

## Slide 55: Two’s Complement Representation
Better: Two’s Complement Representation
Leading 1’s for negative numbers
To negate any number:
    complement all the bits
    then add 1
Notes: add 1 and *discard carry*

## Slide 56: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives
(two’s complement: flip then add 1):
~0 = 1111 -0 = 0000
~1 = 1110 -1 = 1111
~2 = 1101 -2 = 1110
~3 = 1100 -3 = 1101
~4 = 1011 -4 = 1100
~5 = 1010 -5 = 1011
~3 = 1001 -6 = 1010
~7 = 1000 -7 = 1001
~8 = 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 57: Two’s Complement Facts
Signed two’s complement
  Negative numbers have leading 1’s
  zero is unique: +0 = - 0
  wraps from largest positive to largest negative
N bits can be used to represent
  unsigned:
    eg: 8 bits 
  signed (two’s complement):
    ex: 8 bits 

## Slide 58: Sign Extension & Truncation
Extending to larger size
Truncate to smaller size
  Copy the leftmost bit into new leading bits
    For positive number, put 0’s in new leading bits
    For negative number, put 1’s in new leading bits
  Drop leading bits so long as sign doesn’t change

## Slide 59: Two’s Complement Addition
Addition with two’s complement signed numbers
Perform addition as usual, regardless of sign (it just works)
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
Cout
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)

## Slide 60: Diversion: 10’s Complement
How does that work?
-154 +283

## Slide 61: Overflow
Overflow
  adding a negative and a positive?
  adding two positives?
  adding two negatives?
Rule of thumb:
Overflow happened iff carry into msb != carry out of msb

## Slide 62: Two’s Complement Adder
Two’s Complement Adder with overflow detection
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
over flow
0

## Slide 63: Binary Subtraction
Two’s Complement Subtraction
Lazy approach
A – B = A + (-B) = A + (B + 1)
R0
R1
R2
R3
over flow
1
A0
B0
A1
B1
A2
B2
A3
B3
Q: What if (-B) overflows?
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 64: A Calculator
decoder
8
8
S 0=add
1=sub
A
B
8

## Slide 65: A Calculator
0
1
adder
mux
mux
decoder
8
8
8
8
8
S
A
B
8
Notes: red herring? constants into mux

## Slide 66: Efficiency and Generality
  Is this design fast enough?
  Can we generalize to 32 bits? 64? more?
A0 B0
R0
A1 B1
R1
A2 B2
R2
A3 B3
R3
C0

## Slide 67: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 68: 4-bit Ripple Carry Adder
A3
B3
R3
C4
A1
B1
R1
A2
B2
R2
A0
B0
C0
R0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb

## Slide 69: Summary
We can now implement any combinational (combinatorial) logic circuit
  Decompose large circuit into manageable blocks
    Encoders, Decoders, Multiplexors, Adders, ...
  Design each block
    Binary encoded numbers for compactness
  Can implement circuits using NAND or NOR gates
  Can implement gates using use P- and N-transistors
  And can add and subtract numbers (in two’s compliment)!
  Next time, state and finite state machines…