## Slide 1: State & Finite State Machines
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H Appendix C.7. C.8, C.10, C.11

## Slide 2: Big Picture: Building a Processor
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 3: Stateful Components
Until now is combinatorial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 4: How can we store and change values?
(a)
(b)
(c)
B
A
C
Ballots
How do we create
vote counter
machine
detect
enc
8
3
7
7LED decode
A
B
S
R
Q
Q
(d) All the above
(e) None

## Slide 5: Unstable Devices
B
A
C

## Slide 6: Bistable Devices
In stable state, A = B
How do we change the state?
A
B
A
B
1
A
B
1
0
0
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 7: SR Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
Q
S | R | Q | Q
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 8: SR Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S=1 and R=1 ?
S
R
Q
Q
S | R | Q | Q
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire

## Slide 9: SR Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S=1 and R=1 ?
S
R
Q
Q
S | R | Q | Q
0 | 0 | Q | Q
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
Q
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire

## Slide 10: (Unclocked) D Latch
Data (D) Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (…after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
D
S
R
Q
Q
S
R
Q
Q
D
D | Q | Q
0 |  | 
1 |  | 
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 11: (Unclocked) D Latch
Data (D) Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (…after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
D
S
R
Q
Q
S
R
Q
Q
D
D | Q | Q
0 | 0 | 1
1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 12: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge

## Slide 13: Edge-triggering
Can design circuits to change on the rising or falling edge
Trigger on rising edge = positive edge-triggered
Trigger on falling edge = negative edge-triggered
Inputs must be stable just before the triggering edge
input
clock

## Slide 14: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 15: D Latch with Clock
S
R
D
clk
Q
Q
S | R | Q | Q
0 | 0 | Q | Q
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
clk | D | Q | Q
0 | 0 | Q | Q
0 | 1 | Q | Q
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 16: D Latch with Clock
S
R
D
clk
Q
Q
clk | D | Q | Q
0 | 0 | Q | Q
0 | 1 | Q | Q
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 17: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data is captured when clock is high
Outputs change only on falling edges
D
Q
Q
D
Q
Q
L
L
clk
D
X
Q
c
X
c
Q
Q
D
clk
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 18: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg

## Slide 19: Clock Methodology
Clock Methodology
Negative edge, synchronous
    Signals must be stable near falling clock edge
Positive edge synchronous
Asynchronous, multiple clocks, . . .
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 20: Metastability and Asynchronous Inputs
Q: What happens if select input changes near clock edge?
A) Multiplexor selects input 0
B) Multiplexor selects input 1
C) Multiplexor chooses either input
D) Unknown
E) None above
A: Google “Buridan’s Principle” by Leslie Lamport
1-bit reg
Clk
0
1
select

## Slide 21: An Example: What will this circuit do?
32-bit
reg
Clk
+1
Run
WE
R
Reset
Decoder

## Slide 22: Recap
We can now build interesting devices with sensors
  Using combinatorial logic
We can also store data values
  In state-holding elements
  Coupled with clocks

## Slide 23: Administrivia
Make sure partner in same Lab Section this week
Lab2 is out
Due in one week, next Monday, start early
Work alone
But, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab
No Homework this week

## Slide 24: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2012sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 28th
  Thursday, March 29th
  Thursday, April 26th
Schedule is subject to change

## Slide 25: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  20% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 26: Finite State Machines

## Slide 27: Revisit Voting Machine
Ballots
How do we create
a vote counter
machine
detect
enc
8
3
7
7LED decode

## Slide 28: Revisit Voting Machine
mux
32
...
reg
detect
enc
3
decoder (3-to-8)
32
32
32
LED dec
3
WE
+1
reg
WE
reg
WE
reg
WE
mux
D
V

## Slide 29: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 30: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 31: Revisit Voting Machine
mux
32
...
reg
detect
enc
3
decoder (3-to-8)
32
32
32
LED dec
3
WE
+1
reg
WE
reg
WE
reg
WE
mux

## Slide 32: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 33: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 34: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: = up or = down
Output: = on or = off
States: = A, = B, = C, or = D

## Slide 35: FSM Example
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 1=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 36: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 37: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 38: Moore Machine Example
Legend
state out
input
startout
A off
B on
C off
D on
down
up
down
down
up
down
up
up
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 39: Example: Digital Door Lock
Digital Door Lock
Inputs:
keycodes from keypad
clock
Outputs:
“unlock” signal
display how many keys pressed so far

## Slide 40: Door Lock: Inputs
Assumptions:
signals are synchronized to clock
Password is B-A-B
K
A
B
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed

## Slide 41: Door Lock: Outputs
Assumptions:
High pulse on U unlocks door
U
D3D2D1D0
4
LED dec
8

## Slide 42: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
any
else
else
B3
”3”
else

## Slide 43: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else

## Slide 44: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Output
Cur. State | Output

## Slide 45: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Output
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”

## Slide 46: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Input | Next State
Cur. State | Input | Next State

## Slide 47: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Input | Next State
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle

## Slide 48: State Table Encoding
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”
U
D3D2D1D0
4
dec
8
D3 | D2 | D1 | D0 | U
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
R
P
Q
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed
K | A | B
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
x | x | x
0 | 0 | 0
1 | x | x
0 | 0 | 0
1 | x | x
S2 | S1 | S0
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
State | S2 | S1 | S0
Idle | 0 | 0 | 0
G1 | 0 | 0 | 1
G2 | 0 | 1 | 0
G3 | 0 | 1 | 1
B1 | 1 | 0 | 0
B2 | 1 | 0 | 1
S2 | S1 | S0 |  | S’2 | S’1 | S’0
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 0 |  | 0 | 0 | 1
0 | 0 | 0 |  | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 1
0 | 0 | 1 |  | 0 | 1 | 0
0 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 0 | 1 |  | 0 | 0 | 0

## Slide 49: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
A
B
C
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 50: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes
  But be wary of asynchronous (un-clocked) inputs
  State Machines or Ad-Hoc Circuits