## Slide 1: Processor
Han Wang
CS3410, Spring 2012
Computer Science
Cornell University
See P&H Chapter 2.16-20, 4.1-4

## Slide 2: Announcements
Project 1 Available
Design Document due in one week.
Final Design due in three weeks.
Work in group of 2.
Use your resources
  FAQ, class notes, book, Lab sections, office hours, Piazza
Make sure you
  Registered for class, can access CMS, have a Section, and have a project partner
  Check online syllabus/schedule, review slides and lecture notes, Office Hours.

## Slide 3: MIPS Register file
MIPS register file
  32 registers, 32-bits each (with r0 wired to zero)
  Write port indexed via RW
    Writes occur on falling edge but only if WE is high
  Read ports indexed via RA, RB
clk
W
32
A
B
r1
r2
…
r31
5
5
5
WE
RW
RA
RB
32
32

## Slide 4: MIPS Register file
Registers
  Numbered from 0 to 31.
  Each register can be referred by number or name.
  $0, $1, $2, $3 … $31
  Or, by convention, each register has a name.
    $16 - $23  $s0 - $s7
    $8 - $15  $t0 - $t7
    $0 is always $zero.
    Patterson and Hennessy p121.

## Slide 5: MIPS Memory
MIPS Memory
  Up to 32-bit address
  32-bit data (but byte addressed)
  Enable + 2 bit memory control
    00: read word (4 byte aligned)
    01: write byte
    10: write halfword (2 byte aligned)
    11: write word (4 byte aligned)
memory
≤ 32
addr
2
mc
32
32
E

## Slide 6: Basic Computer System
Let’s build a MIPS CPU
  …but using (modified) Harvard architecture
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 7: Agenda
Stages of datapath
Datapath Walkthroughs
Detailed design / Instruction format

## Slide 8: Levels of Interpretation
High Level Language
  C, Java, Python, Ruby, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Assembly Language
  No symbols (except labels)
  One operation per statement
Machine Langauge
  Binary-encoded assembly
  Labels become addresses
ALU, Control, Register File, …
Machine Implementation

## Slide 9: Instruction Set Architecture
Instruction Set Architecture (ISA)
  Different CPU architecture specifies different set of instructions. Intel x86, IBM PowerPC, Sun Sparc, MIPS, etc.
MIPS
  ≈ 200 instructions, 32 bits each, 3 formats
    mostly orthogonal
  all operands in registers
    almost all are 32 bits each, can be used interchangeably
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in special registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]

## Slide 10: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  unconditional jumps
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 11: Addition and Subtraction
Addition
  add $s0 $s2 $s3 (in MIPS)
  Equivalent to a = b + c (in C)
    $s0, $s2, $s3 are associated with a, b and c.
Subtraction
  sub $s0 $s2 $s3 (in MIPS)
  Equivalent to d = e – f (in C)
    $s0, $s2, $s3 are associated with d, e and f.

## Slide 12: Five Stages of MIPS datapath
Basic CPU execution loop
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
addu $s0, $s2, $s3
slti $s0, $s2, 4
lw $s0, 20($s3)
j 0xdeadbeef

## Slide 13: Stages of datapath (1/5)
Stage 1: Instruction Fetch
  Fetch 32-bit instruction from memory. (Instruction cache or memory)
  Increment PC accordingly.
    +4, byte addressing
    +N

## Slide 14: Stages of datapath (2/5)
Stage 2: Instruction Decode
  Gather data from the instruction
  Read opcode to determine instruction type and field length
  Read in data from register file
    for addu, read two registers.
    for addi, read one registers.
    for jal, read no registers.

## Slide 15: Stages of datapath (3/5)
Stage 3: Execution (ALU)
  Useful work is done here (+, -, *, /), shift, logic operation, comparison (slt).
  Load/Store?
    lw $t2, 32($t3)
    Compute the address of the memory.

## Slide 16: Stages of datapath (4/5)
Stage 4: Memory access
  Used by load and store instructions only.
  Other instructions will skip this stage.
  This stage is expected to be fast, why?

## Slide 17: Stages of datapath (5/5)
Stage 5:
  For instructions that need to write value to register.
  Examples: arithmetic, logic, shift, etc, load.
  Store, branches, jump??

## Slide 18: Datapath and Clocking
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB

## Slide 19: Datapath walkthrough
addu $s0, $s2, $s3 # s0 = s2 + s3
  Stage 1: fetch instruction, increment PC
  Stage 2: decode to determine it is an addu, then read s2 and s3.
  Stage 3: add s2 and s3
  Stage 4: skip
  Stage 5: write result to s0

## Slide 20: Example: ADDU instruction
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem

## Slide 21: Datapath walkthrough
slti $s0, $s2, 4
  #if (s2 < 4), s0 = 1, else s0 = 0
  Stage 1: fetch instruction, increment PC.
  Stage 2: decode to determine it is a slti, then read register s2.
  Stage 3: compare s2 with 4.
  Stage 4: do nothing
  Stage 5: write result to s0.

## Slide 22: Example: SLTI instruction
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem

## Slide 23: Datapath walkthrough
lw $s0, 20($s3) # s0 = Mem[s3+20]
    R[rt] = M[R[rs] + SignExtImm]
  Stage 1: fetch instruction, increment PC.
  Stage 2: decode to determine it is lw, then read register s3.
  Stage 3: add 20 to s3 to compute address.
  Stage 4: access memory, read value at memory address s3+20
  Stage 5: write value to s0.

## Slide 24: Example: LW instruction
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem

## Slide 25: Datapath walkthrough
j 0xdeadbeef
    PC = Jumpaddr
  Stage 1: Fetch instruction, increment PC.
  Stage 2: decode and determine it is a jal, update PC to 0xdeadbeef.
  Stage 3: skip
  Stage 4: skip
  Stage 5: skip

## Slide 26: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 27: Arithmetic Instructions
op | rs | rt | rd | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x21 | ADDU rd, rs, rt | R[rd] = R[rs] + R[rt]
0x0 | 0x23 | SUBU rd, rs, rt | R[rd] = R[rs] – R[rt]
0x0 | 0x25 | OR rd, rs, rt | R[rd] = R[rs] ¦ R[rt]
0x0 | 0x26 | XOR rd, rs, rt | R[rd] = R[rs]  R[rt]
0x0 | 0x27 | NOR rd, rs rt | R[rd] = ~ ( R[rs] ¦ R[rt] )
00000001000001100010000000100110
R-Type

## Slide 28: Instruction Fetch
Instruction Fetch Circuit
  Fetch instruction from memory
  Calculate address of next instruction
  Repeat
Program Memory
inst
32
PC
2
00
32
+4

## Slide 29: Arithmetic and Logic
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4

## Slide 30: Example Programs
r4 = (r1 + r2) | r3
r8 = 4*r3 + r4 – 1
r9 = 9
ADDU rd, rs, rt
SUBU rd, rs, rt
OR rd, rs, rt
XOR rd, rs, rt
NOR rd, rs rt
Notes: -1: NOR r1, r0, r0
1: SUB r1, r0, r1
2: ADDU r2, r2, r2
4: ADDU r2, r2, r2
8: ADDU r2, r2, r2
9: ADDU r9, r1, r2

## Slide 31
Instruction fetch + decode + ALU
= Babbage’s engine
+ speed
+ reliability
– hand crank
Notes: A Babbage engine allows the values of the polynomial to be produced without ever having to multiply. A babbage engine only needs to be able to add!
This is why a babbage engine is also called a difference engine
A Babbage Engine (Difference Engine) is an automatic, mechanical calculator designed to tabulate polynomial functions. Both logarithmic and trigonometric functions can be approximated by polynomials, so a difference engine can compute many useful sets of numbers. -- http://en.wikipedia.org/wiki/Difference_engine

## Slide 32: Arithmetic Instructions: Shift
op | - | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rs, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rs, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rs, shamt | R[rd] = R[rs] >> shamt (sign ext.)
00000000000001000100000110000011
ex: r5 = r3 * 8
R-Type

## Slide 33: Shift
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
shamt

## Slide 34: Arithmetic Instructions: Immediates
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + imm
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & imm
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ imm
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + sign_extend(imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)
op | rs | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00100100101001010000000000000101
I-Type
ex: r5 += 5
ex: r9 = -1
ex: r9 = 65535

## Slide 35: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 36: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 37: Arithmetic Instructions: Immediates
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00111100000001010000000000000101
I-Type
ex: r5 = 0xdeadbeef

## Slide 38: Immediates
5
imm
5
5
control
extend
+4
shamt
control
Reg. File
PC
Prog.
Mem
ALU
inst
16
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 39: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 40: Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10100100101000010000000000000010
base + offset addressing
I-Type
signed offsets

## Slide 41: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 42: Example
int h, A[];
A[12] = h + A[8];
Notes: lw, t0, 32(s3)
add t0, s2, t0
sw t0, 48(s3)

## Slide 43: Control Flow: Absolute Jump
Absolute addressing for jumps
  Jump from 0x30000000 to 0x20000000? NO Reverse? NO
    But: Jumps from 0x2FFFFFFF to 0x3xxxxxxx are possible, but not reverse
  Trade-off: out-of-region jumps vs. 32-bit instruction encoding
MIPS Quirk:
  jump targets computed using already incremented PC
op | mnemonic | description
0x2 | J target | PC = target
op | immediate
6 bits | 26 bits
00001010100001001000011000000011
J-Type
op | mnemonic | description
0x2 | J target | PC = target ¦¦ 00
op | mnemonic | description
0x2 | J target | PC = (PC+4)31..28 ¦¦ target ¦¦ 00

## Slide 44: Absolute Jump
long jump? computed jump?
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 45: Control Flow: Jump Register
op | rs | - | - | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R-Type

## Slide 46: Jump Register
+4
||
tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 47: Examples (2)
jump to 0xabcd1234
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe00
else jump to 0xabcd1234

## Slide 48: Examples (2)
jump to 0xabcd1234
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe0
else jump to 0xabcd1234

## Slide 49: Control Flow: Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
00010000101000010000000000000011
signed offsets
I-Type

## Slide 50: Examples (3)
if (i == j) { i = i * 4; }
else { j = i - j; }
s1
s0

## Slide 51: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp

## Slide 52: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp

## Slide 53: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)

## Slide 54: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp

## Slide 55: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 PC = (PC+4)32..29 ¦¦ target ¦¦ 00
op | immediate
6 bits | 26 bits
00001100000001001000011000000010
J-Type

## Slide 56: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4

## Slide 57: Memory Layout
Examples:
# r5 contains 0x5 sb r5, 2(r0)
M[R[rs] + SigExtImm](7:0) = R[rd](7:0) lb r6, 2(r0) sw r5, 8(r0) lb r7, 8(r0) lb r8, 11(r0)
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff

## Slide 58: Endianness
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word

## Slide 59: Next Time
CPU Performance
Pipelined CPU