## Slide 1: MIPS Pipeline
See P&H Chapter 4.6

## Slide 2: A Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
Review: Single cycle processor

## Slide 3: What determines performance of Processor?
A) Critical Path
B) Clock Cycle Time
C) Cycles Per Instruction (CPI)
D) All of the above
E) None of the above

## Slide 4: Review: Single Cycle Processor
Advantages
  Single Cycle per instruction make logic and clock simple
Disadvantages
  Since instructions take different time to finish, memory and functional unit are not efficiently utilized.
  Cycle time is the longest delay.
    Load instruction
  Best possible CPI is 1
    However, lower MIPS and longer clock period (lower clock frequency); hence, lower performance.

## Slide 5: Review: Multi Cycle Processor
Advantages
  Better MIPS and smaller clock period (higher clock frequency)
  Hence, better performance than Single Cycle processor
Disadvantages
  Higher CPI than single cycle processor
Pipelining: Want better Performance
  want small CPI (close to 1) with high MIPS and short clock period (high clock frequency)
  CPU time = instruction count x CPI x clock cycle time

## Slide 6
Single Cycle vs Pipelined Processor
See: P&H Chapter 4.5

## Slide 7: The Kids
Alice
Bob
They don’t always get along…

## Slide 8: The Bicycle

## Slide 9: The Materials
Saw
Drill
Glue
Paint

## Slide 10: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 11: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 12: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:
CPI =

## Slide 13: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
Alice
Bob
Carol
Dave

## Slide 14: Pipelined Performance
time 1 2 3 4 5 6 7…
What if some tasks don’t need drill?
Latency:
Throughput:
Concurrency:
Notes: Throughput: 1 task / cycle
Delay: 4 cycles / task
Parallelism: 4 concurrent tasks

## Slide 15: Lessons
Principle:
Throughput increased by parallel execution
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (Thursday)

## Slide 16: A Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
Review: Single cycle processor

## Slide 17: A Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
register file
control
alu
imm
memory
din
dout
addr
inst
PC
memory
compute jump/branch targets
new pc
+4
extend

## Slide 18: Basic Pipeline
Five stage “RISC” load-store architecture
  Instruction fetch (IF)
    get instruction from memory, increment PC
  Instruction Decode (ID)
    translate opcode into control signals and read registers
  Execute (EX)
    perform ALU operation, compute jump/branch targets
  Memory (MEM)
    access memory if needed
  Writeback (WB)
    update register file
Notes: This is simpler than the MIPS, but we’re using it to get the concepts across – everything you see here applies to MIPS, but we have to deal w/ fewer bits in these examples (that’s why I like them)

## Slide 19: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Clock cycle
Latency:
Throughput:
Concurrency:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Notes: CPI = 1 (inverse of throughput)

## Slide 20: Principles of Pipelined Implementation
Break instructions across multiple clock cycles (five, in this case)
Design a separate stage for the execution performed during each clock cycle
Add pipeline registers (flip-flops) to isolate signals between different stages

## Slide 21
Pipelined Processor
See: P&H Chapter 4.6

## Slide 22: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 23: IF
Stage 1: Instruction Fetch
Fetch a new instruction every cycle
  Current PC is index to instruction memory
  Increment the PC at end of cycle (assume no branches for now)
Write values of interest to pipeline register (IF/ID)
  Instruction bits (for later decoding)
  PC+4 (for later computing branch targets)
  Next stage will read this pipeline register
  Anything needed by later pipeline stages

## Slide 24: IF
PC
instruction memory
new pc
addr
mc
+4

## Slide 25: IF
PC
instruction memory
new pc
inst
addr
mc
00 = read word
1
IF/ID
WE
1
Rest of pipeline
+4
PC+4
pcsel
pcreg
pcrel
pcabs

## Slide 26: ID
Stage 2: Instruction Decode
On every cycle:
  Read IF/ID pipeline register to get instruction bits
  Decode instruction, generate control signals
  Read from register file
Write values of interest to pipeline register (ID/EX)
  Control information, Rd index, immediates, offsets, …
  Contents of Ra, Rb
  PC+4 (for computing branch targets later)

## Slide 27: ID
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
imm
Notes: Early decode: decode all instr in ID, pass control signals to later stages
Late decode: decode some instr in ID, pass instr so each stage computes its own control signals

## Slide 28: ID
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
extend
imm
decode
result
dest
Notes: Early decode: decode all instr in ID, pass control signals to later stages
Late decode: decode some instr in ID, pass instr so each stage computes its own control signals

## Slide 29: EX
Stage 3: Execute
On every cycle:
  Read ID/EX pipeline register to get values and control bits
  Perform ALU operation
  Compute targets (PC+4+offset, etc.) in case this is a branch
  Decide if jump/branch should be taken
Write values of interest to pipeline register (EX/MEM)
  Control information, Rd index, …
  Result of ALU operation
  Value in case this is a memory store instruction

## Slide 30: EX
Stage 2: Instruction Decode
pcrel
pcabs
ctrl
EX/MEM
Rest of pipeline
B
D
ctrl
ID/EX
PC+4
B
A
alu
j
+
||
branch?
imm
pcsel
pcreg
target

## Slide 31: MEM
Stage 4: Memory
On every cycle:
  Read EX/MEM pipeline register to get values and control bits
  Perform memory load/store if needed
    address is ALU result
Write values of interest to pipeline register (MEM/WB)
  Control information, Rd index, …
  Result of memory operation
  Pass result of ALU operation

## Slide 32: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target

## Slide 33: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target
branch?
pcsel
pcrel
pcabs
pcreg

## Slide 34: WB
Stage 5: Write-back
On every cycle:
  Read MEM/WB pipeline register to get values and control bits
  Select value and write to register file

## Slide 35: WB
Stage 4: Memory
ctrl
MEM/WB
M
D

## Slide 36: WB
Stage 4: Memory
ctrl
MEM/WB
M
D
result
dest

## Slide 37
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd

## Slide 38: Administrivia
HW2 due today
  Fill out Survey online. Receive credit/points on homework for survey:
  https://cornell.qualtrics.com/SE/?SID=SV_5olFfZiXoWz6pKI
  Survey is anonymous
Project1 (PA1) due week after prelim
  Continue working diligently. Use design doc momentum
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 39: Administrivia
Prelim1: next Tuesday, February 28th in evening
  We will start at 7:30pm sharp, so come early
  Prelim Review: This Wed / Fri, 3:30-5:30pm, in 155 Olin
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of this week
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, HW2, Lab0, Lab1, Lab2

## Slide 40: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2012sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 28th
  Thursday, March 29th
  Thursday, April 26th
Schedule is subject to change

## Slide 41: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  20% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 42: Example: Sample Code (Simple)
Assume eight-register machine
Run the following code on a pipelined datapath
  add r3 r1 r2 ; reg 3 = reg 1 + reg 2
  nand r6 r4 r5 ; reg 6 = ~(reg 4 & reg 5)
  lw r4 20 (r2) ; reg 4 = Mem[reg2+20]
  add r5 r2 r5 ; reg 5 = reg 2 + reg 5
  sw r7 12(r3) ; Mem[reg3+12] = reg 7
Slides thanks to Sally McKee

## Slide 43: Example: : Sample Code (Simple)
add r3, r1, r2; nand r6, r4, r5; lw r4, 20(r2); add r5, r2, r5; sw r7, 12(r3);

## Slide 44: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 45: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 46: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add |  |  |  |  |  |  |  |  | 
nand |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
Clock cycle
Latency:
Throughput:
Concurrency:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Notes: CPI = 1 (inverse of throughput)

## Slide 47
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
op
Rt
imm
valB
valA
PC+4
PC+4
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
Bits 26-31
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Rd

## Slide 48
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nop
0
0
0
0
0
0
0
nop
0
0
nop
0
0
0
0
nop
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
Initial
State
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
M
U
X
0

## Slide 49
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nop
0
0
0
0
4
0
0
nop
0
0
nop
0
0
0
0
add 3 1 2
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
Fetch:
add 3 1 2
add 3 1 2
Time: 1
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
M
U
X
0

## Slide 50
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
add
3
9
36
4
8
0
0
nop
0
0
nop
0
0
0
0
nand 6 4 5
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
1
2
Bits 26-31
data
dest
Fetch:
nand 6 4 5
nand 6 4 5 add 3 1 2
Time: 2
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
2
M
U
X
3

## Slide 51
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nand
6
7
18
8
12
4
45
add
3
9
nop
0
0
0
0
lw 4 20(2)
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
4
5
Bits 26-31
data
dest
Fetch:
lw 4 20(2)
lw 4 20(2) nand 6 4 5 add 3 1 2
Time: 3
36
9
3
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
5
M
U
X
6
3
2
Notes: 0x 00 0111
0x 10 0010
And = 10
Nand = 11111 1101

## Slide 52
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
lw
20
18
9
12
16
8
-3
nand
6
7
add
3
45
0
0
add 5 2 5
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
2
4
Bits 26-31
data
dest
Fetch:
add 5 2 5
add 5 2 5 lw 4 20(2) nand 6 4 5 add 3 1 2
Time: 4
18
7
6
45
3
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
4
M
U
X
0
6
5

## Slide 53
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
add
5
7
9
16
20
12
29
lw
4
18
nand
6
-3
0
0
sw 7 12(3)
9
45
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
2
5
Bits 26-31
data
dest
Fetch:
sw 7 12(3)
sw 7 12(3) add 5 2 5 lw 4 20 (2) nand 6 4 5 add 3 1 2
Time: 5
9
20
4
-3
6
45
3
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
5
M
U
X
5
0
4

## Slide 54
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
sw
12
22
45
20
16
16
add
5
7
lw
4
29
99
0
9
45
18
7
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
3
7
Bits 26-31
data
dest
No more
instructions
sw 7 12(3) add 5 2 5 lw 4 20(2) nand 6 4 5
Time: 6
9
7
5
29
4
-3
6
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
7
M
U
X
0
5
5

## Slide 55
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
20
57
sw
7
22
add
5
16
0
0
9
45
99
7
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
No more
instructions
nop nop sw 7 12(3) add 5 2 5 lw 4 20(2)
Time: 7
45
7
12
16
5
99
4
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
0
7

## Slide 56
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
sw
7
57
0
9
45
99
16
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
No more
instructions
nop nop nop sw 7 12(3) add 5 2 5
Time: 8
22
57
22
16
5
Slides thanks to Sally McKee
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X

## Slide 57
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
9
45
99
16
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 21-23
data
dest
No more
instructions
nop nop nop nop sw 7 12(3)
Time: 9
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X

## Slide 58: Pipelining Recap
Powerful technique for masking latencies
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)

## Slide 59
0:add 1:nand 2:lw 3:add 4:sw
r0 r1 r2 r3 r4 r5 r6 r7
0
36
9
12
18
7
41
22
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rd
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
77
add r3, r1, r2
nand r6, r4, r5 add r3, r1, r2
lw r4, 20(r2) nand r6, r4, r5 add r3, r1, r2
add r5, r2, r5 lw r4, 20(r2) nand r6, r4, r5 add r3, r1, r2
sw r7, 12(r3) add r5, r2, r5 lw r4, 20(r2) nand r6, r4, r5 add r3, r1, r2
sw r7, 12(r3) add r5, r2, r5 lw r4, 20(r2) nand r6, r4, r5
sw r7, 12(r3) add r5, r2, r5 lw r4, 20(r2)
sw r7, 12(r3) add r5, r2, r5
sw r7, 12(r3)
Rd
Ra
Rb
D
B
A