## Slide 1: Pipeline Hazards
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H Appendix 4.7

## Slide 2: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 3
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Pipelined Processor

## Slide 4: Administrivia
Prelim1: next Tuesday, February 28th in evening
  Location: GSH132: Goldwin Smith Hall room 132
  Time: We will start at 7:30pm sharp, so come early
  Prelim Review: This Wed / Fri, 3:30-5:30pm, in 155 Olin
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of this week
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, HW2, Lab0, Lab1, Lab2

## Slide 5: Administrivia
HW2 was due two days ago!
  Fill out Survey online. Receive credit/points on homework for survey:
  https://cornell.qualtrics.com/SE/?SID=SV_5olFfZiXoWz6pKI
  Survey is anonymous
Project1 (PA1) due week after prelim
  Continue working diligently. Use design doc momentum
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 6: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2012sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 28th
  Thursday, March 29th
  Thursday, April 26th
Schedule is subject to change

## Slide 7: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  20% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 8: Goals for Today
Data Hazards
  Data dependencies
  Problem, detection, and solutions
    (delaying, stalling, forwarding, bypass, etc)
  Forwarding unit
  Hazard detection unit
Next time
  Control Hazards
  What is the next instruction to execute if
  a branch is taken? Not taken?

## Slide 9: Broken Example
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
sub r5, r3, r4
lw r6, 4(r3)
or r5, r3, r5
sw r6, 12(r3)
add r3, r1, r2

## Slide 10: What Can Go Wrong?
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (IF/ID.rA != 0 && (IF/ID.rA == ID/EX.rD || IF/ID.rA == EX/M.rD || IF/ID.rA == M/WB.rD))
|| (same for rB)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 11: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
Rd

## Slide 12: Resolving Data Hazards
What to do if data hazard detected?
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 13: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
Notes: find hazards first, then draw

## Slide 14: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 15: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 16: Forwarding
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 

## Slide 17: Forwarding
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r4 |  |  |  |  |  |  |  |  | 
lw r6, 4(r3) |  |  |  |  |  |  |  |  | 
or r5, r3, r5 |  |  |  |  |  |  |  |  | 
sw r6, 12(r3) |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX D=55 | MEM D=55 | WB r5=55 |  |  | 
 |  | IF | ID 33=r3 | EX D=? | MEM D=66 | WB r6=66 |  | 
 |  |  | IF | ID 33=r3 55=r5 | EX | MEM | WB | 
 |  |  |  | IF | ID 33=r3 66=r6 | EX | MEM | 
Notes: identify hazards then draw; if “or” had used r6, would have needed to stall

## Slide 18: Forwarding
Forward correct value from?
  ALU output: too late in cycle?
  EX/MEM.D pipeline register (output from ALU)
  WB data value (output from ALU or memory)
  MEM output: too late in cycle, on critical path
to?
  ID (just after register file)
    maybe pointless?
  EX, just after ID/EX.A and ID/EX.B are read
  MEM, just after EX/MEM.B is read: on critical path
data mem
B
A
B
D
M
D
inst mem
D
B
A
1
2
3
b
c
4
a
Notes: Forward correct value from?
  ALU output: too late in cycle
  EX/MEM.D pipeline register (output from ALU)
  WB data value (output from ALU or memory)
  MEM output: too late in cycle
to?
  ID (just after register file): pointless?
  EX, just after ID/EX.A and ID/EX.B are read
  MEM, just after EX/MEM.B is read: on critical path

## Slide 19: Forwarding Path 1
add r4, r1, r2 |  |  |  |  |  |  |  |  | 
nop |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: bypass from WB to mux in EX

## Slide 20: WB to EX Bypass
WB to EX Bypass
  EX needs value being written by WB
Resolve:
Add bypass from WB final value to start of EX
Detect:
Notes: ((ID/EX.Ra == MEM/WB.Rd) or (ID/EX.Rb == MEM/WB.Rd)) and (EX needs A or B) and (WB is writing a register)

## Slide 21: Forwarding Path 2
add r4, r1, r2 |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: draw bypass from WB to mux in EX

## Slide 22: MEM to EX Bypass
MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
Resolve:
Add a bypass from EX/MEM.D to start of EX
Detect:
Notes: ((ID/EX.Ra == EX/MEM.Rd) or (ID/EX.Rb == EX/MEM.Rd)) and (MEM will be writing a register) and (MEM is not a load instruction)

## Slide 23: Forwarding Datapath
data mem
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
Notes: draw control signals

## Slide 24: Tricky Example
data mem
inst mem
D
B
A
add r1, r1, r2 |  |  |  |  |  |  |  |  | 
SUB r1, r1, r3 |  |  |  |  |  |  |  |  | 
OR r1, r4, r1 |  |  |  |  |  |  |  |  | 
Notes: which paths get used

## Slide 25: More Data Hazards
add r4, r1, r2 |  |  |  |  |  |  |  |  | 
nop |  |  |  |  |  |  |  |  | 
nop |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A

## Slide 26: Register File Bypass
Register File Bypass
  Reading a value that is currently being written
Detect:
((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
Resolve:
Add a bypass around register file (WB to ID)
Better: (Hack) just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle

## Slide 27: Memory Load Data Hazard
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: requires one bubble

## Slide 28: Resolving Memory Load Hazard
Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Resolution:
  MIPS 2000/3000: one delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 29: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 30: More Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 31: More Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 32: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 33: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
ori r2, r0, 1 |  |  |  |  |  |  |  |  | 
L: or r3, r1, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch

## Slide 34: Control Hazards: Speculative Execution
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC not known until 2 cycles after branch/jump
Stall
Delay Slot
Speculative Execution
  Guess direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 35: Loops

## Slide 36: Branch Prediction

## Slide 37: Pipelining: What Could Possibly Go Wrong?
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard