## Slide 1: Pipeline Control Hazards and Instruction Variations
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H Appendix 4.8

## Slide 2: Goals for Today
Recap: Data Hazards
Control Hazards
  What is the next instruction to execute if a branch is taken? Not taken?
  How to resolve control hazards
  Optimizations
Next time: Instruction Variations
  Instruction Set Architecture Variations
    ARM
    X86
  RISC vs CISC
  The Assembler

## Slide 3: Recall: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 4: Recall: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 5: Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
forward unit
Rd
detect hazard

## Slide 6: Resolving Data Hazards
What to do if data hazard detected
  Stall
  Reorder instructions in SW
  Forward/Bypass
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 7: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
Notes: find hazards first, then draw

## Slide 8: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 9: Forwarding
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 

## Slide 10: Forwarding Datapath
data mem
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
Notes: draw control signals

## Slide 11: Forwarding Datapath
MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
  Resolve:
  Add a bypass from EX/MEM.D to start of EX
How to detect? Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for rB)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 12: Forwarding Datapath
WB to EX Bypass
  EX needs value being written by WB
  Resolve:
  Add bypass from WB final value to start of EX
How to detect? Logic in Ex Stage:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
not (ID/Ex.WE && Ex/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for rB)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 13: Forwarding Datapath
Register File Bypass
  Reading a value that is currently being written
  Detect:
  ((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
  Resolve:
  Add a bypass around register file (WB to ID)
Better Soln: (Hack) just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 14: Quiz 2
add r3, r1, r2 nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Notes: Find all hazards, and say how they are resolved

## Slide 15: Memory Load Data Hazard
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: requires one bubble

## Slide 16: Resolving Memory Load Hazard
Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Resolution:
  MIPS 2000/3000: one delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
For stall, how to detect? Logic in ID Stage
    Stall = ID/Ex.MemRead &&
    (IF/ID.Ra == ID/Ex.Rd || IF/ID.Rb == ID/Ex.Rd)
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 17: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 18: Administrivia
Prelim1: today Tuesday, February 28th in evening
  Location: GSH132: Goldwin Smith Hall room 132
  Time: We will start at 7:30pm sharp, so come early
  Closed Book: NO NOTES, BOOK, CALCULATOR, CELL PHONE
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of last week
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, HW2, Lab0, Lab1, Lab2

## Slide 19: Administrivia
Online Survey results
  More chairs in lab sections
  Better synchronization between lecture and homework
  Lab and lecture may be a bit out of sync at times
Project1 (PA1) due next Monday, March 5th
  Continue working diligently. Use design doc momentum
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 20: Control Hazards
What about branches?
  Can we forward/bypass values for branches?
    We can move branch calc from EX to ID
    will require new bypasses into ID stage; or can just zap the second instruction
  What happens to instructions following a branch, if branch taken?
    Need to zap/flush instructions
  Is there still a performance penalty for branches
    Yes, need to stall, then may need to zap (flush) subsequent instuctions that have already been fetched.
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 21: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 22: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 23: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 24: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 25: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
ori r2, r0, 1 |  |  |  |  |  |  |  |  | 
L: or r3, r1, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch

## Slide 26: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC not known until 2 cycles after branch/jump
Stall
Delay Slot
Speculative Execution
  “Guess” direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 27: Loops

## Slide 28: Branch Prediction

## Slide 29: Branch Prediction

## Slide 30: Pipelining: What Could Possibly Go Wrong?
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard