## Slide 1: Calling Conventions
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H 2.8 and 2.12

## Slide 2: Goals for Today
Calling Convention for Procedure Calls
Enable code to be reused by allowing code snippets to be invoked
Will need a way to
  call the routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register

## Slide 3: Procedure Call Take 1: Use Jumps
main:
j mult
Laftercall1:
add $1,$2,$3
j mult
Laftercall2:
sub $3,$4,$5
mult:
…
…
j Laftercall1
Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back
What happens when there are multiple calls from different call sites?

## Slide 4: Jump And Link
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register $31
Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register $31

## Slide 5: Procedure Call Take 2: JAL/JR
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
…
…
jr $31
JAL saves the PC in register $31
Subroutine returns by jumping to $31
What happens for recursive invocations?

## Slide 6: Procedure Call Take 2: JAL/JR
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
…
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
jr $31
Recursion overwrites contents of $31
Need to save and restore the register contents

## Slide 7: Call Stacks
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
sp
Laftercall1
Linside
high mem
low mem

## Slide 8: Stack Growth
Stacks start at a high address in memory
Stacks grow down as frames are pushed on
  Recall that the data region starts at a low address and grows up
  The growth potential of stacks and data region are not artificially limited

## Slide 9: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)

## Slide 10: Take 3: JAL/JR with Activation Records
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
addiu $sp,$sp,-4
sw $31, 0($sp)
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
lw $31, 0($sp)
addiu $sp,$sp,4
jr $31
Stack used to save and restore contents of $31
sp
Laftercall1
Linside
high mem
low mem
Linside
Linside
sp
sp

## Slide 11: Take 3: JAL/JR with Activation Records
Stack used to save and restore contents of $31
How about arguments?
sp
Laftercall1
Linside
high mem
low mem
Linside
Linside
sp
sp
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
addiu $sp,$sp,-4
sw $31, 0($sp)
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
lw $31, 0($sp)
addiu $sp,$sp,4
jr $31

## Slide 12: Arguments & Return Values
Need consistent way of passing arguments and getting the result of a subroutine invocation
Given a procedure signature, need to know where arguments should be placed
  int min(int a, int b);
  int subf(int a, int b, int c, int d, int e);
  int isalpha(char c);
  int treesort(struct Tree *root);
  struct Node *createNode();
  struct Node mynode();
Too many combinations of char, short, int, void *, struct, etc.
  MIPS treats char, short, int and void * identically

## Slide 13: Simple Argument Passing
First four arguments are passed in registers
  Specifically, $4, $5, $6 and $7, aka $a0, $a1, $a2, $a3
The returned result is passed back in a register
  Specifically, $2, aka $v0
main:
li $a0, 6
li $a1, 7
jal min
// result in $v0

## Slide 14: Conventions so far:
  args passed in $a0, $a1, $a2, $a3
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
Q: What about argument lists?

## Slide 15: Many Arguments
What if there are more than 4 arguments?
Use the stack for the additional arguments
  “spill”
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
li $8, 4
addiu $sp,$sp,-4
sw $8, 0($sp)
jal subf
// result in $v0
sp
4

## Slide 16: Many Arguments
What if there are more than 4 arguments?
Use the stack for the additional arguments
  “spill”
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
addiu $sp,$sp,-8
li $8, 4
sw $8, 0($sp)
li $8, 5
sw $8, 4($sp)
jal subf
// result in $v0
sp
5
4

## Slide 17: Variable Length Arguments
printf(“Coordinates are: %d %d %d\n”, 1, 2, 3);
Could just use the regular calling convention, placing first four arguments in registers, spilling the rest onto the stack
  Callee requires special-case code
  if(argno == 1) use a0, … else if (argno == 4) use a3, else use stack offset
Best to use an (initially confusing but ultimately simpler) approach:
  Pass the first four arguments in registers, as usual
  Pass the rest on the stack
  Reserve space on the stack for all arguments, including the first four
Simplifies functions that use variable-length arguments
  Store a0-a3 on the slots allocated on the stack, refer to all arguments through the stack

## Slide 18: Register Layout on Stack
First four arguments are in registers
The rest are on the stack
There is room on the stack for the first four arguments, just in case
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
addiu $sp,s$p,-24
li $8, 4
sw $8, 16($sp)
li $8, 5
sw $8, 20($sp)
jal subf
// result in$ v0
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5

## Slide 19: Frame Layout on Stack
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5
blue() {
pink(0,1,2,3,4,5);
}
sp
return address

## Slide 20: Frame Layout on Stack
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5
return address
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
…
}
sp
return address

## Slide 21: Conventions so far:
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed on the stack
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments to sub-functions
Notes: note: arguments are in caller’s frame, not callee

## Slide 22: MIPS Register Conventions so far:
r0 | $zero | zero
r1 | $at | assembler temp
r2 |  | 
r3 |  | 
r4 |  | 
r5 |  | 
r6 |  | 
r7 |  | 
r8 |  | 
r9 |  | 
r10 |  | 
r11 |  | 
r12 |  | 
r13 |  | 
r14 |  | 
r15 |  | 
r16 |  | 
r17 |  | 
r18 |  | 
r19 |  | 
r20 |  | 
r21 |  | 
r22 |  | 
r23 |  | 
r24 |  | 
r25 |  | 
r26 | $k0 | reserved for OS kernel
r27 | $k1 | 
r28 |  | 
r29 |  | 
r30 |  | 
r31 | $ra | return address
 | $v0 | function return values
 | $v1 | 
 | $a0 | function arguments
 | $a1 | 
 | $a2 | 
 | $a3 | 
Notes: why $at? BLT psuedo-instruction and others

## Slide 23: Java vs C: Pointers and Structures
Pointers are 32-bits, treat just like ints
Pointers to structs are pointers
C allows passing whole structs
  int distance(struct Point p1, struct Point p2);
  Treat like a collection of consecutive 32-bit arguments, use registers for first 4 words, stack for rest
  Inefficient and to be avoided, better to use int distance(struct Point *p1, struct Point *p2); in all cases

## Slide 24: Globals and Locals
Global variables are allocated in the “data” region of the program
  Exist for all time, accessible to all routines
Local variables are allocated within the stack frame
  Exist solely for the duration of the stack frame
Dangling pointers are pointers into a destroyed stack frame
  C lets you create these, Java does not
  int *foo() { int a; return &a; }

## Slide 25: Global and Locals
How does a function load global data?
  global variables are just above 0x10000000
Convention: global pointer
  r28 is $gp (pointer into middle of global data section) $gp = 0x10008000
  Access most global data using LW at $gp +/- offset LW $v0, 0x8000($gp) LW $v1, 0x7FFF($gp)
Notes: # data at 0x10000000
# data at 0x1000FFFF
(64KB range)

## Slide 26: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)

## Slide 27: Frame Pointer
It is often cumbersome to keep track of location of data on the stack
  The offsets change as new values are pushed onto and popped off of the stack
Keep a pointer to the top of the stack frame
  Simplifies the task of referring to items on the stack
A frame pointer, $30, aka $fp
  Value of $sp upon procedure entry
  Can be used to restore $sp on exit

## Slide 28: Register Usage
Suppose a routine would like to store a value in a register
Two options: callee-save and caller-save
Callee-save:
  Assume that one of the callers is already using that register to hold a value of interest
  Save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $31
Caller-save:
  Assume that a caller can clobber any one of the registers
  Save the previous contents of the register before proc call
  Restore after the call
MIPS calling convention supports both

## Slide 29: Callee-Save
Assume caller is using the registers
Save on entry, restore on exit
Pays off if caller is actually using the registers, else the save and restore are wasted
main:
addiu $sp,$sp,-32
sw $31,28($sp)
sw $30, 24($sp)
sw $17, 20($sp)
sw $16, 16($sp)
addiu $30, $sp, 28
…
[use $16 and $17]
…
lw $31,28($sp)
lw $30,24($sp)
lw $17, 20$sp)
lw $16, 16($sp)
addiu $sp,$sp,32

## Slide 30: Callee-Save
Assume caller is using the registers
Save on entry, restore on exit
Pays off if caller is actually using the registers, else the save and restore are wasted
main:
addiu $sp,$sp,-32
sw $ra,28($sp)
sw $fp, 24($sp)
sw $s1, 20($sp)
sw $s0, 16($sp)
addiu $fp, $sp, 28
…
[use $s0 and $s1]
…
lw $ra,28($sp)
lw $fp,24($sp)
lw $s1, 20$sp)
lw $s0, 16($sp)
addiu $sp,$sp,32

## Slide 31: Caller-Save
Assume the registers are free for the taking, clobber them
But since other subroutines will do the same, must protect values that will be used later
By saving and restoring them before and after subroutine invocations
Pays off if a routine makes few calls to other routines with values that need to be preserved
main:
…
[use $8 & $9]
…
addiu $sp,$sp,-8
sw $9, 4($sp)
sw $8, 0($sp)
jal mult
lw $9, 4($sp)
lw $8, 0($sp)
addiu $sp,$sp,8
…
[use $8 & $9]

## Slide 32: Caller-Save
Assume the registers are free for the taking, clobber them
But since other subroutines will do the same, must protect values that will be used later
By saving and restoring them before and after subroutine invocations
Pays off if a routine makes few calls to other routines with values that need to be preserved
main:
…
[use $t0 & $t1]
…
addiu $sp,$sp,-8
sw $t1, 4($sp)
sw $t0, 0($sp)
jal mult
lw $t1, 4($sp)
lw $t0, 0($sp)
addiu $sp,$sp,8
…
[use $t0 & $t1]

## Slide 33: Frame Layout on Stack
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
fp
sp
# allocate frame
# save $ra
# save old $fp
# save ...
# save ...
# set new frame pointer
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame

## Slide 34: Frame Layout on Stack
sp
blue() {
pink(0,1,2,3,4,5);
}
saved fp
saved ra
fp
arguments
saved regs

## Slide 35: Frame Layout on Stack
sp
arguments
saved ra
local variables
saved regs
arguments
saved regs
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
saved fp
saved ra
saved fp
fp

## Slide 36: Frame Layout on Stack
sp
arguments
saved ra
local variables
saved regs
arguments
saved regs
saved ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp

## Slide 37: Buffer Overflow
sp
arguments
saved ra
local variables
saved regs
arguments
saved regs
saved ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp

## Slide 38: MIPS Register Recap
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 39: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 40: Recap: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL
    to sub-functions)
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?