## Slide 1: Caches
Han Wang
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H 5.1, 5.2 (except writes)

## Slide 2: Announcements
This week:
PA2 Work-in-progress submission
Next six weeks:
Two labs and two projects
Prelim2 will be Thursday, March 29th

## Slide 3: Goals for Today: caches
Caches vs memory vs tertiary storage
  Tradeoffs: big & slow vs small & fast
    Best of both worlds
  working set: 90/10 rule
  How to predict future: temporal & spacial locality
Cache organization, parameters and tradeoffs associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty

## Slide 4: Agenda
Memory Hierarchy Overview
The Principle of Locality
Direct-Mapped Cache
Fully Associative Cache

## Slide 5: Performance
CPU clock rates ~0.2ns – 2ns (5GHz-500MHz)
Technology Capacity $/GB Latency
Tape 1 TB $.17 100s of seconds
Disk 2 TB $.03 Millions of cycles (ms)
SSD (Flash) 128 GB $2 Thousands of cycles (us)
DRAM 8 GB $10 (10s of ns)
SRAM off-chip 8 MB $4000 5-15 cycles (few ns)
SRAM on-chip 256 KB ??? 1-3 cycles (ns)
Others: eDRAM aka 1-T SRAM, FeRAM, CD, DVD, …
Q: Can we create illusion of cheap + large + fast?
50-300 cycles
Notes: Capacity and latency are closely coupled
Cost is inversely proportional

## Slide 6: Memory Pyramid
Memory Pyramid
Disk (Many GB – few TB)
Memory (128MB – few GB)
L2 Cache (½-32MB)
RegFile
100s bytes
< 1 cycle access
1-3 cycle access
5-15 cycle access
50-300 cycle access
L3 becoming more common (eDRAM ?)
These are rough numbers: mileage may vary for latest/greatest Caches usually made of SRAM (or eDRAM)
L1 Cache
(several KB)
1000000+ cycle access
Notes: L1 L2 and even L3 all on-chip these days using SRAM and eDRAM

## Slide 7: A Typical System
Notes: Draw a typical system

## Slide 8: Memory Hierarchy
Memory closer to processor
  small & fast
  stores active data
Memory farther from processor
  big & slow
  stores inactive data

## Slide 9: Active vs Inactive Data
Assumption: Most data is not active.
Q: How to decide what is active?
A: Programmer decides
A: Compiler decides
A: OS decides at run-time
A: Hardware decides at run-time
Notes: 90/10 rule

## Slide 10: Insight of Caches
Q: What is “active” data?
If Mem[x] is was accessed recently...
… then Mem[x] is likely to be accessed soon
  Exploit temporal locality:
… then Mem[x ± ε] is likely to be accessed soon
  Exploit spatial locality:
put entire block containing Mem[x] higher in the pyramid
put recently accessed Mem[x] higher in the pyramid
A: Data that will be used soon
Notes: soon = frequency of loads

## Slide 11: Locality Analogy
Writing a report on a specific topic.
While at library, check out books and keep them on desk.
If need more, check them out and bring to desk.
  But don’t return earlier books since might need them
  Limited space on desk; Which books to keep?
You hope this collection of ~20 books on desk enough to write report, despite 20 being only 0.00002% of books in Cornell libraries

## Slide 12: Two types of Locality
Temporal Locality (locality in time)
  If a memory location is referenced then it will tend to be referenced again soon
   Keep most recently accessed data items closer to the processor
Spatial Locality (locality in space)
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
   Move blocks consisting of contiguous words closer to the processor

## Slide 13: Locality
Memory trace
0x7c9a2b18
0x7c9a2b19
0x7c9a2b1a
0x7c9a2b1b
0x7c9a2b1c
0x7c9a2b1d
0x7c9a2b1e
0x7c9a2b1f
0x7c9a2b20
0x7c9a2b21
0x7c9a2b22
0x7c9a2b23
0x7c9a2b28
0x7c9a2b2c
0x0040030c
0x00400310
0x7c9a2b04
0x00400314
0x7c9a2b00
0x00400318
0x0040031c
...
int n = 4;
int k[] = { 3, 14, 0, 10 };
int fib(int i) {
  if (i <= 2) return i;
  else return fib(i-1)+fib(i-2);
}
int main(int ac, char **av) {
for (int i = 0; i < n; i++) {
printi(fib(k[i]));
prints("\n");
}
}

## Slide 14: Memory Hierarchy
Memory closer to processor is fast but small
  usually stores subset of memory farther away
    “strictly inclusive”
  alternatives:
    strictly exclusive
    mostly inclusive
  Transfer whole blocks (cache lines):
  4kb: disk ↔ ram
  256b: ram ↔ L2
  64b: L2 ↔ L1

## Slide 15: Cache Lookups (Read)
Processor tries to access Mem[x]
Check: is block containing Mem[x] in the cache?
  Yes: cache hit
    return requested data from cache line
  No: cache miss
    read block from memory (or lower level cache)
    (evict an existing cache line to make room)
    place new block in cache
    return requested data
     and stall the pipeline while all of this happens

## Slide 16: Cache Organization
Cache has to be fast and dense
  Gain speed by performing lookups in parallel
    but requires die real estate for lookup logic
  Reduce lookup logic by limiting where in the cache a block might be placed
    but might reduce cache effectiveness
Cache Controller
CPU
Notes: draw: dram on right; sram in controller; lookup logic;

## Slide 17: Three common designs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Associative
Memory
Cache

## Slide 18: Three common designs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Associative
Memory
Cache

## Slide 19: Three common designs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Associative
Memory
2-way set-associative $
way0
way1

## Slide 20: TIO: Mapping the Memory Address
Lowest bits of address (Offset) determine which byte within a block it refers to.
Full address format:
n-bit Offset means a block is how many bytes?
n-bit Index means cache has how many blocks?
Tag
Memory Address
Index
Offset

## Slide 21: Direct Mapped Cache
Direct Mapped Cache
  Each block number mapped to a single cache line index
  Simplest hardware
line 0 |  |  |  | 
line 1 |  |  |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 22: Direct Mapped Cache
Direct Mapped Cache
  Each block number mapped to a single cache line index
  Simplest hardware
line 0 |  | 
line 1 |  | 
line 2 |  | 
line 3 |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
0x000040 | 
0x000044 | 
0x000048 | 
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 23: Tags and Offsets
Assume sixteen 64-byte cache lines
0x7FFF3D4D = 0111 1111 1111 1111 0011 1101 0100 1101
Need meta-data for each cache line:
  valid bit: is the cache line non-empty?
  tag: which block is stored in this line (if valid)
Q: how to check if X is in the cache?
Q: how to clear a cache line?
Notes: bottom 2 = byte offset within word
bottom 6 = byte offset within cache line
next 4 = cache line index
remaining = tag

## Slide 24: A Simple Direct Mapped Cache
Memory
Direct Mapped Cache
Processor
lb $1  M[ 1 ]
lb $2  M[ 13 ]
lb $3  M[ 0 ]
lb $3  M[ 6 ]
lb $2  M[ 5 ]
lb $2  M[ 6 ]
lb $2  M[ 10 ]
lb $2  M[ 12 ]
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
A =
Notes: 4 cache lines
line size = 2 bytes
offset is 1 bit
index is 2 bits
tag is 2 bits

## Slide 25: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data

## Slide 26: Direct Mapped Cache Size
n bit index, m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Tag Index Offset
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-n-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 9bit index, 17 bit tag  18*512 = 16*512+1024 = 1024bytes + 128 bytes = 1152 bytes overhead

## Slide 27: Cache Performance
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle per word, plus 3 cycle per consecutive word
Performance depends on:
Access time for hit, miss penalty, hit rate
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 28: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 29: Avoiding Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Other Misses
  Buy more SRAM
  Use a more flexible cache design
Notes: fix program, prefetching = special instructions, prediction in CPU, prediction in cache controller, …

## Slide 30
Bigger cache doesn’t always help…
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, …
Hit rate with four direct-mapped 2-byte cache lines?
With eight 2-byte cache lines?
With four 4-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
Notes: What program is this? Memcpy

## Slide 31: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted…
  … because some other access with the same index
  Conflict Miss
… because the cache is too small
  i.e. the working set of program is larger than the cache
  Capacity Miss
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 32: Avoiding Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Capacity Misses
  Buy more SRAM
Conflict Misses
  Use a more flexible cache design

## Slide 33: Three common designs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Associative

## Slide 34: A Simple Fully Associative Cache
Memory
Fully Associative Cache
Processor
lb $1  M[ 1 ]
lb $2  M[ 13 ]
lb $3  M[ 0 ]
lb $3  M[ 6 ]
lb $2  M[ 5 ]
lb $2  M[ 6 ]
lb $2  M[ 10 ]
lb $2  M[ 12 ]
V tag data
$1
$2
$3
$4
Using byte addresses in this example! Addr Bus = 5 bits
0 | 101
1 | 103
2 | 107
3 | 109
4 | 113
5 | 127
6 | 131
7 | 137
8 | 139
9 | 149
10 | 151
11 | 157
12 | 163
13 | 167
14 | 173
15 | 179
16 | 181
Hits: Misses:
A =
Notes: 4 cache lines
line size = 2 words
offset is 1 bit
tag is 4 bits

## Slide 35: Fully Associative Cache (Reading)
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 36: Fully Associative Cache Size
m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Tag Offset
, 2n cache lines
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 26 bit tag  27*512 = 24*512+1536 = 1536bytes + 192 bytes = 1728bytes overhead

## Slide 37
Fully-associative reduces conflict misses...
… assuming good eviction strategy
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, 20, …
Hit rate with four fully-associative 2-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
Notes: No temporal locality, but lots of spacial locality  larger blocks would help

## Slide 38
… but large block size can still reduce hit rate
vector add trace: 0, 100, 200, 1, 101, 201, 2, 202, …
Hit rate with four fully-associative 2-byte cache lines?
With two fully-associative 4-byte cache lines?

## Slide 39: Misses
Cache misses: classification
Cold (aka Compulsory)
  The line is being referenced for the first time
Capacity
  The line was evicted because the cache was too small
  i.e. the working set of program is larger than the cache
Conflict
  The line was evicted because of another access whose index conflicted
Notes: conflict can’t happen with fully associative
block size influences cold misses

## Slide 40: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  big & fast memory built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty
Next up: other designs; writing to caches