## Slide 1: Caches
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H 5.1, 5.2 (except writes)

## Slide 2: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast

## Slide 3: Administrivia
Prelim2 today, Thursday, March 29th at 7:30pm
  Location is Phillips 101 and prelim2 starts at 7:30pm
Project2 due next Monday, April 2nd

## Slide 4: Goals for Today: caches
Examples of caches:
  Direct Mapped
  Fully Associative
  N-way set associative
Performance and comparison
  Hit ratio (conversly, miss ratio)
  Average memory access time (AMAT)
  Cache size

## Slide 5: Cache Performance
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle per word, plus 3 cycle per consecutive word
Performance depends on:
Access time for hit, miss penalty, hit rate
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 6: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 7: Avoiding Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Other Misses
  Buy more SRAM
  Use a more flexible cache design
Notes: fix program, prefetching = special instructions, prediction in CPU, prediction in cache controller, …

## Slide 8
Bigger cache doesn’t always help…
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, …
Hit rate with four direct-mapped 2-byte cache lines?
With eight 2-byte cache lines?
With four 4-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
Notes: What program is this? Memcpy

## Slide 9: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted…
  … because some other access with the same index
  Conflict Miss
… because the cache is too small
  i.e. the working set of program is larger than the cache
  Capacity Miss
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 10: Avoiding Misses
Q: How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Capacity Misses
  Buy more SRAM
Conflict Misses
  Use a more flexible cache design

## Slide 11: Three common designs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Associative

## Slide 12: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 13: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 8
Hits: 3
Cache
00
tag data
2
100
110
150
140
1
1
0
0
0
00
230
220
1
0
180
190
150
140
110
100
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits
M
M
H
H
H
M
M
M
M
M
M

## Slide 14: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 15: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 3
Hits: 8
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0110
220
230
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits
M
M
H
H
H
M
H
H
H
H
H

## Slide 16: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Using byte addresses in this example! Addr Bus = 5 bits
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 17: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4
Hits: 7
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Using byte addresses in this example! Addr Bus = 5 bits
M
M
H
H
H
M
M
H
H
H
H
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 18
Cache Size

## Slide 19: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
=
hit?
data
word select
32bits

## Slide 20: Direct Mapped Cache Size
n bit index, m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Tag Index Offset
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-n-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 9bit index, 17 bit tag  18*512 = 16*512+1024 = 1024bytes + 128 bytes = 1152 bytes overhead

## Slide 21: Direct Mapped Cache Size
n bit index, m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Cache of size 2n blocks
Block size of 2m bytes
Tag field: 32 – (n + m)
Valid bit: 1
Bits in cache: 2n x (block size + tag size + valid bit size)
= 2n (2m bytes x 8 bits-per-byte + (32-n-m) + 1)
Tag Index Offset
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-n-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 9bit index, 17 bit tag  18*512 = 16*512+1024 = 1024bytes + 128 bytes = 1152 bytes overhead

## Slide 22: Fully Associative Cache (Reading)
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 23: Fully Associative Cache Size
m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Tag Offset
, 2n cache lines
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 26 bit tag  27*512 = 24*512+1536 = 1536bytes + 192 bytes = 1728bytes overhead

## Slide 24: Fully Associative Cache Size
m bit offset
Q: How big is cache (data only)?
Q: How much SRAM needed (data + overhead)?
Cache of size 2n blocks
Block size of 2m bytes
Tag field: 32 – m
Valid bit: 1
Bits in cache: 2n x (block size + tag size + valid bit size)
= 2n (2m bytes x 8 bits-per-byte + (32-m) + 1)
Tag Offset
, 2n cache lines
Notes: (2**m bytes per line) (2**n lines) = 2**(n+m) bytes of data
(1+(32-m) bits of overhead per line) (2**n lines)
Some numbers: 32Kb cache, 64byte line size  512 lines, 6bit offset, 26 bit tag  27*512 = 24*512+1536 = 1536bytes + 192 bytes = 1728bytes overhead

## Slide 25
Fully-associative reduces conflict misses...
… assuming good eviction strategy
Mem access trace: 0, 16, 1, 17, 2, 18, 3, 19, 4, 20, …
Hit rate with four fully-associative 2-byte cache lines?
0 | 
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | 
12 | 
13 | 
14 | 
15 | 
16 | 
17 | 
18 | 
19 | 
20 | 
21 | 
Notes: No temporal locality, but lots of spacial locality  larger blocks would help

## Slide 26
… but large block size can still reduce hit rate
vector add trace: 0, 100, 200, 1, 101, 201, 2, 202, …
Hit rate with four fully-associative 2-byte cache lines?
With two fully-associative 4-byte cache lines?

## Slide 27: Misses
Cache misses: classification
Cold (aka Compulsory)
  The line is being referenced for the first time
Capacity
  The line was evicted because the cache was too small
  i.e. the working set of program is larger than the cache
Conflict
  The line was evicted because of another access whose index conflicted
Notes: conflict can’t happen with fully associative
block size influences cold misses

## Slide 28: Cache Tradeoffs
Direct Mapped
+ Smaller
+ Less
+ Less
+ Faster
+ Less
+ Very
– Lots
– Low
– Common
Fully Associative
Larger –
More –
More –
Slower –
More –
Not Very –
Zero +
High +
?
Tag Size
SRAM Overhead
Controller Logic
Speed
Price
Scalability
# of conflict misses
Hit rate
Pathological Cases?

## Slide 29: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  big & fast memory built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty
Next up: other designs; writing to caches