## Slide 1: Caches (Writing)
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
P & H Chapter 5.2-3, 5.5

## Slide 2: Goals for Today
Cache Parameter Tradeoffs
Cache Conscious Programming
Writing to the Cache
  Write-through vs Write back

## Slide 3
Cache Design Tradeoffs

## Slide 4: Cache Design
Need to determine parameters:
  Cache size
  Block size (aka line size)
  Number of ways of set-associativity (1, N, )
  Eviction policy
  Number of levels of caching, parameters for each
  Separate I-cache from D-cache, or Unified cache
  Prefetching policies / instructions
  Write policy

## Slide 5: A Real Example
> dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2011)

## Slide 6: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 7: Basic Cache Organization
Q: How to decide block size?
A: Try it and see
But: depends on cache size, workload, associativity, …
Experimental approach!

## Slide 8: Experimental Results
Notes: For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and miss penalty (time to fetch block) is larger

## Slide 9: Tradeoffs
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 10
Cache Conscious Programming

## Slide 11: Cache Conscious Programming
Every access is a cache miss!
(unless entire matrix can fit in cache)
// H = 12, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];
1 | 11 | 21 |  |  |  |  |  |  | 
 |  | 2 | 12 | 22 |  |  |  |  | 
 |  |  |  | 3 | 13 | 23 |  |  | 
 |  |  |  |  |  | 4 | 14 | 24 | 
 |  |  |  |  |  |  |  | 5 | 15
25 |  |  |  |  |  |  |  |  | 
6 | 16 | 26 |  |  |  |  |  |  | 
 |  | 7 | 17 | … |  |  |  |  | 
 |  |  |  | 8 | 18 |  |  |  | 
 |  |  |  |  |  | 9 | 19 |  | 
 |  |  |  |  |  |  |  | 10 | 20

## Slide 12: Cache Conscious Programming
Block size = 4  75% hit rate
Block size = 8  87.5% hit rate
Block size = 16  93.75% hit rate
And you can easily prefetch to warm the cache.
// H = 12, W = 10
int A[H][W];
for(y=0; y < H; y++)
for(x=0; x < W; x++)
sum += A[y][x];
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
11 | 12 | 13 | … |  |  |  |  |  | 

## Slide 13
Writing with Caches

## Slide 14: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    random: select one of the lines at random
    round-robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 15: Cached Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 16: What about Stores?
Where should you write the result of a store?
  If that memory location is in the cache?
    Send it to the cache
    Should we also send it to memory right away?
    (write-through policy)
    Wait until we kick the block out (write-back policy)
  If it is not in the cache?
    Allocate the line (put it in the cache)?
    (write allocate policy)
    Write it directly to memory without allocation?
    (no write allocate policy)

## Slide 17: Write Allocation Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is not in the cache…
Write-Allocate
  allocate a cache line for new data (and maybe write-through)
No-Write-Allocate
  ignore cache, just go to main memory

## Slide 18: Handling Stores (Write-Through)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
Assume write-allocate
policy
Using byte addresses in this example! Addr Bus = 5 bits
Fully Associative Cache
2 cache lines
2 word block
3 bit tag field
1 bit block offset field

## Slide 19: Write-Through (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0

## Slide 20: Write-Through (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 1
Hits: 0
lru
1
0
29
78
29
M

## Slide 21: Write-Through (REF 2)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 1
Hits: 0
lru
1
0
29
78
29
M

## Slide 22: Write-Through (REF 2)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 0
lru
1
1
29
78
29
162
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M

## Slide 23: Write-Through (REF 3)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 0
lru
1
1
29
78
29
162
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M

## Slide 24: Write-Through (REF 3)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
011
120
71
173
21
28
200
225
Misses: 2
Hits: 1
lru
1
1
29
29
162
173
173
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H

## Slide 25: Write-Through (REF 4)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
011
173
120
71
173
21
28
200
225
Misses: 2
Hits: 1
lru
1
1
29
173
29
162
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H

## Slide 26: Write-Through (REF 4)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 3
Hits: 1
lru
1
1
29
173
29
173
150
71
29
29
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M

## Slide 27: Write-Through (REF 5)
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 3
Hits: 1
lru
1
1
29
173
29
173
29
71
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M

## Slide 28: Write-Through (REF 5)
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 1
lru
1
1
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M

## Slide 29: Write-Through (REF 6)
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 1
lru
1
1
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
29
M
M
H
M
M

## Slide 30: Write-Through (REF 6)
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 2
lru
1
1
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
29
M
M
H
M
M
H

## Slide 31: Write-Through (REF 7)
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 2
lru
1
1
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
29
M
M
H
M
M
H

## Slide 32: Write-Through (REF 7)
29
123
29
162
18
29
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 3
lru
1
1
29
29
71
29
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
29
M
M
H
M
M
H
H

## Slide 33: How Many Memory References?
Write-through performance
Each miss (read or write) reads a block from mem
  4 misses  8 mem reads
Each store writes an item to mem
  4 mem writes
Evictions don’t need to write to mem
  no need for dirty bit

## Slide 34: Write-Through (REF 8,9)
29
123
29
162
18
29
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 3
lru
1
1
29
29
71
29
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
29
29
29
M
M
H
M
M
H
H

## Slide 35: Write-Through (REF 8,9)
29
123
29
162
18
29
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
101
V tag data
$0
$1
$2
$3
Memory
010
173
120
71
173
21
28
200
225
Misses: 4
Hits: 5
lru
1
1
29
29
71
29
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
29
29
29
M
M
H
M
M
H
H
H
H

## Slide 36: Write-Through vs. Write-Back
Can we also design the cache NOT to write all stores immediately to memory?
  Keep the most current copy in cache, and update memory when that data is evicted (write-back policy)
  Do we need to write-back all evicted lines?
  No, only blocks that have been stored into (written)

## Slide 37: Write-Back Meta-Data
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 38: Handling Stores (Write-Back)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Using byte addresses in this example! Addr Bus = 4 bits
Assume write-allocate
policy
Fully Associative Cache
2 cache lines
2 word block
3 bit tag field
1 bit block offset field

## Slide 39: Write-Back (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]

## Slide 40: Write-Back (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 1
Hits: 0
0
1
0
lru
29
78
29
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M

## Slide 41: Write-Back (REF 2)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 1
Hits: 0
0
1
0
lru
29
78
29
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M

## Slide 42: Write-Back (REF 2)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 0
0
0
1
1
lru
29
78
29
162
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M

## Slide 43: Write-Back (REF 3)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 0
0
0
1
1
lru
29
78
162
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
29
173
M
M

## Slide 44: Write-Back (REF 3)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 1
1
0
1
1
lru
29
173
29
162
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H

## Slide 45: Write-Back (REF 4)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 1
1
0
1
1
lru
29
173
29
162
173
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H

## Slide 46: Write-Back (REF 4)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 3
Hits: 1
1
1
1
1
lru
29
173
29
173
29
71
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M

## Slide 47: Write-Back (REF 5)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 3
Hits: 1
1
1
1
1
lru
29
173
29
173
29
71
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M

## Slide 48: Write-Back (REF 5)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
000
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 3
Hits: 1
1
1
1
1
lru
29
173
29
173
29
71
173
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M

## Slide 49: Write-Back (REF 5)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 1
0
1
1
1
lru
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M

## Slide 50: Write-Back (REF 6)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 1
0
1
1
1
lru
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M

## Slide 51: Write-Back (REF 6)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 2
0
1
1
1
lru
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M
H

## Slide 52: Write-Back (REF 7)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 2
0
1
1
1
lru
29
29
71
33
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M
H

## Slide 53: Write-Back (REF 7)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 3
1
1
1
1
lru
29
29
71
29
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M
H
H

## Slide 54: How Many Memory References?
Write-back performance
Each miss (read or write) reads a block from mem
  4 misses  8 mem reads
Some evictions write a block to mem
  1 dirty eviction  2 mem writes
  (+ 2 dirty evictions later  +4 mem writes)

## Slide 55: How many memory references?
Each miss reads a block
  Two words in this cache
Each evicted dirty cache line writes a block
Total reads: six words
Total writes: 4/6 words (after final eviction)

## Slide 56: Write-Back (REF 8,9)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 3
1
1
1
1
lru
29
29
71
29
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M
H
H

## Slide 57: Write-Back (REF 8,9)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
101
V d tag data
$0
$1
$2
$3
Memory
010
78
120
71
173
21
28
200
225
Misses: 4
Hits: 5
1
1
1
1
lru
29
29
71
29
28
33
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
H
M
M
H
H
H
H

## Slide 58: How Many Memory References?
Write-back performance
Each miss (read or write) reads a block from mem
  4 misses  8 mem reads
Some evictions write a block to mem
  1 dirty eviction  2 mem writes
  (+ 2 dirty evictions later  +4 mem writes)
By comparison write-through was
  Reads: eight words
  Writes: 4/6/8 etc words
  Write-through or Write-back?

## Slide 59: Write-through vs. Write-back
Write-through is slower
  But cleaner (memory always consistent)
Write-back is faster
  But complicated when multi cores sharing memory

## Slide 60: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 61: Performance Tradeoffs
Q: Hit time: write-through vs. write-back?
A: Write-through slower on writes.
Q: Miss penalty: write-through vs. write-back?
A: Write-back slower on evictions.

## Slide 62: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: What does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 63: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 64: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
May need to snoop on other CPU’s cache activity
Invalidate cache line when other CPU writes
Flush write-back caches before other CPU reads
Or the reverse: Before writing/reading…
Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net

## Slide 65: Administrivia
Prelim2 results
  Mean 68.9 (median 71), standard deviation 13.0
  Prelims available in Upson 360 after today
  Regrade requires written request
    Whole test is regraded

## Slide 66: Administrivia
Lab3 due next Monday, April 9th
HW5 due next Tuesday, April 10th

## Slide 67: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  (big & fast) built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate

## Slide 68: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
Multi-core / Multi-Processor is complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right