## Slide 1: Virtual Memory
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
P & H Chapter 5.4 (up to TLBs)

## Slide 2: Goals for Today
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching

## Slide 3: Virtual Memory

## Slide 4: Big Picture: Multiple Processes
How to Run multiple processes?
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 5: Big Picture: (Virtual) Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast

## Slide 6: Big Picture: (Virtual) Memory
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Processor
Memory
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
Memory: big & slow vs Caches: small & fast

## Slide 7: Processor & Memory
CPU address/data bus...
… routed through caches
… to main memory
  Simple, fast, but…
Q: What happens for LW/SW to an invalid location?
  0x000000000 (NULL)
  uninitialized pointer
A: Need a memory management unit (MMU)
  Throw (and/or handle) an exception
CPU
Text
Data
Stack
Heap
Memory
0x000…0
0x7ff…f
0xfff…f

## Slide 8: Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
A: The addresses will conflict
  Even though, CPUs may take
  turns using memory bus
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 9: Multiple Processes
Q: Can we relocate second program?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 10: Solution? Multiple processes/processors
Q: Can we relocate second program?
A: Yes, but…
  What if they don’t fit?
  What if not contiguous?
  Need to recompile/relink?
  …
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap

## Slide 11
All problems in computer science can be solved by another level of indirection.
– David Wheeler
– or, Butler Lampson
– or, Leslie Lamport
– or, Steve Bellovin

## Slide 12: Virtual Memory
Virtual Memory: A Solution for All Problems
Each process has its own virtual address space
  Programmer can code as if they own all of memory
On-the-fly at runtime, for each memory access
  all access is indirect through a virtual address
  translate fake virtual address to a real physical address
  redirect load/store to the physical address

## Slide 13: Address Space
wikipedia

## Slide 14: Address Space
Programs load/store to virtual addresses
Actual memory uses physical addresses
Memory Management Unit (MMU)
  Responsible for translating on the fly
  Essentially, just a big array of integers: paddr = PageTable[vaddr];
CPU
MMU
A
B
C
X
Y
Z
X
Y
Z
C
B
A
CPU
MMU
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 15: Virtual Memory Advantages
Advantages
Easy relocation
  Loader puts code anywhere in physical memory
  Creates virtual mappings to give illusion of correct layout
Higher memory utilization
  Provide illusion of contiguous memory
  Use all physical memory, even physical address 0x0
Easy sharing
  Different mappings for different programs / cores
And more to come…

## Slide 16
Address Translation
Pages, Page Tables, and
the Memory Management Unit (MMU)

## Slide 17: Address Translation
Attempt #1: How does MMU translate addresses?
paddr = PageTable[vaddr];
Granularity?
  Per word…
  Per block…
  Variable..…
Typical:
  4KB – 16KB pages
  4MB – 256MB jumbo pages
Notes: per word … too expensive: 4GB PageTable arrray
per block… ?
Variable … complicated hardware
We will stick to 4kb pages

## Slide 18: Address Translation
Attempt #1: For any access to virtual address:
  Calculate virtual page number and page offset
  Lookup physical page number at PageTable[vpn]
  Calculate physical address as ppn:offset
vaddr
Page Offset
Virtual page number
Page offset
Physical page number
Lookup in PageTable
paddr
Notes: 4kb pages = 12 bits for page offset, 20 bits for VPN

## Slide 19: Simple PageTable
Q: Where to store page tables?
A: In memory, of course… Special page table base register (CR3:PTBR on x86) (Cop0:ContextRegister on MIPS)
CPU
MMU
Data
Read Mem[0x4123B538]
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Notes: VADDR = 0x00401538
PFN = VADDR/4kb = VADDR>>12 = 0x401
PageTableEntry at 0x90000804 contains 0x4123B000
Data at 0x4123B538

## Slide 20: Simple PageTable
vpn | pgoff
 | Physical Page Number
 | 0x10045
 | 0xC20A3
 | 0x4123B
 | 0x10044
vaddr
PTBR
0x00000000
0x90000000
0x10045000
0xC20A3000
0x10044000
0x4123B000

## Slide 21: Invalid Pages
Cool Trick #1: Don’t map all pages
Need valid bit for each page table entry
Q: Why?
A: now access to NULL will fail
A: we might not have that much physical memory
V |  | Physical Page Number
0 |  | 
1 |  | 0x10045
0 |  | 
0 |  | 
1 |  | 0xC20A3
1 |  | 0x4123B
1 |  | 0x10044
0 |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Notes: A: now access to NULL will fail
A: we might not have that much physical memory

## Slide 22: Page Size Example
Overhead for VM Attempt #1 (example)
Virtual address space (for each process):
  total memory: 232 bytes = 4GB
  page size: 212 bytes = 4KB
  entries in PageTable?
  size of PageTable?
Physical address space:
  total memory: 229 bytes = 512MB
  overhead for 10 processes?
Notes: 220 entries in pagetable, so 222 bytes = 4MB (w/ 4byte entries), so 40MB (25% of total!)
Q: Can we possibly have a “full” pagetable?
A: Not enough physical memory pages – some pagetable entries will be duplicates!

## Slide 23: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses?
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
Multi-level PageTable
* x86 does exactly this
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 24: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses? Multi-level PageTable
Q: Benefits?
A: Don’t need 4MB contiguous physical memory
A: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks
A: Performance: Longer lookups
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 25: Page Permissions
Cool Trick #2: Page permissions!
Keep R, W, X permission bits for each page table entry
Q: Why?
A: can make code read-only, executable;
make data read-write but not executable; etc.
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0x10045
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x10044
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 26: Aliasing
Cool Trick #3: Aliasing
Map the same physical page at several virtual addresses
Q: Why?
A: can make different views of same
data with different permissions
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x10044
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Notes: A: can make different views of same data with different permissions

## Slide 27
Paging

## Slide 28: Paging
Can we run process larger than physical memory?
  The “virtual” in “virtual memory”
View memory as a “cache” for secondary storage
  Swap memory pages out to disk when not in use
  Page them back in when needed
Assumes Temporal/Spatial Locality
  Pages used recently most likely to be used again soon

## Slide 29: Paging
Cool Trick #4: Paging/Swapping
Need more bits:
Dirty, RecentlyUsed, …
V | R | W | X | D | Physical Page Number
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 0x10045
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
0 |  |  |  | 0 | disk sector 200
0 |  |  |  | 0 | disk sector 25
1 |  |  |  | 1 | 0x00000
0 |  |  |  |  | invalid
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
25
200
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 30: Summary
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
Next time
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching

## Slide 31: Administrivia
Lab3 is due next Monday
  Extra Lab Help session:
  Saturday, April 7th, 12:00-2:30pm in CSUGLab
HW5 is due next Tuesday
  Download updated version. Use updated version.
  Online Survey available later this evening