## Slide 1: Virtual Memory 3
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
P & H Chapter 5.4

## Slide 2: Goals for Today
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching

## Slide 3: Virtual Memory

## Slide 4: Big Picture: Multiple Processes
How to Run multiple processes?
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 5: Big Picture: (Virtual) Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast

## Slide 6: Big Picture: (Virtual) Memory
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Processor
Memory
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
Memory: big & slow vs Caches: small & fast

## Slide 7: Processor & Memory
CPU address/data bus...
… routed through caches
… to main memory
  Simple, fast, but…
Q: What happens for LW/SW to an invalid location?
  0x000000000 (NULL)
  uninitialized pointer
A: Need a memory management unit (MMU)
  Throw (and/or handle) an exception
CPU
Text
Data
Stack
Heap
Memory
0x000…0
0x7ff…f
0xfff…f

## Slide 8: Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
A: The addresses will conflict
  Even though, CPUs may take
  turns using memory bus
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 9: Multiple Processes
Q: Can we relocate second program?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 10: Solution? Multiple processes/processors
Q: Can we relocate second program?
A: Yes, but…
  What if they don’t fit?
  What if not contiguous?
  Need to recompile/relink?
  …
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap

## Slide 11
All problems in computer science can be solved by another level of indirection.
– David Wheeler
– or, Butler Lampson
– or, Leslie Lamport
– or, Steve Bellovin
  paddr = PageTable[vaddr];

## Slide 12
Performance

## Slide 13: Performance Review
Virtual Memory Summary
PageTable for each process:
  4MB contiguous in physical memory, or multi-level, …
  every load/store translated to physical addresses
  page table miss = page fault load the swapped-out page and retry instruction, or kill program if the page really doesn’t exist, or tell the program it made a mistake

## Slide 14: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses?
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
Multi-level PageTable
* x86 does exactly this
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 15: Page Table Review
x86 Example: 2 level page tables, assume… 32 bit vaddr, 32 bit paddr 4k PDir, 4k PTables, 4k Pages
Q:How many bits for a physical page number?
A: 20
Q: What is stored in each PageTableEntry?
A: ppn, valid/dirty/r/w/x/…
Q: What is stored in each PageDirEntry?
A: ppn, valid/?/…
Q: How many entries in a PageDirectory?
A: 1024 four-byte PDEs
Q: How many entires in each PageTable?
A: 1024 four-byte PTEs
PDE
PTBR
PDE
PDE
PDE
PTE
PTE
PTE
PTE
Notes: byte offset = 0x44c
PTI = 0x12a
PDI = 0x205

## Slide 16: Page Table Review Example
x86 Example: 2 level page tables, assume… 32 bit vaddr, 32 bit paddr 4k PDir, 4k PTables, 4k Pages PTBR = 0x10005000 (physical)
Write to virtual address 0x7192a44c… Q: Byte offset in page? PT Index? PD Index?
(1) PageDir is at 0x10005000, so… Fetch PDE from physical address 0x1005000+(4*PDI)
  suppose we get {0x12345, v=1, …}
(2) PageTable is at 0x12345000, so… Fetch PTE from physical address 0x12345000+(4*PTI)
  suppose we get {0x14817, v=1, d=0, r=1, w=1, x=0, …}
(3) Page is at 0x14817000, so… Write data to physical address? Also: update PTE with d=1
PDE
PTBR
PDE
PDE
PDE
PTE
PTE
PTE
PTE
0x1481744c
Notes: byte offset = 0x44c
PTI = 0x12a
PDI = (0x719 >> 2) = 0x1c6

## Slide 17: Performance Review
Virtual Memory Summary
PageTable for each process:
  4MB contiguous in physical memory, or multi-level, …
  every load/store translated to physical addresses
  page table miss: load a swapped-out page and retry instruction, or kill program
Performance?
  terrible: memory is already slow translation makes it slower
Solution?
  A cache, of course
Notes: 4x slower!
Pipelining? No. Parallelization? No.

## Slide 18
Making Virtual Memory Fast
  The Translation Lookaside Buffer (TLB)

## Slide 19: Translation Lookaside Buffer (TLB)
Hardware Translation Lookaside Buffer (TLB)
A small, very fast cache of recent address mappings
  TLB hit: avoids PageTable lookup
  TLB miss: do PageTable lookup, cache result for later

## Slide 20: TLB Diagram
V | R | W | X | D | 
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  | 0 | 
1 |  |  |  | 1 | 
0 |  |  |  |  | invalid
V | R | W | X | D | tag | ppn
V |  | 
0 |  | invalid
0 |  | invalid
0 |  | invalid
1 |  | 
0 |  | invalid
1 |  | 
1 |  | 
0 |  | invalid

## Slide 21: A TLB in the Memory Hierarchy
(1) Check TLB for vaddr (~ 1 cycle)
(2) TLB Miss: traverse PageTables for vaddr
(3a) PageTable has valid entry for in-memory page
  Load PageTable entry into TLB; try again (tens of cycles)
(3b) PageTable has entry for swapped-out (on-disk) page
  Page Fault: load from disk, fix PageTable, try again (millions of cycles)
(3c) PageTable has invalid entry
  Page Fault: kill process
CPU
TLB
Lookup
Cache
Mem
Disk
PageTable
Lookup
(2) TLB Hit
  compute paddr, send to cache
Notes: TLB miss in hardware usually, but not always
PageTable stuff in software

## Slide 22: TLB Coherency
TLB Coherency: What can go wrong?
A: PageTable or PageDir contents change
  swapping/paging activity, new shared pages, …
A: Page Table Base Register changes
  context switch between processes
Notes: Fully transparent

## Slide 23: Translation Lookaside Buffers (TLBs)
When PTE changes, PDE changes, PTBR changes….
Full Transparency: TLB coherency in hardware
  Flush TLB whenever PTBR register changes [easy – why?]
  Invalidate entries whenever PTE or PDE changes [hard – why?]
TLB coherency in software
If TLB has a no-write policy…
  OS invalidates entry after OS modifies page tables
  OS flushes TLB whenever OS does context switch
Notes: process ID could just be the PTBR for the process

## Slide 24: TLB Parameters
TLB parameters (typical)
  very small (64 – 256 entries), so very fast
  fully associative, or at least set associative
  tiny block size: why?
Intel Nehalem TLB (example)
  128-entry L1 Instruction TLB, 4-way LRU
  64-entry L1 Data TLB, 4-way LRU
  512-entry L2 Unified TLB, 4-way LRU

## Slide 25
Virtual Memory meets Caching
  Virtually vs. physically addressed caches
  Virtually vs. physically tagged caches

## Slide 26: Virtually Addressed Caching
Q: Can we remove the TLB from the critical path?
A: Virtually-Addressed Caches
CPU
TLB
Lookup
Virtually
Addressed
Cache
Mem
Disk
PageTable
Lookup
Notes: A: have to flush entire cache on context switch
A:
Doing synonym updates requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits

## Slide 27: Virtual vs. Physical Caches
CPU
Cache
SRAM
Memory
DRAM
addr
data
MMU
Cache
SRAM
MMU
CPU
Memory
DRAM
addr
data
Cache works on physical addresses
Cache works on virtual addresses
Q: What happens on context switch?
Q: What about virtual memory aliasing?
Q: So what’s wrong with physically addressed caches?
Notes: A1: Physically-addressed: nothing; Virtually-addressed: need to flush cache
A2: Physically-addressed: nothing; Virtually-addressed: problems

## Slide 28: Indexing vs. Tagging
Physically-Addressed Cache
  slow: requires TLB (and maybe PageTable) lookup first
Virtually-Indexed, Virtually Tagged Cache
  fast: start TLB lookup before cache lookup finishes
  PageTable changes (paging, context switch, etc.)
     need to purge stale cache lines (how?)
  Synonyms (two virtual mappings for one physical page)
     could end up in cache twice (very bad!)
Virtually-Indexed, Physically Tagged Cache
  ~fast: TLB lookup in parallel with cache lookup
  PageTable changes  no problem: phys. tag mismatch
  Synonyms  search and evict lines with same phys. tag
Virtually-Addressed Cache

## Slide 29: Indexing vs. Tagging

## Slide 30: Typical Cache Setup
CPU
L2 Cache
SRAM
Memory
DRAM
addr
data
MMU
Typical L1: On-chip virtually addressed, physically tagged
Typical L2: On-chip physically addressed
Typical L3: On-chip …
L1 Cache
SRAM
TLB SRAM

## Slide 31: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Direct, n-way, fully associative
What block is replaced on miss?
  LRU, Random, LFU, …
How are writes handled?
  No-write (w/ or w/o automatic invalidation)
  Write-back (fast, block at time)
  Write-through (simple, reason about consistency)
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 32: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Caches: direct/n-way/fully associative (fa)
  VM: fa, but with a table of contents to eliminate searches
  TLB: fa
What block is replaced on miss?
  varied
How are writes handled?
  Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
  VM: write-back
  TLB: usually no-write
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 33: Summary of Cache Design Parameters
 | L1 | Paged Memory | TLB
Size (blocks) | 1/4k to 4k | 16k to 1M | 64 to 4k
Size (kB) | 16 to 64 | 1M to 4G | 2 to 16
Block size (B) | 16-64 | 4k to 64k | 4-32
Miss rates | 2%-5% | 10-4 to 10-5% | 0.01% to 2%
Miss penalty | 10-25 | 10M-100M | 100-1000