## Slide 1: Synchronization
P&H Chapter 2.11
Han Wang
CS 3410, Spring 2012
Computer Science
Cornell University

## Slide 2: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  Assume physical addresses (ignore virtual memory)
  Assume uniform memory access (ignore NUMA)
Core0
Core1
CoreN
Cache
Cache
Cache
Memory
I/O
Interconnect
...
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 3: Fo
Synchronization
The need for synchronization arises whenever
there are concurrent processes in a system.
(even in a uni-processor system)
Fork
P1
P2
Join
Producer
Consumer
Forks and Joins: In parallel programming,
a parallel process may want to wait until
several events have occurred.
Producer-Consumer: A consumer process
must wait until the producer process has
produced data
Exclusive use of a resource: Operating
system has to ensure that only one
process uses a resource at a given time
Notes: User level software routine, but rely on hardware-supplied synchronization primitives.

## Slide 4: Processes and Threads
Process
OS abstraction of a running computation
  The unit of execution
  The unit of scheduling
  Execution state + address space
From process perspective
  a virtual CPU
  some virtual memory
  a virtual keyboard, screen, …
Thread
OS abstraction of a single thread of control
  The unit of scheduling
  Lives in one single process
From thread perspective
  one virtual CPU core on a virtual multi-core machine
All you need to know about OS (for today)
Thread is much more lightweight.
Notes: d/Unit of scheduling/
s/execution state/one or more threads/
s/virtual CPU/virtual multi-core machine/

## Slide 5
Thread A Thread B for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }

## Slide 6
Thread A Thread B for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW $t0, addr(x) LW $t0, addr(x) ADDI $t0, $t0, 1 ADDI $t0, $t0, 1 SW $t0, addr(x) SW $t0, addr(x) } }
Notes: Any interleave.

## Slide 7
Possible interleaves:
Notes: Write down possible interleaves.

## Slide 8: Atomic operation
To understand concurrent processes, we need to understand the underlying indivisible operations.
Atomic operation: an operation that always runs to the end or not at all.
Indivisible. Its can not be stopped in the middle.
Fundamental building blocks.
Execution of a single instruction is atomic.
Examples:
Atomic exchange.
Atomic compare and swap.
Atomic fetch and increment.
Atomic memory operation.

## Slide 9: Agenda
Why cache coherency is not sufficient?
HW support for synchronization
Locks + barriers

## Slide 10: Coherence Defined
Cache coherence defined...
Informal: Reads return most recently written value
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
  P1 writes X before P2 reads X  read returns written value
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
Notes: second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 11: Cache Coherence Problem
Shared Memory Multiprocessor (SMP)
What could possibly go wrong?
...
x = x+1
...
...
while (x==5) { // wait
}
...
Core0
Core1
Core3
I/O
Interconnect
...
Notes: show assembly: LW, ADDI, SW; LW, LW, LW, …
show table of cycles: Core3 load, Core0 modify, core 3 never finishes
stale data -> Cache Coherence
Does write-through or write-back cache help? no

## Slide 12: Snooping
Recall: Snooping for Hardware Cache Coherence
  All caches monitor bus and all other caches
  Bus read: respond if you have dirty data
  Bus write: update/invalidate your copy of data
Core0
Cache
Memory
I/O
Interconnect
Snoop
Core1
Cache
Snoop
CoreN
Cache
Snoop
...
Notes: In reality: very complicated, lots of corner cases

## Slide 13: Is cache coherence sufficient?
Example with cache coherence:
P1 P2
x = x +1 while (x==5) ;
Notes: Is cache coherence enough? Maybe?

## Slide 14: Is cache coherence sufficient?
Example with cache coherence:
P1 P2
x = x +1 x = x + 1
 happens even on single-core (context switches!)
Notes: Is cache coherence enough? No
This bug happens on single core too

## Slide 15: Hardware Primitive: Test and Set
Test-and-set is a typical way to achieve synchronization when only one processor is allowed to access a critical section.
Hardware atomic equivalent of…
int test_and_set(int *m) {
old = *m;
*m = 1;
return old;
}
If return value is 0, then you succeeded in acquiring the test-and-set.
If return value is non-0, then you did not succeed.
How do you "unlock" a test-and-set?
Test-and-set on Intel:
xchg dest, src
Exchanges destination and source.
How do you use it?
Notes: test_and_set(int *
Mutex init:
*lock = 0;
sw $0, 0($a0)
Mutex lock:
while (ats(lock, 1));
again: ats $t0, 0($a0)
bne $t0, $0, again
Mutex unlock:
*lock = 0;
sw $0, 0($a0)

## Slide 16: Using test-and-set for mutual exclusion
Use test-and-set to implement mutex / spinlock / crit. sec.
int m = 0;
...
while (test_and_set(&m)) { /* skip */ };
m = 0;
Notes: spin until lock is acquired
note: lock can’t be in a register (some compiler trickery required to ensure lock variable is in memory)

## Slide 17: Hardware Primitive: LL & SC
LL: load link (sticky load) returns the value in a memory location.
SC: store conditional: stores a value to the memory location ONLY if that location hasn’t changed since the last load-link.
If update has occurred, store-conditional will fail.
LL rt, immed(rs) (“load linked”) — rt ← Memory[rs+immed]
SC rt, immed(rs) (“store conditional”) —
if no writes to Memory[rs+immed] since ll:
Memory[rs+immed] ← rt; rt ← 1
otherwise:
rt ← 0
Notes: R4 and 0(R1) atomically exchanged.

## Slide 18: Operation of LL & SC.
try: mov R3, R4 ;mov exchange value
ll R2, 0(R1) ;load linked
sc R3, 0(R1) ;store conditional
beqz R3, try ;branch store fails
mov R4, R2 ;put load value in R4
Any time a processor intervenes and modifies the value in memory between the ll and sc instruction, the sc returns 0 in R3, causing the code to try again.

## Slide 19: mutex from LL and SC
fmutex_lock(int *m) {
again:
LL t0, 0(a0)
BNE t0, zero, again
ADDI t0, t0, 1
SC t0, 0(a0)
BEQ t0, zero, again
}
Linked load / Store Conditional
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 20: More example on LL & SC
try: ll R2, 0(R1) ;load linked
addi R3, R2, #1
sc R3, 0(R1) ;store condi
beqz R3, try ;branch store fails
This has a name!
Notes: LL instruction is inspired by the snoopy bus cache protocol. Why??
Typically LL/SC are implemented via a snoopy bus protocol: a memory location is "linked" by putting its address into a snooper. If another location writes to it, the link is broken so that SC will fail. CPU will set LLbit, LLbit will reset if link breaks.

## Slide 21: Hardware Primitive: CAS
Compare and Swap
Compares the contents of a memory location with a value and if they are the same, then modifies the memory location to a new value.
CAS on Intel:
cmpxchg loc, val
Compare value stored at memory location loc to contents of the Compare Value Application Register.
  If they are the same, then set loc to val.
  ZF flag is set if the compare was true, else ZF is 0

## Slide 22: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
- compare and exchange (x86, ARM deprecated)
- linked load / store conditional (MIPS, ARM, PowerPC, DEC Alpha, …)
Notes: hardware implementation: lock bus while read-modify-write cycle happens, very expensive

## Slide 23: Spin waiting
Also called: spinlock, busy waiting, spin waiting, …
  Efficient if wait is short
  Wasteful if wait is long
Possible heuristic:
  spin for time proportional to expected wait time
  If time runs out, context-switch to some other thread

## Slide 24: Spin Lock
Read lock
variable
Succeed?
(=0?)
Try to lock variable using ll&sc:
read lock variable and set it
to locked value (1)
Unlocked?
(=0?)
No
Yes
No
Begin update of
shared data
Finish update of
shared data
Yes
.
.
.
unlock variable:
set lock variable
to 0
Spin
atomic
operation
The single winning processor will read a 0 - all others processors will read the 1 set by the winning processor
Notes: The losers will continue to write the variable with the locked value of 1, but that is okay!

## Slide 25: Example
_itmask # enter critical section
# lock acquisition loop
LL r1, 0(r4) # r1 <= M[r4]
BNEZ r1, loop # retry if lock already taken (r1 != 0)
ORI r1, r0, 1 # r1 <= 1
SC r1, 0(r4) # if atomic (M[r4] <= 1 / r1 <= 1) else (r1 <= 0)
BEQZ r1, loop # retry if not atomic (r1 == 0) ...
# lock release
ORI r1, r0, 0 # r1 <= 0
SW r1, 0(r4) # M[r4] <= 0
_itunmask # exit critical section

## Slide 26: How do we fix this?
Thread A Thread B for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) {
x = x + 1; x = x + 1;
} }
acquire_lock(m); acquire_lock(m);
release_lock(m); release_lock(m);

## Slide 27: Guidelines for successful mutexing
Insufficient locking can cause races
  Skimping on mutexes? Just say no!
Poorly designed locking can cause deadlock
  know why you are using mutexes!
  acquire locks in a consistent order to avoid cycles
  use lock/unlock like braces (match them lexically)
    lock(&m); …; unlock(&m)
    watch out for return, goto, and function calls!
    watch out for exception/error conditions!
  P1: lock(m1); lock(m2);
  P2: lock(m2); lock(m1);

## Slide 28: Summing Numbers on a SMP
sum[Pn] = 0;
for (i = 1000*Pn; i< 1000*(Pn+1); i = i + 1)
sum[Pn] = sum[Pn] + A[i];
/* each processor sums its
/* subset of vector A
repeat /* adding together the
/* partial sums
synch(); /*synchronize first
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
half = half/2
if (Pn<half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1); /*final sum in sum[0]
A[i];
/* each processor sums its
/* subset of vector A

## Slide 29: Barrier Synchronization
P0
P1
P2
P3
P4
P5
P6
P7
P8
P9
P0
P1
P2
P3
P4
P0
P1
P0

## Slide 30: Simple Barrier Synchronization
lock();
if(count==0) release=FALSE; /* First resets release */
count++; /* Count arrivals */
unlock();
if(count==total) /* All arrived */
{
count=0; /* Reset counter */
release = TRUE; /* Release processes */
}
else /* Wait for more to come */
{
while (!release); /* Wait for release */
}
Problem: deadlock possible if reused
  Two processes: fast and slow
  Slow arrives first, reads release, sees FALSE
  Fast arrives, sets release to TRUE, goes on to execute other code, comes to barrier again, resets release to FALSE, starts spinning on wait for release
  Slow now reads release again, sees FALSE again
  Now both processors are stuck and will never leave

## Slide 31: Correct Barrier Synchronization
localSense=!localSense; /* Toggle local sense */
lock();
count++; /* Count arrivals */
if(count==total){ /* All arrived */
count=0; /* Reset counter */
release=localSense; /* Release processes */
}
unlock();
while(release!=localSense); /* Wait to be released */
Release in first barrier acts as reset for second
  When fast comes back it does not change release, it just waits for it to become FALSE
  Slow eventually sees release is TRUE, stops waiting, does work, comes back, sets release to FALSE, and both go forward.
initially localSense = FALSE, release = FALSE

## Slide 32: Large-Scale Systems: Barriers
Barrier with many processors
  Have to update counter one by one – takes a long time
  Solution: use a combining tree of barriers
    Example: using a binary tree
    Pair up processors, each pair has its own barrier
      E.g. at level 1 processors 0 and 1 synchronize on one barrier, processors 2 and 3 on another, etc.
    At next level, pair up pairs
      Processors 0 and 2 increment a count a level 2, processors 1 and 3 just wait for it to be released
      At level 3, 0 and 4 increment counter, while 1, 2, 3, 5, 6, and 7 just spin until this level 3 barrier is released
      At the highest level all processes will spin and a few “representatives” will be counted.
    Works well because each level fast and few levels
      Only 2 increments per level, log2(numProc) levels
      For large numProc, 2*log2(numProc) still reasonably small

## Slide 33: Beyond Mutexes
Lanaguage-level synchronization
Conditional variables
Monitors
Semaphores

## Slide 34
Software Support for Synchronization and Coordination:
Programs and Processes

## Slide 35: Processes
How do we cope with lots of activity?
Simplicity? Separation into processes
Reliability? Isolation
Speed? Program-level parallelism
gcc
emacs
nfsd
lpr
ls
www
emacs
nfsd
lpr
ls
www
OS
OS
Notes: (isolation e.g. virtual memory)
(parallelism e.g. during I/O)

## Slide 36: Process and Program
Process
OS abstraction of a running computation
  The unit of execution
  The unit of scheduling
  Execution state + address space
From process perspective
  a virtual CPU
  some virtual memory
  a virtual keyboard, screen, …
Program
“Blueprint” for a process
  Passive entity (bits on disk)
  Code + static data
Notes: A virtual machine of sorts
Draw saved PTBR and Registers table

## Slide 37: Role of the OS
Role of the OS
Context Switching
  Provides illusion that every process owns a CPU
Virtual Memory
  Provides illusion that process owns some memory
Device drivers & system calls
  Provides illusion that process owns a keyboard, …
To do:
How to start a process?
How do processes communicate / coordinate?
Notes: Draw OS on next slide

## Slide 38: Role of the OS
Notes: Draw OS and Process state

## Slide 39
Creating Processes:
Fork

## Slide 40: How to create a process?
Q: How to create a process?
A: Double click
After boot, OS starts the first process
…which in turn creates other processes
  parent / child  the process tree
Notes: 1st process = init

## Slide 41: pstree example
$ pstree | view -
init-+-NetworkManager-+-dhclient
|-apache2
|-chrome-+-chrome
| `-chrome
|-chrome---chrome
|-clementine
|-clock-applet
|-cron
|-cupsd
|-firefox---run-mozilla.sh---firefox-bin-+-plugin-cont
|-gnome-screensaver
|-grep
|-in.tftpd
|-ntpd
`-sshd---sshd---sshd---bash-+-gcc---gcc---cc1
|-pstree
|-vim
`-view

## Slide 42: Processes Under UNIX
Init is a special case. For others…
Q: How does parent process create child process?
A: fork() system call
Wait. what? int fork() returns TWICE!
Notes: 1. creates new address space (Copy-On-Write duplicate of parent’s)
2. creates new execution state in OS process table (Exact copy of parent’s)
3. returns child’s id to parent (context[parent_id]->v0 = child_id)
4. returns zero to child (context[child_id]->v0 = 0)

## Slide 43: Example
main(int ac, char **av) {
int x = getpid(); // get current process ID from OS
char *hi = av[1]; // get greeting from command line
printf(“I’m process %d\n”, x);
int id = fork();
if (id == 0)
printf(“%s from %d\n”, hi, getpid());
else
printf(“%s from %d, child is %d\n”, hi, getpid(), id);
}
$ gcc -o strange strange.c
$ ./strange “Hey”
I’m process 23511
Hey from 23512
Hey from 23511, child is 23512
Notes: Draw OS state

## Slide 44: Inter-process Communication
Parent can pass information to child
  In fact, all parent data is passed to child
  But isolated after (C-O-W ensures changes are invisible)
Q: How to continue communicating?
A: Invent OS “IPC channels” : send(msg), recv(), …
Notes: IPC = inter-process communication
sockets, RMI, ipc, unix-domain sockets, pipes

## Slide 45: Inter-process Communication
Parent can pass information to child
  In fact, all parent data is passed to child
  But isolated after (C-O-W ensures changes are invisible)
Q: How to continue communicating?
A: Shared (Virtual) Memory!
Notes: Before fork: allocate pages, mark as “shared”
During fork: don’t set copy-on-write for these pages
After fork: either can read/write

## Slide 46
Processes and Threads

## Slide 47: Processes are heavyweight
Parallel programming with processes:
  They share almost everything code, shared mem, open files, filesystem privileges, …
  Pagetables will be almost identical
  Differences: PC, registers, stack
Recall: process = execution context + address space
Notes: pstree example: Firefox downloader, renderer, toolbar, etc.
Idea: multiple execution contexts sharing a single address space!

## Slide 48: Processes and Threads
Process
OS abstraction of a running computation
  The unit of execution
  The unit of scheduling
  Execution state + address space
From process perspective
  a virtual CPU
  some virtual memory
  a virtual keyboard, screen, …
Thread
OS abstraction of a single thread of control
  The unit of scheduling
  Lives in one single process
From thread perspective
  one virtual CPU core on a virtual multi-core machine
Notes: d/Unit of scheduling/
s/execution state/one or more threads/
s/virtual CPU/virtual multi-core machine/

## Slide 49: Multithreaded Processes

## Slide 50: Threads
#include <pthread.h>
int counter = 0;
void PrintHello(int arg) {
printf(“I’m thread %d, counter is %d\n”, arg, counter++);
... do some work ...
pthread_exit(NULL);
}
int main () {
for (t = 0; t < 4; t++) {
printf(“in main: creating thread %d\n", t);
pthread_create(NULL, NULL, PrintHello, t);
}
pthread_exit(NULL);
}

## Slide 51: Threads versus Fork
in main: creating thread 0
I’m thread 0, counter is 0
in main: creating thread 1
I’m thread 1, counter is 1
in main: creating thread 2
in main: creating thread 3
I’m thread 3, counter is 2
I’m thread 2, counter is 3
If processes?

## Slide 52: Example Multi-Threaded Program
Example: Apache web server
void main() { setup();
while (c = accept_connection()) {
req = read_request(c);
hits[req]++; send_response(c, req);
}
cleanup();
}
Notes: Use fork
Use threads

## Slide 53: Race Conditions
Example: Apache web server
Each client request handled by a separate thread (in parallel)
  Some shared state: hit counter, ...
(look familiar?)
Timing-dependent failure  race condition
  hard to reproduce  hard to debug
Thread 52
...
hits = hits + 1;
...
Thread 205
...
hits = hits + 1;
...
Thread 52
read hits
addi
write hits
Thread 205
read hits
addi
write hits
Notes: What happens when two threads execute concurrently?
sequential with threads
between threads is unsynchronized

## Slide 54: Programming with threads
Within a thread: execution is sequential
Between threads?
  No ordering or timing guarantees
  Might even run on different cores at the same time
Problem: hard to program, hard to reason about
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Cache coherency isn’t sufficient…
Need explicit synchronization to make sense of concurrency!

## Slide 55
Managing Concurrency
Races, Critical Sections, and Mutexes

## Slide 56: Goals
Concurrency Goals
Liveness
  Make forward progress
Efficiency
  Make good use of resources
Fairness
  Fair allocation of resources between threads
Correctness
  Threads are isolated (except when they aren’t)

## Slide 57: Race conditions
Race Condition
Timing-dependent error when accessing shared state
  Depends on scheduling happenstance … e.g. who wins “race” to the store instruction?
Concurrent Program Correctness = all possible schedules are safe
  Must consider every possible permutation
  In other words…
… the scheduler is your adversary

## Slide 58: Critical sections
What if we can designate parts of the execution as critical sections
  Rule: only one thread can be “inside”
Thread 52
read hits
addi
write hits
Thread 205
read hits
addi
write hits
Notes: Show picture

## Slide 59: Interrupt Disable
Q: How to implement critical section in code?
A: Lots of approaches….
Disable interrupts?
CSEnter() = disable interrupts (including clock)
CSExit() = re-enable interrupts
Works for some kernel data-structures
Very bad idea for user code
read hits
addi
write hits
Notes:   but only within a single core: why?
  (important events are delayed… forever?)

## Slide 60: Preemption Disable
Q: How to implement critical section in code?
A: Lots of approaches….
Modify OS scheduler?
CSEnter() = syscall to disable context switches
CSExit() = syscall to re-enable context switches
Doesn’t work if interrupts are part of the problem
Usually a bad idea anyway
read hits
addi
write hits
Notes: (e.g. won’t work for many kernel datastructures)
(caller forgets to CSExit? Or waits a long time?)

## Slide 61: Mutexes
Q: How to implement critical section in code?
A: Lots of approaches….
Mutual Exclusion Lock (mutex)
acquire(m): wait till it becomes free, then lock it
release(m): unlock it
apache_got_hit() {
pthread_mutex_lock(m);
hits = hits + 1;
pthread_mutex_unlock(m)
}

## Slide 62
Q: How to implement mutexes?
Notes: A: next time…