## Slide 1: Synchronization II
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
P&H Chapter 2.11

## Slide 2: Administrivia
Pizza party: PA3 Games Night
  Friday, April 27th, 5:00-7:00pm
  Location: Upson B17
Prelim3 Review
  Today, Tuesday, April 24th, 5:30-7:30pm
  Location: Hollister 110
Prelim 3
  Thursday, April 26th, 7:30pm
  Location: Olin 155
PA4: Final project out next week
  Demos: May 14-16
  Will not be able to use slip days

## Slide 3: Goals for Today
Synchronization
  Threads and processes
  Critical sections, race conditions, and mutexes
  Atomic Instructions
    HW support for synchronization
    Using sync primitives to build concurrency-safe data structures
    Cache coherency causes problems
    Locks + barriers
  Language level synchronization

## Slide 4: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory (e.g. ATS, BTS; x86)
  Or an atomic pair of instructions (e.g. LL and SC; MIPS)

## Slide 5: Synchronization in MIPS
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: MOVE $t0,$s4 ;copy exchange value
  LL $t1,0($s1) ;load linked
  SC $t0,0($s1) ;store conditional
  BEQZ $t0,try ;branch store fails
  MOVE $s4,$t1 ;put load value in $s4

## Slide 6: Programming with Threads
Need it to exploit multiple processing units
…to provide interactive applications
…to parallelize for multicore
…to write servers that handle many clients
Problem: hard even for experienced programmers
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Needed: synchronization of threads

## Slide 7: Programming with Threads
Concurrency poses challenges for:
Correctness
  Threads accessing shared memory should not interfere with each other
Liveness
  Threads should not get stuck, should make forward progress
Efficiency
  Program should make good use of available computing resources (e.g., processors).
Fairness
  Resources apportioned fairly between threads

## Slide 8: Two threads, one counter
Example: Web servers use concurrency
Multiple threads handle client requests in parallel.
Some shared state, e.g. hit counts:
  each thread increments a shared counter to track number of hits
What happens when two threads execute concurrently?
…
hits = hits + 1;
…
…
LW R0, hitsloc
ADDI R0, r0, 1
SW R0, hitsloc
…

## Slide 9: Shared counters
Possible result: lost update!
Timing-dependent failure  race condition
  hard to reproduce  Difficult to debug
addu/sw: hits = 0 + 1
lw (0)
addu/sw: hits = 0 + 1
lw (0)
T1
T2
hits = 1
hits = 0
time

## Slide 10: Race conditions
Def: timing-dependent error involving access to shared state
  Whether it happens depends on how threads scheduled: who wins “races” to instruction that updates state vs. instruction that accesses state
  Races are intermittent, may occur rarely
    Timing dependent = small changes can hide bug
  A program is correct only if all possible schedules are safe
    Number of possible schedule permutations is huge
    Need to imagine an adversary who switches contexts at the worst possible time

## Slide 11: Critical sections
To eliminate races: use critical sections that only one thread can be in
  Contending threads must wait to enter
CSEnter();
  Critical section
CSExit();
T1
T2
time
CSEnter();
  Critical section
CSExit();
T1
T2

## Slide 12: Mutexes
Critical sections typically associated with mutual exclusion locks (mutexes)
Only one thread can hold a given mutex at a time
Acquire (lock) mutex on entry to critical section
  Or block if another thread already holds it
Release (unlock) mutex on exit
  Allow one waiting thread (if any) to acquire & proceed
pthread_mutex_lock(&m);
  hits = hits+1;
pthread_mutex_unlock(&m);
T1
T2
pthread_mutex_lock(&m);
  hits = hits+1;
pthread_mutex_unlock(&m);
pthread_mutex_init(&m);

## Slide 13: Mutexes
Q: How to implement critical section in code?
A: Lots of approaches….
Mutual Exclusion Lock (mutex)
lock(m): wait till it becomes free, then lock it
unlock(m): unlock it
safe_increment() {
pthread_mutex_lock(&m);
hits = hits + 1;
pthread_mutex_unlock(&m)
}

## Slide 14
Hardware Support for Synchronization

## Slide 15: Synchronization in MIPS
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: MOVE $t0,$s4 ;copy exchange value
  LL $t1,0($s1) ;load linked
  SC $t0,0($s1) ;store conditional
  BEQZ $t0,try ;branch store fails
  MOVE $s4,$t1 ;put load value in $s4

## Slide 16: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
while(test_and_test(m)){}
}
int test_and_set(int *m) {
old = *m;
*m = 1;
return old;
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 17: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
while(test_and_test(m)){}
}
int test_and_set(int *m) {
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
MOVE $v0, $t1
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 18: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
*m = 0;
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 19: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
SW $zero, 0($a0)
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 20: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
Notes: hardware implementation: lock bus while read-modify-write cycle happens, very expensive

## Slide 21: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
- compare and exchange (x86, ARM deprecated)
- linked load / store conditional (MIPS, ARM, PowerPC, DEC Alpha, …)
Notes: hardware implementation: lock bus while read-modify-write cycle happens, very expensive

## Slide 22: Synchronization
Synchronization techniques
clever code
  must work despite adversarial scheduler/interrupts
  used by: hackers
  also: noobs
disable interrupts
  used by: exception handler, scheduler, device drivers, …
disable preemption
  dangerous for user code, but okay for some kernel code
mutual exclusion locks (mutex)
  general purpose, except for some interrupt-related cases
Notes: device drivers if interrupts always go to same core

## Slide 23
Using synchronization primitives to build
concurrency-safe datastructures

## Slide 24: Broken invariants
Access to shared data must be synchronized
  goal: enforce datastructure invariants
// invariant: // data is in A[h … t-1]
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
A[t] = c;
t++;
}
// consumer: take from list head
char get() {
while (h == t) { };
char c = A[h];
h++;
return c;
}
1
2
3
head
tail
Notes: draw picture
invariant broken just before last/first increments
needs: make the list into a ring buffer, add code in writer to wait if list is full

## Slide 25: Protecting an invariant
Rule of thumb: all updates that can affect invariant become critical sections
// invariant: (protected by m) // data is in A[h … t-1]
pthread_mutex_t *m = pthread_mutex_create();
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
pthread_mutex_lock(m);
A[t] = c;
t++;
pthread_mutex_unlock(m);
}
// consumer: take from list head
char get() {
pthread_mutex_lock(m);
while(h == t) {}
char c = A[h];
h++;
pthread_mutex_unlock(m);
return c;
}
Notes: bug: can’t do busy waiting inside mutex… what to do?

## Slide 26: Guidelines for successful mutexing
Insufficient locking can cause races
  Skimping on mutexes? Just say no!
Poorly designed locking can cause deadlock
  know why you are using mutexes!
  acquire locks in a consistent order to avoid cycles
  use lock/unlock like braces (match them lexically)
    lock(&m); …; unlock(&m)
    watch out for return, goto, and function calls!
    watch out for exception/error conditions!
  P1: lock(m1); lock(m2);
  P2: lock(m2); lock(m1);

## Slide 27
Cache Coherency
causes yet more trouble

## Slide 28: Remember: Cache Coherence
Recall: Cache coherence defined...
Informal: Reads return most recently written value
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
  P1 writes X before P2 reads X  read returns written value
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
Notes: Last condition: sequential consitency

## Slide 29: Relaxed consistency implications
Ideal case: sequential consistency
  Globally: writes appear in interleaved order
  Locally: other core’s writes show up in program order
In practice: not so much…
  write-back caches  sequential consistency is tricky
  writes appear in semi-random order
  locks alone don’t help
* MIPS has sequential consistency; Intel does not
Notes: locks don’t help

## Slide 30: Acquire/release
Memory Barriers and Release Consistency
  Less strict than sequential consistency; easier to build
One protocol:
  Acquire: lock, and force subsequent accesses after
  Release: unlock, and force previous accesses before
  P1: ...
  acquire(m);
  A[t] = c;
  t++; release(m);
  P2: ...
  acquire(m);
  A[t] = c;
  t++; unlock(m);
Moral: can’t rely on sequential consistency (so use synchronization libraries)
Notes: require hardware support
pthread_mutex has built-in memory barriers to implement acquire/release semantics

## Slide 31
Are Locks + Barriers enough?

## Slide 32: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
acquire(L);
char c = A[h];
h++;
release(L);
return c;
}
head
last==head
empty
while(empty) {}

## Slide 33: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
acquire(L);
char c = A[h];
h++;
release(L);
return c;
}
char get() {
acquire(L);
while (h == t) { };
char c = A[h];
h++;
release(L);
return c;
}
char get() {
while (h == t) { };
acquire(L);
char c = A[h];
h++;
release(L);
return c;
}
Dilemma: Have to check while holding lock,
head
last==head
empty

## Slide 34: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
acquire(L);
char c = A[h];
h++;
release(L);
return c;
}
char get() {
acquire(L);
while (h == t) { };
char c = A[h];
h++;
release(L);
return c;
}
Dilemma: Have to check while holding lock,
but cannot wait while hold lock

## Slide 35: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
do {
acquire(L);
empty = (h == t);
if (!empty) {
c = A[h];
h++;
}
release(L);
} while (empty);
return c;
}

## Slide 36
Language-level Synchronization

## Slide 37: Condition variables
Use [Hoare] a condition variable to wait for a condition to become true (without holding lock!)
wait(m, c) :
  atomically release m and sleep, waiting for condition c
  wake up holding m sometime after c was signaled
signal(c) : wake up one thread waiting on c
broadcast(c) : wake up all threads waiting on c
POSIX (e.g., Linux): pthread_cond_wait, pthread_cond_signal, pthread_cond_broadcast

## Slide 38: Using a condition variable
wait(m, c) : release m, sleep until c, wake up holding m
signal(c) : wake up one thread waiting on c
char get() {
lock(m);
while (t == h)
wait(m, not_empty);
char c = A[h];
h = (h+1) % n;
unlock(m);
signal(not_full);
return c;
}
cond_t *not_full = ...;
cond_t *not_empty = ...;
mutex_t *m = ...;
void put(char c) {
lock(m);
while ((t-h) % n == 1)
wait(m, not_full);
A[t] = c;
t = (t+1) % n;
unlock(m);
signal(not_empty);
}

## Slide 39: Monitors
A Monitor is a concurrency-safe datastructure, with…
  one mutex
  some condition variables
  some operations
All operations on monitor acquire/release mutex
  one thread in the monitor at a time
Ring buffer was a monitor
Java, C#, etc., have built-in support for monitors

## Slide 40: Java concurrency
Java objects can be monitors
  “synchronized” keyword locks/releases the mutex
  Has one (!) builtin condition variable
    o.wait() = wait(o, o)
    o.notify() = signal(o)
    o.notifyAll() = broadcast(o)
  Java wait() can be called even when mutex is not held. Mutex not held when awoken by signal(). Useful?

## Slide 41: More synchronization mechanisms
Lots of synchronization variations… (can implement with mutex and condition vars.)
Reader/writer locks
  Any number of threads can hold a read lock
  Only one thread can hold the writer lock
Semaphores
  N threads can hold lock at the same time
Message-passing, sockets, queues, ring buffers, …
  transfer data and synchronize

## Slide 42: Summary
Hardware Primitives: test-and-set, LL/SC, barrier, ...
… used to build …
Synchronization primitives: mutex, semaphore, ...
… used to build …
Language Constructs: monitors, signals, ...