## Slide 1: Gates and Logic: From switches to Transistors, Logic Gates and Logic Circuits
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See: P&H Appendix C.2 and C.3 (Also, see C.0 and C.1)

## Slide 2: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 3: A switch
Acts as a conductor or insulator
Can be used to build amazing things…
The Bombe used to break the German
Enigma machine during World War II
Notes: Pictures show the Bombe built by Alan Turing to break the enigma machine ciphers.
They were Fixed-Program Computers came before stored-program computers (general purpose)
The former required re-wiring (e.g. ENIAC took 3 weeks to “re-wire”).

## Slide 4: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
+
-
-
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A
B
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
+
Notes: Speed and size of a mechanical switch

## Slide 5: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
-
-
A
B
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
OR
AND
Notes: Speed and size of a mechanical switch

## Slide 6: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
-
-
A
B
A
B
A | B | Light
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
A | B | Light
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Truth Table
0 = OFF
1 = ON
OR
AND
Notes: Speed and size of a mechanical switch

## Slide 7: Basic Building Blocks: Switches to Logic Gates
Did you know?
George Boole Inventor of the idea of logic gates. He was born in Lincoln, England and he was the son of a shoemaker in a low class family.
A
B
A
B
George Boole,(1815-1864)
OR
AND
Notes: E.g. logic statements:
“Jane will only go to the cinema tonight if a good film is on AND she has enough money.”
“Stuart will only go to the birthday party on Sunday if Katie OR Sujit is going too.”

## Slide 8: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 9: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
A
B
A
B
In
Notes: Flash Drives
Create truth table of AND or OR: state what they do

## Slide 10: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
Notes: Flash Drives
Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 11: Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
Notes: Flash Drives
Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 12: Activity#1.A: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a | b | Out
a
b
Out
Notes: Fill out table
Put, NOT, AND, OR labels in box

## Slide 13: Activity#1: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a
b
d
Out
a | b | d | Out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: Fill out table

## Slide 14: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 15: Next Goal
Given a Logic function, create a Logic Circuit that implements the Logic Function…
…and, with the minimum number of logic gates
Fewer gates: A cheaper ($$$) circuit!
Notes: Can get logic circuit from truth table
Minimize logic circuit through algebraic reductions or Karnaugh Maps

## Slide 16: Logic Gates
NOT:
AND:
OR:
XOR:
L
ogic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 17: Logic Gates
NOT:
AND:
OR:
XOR:
L
ogic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
In
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
XNOR:
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 18: Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 19: Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
NAND:
  out = = !(a & b) =  (a  b)
NOR:
  out = = !(a | b) =  (a  b)
XNOR:
  out = = ab +
  .
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 20: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a ∙ 0 =
  a ∙ 1 =
  a ∙ ā =
Notes: Minimization activity
Maybe use picture to go through
Complement a+ā=1 and aā=0

## Slide 21: Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  =
  =
  a + a b =
  a(b+c) =
  =
Notes: Minimization activity
Maybe use picture to go through
  De Morgan’s Law: = ∙ and = +
Minimization activity
Maybe use picture to go through
  De Morgan’s Law: ((a+b)) ̅ = a ̅ ∙ b ̅ and ((a ∙b)) ̅ = a ̅ + b ̅

## Slide 22: Logic Manipulation
functions: gates ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 23: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 24
Notes: Think-Pair-Share: Why does minimization matter

## Slide 25: Next Goal
How to standardize minimizing logic circuits?

## Slide 26: Logic Minimization
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: Draw circuit and go through out=true cases
Have not done cheaply yet

## Slide 27: Logic Minimization
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Write minterm’s
sum of products:
OR of all minterms where out=1
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
Notes: Show what out equals

## Slide 28: Karnaugh Maps
        How does one find the most efficient equation?
          Manipulate algebraically until…?
          Use Karnaugh maps (optimize visually)
          Use a software optimizer
          For large circuits
          Decomposition & reuse of building blocks

## Slide 29: Minimization with Karnaugh maps (1)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields?
  out =

## Slide 30: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields?
  out =
Karnaugh maps identify which inputs are (ir)relevant to the output
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 31: Minimization with Karnaugh maps (2)
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields?
  out =
Karnaugh map minimization
  Cover all 1’s
  Group adjacent blocks of 2n 1’s that yield a rectangular shape
  Encode the common features of the rectangle
    out = ab + ac
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab

## Slide 32: Karnaugh Minimization Tricks (1)
Minterms can overlap
  out =
Minterms can span 2, 4, 8 or more cells
  out =
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 33: Karnaugh Minimization Tricks (2)
The map wraps around
  out =
  out =
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 34: Karnaugh Minimization Tricks (3)
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out =
  assume middle x’s = 0
  assume 4th column x = 1
  out =
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 35: Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d
a | b | d | out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: What is the truth table

## Slide 36: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.
Any logic function can be implemented as “sum of products”. Karnaugh Maps minimize number of gates.
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 37: Goals for Today
From Transistors to Gates to Logic Circuits
Logic Gates
  From transistors
  Truth Tables
Logic Circuits
  Identity Laws
  From Truth Tables to Circuits (Sum of Products)
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 38: NMOS and PMOS Transistors
NMOS Transistor
Connect source to drain when VG = Vsupply
N-channel transistor
VS = 0 V
VG
VG = VSupply
VG = 0 V
PMOS Transistor
Connect source to drain when VG = 0 V
P-channel transistor
VG
VG = VSupply
VG = 0 V
VD
VD = 0V
Closed switch
When VG = Vsupply
Closed switch
When VG = 0 V
Vsupply
VS = Vsupply
Vsupply
Vsupply
VD
VS: voltage at the source
VD: voltage at the drain
Vsupply: max voltage (aka a logical 1)
(ground): min voltage (aka a logical 0)
VD = Vsupply

## Slide 39: NMOS and PMOS Transistors
NMOS Transistor
Connect source to drain when gate = 1
N-channel transistor
D
S = 0V
G
G = 1
G = 0
PMOS Transistor
Connect source to drain when gate = 0
P-channel transistor
Vsupply
D
G
G = 1
G = 0
D = 0
Closed switch
When VG = Vsupply
Closed switch
When VG = 0 V
S = Vsupply
Vsupply
Vsupply
D = 1
VS: voltage at the source
VD: voltage at the drain
Vsupply: max voltage (aka a logical 1)
(ground): min voltage (aka a logical 0)

## Slide 40: Inverter
A | Out
0 | 1
1 | 0
Function: NOT
Called an inverter
Symbol:
Useful for taking the inverse of an input
CMOS: complementary-symmetry metal–oxide–semiconductor
in
out
Truth table
A
out
Vdd = hi
Vss = gnd
A = 0

## Slide 41: NAND Gate
A | B | out
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
Function: NAND
Symbol:
b
a
out
A
out
Vdd
B
B
A
Vdd
Vss

## Slide 42: NOR Gate
A
out
Vss
Vdd
B
B
A
Vss
A | B | out
0 | 0 | 1
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
b
a
out
Function: NOR
Symbol:
Notes: Example

## Slide 43: Building Functions (Revisited)
NOT:
AND:
OR:
NAND and NOR are universal
  Can implement any function with NAND or just NOR gates
  useful for manufacturing
Notes: Flash Drives
Create truth table of AND or OR: state what they do

## Slide 44: Building Functions (Revisited)
NOT:
AND:
OR:
NAND and NOR are universal
  Can implement any function with NAND or just NOR gates
  useful for manufacturing
b
a
b
a
a
Notes: Flash Drives
Create truth table of AND or OR: state what they do

## Slide 45: Logic Gates
One can buy gates separately
  ex. 74xxx series of integrated circuits
  cost ~$1 per chip, mostly for packaging and testing
Cumbersome, but possible to build devices using gates put together manually

## Slide 46: Then and Now
The first transistor
  on a workbench at
  AT&T Bell Labs in 1947
  Bardeen, Brattain, and Shockley
An Intel Westmere
  1.17 billion transistors
  240 square millimeters
  Six processing cores
http://www.theregister.co.uk/2010/02/03/intel_westmere_ep_preview/
Notes: John Bardeen
Walter Brattain
William Shockley

## Slide 47: Summary
Most modern devices are made from billions of on /off switches called transistors
  We will build a processor in this course!
  Transistors made from semiconductor materials:
    MOSFET – Metal Oxide Semiconductor Field Effect Transistor
    NMOS, PMOS – Negative MOS and Positive MOS
    CMOS – Complimentary MOS made from PMOS and NMOS transistors
  Transistors used to make logic gates and logic circuits
We can now implement any logic circuit
  Can do it efficiently, using Karnaugh maps to find the minimal terms required
  Can use either NAND or NOR gates to implement the logic circuit
  Can use P- and N-transistors to implement NAND or NOR gates

## Slide 48: Big Picture: Abstraction
Hide complexity through simple abstractions
  Simplicity
    Box diagram represents inputs and outputs
  Complexity
    Hides underlying P- and N-transistors and atomic interactions
in
out
Vdd
Vss
in
out
out
a
d
b
a
b
d
out