## Slide 1: State and Finite State Machines
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See P&H Appendix C.7. C.8, C.10, C.11

## Slide 2: Stateful Components
Until now is combinatorial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 3: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 4: Goal
How do we store store one bit?

## Slide 5: First Attempt: Unstable Devices
B
A
C

## Slide 6: Second Attempt: Bistable Devices
A
B
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 7: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Can you store a value (with this circuit)?
Can you change its value?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 8: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q

## Slide 9: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 10: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
S
R
Q

## Slide 11: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 12: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 13: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 14: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 15: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 16: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 17: Edge-triggering
Can design circuits to change on the rising or falling edge
Trigger on rising edge = positive edge-triggered
Trigger on falling edge = negative edge-triggered
Inputs must be stable just before the triggering edge
input
clock

## Slide 18: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 19: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 20: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 21: Sixth Attempt: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
L
L
clk
D
X
Q
c
X
c
Q
D
clk
0
0
1
0
1
Activity#1: Fill in timing graph and values for X and Q
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 22: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 23: Next Goal
How do we store more than one bit, N bits?

## Slide 24: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 25: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is be created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 26: An Example: What will this circuit do?
32-bit
reg
Clk
+1
Run
WE
R
Reset
Decoder

## Slide 27: Recap
We can now build interesting devices with sensors
  Using combinatorial logic
We can also store data values
  In state-holding elements
  Coupled with clocks

## Slide 28: Administrivia
Make sure to go to your Lab Section this week
Design Doc for Lab1 due in one week, next Monday, Feb 4th
Completed Lab1 due in two weeks, Monday, Feb 11th
Work alone
Homework1 is out
Due in one week, next Wednesday, start early
Work alone
But, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 29: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2013sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 26th
  Thursday, March 28th
  Thursday, April 25th
Schedule is subject to change

## Slide 30: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  20% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 31: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 32: Finite State Machines

## Slide 33: Next Goal
How do we design logic circuits with state?

## Slide 34: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 35: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 36: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic
Notes: Put sequential logic term on slide

## Slide 37: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 38: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/on
up/off
down/on
up/off
up/off
Input: = up or = down
Output: = on or = off
States: = A, = B, = C, or = D
Notes: Say left of slash is input and right is output

## Slide 39: FSM Example
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 1=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 40: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 41: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 42: Moore Machine Example
Legend
state out
input
startout
A off
B on
C off
D on
down
up
down
down
up
down
up
up
Input: up or down
Output: on or off
States: A, B, C, or D
Notes: Also show a mealy machine

## Slide 43: Activity #2: Create a Mealy FSM for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
  How many states are needed to represent FSM?
  Draw and Fill in FSM diagram
…10110
…01111
…00101
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Notes: Ask as a clicker question

## Slide 44: FSM: State Diagram
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
…10110
…01111
…00101
a
b
z
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 45: Serial Adder: State Table
a | b | Current state | z | Next state
(2) Write down all input and state combinations
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 46: Serial Adder: State Table
a | b | Current state | z | Next state
(3) Encode states, inputs, and outputs as bits
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 47: Serial Adder: Circuit
(4) Determine logic equations for next state and outputs
Combinational Logic Equations
  .
Next State
Current State
Input
Output
Comb. Logic
a
b
D
Q
s
z
s'
s'
Next State
a | b | s | z | s'
Notes: Practice minimizing circuit w/a Karnaugh map

## Slide 48: Example: Digital Door Lock
Digital Door Lock
Inputs:
  keycodes from keypad
  clock
Outputs:
  “unlock” signal
  display how many keys pressed so far

## Slide 49: Door Lock: Inputs
Assumptions:
  signals are synchronized to clock
  Password is B-A-B
K
A
B
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed
Notes: How many states, another clicker question

## Slide 50: Door Lock: Outputs
Assumptions:
  High pulse on U unlocks door
U
D3D2D1D0
4
LED dec
8
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 51: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
any
else
else
B3
”3”
else
(1) Draw a state diagram (e.g. Moore Machine)

## Slide 52: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
(1) Draw a state diagram (e.g. Moore Machine)
Notes: Works, but gives extra information revealing a secret

## Slide 53: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Output
(2) Write output and next-state tables

## Slide 54: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Output
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”
(2) Write output and next-state tables

## Slide 55: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Input | Next State
Cur. State | Input | Next State
(2) Write output and next-state tables

## Slide 56: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
else
any
else
else
Cur. State | Input | Next State
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle
(2) Write output and next-state tables

## Slide 57: State Table Encoding
(3) Encode states, inputs, and outputs as bits
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”
U
D3D2D1D0
4
dec
8
D3 | D2 | D1 | D0 | U
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
K
A
B
S2 | S1 | S0
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed
State | S2 | S1 | S0
Idle | 0 | 0 | 0
G1 | 0 | 0 | 1
G2 | 0 | 1 | 0
G3 | 0 | 1 | 1
B1 | 1 | 0 | 0
B2 | 1 | 0 | 1
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle
S2 | S1 | S0 |  | S’2 | S’1 | S’0
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 0 |  | 0 | 0 | 1
0 | 0 | 0 |  | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 1
0 | 0 | 1 |  | 0 | 1 | 0
0 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 0 | 1 |  | 0 | 0 | 0
K | A | B
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
x | x | x
0 | 0 | 0
1 | x | x
0 | 0 | 0
1 | x | x

## Slide 58: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 59: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
D3 | D2 | D1 | D0 | U
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
S2 | S1 | S0
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
(4) Determine logic equations for next state and outputs
U = S1S0
D0 = S0 + S1S0 + S2
D1 = S1S0 + S1S0 + S1S0

## Slide 60: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
(4) Determine logic equations for next state and outputs
S2 | S1 | S0 |  | S’2 | S’1 | S’0
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 0 |  | 0 | 0 | 1
0 | 0 | 0 |  | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 1
0 | 0 | 1 |  | 0 | 1 | 0
0 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 0 | 1 |  | 0 | 0 | 0
K | A | B
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
x | x | x
0 | 0 | 0
1 | x | x
0 | 0 | 0
1 | x | x
S2’ = KA + S0KB + S2 + S1S0K + S2 S0
D0 = S0 + S1S0 + S2
D1 = S1S0 + S1S0 + S1S0
Notes: Write down and compare S2’

## Slide 61: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes
  State Machines or Ad-Hoc Circuits