## Slide 1: Memory
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University

## Slide 2: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 3: Administrivia
Make sure partner in same Lab Section this week
Lab2 is out
Due in one week, next Monday, start early
Work alone
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab
No Homework this week

## Slide 4: Administrivia
Make sure to go to your Lab Section this week
  Find project partners this week (for upcoming project1 next week)
  Lab2 due in class this week (it is not homework)
  Design Doc for Lab1 due yesterday, Monday, Feb 4th
  Completed Lab1 due next week, Monday, Feb 11th
  Work alone
Homework1 is due Wednesday
  Work alone
BUT, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab
Second C Primer: Thursday, B14 Hollister, 6-8pm

## Slide 5: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2013sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 26th
  Thursday, March 28th
  Thursday, April 25th
Schedule is subject to change

## Slide 6: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 7: Goals for today
Memory
  CPU: Register Files (i.e. Memory w/in the CPU)
  Scaling Memory: Tri-state devices
  Cache: SRAM (Static RAM—random access memory)
  Memory: DRAM (Dynamic RAM)

## Slide 8: Goal:
How do we store results from ALU computations?
How do we use stored results in subsequent operations?
Register File
How does a Register File work? How do we design it?

## Slide 9: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 10: Register File
Register File
  N read/write registers
  Indexed by register number
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
W
32
32
32
1
5
5
5

## Slide 11: Tradeoffs
Register File tradeoffs
  + Very fast (a few gate delays for
  both read and write)
  + Adding extra ports is
  straightforward
  – Doesn’t scale
  e.g. 32MB register file with
  32 bit registers
  Need 32x 1M-to-1 multiplexor
  and 32x 10-to-1M decoder
  How many logic gates/transistors?
a
b
c
d
e
f
g
h
s2
s1
s0
8-to-1 mux
Notes: Need two transistors per input of a logic gate
20 = 1024 = 1k
220 = 1M
230 = 1G
240 = 1T

## Slide 12: Takeway
Register files are very fast storage (only a few gate delays), but does not scale to large memory sizes.

## Slide 13: Goals for today
Memory
  CPU: Register Files (i.e. Memory w/in the CPU)
  Scaling Memory: Tri-state devices
  Cache: SRAM (Static RAM—random access memory)
  Memory: DRAM (Dynamic RAM)

## Slide 14: Next Goal
How do we scale/build larger memories?

## Slide 15: Building Large Memories
Need a shared bus (or shared bit line)
  Many FlipFlops/outputs/etc. connected to single wire
  Only one output drives the bus at a time
  How do we build such a device?
S0
D0
shared line
S1
D1
S2
D2
S3
D3
S1023
D1023

## Slide 16: Tri-State Devices
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (high impedance)
Notes: z, z 0, 1

## Slide 17: Tri-State Devices
D
Q
E
Vsupply
Gnd
D
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (high impedance)
Notes: z, z 0, 1

## Slide 18: Shared Bus
S0
D0
shared line
S1
D1
S2
D2
S3
D3
S1023
D1023

## Slide 19: Takeway
Register files are very fast storage (only a few gate delays), but does not scale to large memory sizes.
Tri-state Buffers allow scaling since multiple registers can be connected to a single output, while only register actually drives the output.

## Slide 20: Goals for today
Memory
  CPU: Register Files (i.e. Memory w/in the CPU)
  Scaling Memory: Tri-state devices
  Cache: SRAM (Static RAM—random access memory)
  Memory: DRAM (Dynamic RAM)

## Slide 21: Next Goal
How do we build large memories?
Use similar designs as Tri-state Buffers to connect multiple registers to output line. Only one register will drive output line.

## Slide 22: SRAM
Static RAM (SRAM)—Static Random Access Memory
  Essentially just D-Latches plus Tri-State Buffers
  A decoder selects which line of memory to access
  (i.e. word line)
  A R/W selector determines the
  type of access
  That line is then coupled to
  the data lines
Data
Address
Decoder

## Slide 23: SRAM
Static RAM (SRAM)—Static Random Access Memory
  Essentially just D-Latches plus Tri-State Buffers
  A decoder selects which line of memory to access
  (i.e. word line)
  A R/W selector determines the
  type of access
  That line is then coupled to
  the data lines
Din
8
Dout
8
22
Address
Chip Select
Write Enable
Output Enable
SRAM
4M x 8
Notes: How many address bits are necessary for a 4M x 8 SRAM module? (i.e. 4M word lines that are each 8 bits wide)?

## Slide 24: SRAM
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
4 x 2 SRAM
E.g. How do we design
a 4 x 2 SRAM Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Notes: How many address bits are necessary for a 4 x 2 SRAM module? (i.e. 4 word lines that are each 2 bits wide)?

## Slide 25: SRAM
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
E.g. How do we design
a 4 x 2 SRAM Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Notes: How do we design a 4 x 2 SRAM Module?
Caption on C.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 26: SRAM
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
Bit line
Word line
E.g. How do we design
a 4 x 2 SRAM Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Notes: How do we design a 4 x 2 SRAM Module?
Caption on C.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 27: SRAM
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
4 x 2 SRAM
E.g. How do we design
a 4 x 2 SRAM Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Notes: Caption on C.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 28: SRAM
22
Address
Dout
Din
Write Enable
Output Enable
4M x 8 SRAM
8
8
E.g. How do we design
a 4M x 8 SRAM Module?
(i.e. 4M word lines that
are each 8 bits wide)?
Chip Select
Notes: Caption on C.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 29: SRAM
12
Address [21-10]
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
12 x
4096
decoder
mux
1024
mux
1024
mux
1024
mux
1024
mux
mux
1024
1024
mux
1024
mux
1024
Dout[7]
1
Dout[6]
1
Dout[5]
1
Dout[4]
1
Dout[3]
1
Dout[2]
1
Dout[1]
1
Dout[0]
1
Address [9-0]
10
4M x 8 SRAM
E.g. How do we design
a 4M x 8 SRAM Module?
Notes: Caption on C.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 30: SRAM
12
Address [21-10]
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
Row
decoder
1024
1024
1024
1024
1024
1024
1024
1024
Address [9-0]
10
4M x 8 SRAM
column selector, sense amp, and I/O circuits
Shared Data Bus
Chip Select (CS)
R/W Enable
8
E.g. How do we design
a 4M x 8 SRAM Module?
Notes: Caption on C.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 31: SRAM Modules and Arrays
A21-0
Bank 2
Bank 3
Bank 4
4M x 8 SRAM
4M x 8 SRAM
4M x 8 SRAM
4M x 8 SRAM
R/W
msb
lsb
CS
CS
CS
CS
Notes: 2, 3, or more step address decode
The first decoder generates the addresses for eight 4M x 4 arrays; then a set of multiplexors is used to select 1 bit from each 4-bit-wide array. This is a much easier design than a single-level decode that would need either an enormous decoder or a gigantic multiplexor. In practice, a modern SRAM of
this size would probably use an even larger number of blocks, each somewhat smaller.

## Slide 32: SRAM Summary
SRAM
A few transistors (~6) per cell
Used for working memory (caches)
But for even higher density…

## Slide 33: Dynamic RAM: DRAM
Dynamic-RAM (DRAM)
  Data values require constant refresh
Gnd
word line
bit line
Capacitor
Notes: value kept in a cell is stored as a charge in a capacitor
To refresh the cell, we merely read its contents and write it back.
Because DRAMs store the charge on a capacitor, it cannot be kept indefinitely and must periodically be refreshed. That is why this memory structure is called dynamic, as opposed to the static storage in an SRAM cell.
The pass transistor acts like a switch: when the signal on the word line is asserted, the switch is closed, connecting the capacitor to the bit line. If the operation is a write, then the value to be written is placed on the bit line. If the value is a 1, the capacitor will be charged. If the value is a 0, then the capacitor will be discharged. Reading is slightly more complex, since the DRAM must detect a very small charge stored in the capacitor. Before activating the word line for a read, the bit line is charged to the voltage that is halfway between the low and high voltage. Then, by activating the word line, the charge on the capacitor is read out onto the bit line. This causes the bit line to move slightly toward the high or low direction, and this change is detected with a sense amplifier, which can detect small changes in voltage.

## Slide 34: DRAM vs. SRAM
Single transistor vs. many gates
  Denser, cheaper ($30/1GB vs. $30/2MB)
  But more complicated, and has analog sensing
Also needs refresh
  Read and write back…
  …every few milliseconds
  Organized in 2D grid, so can do rows at a time
  Chip can do refresh internally
Hence… slower and energy inefficient

## Slide 35: Memory
Register File tradeoffs
  + Very fast (a few gate delays for both read and write)
  + Adding extra ports is straightforward
  – Expensive, doesn’t scale
  – Volatile
Volatile Memory alternatives: SRAM, DRAM, …
  – Slower
  + Cheaper, and scales well
  – Volatile
  Non-Volatile Memory (NV-RAM): Flash, EEPROM, …
  + Scales well
  – Limited lifetime; degrades after 100000 to 1M writes

## Slide 36: Summary
We now have enough building blocks to build machines that can perform non-trivial computational tasks
Register File: Tens of words of working memory
SRAM: Millions of words of working memory
DRAM: Billions of words of working memory
NVRAM: long term storage (usb fob, solid state disks, BIOS, …)
Next time we will build a simple processor!