## Slide 1: Processor
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See P&H Chapter 2.16-20, 4.1-4

## Slide 2: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 3: Goal for Today
Understanding the basics of a processor
  We now have enough building blocks to build machines that can perform non-trivial computational tasks
  Putting it all together:
  Arithmetic Logic Unit (ALU)—Lab0 & 1, Lecture 2 & 3
  Register File—Lecture 4 and 5
  Memory—Lecture 5
    SRAM: cache
    DRAM: main memory
  Instruction-types
  Instruction Datapaths

## Slide 4: MIPS Register File
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 5: MIPS Register file
MIPS register file
  32 registers, 32-bits each (with r0 wired to zero)
  Write port indexed via RW
    Writes occur on falling edge but only if WE is high
  Read ports indexed via RA, RB
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
WE
32
32
32
1
5
5
5

## Slide 6: MIPS Register file
MIPS register file
  32 registers, 32-bits each (with r0 wired to zero)
  Write port indexed via RW
    Writes occur on falling edge but only if WE is high
  Read ports indexed via RA, RB
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
r1
r2
…
r31

## Slide 7: MIPS Register file
Registers
  Numbered from 0 to 31.
  Each register can be referred by number or name.
  $0, $1, $2, $3 … $31
  Or, by convention, each register has a name.
    $16 - $23  $s0 - $s7
    $8 - $15  $t0 - $t7
    $0 is always $zero.
    Patterson and Hennessy p121.

## Slide 8: MIPS Memory
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 9: MIPS Memory
MIPS Memory
  Up to 32-bit address
  32-bit data (but byte addressed)
  Enable + 2 bit memory control (mc)
    00: read word (4 byte aligned)
    01: write byte
    10: write halfword (2 byte aligned)
    11: write word (4 byte aligned)
memory
32
addr
2
mc
32
32
E

## Slide 10: Putting it all together: Basic Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu
Notes: A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two

## Slide 11: Putting it all together: Basic Processor
Let’s build a MIPS CPU
  …but using (modified) Harvard architecture
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 12: Takeaway
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two

## Slide 13: Next Goal
How do we create computer programs and execute machine instructions?

## Slide 14: Levels of Interpretation: Instructions
Programs written in a
High Level Language
  C, Java, Python, Ruby, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Need translation to a lower-
level computer understandable
format
  Assembly is human readable machine language
  Processors operate on Machine Language
ALU, Control, Register File, …
Machine Implementation

## Slide 15: Levels of Interpretation: Instructions
High Level Language
  C, Java, Python, Ruby, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Assembly Language
  No symbols (except labels)
  One operation per statement
Machine Langauge
  Binary-encoded assembly
  Labels become addresses
ALU, Control, Register File, …
Machine Implementation

## Slide 16: Instruction Usage
Instructions are stored in memory, encoded in binary
A basic processor
  fetches
  decodes
  executes
one instruction at a time
pc
adder
cur inst
decode
regs
execute
addr
data
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
op=addi r0 r2 10

## Slide 17: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  unconditional jumps
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 18: Instruction Set Architecture
The types of operations permissible in machine language define the ISA
  MIPS: load/store, arithmetic, control flow, …
  VAX: load/store, arithmetic, control flow, strings, …
  Cray: vector operations, …
Two classes of ISAs
  Reduced Instruction Set Computers (RISC)
  Complex Instruction Set Computers (CISC)
We’ll study the MIPS ISA in this course

## Slide 19: Instruction Set Architecture
Instruction Set Architecture (ISA)
  Different CPU architecture specifies different set of instructions. Intel x86, IBM PowerPC, Sun Sparc, MIPS, etc.
MIPS
  ≈ 200 instructions, 32 bits each, 3 formats
    mostly orthogonal
  all operands in registers
    almost all are 32 bits each, can be used interchangeably
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in special registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]

## Slide 20: Instructions
Load/store architecture
  Data must be in registers to be operated on
  Keeps hardware simple
Emphasis on efficient implementation
Integer data types:
  byte: 8 bits
  half-words: 16 bits
  words: 32 bits
MIPS supports signed and unsigned data types

## Slide 21: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 22: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 23: Takeaway

## Slide 24: Next Goal
How are instructions executed?
What are the datapaths for different instruction-types

## Slide 25: Five Stages of MIPS Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor

## Slide 26: Five Stages of MIPS datapath
Basic CPU execution loop
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
Instruction types/format
Arithmetic/Register: addu $s0, $s2, $s3
Arithmetic/Immediate: slti $s0, $s2, 4
Memory: lw $s0, 20($s3)
Control/Jump: j 0xdeadbeef

## Slide 27: Stages of datapath (1/5)
Stage 1: Instruction Fetch
  Fetch 32-bit instruction from memory. (Instruction cache or memory)
  Increment PC accordingly.
    +4, byte addressing
    +N
PC
Prog.
Mem
+4
inst

## Slide 28: Stages of datapath (2/5)
Stage 2: Instruction Decode
  Gather data from the instruction
  Read opcode to determine instruction type and field length
  Read in data from register file
    for addu, read two registers.
    for addi, read one registers.
    for jal, read no registers.
5
5
5
control
Reg. File

## Slide 29: Stages of datapath (2/5)
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 30: Stages of datapath (3/5)
Stage 3: Execution (ALU)
  Useful work is done here (+, -, *, /), shift, logic operation, comparison (slt).
  Load/Store?
    lw $t2, 32($t3)
    Compute the address of the memory.
ALU

## Slide 31: Stages of datapath (4/5)
Stage 4: Memory access
  Used by load and store instructions only.
  Other instructions will skip this stage.
  This stage is expected to be fast, why?
Data
Mem
Target addr
from ALU
R/W
Data from
memory

## Slide 32: Stages of datapath (5/5)
Stage 5:
  For instructions that need to write value to register.
  Examples: arithmetic, logic, shift, etc, load.
  Store, branches, jump??
Reg. File
PC
WriteBack
from ALU
or Memory
New instruction address
If branch or jump

## Slide 33: Datapath and Clocking
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB

## Slide 34: Takeaway

## Slide 35: Next Goal
MIPS Instruction datapaths

## Slide 36: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 37: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 38: Arithmetic Instructions
op | rs | rt | rd | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x21 | ADDU rd, rs, rt | R[rd] = R[rs] + R[rt]
0x0 | 0x23 | SUBU rd, rs, rt | R[rd] = R[rs] – R[rt]
0x0 | 0x25 | OR rd, rs, rt | R[rd] = R[rs] ¦ R[rt]
0x0 | 0x26 | XOR rd, rs, rt | R[rd] = R[rs]  R[rt]
0x0 | 0x27 | NOR rd, rs rt | R[rd] = ~ ( R[rs] ¦ R[rt] )
00000001000001100010000000100110
R-Type

## Slide 39: Instruction Fetch
Instruction Fetch Circuit
  Fetch instruction from memory
  Calculate address of next instruction
  Repeat
Program Memory
inst
32
PC
2
00
32
+4

## Slide 40: Arithmetic and Logic
5
ALU
5
5
Reg. File
PC
Prog.
Mem
inst
+4
control

## Slide 41: Arithmetic Instructions: Shift
op | - | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rs, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rs, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rs, shamt | R[rd] = R[rs] >> shamt (sign ext.)
00000000000001000100000110000011
ex: r5 = r3 * 8
R-Type

## Slide 42: Shift
5
ALU
5
5
Reg. File
PC
Prog.
Mem
inst
+4
shamt
control

## Slide 43: Arithmetic Instructions: Immediates
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + imm
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & imm
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ imm
op | rs | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00100100101001010000000000000101
I-Type
ex: r5 += 5
ex: r9 = -1
ex: r9 = 65535
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + sign_extend(imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)

## Slide 44: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
control

## Slide 45: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
control

## Slide 46: Arithmetic Instructions: Immediates
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 bits | 5 bits | 5 bits | 16 bits
00111100000001010000000000000101
I-Type
ex: r5 = 0xdeadbeef

## Slide 47: Immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
inst
16
control
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 48: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 49: Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10100100101000010000000000000010
base + offset addressing
I-Type
signed offsets

## Slide 50: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 51: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 52: Control Flow: Absolute Jump
Absolute addressing for jumps
  Jump from 0x30000000 to 0x20000000? NO Reverse? NO
    But: Jumps from 0x2FFFFFFF to 0x3xxxxxxx are possible, but not reverse
  Trade-off: out-of-region jumps vs. 32-bit instruction encoding
MIPS Quirk:
  jump targets computed using already incremented PC
op | mnemonic | description
0x2 | J target | PC = target
op | immediate
6 bits | 26 bits
00001010100001001000011000000011
J-Type
op | mnemonic | description
0x2 | J target | PC = target ¦¦ 00
op | mnemonic | description
0x2 | J target | PC = (PC+4)31..28 ¦¦ target ¦¦ 00

## Slide 53: Absolute Jump
long jump? computed jump?
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 54: Control Flow: Jump Register
op | rs | - | - | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R-Type

## Slide 55: Jump Register
+4
||
tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 56: Control Flow: Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
00010000101000010000000000000011
signed offsets
I-Type

## Slide 57: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp

## Slide 58: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp

## Slide 59: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)

## Slide 60: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp

## Slide 61: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 PC = (PC+4)32..29 ¦¦ target ¦¦ 00
op | immediate
6 bits | 26 bits
00001100000001001000011000000010
J-Type

## Slide 62: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4

## Slide 63: Next Time
CPU Performance
Pipelined CPU