## Slide 1: CPU Performance Pipelined CPU
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See P&H Chapters 1.4 and 4.5

## Slide 2: Big Picture: Building a Processor
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 3: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency
Pipelining
  Intuition on Latency vs throuput

## Slide 4
Memory Layout and
Control instructions

## Slide 5: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 6: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 7: Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10101100101000010000000000000100
base + offset addressing
I-Type
signed offsets
ex: = Mem[4+r5] = r1 # SW r1, 4(r5)

## Slide 8: Endianness
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word

## Slide 9: Memory Layout
Examples (big/little endian):
# r5 contains 5 (0x00000005)
SB r5, 2(r0)
LB r6, 2(r0)
SW r5, 8(r0)
LB r7, 8(r0)
LB r8, 11(r0)
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff
Notes: Big Endian means store MSB (most significant byte) first

## Slide 10: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 11: Control Flow: Absolute Jump
Absolute addressing for jumps
  Jump from 0x30000000 to 0x20000000? NO Reverse? NO
    But: Jumps from 0x2FFFFFFF to 0x3xxxxxxx are possible, but not reverse
  Trade-off: out-of-region jumps vs. 32-bit instruction encoding
MIPS Quirk:
  jump targets computed using already incremented PC
op | Mnemonic | Description
0x2 | J target | PC = target
op | immediate
6 bits | 26 bits
00001010100001001000011000000011
J-Type
op | Mnemonic | Description
0x2 | J target | PC = target ¦¦ 00
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28 ¦¦ target ¦¦ 00
(PC+4)31..28 will be the same
Notes: ex: j 0xa12180c == j 168957964
PC = (PC+4)31..28||0xa12180c

## Slide 12: Absolute Jump
long jump? computed jump?
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
J
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28 ¦¦ target ¦¦ 00

## Slide 13: Control Flow: Jump Register
op | rs | - | - | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R-Type

## Slide 14: Jump Register
+4
||
tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R[r3]
JR

## Slide 15: Examples
E.g. Use Jump or Jump Register instruction to
jump to 0xabcd1234
But, what about a jump based on a condition?
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe00
else jump to 0xabcd1234

## Slide 16: Control Flow: Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
00010000101000010000000000000011
signed offsets
I-Type

## Slide 17: Examples (2)
if (i == j) { i = i * 4; }
else { j = i - j; }
s1
s0

## Slide 18: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
Could have used ALU for branch cmp
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
R[r5]
BEQ
R[r1]

## Slide 19: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
Conditional Jumps (cont.)

## Slide 20: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
R[r5]
BEQ

## Slide 21: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28 ¦¦ (target << 2)
op | immediate
6 bits | 26 bits
00001100000001001000011000000010
J-Type
Function/procedure calls
op | mnemonic | description
0x2 | J target | PC = (PC+4)31..28 ¦¦ (target << 2)
Discuss later
Notes: 0x0121808 == 1185800

## Slide 22: Absolute Jump
tgt
+4
||
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28 ¦¦ (target << 2)
R[r31]
PC+8

## Slide 23: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency
Pipelining
  Intuition on Latency vs throughput

## Slide 24: Next Goal
How do we measure performance?
What is the performance of a single cycle CPU?
See: P&H 1.4

## Slide 25: Performance
How to measure performance?
  GHz (billions of cycles per second)
  MIPS (millions of instructions per second)
  MFLOPS (millions of floating point operations per second)
  Benchmarks (SPEC, TPC, …)
Metrics
  latency: how long to finish my program
  throughput: how much work finished per unit time

## Slide 26: Latency: Processor Clock Cycle
Critical Path
  Longest path from a register output to a register input
  Determines minimum cycle, maximum clock frequency
How do we make the CPU perform better
(e.g. cheaper, cooler, go “faster”, …)?
  Optimize for delay on the critical path
  Optimize for size / power / simplicity elsewhere

## Slide 27: Latency: Optimize Delay on Critical Path
E.g. Adder performance
32 Bit Adder Design | Space | Time
Ripple Carry | ≈ 300 gates | ≈ 64 gate delays
2-Way Carry-Skip | ≈ 360 gates | ≈ 35 gate delays
3-Way Carry-Skip | ≈ 500 gates | ≈ 22 gate delays
4-Way Carry-Skip | ≈ 600 gates | ≈ 18 gate delays
2-Way Look-Ahead | ≈ 550 gates | ≈ 16 gate delays
Split Look-Ahead | ≈ 800 gates | ≈ 10 gate delays
Full Look-Ahead | ≈ 1200 gates | ≈ 5 gate delays

## Slide 28: Throughput: Multi-Cycle Instructions
Strategy 2
  Multiple cycles to complete a single instruction
E.g: Assume:
  load/store: 100 ns
  arithmetic: 50 ns
  branches: 33 ns
  Multi-Cycle CPU
  30 MHz (33 ns cycle) with
    3 cycles per load/store
    2 cycles per arithmetic
    1 cycle per branch
  Faster than Single-Cycle CPU?
  10 MHz (100 ns cycle) with
    1 cycle per instruction
ms = 10-3 second
us = 10-6 seconds
ns = 10-9 seconds
10 MHz
20 MHz
30 MHz
Notes: 100ns = 10MHz; 50ns = 20MHz; 33ns = 30 MHz

## Slide 29: Cycles Per Instruction (CPI)
Instruction mix for some program P, assume:
  25% load/store ( 3 cycles / instruction)
  60% arithmetic ( 2 cycles / instruction)
  15% branches ( 1 cycle / instruction)
Multi-Cycle performance for program P:
3 * .25 + 2 * .60 + 1 * .15 = 2.1
average cycles per instruction (CPI) = 2.1
Multi-Cycle @ 30 MHz
Single-Cycle @ 10 MHz
800 MHz PIII “faster” than 1 GHz P4

## Slide 30: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2
  15% branches, CPI = 1

## Slide 31: Amdahl’s Law
Amdahl’s Law
Execution time after improvement =
Or:
Speedup is limited by popularity of improved feature
Corollary:
Make the common case fast
Caveat:
Law of diminishing returns
execution time affected by improvement
amount of improvement
+ execution time unaffected
contribution to execution time

## Slide 32: Administrivia
Required: partner for group project
Project1 (PA1) and Homework2 (HW2) are both out
PA1 Design Doc and HW2 due in one week, start early
Work alone on HW2, but in group for PA1
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 33: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2013sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 26th
  Thursday, March 28th
  Thursday, April 25th
Schedule is subject to change

## Slide 34: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 35
Pipelining
See: P&H Chapter 4.5

## Slide 36: The Kids
Alice
Bob
They don’t always get along…

## Slide 37: The Bicycle

## Slide 38: The Materials
Saw
Drill
Glue
Paint

## Slide 39: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 40: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 41: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:

## Slide 42: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
Alice
Bob
Carol
Dave

## Slide 43: Pipelined Performance
time 1 2 3 4 5 6 7…
What if some tasks don’t need drill?
Latency:
Throughput:
Concurrency:
Notes: Throughput: 1 task / cycle
Delay: 4 cycles / task
Parallelism: 4 concurrent tasks

## Slide 44: Pipeline Hazards
0h 1h 2h 3h…
Q: What if glue step of task 3 depends on output of task 1?
Latency:
Throughput:
Concurrency:
Notes: A: Insert stalls as needed in task 3… and delay task 4+
Q: What is executing in glue stage?
A: Nothing
Performance is harder to predict

## Slide 45: Lessons
Principle:
Throughput increased by parallel execution
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (next week)

## Slide 46: A Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 47: A Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
register file
control
alu
imm
memory
din
dout
addr
inst
PC
memory
compute jump/branch targets
new pc
+4
extend

## Slide 48: Basic Pipeline
Five stage “RISC” load-store architecture
  Instruction fetch (IF)
    get instruction from memory, increment PC
  Instruction Decode (ID)
    translate opcode into control signals and read registers
  Execute (EX)
    perform ALU operation, compute jump/branch targets
  Memory (MEM)
    access memory if needed
  Writeback (WB)
    update register file
Notes: This is simpler than the MIPS, but we’re using it to get the concepts across – everything you see here applies to MIPS, but we have to deal w/ fewer bits in these examples (that’s why I like them)

## Slide 49: Principles of Pipelined Implementation
Break instructions across multiple clock cycles (five, in this case)
Design a separate stage for the execution performed during each clock cycle
Add pipeline registers (flip-flops) to isolate signals between different stages