## Slide 1: Pipeline Hazards
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See P&H Chapter 4.7

## Slide 2: Goals for Today
Data Hazards
  Revisit Pipelined Processors
  Data dependencies
  Problem, detection, and solutions
    (delaying, stalling, forwarding, bypass, etc)
  Hazard detection unit
  Forwarding unit
Next time
  Control Hazards
  What is the next instruction to execute if
  a branch is taken? Not taken?

## Slide 3: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 4: Recall: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 5: Recall: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 6: Recall: MIPS Instruction Types
Arithmetic/Logical
  ADD, ADDU, SUB, SUBU, AND, OR, XOR, NOR, SLT, SLTU
  ADDI, ADDIU, ANDI, ORI, XORI, LUI, SLL, SRL, SLLV, SRLV, SRAV, SLTI, SLTIU
  MULT, DIV, MFLO, MTLO, MFHI, MTHI
Memory Access
  LW, LH, LB, LHU, LBU, LWL, LWR
  SW, SH, SB, SWL, SWR
Control flow
  BEQ, BNE, BLEZ, BLTZ, BGEZ, BGTZ
  J, JR, JAL, JALR, BEQL, BNEL, BLEZL, BGTZL
Special
  LL, SC, SYSCALL, BREAK, SYNC, COPROC

## Slide 7: Pipelined Processor
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
compute jump/branch targets
+4
Fetch
Decode
Execute
Memory
WB

## Slide 8: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 9: Example: : Sample Code (Simple)
add r3, r1, r2; nand r6, r4, r5; lw r4, 20(r2); add r5, r2, r5; sw r7, 12(r3);

## Slide 10: Example: Sample Code (Simple)
Assume eight-register machine
Run the following code on a pipelined datapath
  add r3 r1 r2 ; reg 3 = reg 1 + reg 2
  nand r6 r4 r5 ; reg 6 = ~(reg 4 & reg 5)
  lw r4 20 (r2) ; reg 4 = Mem[reg2+20]
  add r5 r2 r5 ; reg 5 = reg 2 + reg 5
  sw r7 12(r3) ; Mem[reg3+12] = reg 7
Slides thanks to Sally McKee

## Slide 11: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add |  |  |  |  |  |  |  |  | 
nand |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
Clock cycle
Latency:
Throughput:
Concurrency:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
CPI =
Notes: CPI = 1 (inverse of throughput)

## Slide 12: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add |  |  |  |  |  |  |  |  | 
nand |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
Clock cycle
Latency:
Throughput:
Concurrency:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Latency: 5 cycles
Throughput: 1 instr/cycle
Concurrency: 5
CPI = 1
Notes: CPI = 1 (inverse of throughput)

## Slide 13
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
op
Rt
imm
valB
valA
PC+4
PC+4
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
Bits 26-31
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Rd

## Slide 14
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nop
0
0
0
0
0
0
0
nop
0
0
nop
0
0
0
0
nop
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
Initial
State
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
M
U
X
0
At time 1,
Fetch
add r3 r1 r2

## Slide 15
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nop
0
0
0
0
4
0
0
nop
0
0
nop
0
0
0
0
add 3 1 2
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
Fetch:
add 3 1 2
add 3 1 2
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
M
U
X
0
/ add
/ 3
/ 4
/ 36
/ 9
/ 2
Time: 1
/ 2

## Slide 16
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
add
3
9
36
4
8
0
0
nop
0
0
nop
0
0
0
0
nand 6 4 5
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
1
2
Bits 26-31
data
dest
Fetch:
nand 6 4 5
nand 6 4 5 add 3 1 2
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
2
M
U
X
3
/ 45
/ add
/ nand
/ 9
/ 6
/ 8
/ 18
/ 7
/ 5
/ 3
/ 4
36
9
3
Time: 2
/ 3

## Slide 17
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nand
6
7
18
8
12
4
45
add
3
9
nop
0
0
0
0
lw 4 20(2)
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
4
5
Bits 26-31
data
dest
Fetch:
lw 4 20(2)
lw 4 20(2) nand 6 4 5 add 3 1 2
36
9
3
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
5
M
U
X
6
3
2
/ 45
/ 3
nand ()
18 = 01 0010
7 = 00 0111
------------------
-3 = 11 1101
/ -3
/ add
/ 18
/ 7
/ nand
/ 7
/ 6
/ 8
Time: 3
/ 4
Notes: 0x 00 0111
0x 10 0010
And = 10
Nand = 11111 1101

## Slide 18
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
lw
20
18
9
12
16
8
-3
nand
6
7
add
3
45
0
0
add 5 2 5
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
2
4
Bits 26-31
data
dest
Fetch:
add 5 2 5
add 5 2 5 lw 4 20(2) nand 6 4 5 add 3 1 2
18
7
6
45
3
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
4
M
U
X
0
6
5
Time: 4

## Slide 19
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
add
5
7
9
16
20
12
29
lw
4
18
nand
6
-3
0
0
sw 7 12(3)
9
45
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
2
5
Bits 26-31
data
dest
Fetch:
sw 7 12(3)
sw 7 12(3) add 5 2 5 lw 4 20 (2) nand 6 4 5 add 3 1 2
9
20
4
-3
6
45
3
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
5
M
U
X
5
0
4
Time: 5

## Slide 20
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
sw
12
22
45
20
16
16
add
5
7
lw
4
29
99
0
9
45
18
7
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
3
7
Bits 26-31
data
dest
No more
instructions
sw 7 12(3) add 5 2 5 lw 4 20(2) nand 6 4 5
9
7
5
29
4
-3
6
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
7
M
U
X
0
5
5
Time: 6

## Slide 21
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
20
57
sw
7
22
add
5
16
0
0
9
45
99
7
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
No more
instructions
nop nop sw 7 12(3) add 5 2 5 lw 4 20(2)
45
7
12
16
5
99
4
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
0
7
Time: 7

## Slide 22
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
sw
7
57
0
9
45
99
16
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
No more
instructions
nop nop nop sw 7 12(3) add 5 2 5
22
57
22
16
5
Slides thanks to Sally McKee
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Time: 8

## Slide 23
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
9
45
99
16
36
-3
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 21-23
data
dest
No more
instructions
nop nop nop nop sw 7 12(3)
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Time: 9

## Slide 24: Takeaway
Pipelining is a powerful technique to mask latencies and increase throughput
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)

## Slide 25: Next Goal
What about data dependencies (also known as a data hazard in a pipelined processor)?
i.e. add r3, r1, r2
sub r5, r3, r4

## Slide 26: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 27: Data Hazards: Broken Example
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
sub r5, r3, r4
lw r6, 4(r3)
or r5, r3, r5
sw r6, 12(r3)
add r3, r1, r2
r3 = 10
r3 = 20
OK
r3 = 10
r3 = 20
time
r3 = 10
r3 = 10
r3 = 10
r3 = 20
r6 = Mem[r3 + 4]

## Slide 28: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect?
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 29
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Data Hazards
IF/ID.Ra ≠ 0 &&
(IF/ID.Ra==ID/Ex.Rd
IF/ID.Ra==Ex/M.Rd
IF/ID.Ra==M/W.Rd)

## Slide 30: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (IF/ID.Ra != 0 &&
(IF/ID.Ra == ID/EX.Rd || IF/ID.Ra == EX/M.Rd || IF/ID.Ra == M/WB.Rd))
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 31: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
Rd
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd

## Slide 32: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.

## Slide 33: Next Goal
What to do if data hazard detected?
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 34: Resolving Data Hazards
What to do if data hazard detected?
Wait/Stall
Reorder in Software (SW)
Forward/Bypass
All the above
None. We will use some other method
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 35: Resolving Data Hazards
What to do if data hazard detected?
Wait/Stall
Reorder in Software (SW)
Forward/Bypass
All the above
None. We will use some other method
Discuss today
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 36: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 37: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
Rd
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
If detect hazard
WE=0
MemWr=0
RegWr=0

## Slide 38: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
time
Notes: find hazards first, then draw

## Slide 39: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
r3 = 10
r3 = 20
time
IF
ID
Ex
M
W
IF
ID
Ex
M
W
IF
ID
Ex
M
ID
ID
ID
IF
IF
IF
IF
ID
Ex
Stalls
3
Stall
Notes: find hazards first, then draw

## Slide 40: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add r3,r1,r2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub r5,r3,r5
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 41: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
nop
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 42: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
nop
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 43: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 44: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Bubbles in pipeline significantly decrease performance.

## Slide 45: Next Goal: Resolving Data Hazards via Forwarding
What to do if data hazard detected?
Wait/Stall
Reorder in Software (SW)
Forward/Bypass
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 46: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register).
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 47: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
forward unit
Notes: draw control signals

## Slide 48: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 49: Forwarding Datapath 1
Ex/MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
  Resolve:
  Add a bypass from EX/MEM.D to start of EX
How to detect? Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 50: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 51: Forwarding Datapath 1
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
Ex
M
W

## Slide 52: Forwarding Datapath 2
Mem/WB to EX Bypass
  EX needs value being written by WB
  Resolve:
  Add bypass from WB final value to start of EX
How to detect? Logic in Ex Stage:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
not (ID/Ex.WE && Ex/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Check pg. 369
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 53: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 54: Forwarding Datapath 2
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M

## Slide 55: Register File Bypass
Register File Bypass
  Reading a value that is currently being written
Detect:
((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
Resolve:
Add a bypass around register file (WB to ID)
Better: (Hack) just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle

## Slide 56: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 57: Register File Bypass
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W

## Slide 58: Forwarding Example
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
r3 = 10
r3 = 20
time
M
W

## Slide 59: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r4 |  |  |  |  |  |  |  |  | 
lw r6, 4(r3) |  |  |  |  |  |  |  |  | 
or r5, r3, r5 |  |  |  |  |  |  |  |  | 
sw r6, 12(r3) |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX D=55 | MEM D=55 | WB r5=55 |  |  | 
 |  | IF | ID 33=r3 | EX D=? | MEM D=66 | WB r6=66 |  | 
 |  |  | IF | ID 33=r3 55=r5 | EX | MEM | WB | 
 |  |  |  | IF | ID 33=r3 66=r6 | EX | MEM | 
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
time
M
W
IF
ID
Ex
M
W
Notes: identify hazards then draw; if “or” had used r6, would have needed to stall

## Slide 60: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
Register File Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 61: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Bubbles (nops) in pipeline significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 62: Administrivia
Prelim1: next Tuesday, February 26th in evening
  Time: We will start at 7:30pm sharp, so come early
  Prelim Review: This Thur 6-8pm in Upson B14 and Fri, 5-7pm in Phillips 203
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of this week
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, HW2, Lab0, Lab1, Lab2

## Slide 63: Administrivia
HW2 is due tomorrow
  Fill out Survey online. Receive credit/points on homework for survey:
  Should have received email from Kathryn Dimiduk
  Survey is anonymous
Project1 (PA1) due week after prelim
  Continue working diligently. Use design doc momentum
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 64: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2013sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 26th
  Thursday, March 28th
  Thursday, April 25th
Schedule is subject to change

## Slide 65: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 66: Quiz
Find all hazards, and say how they are resolved: add r3, r1, r2 sub r3, r2, r1 nand r4, r3, r1 or r0, r3, r4 xor r1, r4, r3 sb r4, 1(r0)
Notes: 6 hazards
be careful of store (no rD)
be careful or r0 (never a hazard)

## Slide 67: Quiz
Find all hazards, and say how they are resolved: add r3, r1, r2 sub r3, r2, r1 nand r4, r3, r1 or r0, r3, r4 xor r1, r4, r3 sb r4, 1(r0)
Hours and hours of debugging!
Notes: 6 hazards
be careful of store (no rD)
be careful or r0 (never a hazard)

## Slide 68: Data Hazard Recap
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf