## Slide 1: Pipeline Control Hazards
Hakim Weatherspoon
CS 3410, Spring 2012
Computer Science
Cornell University
See P&H Appendix 4.8

## Slide 2: Goals for Today
Recap: Data Hazards
Control Hazards
  What is the next instruction to execute if a branch is taken? Not taken?
  How to resolve control hazards
  Optimizations

## Slide 3: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 4: Recall: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 5: Recall: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 6: Recall: MIPS Instruction Types
Arithmetic/Logical
  ADD, ADDU, SUB, SUBU, AND, OR, XOR, NOR, SLT, SLTU
  ADDI, ADDIU, ANDI, ORI, XORI, LUI, SLL, SRL, SLLV, SRLV, SRAV, SLTI, SLTIU
  MULT, DIV, MFLO, MTLO, MFHI, MTHI
Memory Access
  LW, LH, LB, LHU, LBU, LWL, LWR
  SW, SH, SB, SWL, SWR
Control flow
  BEQ, BNE, BLEZ, BLTZ, BGEZ, BGTZ
  J, JR, JAL, JALR, BEQL, BNEL, BLEZL, BGTZL
Special
  LL, SC, SYSCALL, BREAK, SYNC, COPROC

## Slide 7: Pipelined Processor
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
compute jump/branch targets
+4
Fetch
Decode
Execute
Memory
WB

## Slide 8: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 9: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add |  |  |  |  |  |  |  |  | 
nand |  |  |  |  |  |  |  |  | 
lw |  |  |  |  |  |  |  |  | 
add |  |  |  |  |  |  |  |  | 
sw |  |  |  |  |  |  |  |  | 
Clock cycle
Latency:
Throughput:
Concurrency:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
CPI =
Notes: CPI = 1 (inverse of throughput)

## Slide 10: Next Goal
What about data dependencies (also known as a data hazard in a pipelined processor)?
i.e. add r3, r1, r2
sub r5, r3, r4

## Slide 11: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 12: Data Hazards
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 13: Data Hazards
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
forward unit
stall = If(IF/ID.Ra ≠ 0 &&
(IF/ID.Ra == ID/Ex.Rd
IF/ID.Ra == Ex/M.Rd
IF/ID.Ra == M/W.Rd))
Rd
Notes: draw control signals

## Slide 14: Data Hazards
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 15: Stalling
  Pause current and all subsequent instructions
“slow down the pipeline”

## Slide 16: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
time
Notes: find hazards first, then draw

## Slide 17: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
r3 = 10
r3 = 20
time
IF
ID
Ex
M
W
IF
ID
Ex
M
W
IF
ID
Ex
M
ID
ID
ID
IF
IF
IF
IF
ID
Ex
Stalls
3
Stall
Notes: find hazards first, then draw

## Slide 18: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add r3,r1,r2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub r5,r3,r5
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 19: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
nop
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 20: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
nop
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 21: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 22: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register).
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 23: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 24: Forwarding Datapath
Ex/MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
  Resolve:
  Add a bypass from EX/MEM.D to start of EX
How to detect? Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for rB)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 25: Forwarding Datapath
Mem/WB to EX Bypass
  EX needs value being written by WB
  Resolve:
  Add bypass from WB final value to start of EX
How to detect? Logic in Ex Stage:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
not (ID/Ex.WE && Ex/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for rB)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 26: Forwarding Datapath
Register File Bypass
  Reading a value that is currently being written
  Detect:
  ((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
  Resolve:
  Add a bypass around register file (WB to ID)
Better Soln: (Hack) just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 27: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 28: Forwarding Datapath
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W

## Slide 29: Memory Load Data Hazard
What happens if data dependency after a load word instruction?
Memory Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 30: Memory Load Data Hazard
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Stall =
If(ID/Ex.MemRead &&
IF/ID.Ra == ID/Ex.Rd
Rd
MC
Notes: draw control signals

## Slide 31: Memory Load Data Hazard
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
sub r6, r4, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Notes: requires one bubble

## Slide 32: Memory Load Data Hazard
Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Resolution:
  MIPS 2000/3000: one delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
For stall, how to detect? Logic in ID Stage
    Stall = ID/Ex.MemRead &&
    (IF/ID.Ra == ID/Ex.Rd || IF/ID.Rb == ID/Ex.Rd)
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 33: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 34: Administrivia
Prelim1: today Tuesday, February 26th in evening
  Location: GSHG76: Goldwin Smith Hall room G76
  Time: We will start at 7:30pm sharp, so come early
  Prelim Review: Today, Thur 6-8pm in Upson B14 and Fri, 5-7pm in Phillips 203
  Closed Book: NO NOTES, BOOK, CALCULATOR, CELL PHONE
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of last week
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, HW2, Lab0, Lab1, Lab2

## Slide 35: Administrivia
HW2 was due yesterday
  Last day to submit tomorrow night, Friday 11:59pm
  HW2 solutions released on Saturday
Project1 (PA1) due next Monday, March 4th
  Continue working diligently. Use design doc momentum
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 36: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2013sp/schedule.html
Slides and Reading for lectures
Office Hours
Homework and Programming Assignments
Prelims (in evenings):
  Tuesday, February 26th
  Thursday, March 28th
  Thursday, April 25th
Schedule is subject to change

## Slide 37: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 38: Next Goal
What about branches?
A control hazard occurs if there is a control instruction (e.g. BEQ) because the program counter (PC) following the control instruction is not known until the control instruction computes if the branch should be taken or not.
e.g.
0x10: beq r1, r2, L
0x14: add r3, r0, r3
0x18: sub r5, r4, r6
0x1C: L: or r3, r2, r4
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 39: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
What happens to instr following a branch, if branch taken?
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 40: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 41: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
10:
14:
18:
1C:
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 42: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not.
If branch taken, then need to zap/flush instructions.
There is a performance penalty for branches:
Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.

## Slide 43: Next Goal
Can we reduce the cost of a control hazard?

## Slide 44: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 45: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 46: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
10:
14:
18:
1C:
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 47: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
  Can optimize and move branch and jump decision to stage 2 (ID)
  i.e. next PC is not known until 1 cycles after branch/jump
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 48: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not. If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.

## Slide 49: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not. If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.

## Slide 50: Next Goal
Can we reduce the cost of a control hazard further?

## Slide 51: Delay Slot
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
    i.e. Whether branch taken or not, instruction following branch is always executed

## Slide 52: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
IF
ID
Ex
M
W
IF
IF
ID
Ex
M
W
10:
14:
18:
1C:
Delay slot
If branch taken next instr still exec'd
branch calc
decide branch
ID
Ex
M
W
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 53: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
IF
ID
Ex
M
W
IF
IF
ID
Ex
M
W
10:
14:
18:
1C:
branch calc
decide branch
ID
Ex
M
W
IF
ID
Ex
M
W
Delay slot
If branch not taken next instr still exec’d
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 54: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
  Can optimize and move branch and jump decision to stage 2 (ID)
  i.e. next PC is not known until 1 cycles after branch/jump
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 55: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not. If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.
Delay Slots can potentially increase performance due to control hazards by putting a useful instruction in the delay slot since the instruction in the delay slot will always be executed. Requires software (compiler) to make use of delay slot. Put nop in delay slot if not able to put useful instruction in delay slot.

## Slide 56: Next Goal
Can we reduce the cost of a control hazard even further?

## Slide 57: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC not known until 2 cycles after branch/jump
Stall
Delay Slot
Speculative Execution
  “Guess” direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 58: Speculative Execution: Loops
Pipeline so far
  “Guess” (predict) branch not taken
We can do better!
  Make prediction based on last branch:
  Predict “take branch” if last branch “taken”
  Or Predict “do not take branch” if last branch “not taken”
  Need one bit to keep track of last branch
inst mem
PC
+4

## Slide 59: Speculative Execution: Loops
While (r3 ≠ 0)
Top: BEQZ r3, End
J Top
End:
Top2: BEQZ r3, End
J Top2
End2:
inst mem
PC
+4

## Slide 60: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not. If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.
Delay Slots can potentially increase performance due to control hazards by putting a useful instruction in the delay slot since the instruction in the delay slot will always be executed. Requires software (compiler) to make use of delay slot.
Speculative execution (guessing/predicting) can reduce costs of control hazards due to branches. If guess correct, no cost to branch. If guess wrong, need to flush pipeline.

## Slide 61: Hazards Summary
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard