## Slide 1: RISC, CISC, and Assemblers
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See P&H Appendix B.1-2, and Chapters 2.8 and 2.12; als 2.16 and 2.17

## Slide 2: Big Picture: Where are we now?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 3: Big Picture: Where are we going?
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
op = addi r0 r5 10
op = addi r5 r5 15
op = r-type r5 r5 shamt=1 func=sll
r0 = 0
r5 = r0 + 10
r5 = r5<<1 #r5 = r5 * 2
r5 = r15 + 15
Notes: 32 bits, 4 bytes

## Slide 4: Goals for Today
Instruction Set Architectures
  ISA Variations (i.e. ARM), CISC, RISC
(Intuition for) Assemblers
  Translate symbolic instructions to binary machine code
  Time for Prelim1 Questions
Next Time
  Program Structure and Calling Conventions

## Slide 5: Next Goal
Is MIPS the only possible instruction set architecture (ISA)?
What are the alternatives?

## Slide 6: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes
What happens when the common case is slow?
  Can we add some complexity in the ISA for a speedup?

## Slide 7: ISA Variations: Conditional Instructions
  while(i != j) {
  if (i > j)
  i -= j;
  else
  j -= i;
  }
  Loop: BEQ Ri, Rj, End // if "NE" (not equal), then stay in loop
  SLT Rd, Rj, Ri // "GT" if (i > j),
  BNE Rd, R0, Else // …
  SUB Ri, Ri, Rj // if "GT" (greater than), i = i-j;
  J Loop
  Else: SUB Rj, Rj, Ri // or "LT" if (i < j)
  J Loop // if "LT" (less than), j = j-i;
End:
In MIPS, performance will be
slow if code has a lot of branches
Notes: At least one NOP (flush of pipeline) may follow a branch

## Slide 8: ISA Variations: Conditional Instructions
  while(i != j) {
  if (i > j)
  i -= j;
  else
  j -= i;
  }
  LOOP: CMP Ri, Rj // set condition "NE" if (i != j)
  // "GT" if (i > j),
  // or "LT" if (i < j)
  SUBGT Ri, Ri, Rj // if "GT" (greater than), i = i-j;
  SUBLE Rj, Rj, Ri // if "LE" (less than or equal), j = j-i;
  BNE loop // if "NE" (not equal), then loop
=
≠
<
>
0
1
0
0
=
≠
<
>
0
0
0
1
=
≠
<
>
1
0
1
0
=
≠
<
>
0
1
0
0
In ARM, can avoid delay due to
Branches with conditional
instructions
Notes: In ARM assembly, the loop avoids the branches around the then and else clauses. Note that if Ri and Rj are equal then neither of the SUB instructions will be executed, optimizing out the need for a conditional branch to implement the while check at the top of the loop, for example had SUBLE (less than or equal) been used.

## Slide 9: ARM: Other Cool operations
Shift one register (e.g. Rc) any amount
Add to another register (e.g. Rb)
Store result in a different register (e.g. Ra)
ADD Ra, Rb, Rc LSL #4
Ra = Rb + Rc<<4
Ra = Rb + Rc x 16

## Slide 10: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 11: ARM instruction formats
All ARM instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
opx | op | rs | rd | opx | rt
4 bits | 8 bits | 4 bits | 4 bits | 8 bits | 4 bits
opx | op | rs | rd | immediate
4 bits | 8 bits | 4 bits | 4 bits | 12 bits
opx | op | immediate (target address)
4 bits | 4 bits | 24 bits
Notes: 9 addressing modes

## Slide 12: Instruction Set Architecture
ISA defines the permissible instructions
  MIPS: load/store, arithmetic, control flow, …
  ARM: similar to MIPS, but more shift, memory, & conditional ops
  VAX: arithmetic on memory or registers, strings, polynomial evaluation, stacks/queues, …
  Cray: vector operations, …
  x86: a little of everything

## Slide 13: ARM Instruction Set Architecture
All ARM instructions are 32 bits long, has 3 formats
Reduced Instruction Set Computer (RISC) properties
  Only Load/Store instructions access memory
  Instructions operate on operands in processor registers
  16 registers
Complex Instruction Set Computer (CISC) properties
  Autoincrement, autodecrement, PC-relative addressing
  Conditional execution
  Multiple words can be accessed from memory with a single instruction (SIMD: single instr multiple data)

## Slide 14: Takeaway
We can reduce the number of instructions to execute a program and possibly increase performance by adding complexity to the ISA.

## Slide 15: Next Goal
How much complexity to add to an ISA?
How does the CISC philosophy compare to RISC?

## Slide 16: Complex Instruction Set Computers (CISC)
People programmed in assembly and machine code!
  Needed as many addressing modes as possible
  Memory was (and still is) slow
CPUs had relatively few registers
  Register’s were more “expensive” than external mem
  Large number of registers requires many bits to index
Memories were small
  Encoraged highly encoded microcodes as instructions
  Variable length instructions, load/store, conditions, etc

## Slide 17: Reduced Instruction Set Computer
Dave Patterson
  RISC Project, 1982
  UC Berkeley
  RISC-I: ½ transistors & 3x faster
  Influences: Sun SPARC, namesake of industry
John L. Hennessy
  MIPS, 1981
  Stanford
  Simple pipelining, keep full
  Influences: MIPS computer system, PlayStation, Nintendo

## Slide 18: Reduced Instruction Set Computer
John Cock
  IBM 801, 1980 (started in 1975)
  Name 801 came from the bldg that housed the project
  Idea: Possible to make a very small and very fast core
  Influences: Known as “the father of RISC Architecture”. Turing Award Recipient and National Medal of Science.

## Slide 19: Complexity
MIPS = Reduced Instruction Set Computer (RlSC)
  ≈ 200 instructions, 32 bits each, 3 formats
  all operands in registers
    almost all are 32 bits each
  ≈ 1 addressing mode: Mem[reg + imm]
x86 = Complex Instruction Set Computer (ClSC)
  > 1000 instructions, 1 to 15 bytes each
  operands in dedicated registers, general purpose registers, memory, on stack, …
    can be 1, 2, 4, 8 bytes, signed or unsigned
  10s of addressing modes
    e.g. Mem[segment + reg + reg*scale + offset]
Notes: DEC PDP-8 has about 8 insructions

## Slide 20: RISC vs CISC
RISC Philosophy
Regularity & simplicity
Leaner means faster
Optimize the common case
Energy efficiency
Embedded Systems
Phones/Tablets
CISC Rebuttal
Compilers can be smart
Transistors are plentiful
Legacy is important
Code size counts
Micro-code!
Desktops/Servers
Notes: RISC:
regularity means no mem-to-mem, few addressing modes… thus load-store
regularity means uniform instruction size… sizeof(common) = sizeof(rare)
lean means fewer, more general instructions… thus bigger programs, more instructions
common case means measurement
CISC:
Compilers can be smart
Transistors are plentiful
Legacy is important
Code size counts
Micro-code!

## Slide 21: ARMDroid vs WinTel
  Android OS on ARM processor
  Windows OS on Intel (x86) processor
Notes:   In 2005, about 98% of the more than one billion mobile phones sold each year used at least one ARM processor.[5] As of 2009, ARM processors account for approximately 90% of all embedded 32-bit RISC processors[6] and are used extensively in consumer electronics, including personal digital assistants (PDAs), tablets, mobile phones, digital media and music players, hand-held game consoles, calculators and computer peripherals such as hard drives and routers.

## Slide 22: Takeaway
We can reduce the number of instructions to execute a program and possibly increase performance by adding complexity to the ISA.
Back in the day… CISC was necessary because everybody programmed in assembly and machine code! Today, CISC ISA’s are still dominate today due to the prevalence of x86 ISA processors. However, RISC ISA’s today such as ARM have an ever increase marketshare (of our everyday life!).
ARM borrows a bit from both RISC and CISC.

## Slide 23: Goals for Today
Instruction Set Architectures
  ISA Variations (i.e. ARM), CISC, RISC
(Intuition for) Assemblers
  Translate symbolic instructions to binary machine code
  Time for Prelim1 Questions
Next Time
  Program Structure and Calling Conventions

## Slide 24: Next Goal
How do we (as humans or compiler) program on top of a given ISA?

## Slide 25: Big Picture: Where are we going?
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
op = addi r0 r5 10
op = addi r5 r5 15
op = r-type r5 r5 shamt=1 func=sll
r0 = 0
r5 = r0 + 10
r5 = r5<<1 #r5 = r5 * 2
r5 = r15 + 15
Notes: 32 bits, 4 bytes

## Slide 26: Assembler
Translates text assembly language to binary machine code
Input: a text file containing MIPS instructions in human readable form
Output: an object file (.o file in Unix, .obj in Windows) containing MIPS instructions in executable form
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111

## Slide 27: Assembler
calc.c
math.c
io.s
libc.o
libm.o
calc.s
math.s
io.o
calc.o
math.o
calc.exe
Compiler
Assembler
linker
Notes: C compiller produces assembly files (contain MIPS assembly, pseudo-instructions, directives, etc.)
MIPS assembler produces object files (contain MIPS machine code, missing symbols, some layout information, etc.)
MIPS linker produces executable file (contains MIPS machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 28: Assembler
Translates text assembly language to binary machine code
Input: a text file containing MIPS instructions in human readable form
Output: an object file (.o file in Unix, .obj in Windows) containing MIPS instructions in executable form
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111

## Slide 29: Assembly Language
Assembly language is used to specify programs at a low-level
Will I program in assembly
A: I do...
  For CS 3410 (and some CS 4410/4411)
  For kernel hacking, device drivers, GPU, etc.
  For performance (but compilers are getting better)
  For highly time critical sections
  For hardware without high level languages
  For new & advanced instructions: rdtsc, debug registers, performance counters, synchronization, ...

## Slide 30: Assembly Language
Assembly language is used to specify programs at a low-level
What does a program consist of?
  MIPS instructions
  Program data (strings, variables, etc)

## Slide 31: Assembler
Assembler:
assembly instructions
+ psuedo-instructions
+ data and layout directives
= executable program
Slightly higher level than plain assembly
e.g: takes care of delay slots
(will reorder instructions or insert nops)

## Slide 32: MIPS Assembly Language Instructions
Arithmetic/Logical
  ADD, ADDU, SUB, SUBU, AND, OR, XOR, NOR, SLT, SLTU
  ADDI, ADDIU, ANDI, ORI, XORI, LUI, SLL, SRL, SLLV, SRLV, SRAV, SLTI, SLTIU
  MULT, DIV, MFLO, MTLO, MFHI, MTHI
Memory Access
  LW, LH, LB, LHU, LBU, LWL, LWR
  SW, SH, SB, SWL, SWR
Control flow
  BEQ, BNE, BLEZ, BLTZ, BGEZ, BGTZ
  J, JR, JAL, JALR, BEQL, BNEL, BLEZL, BGTZL
Special
  LL, SC, SYSCALL, BREAK, SYNC, COPROC

## Slide 33: Pseudo-Instructions
Pseudo-Instructions
NOP # do nothing
  SLL r0, r0, 0
MOVE reg, reg # copy between regs
  ADD R2, R0, R1 # copies contents of R1 to R2
LI reg, imm # load immediate (up to 32 bits)
LA reg, label # load address (32 bits)
B label # unconditional branch
BLT reg, reg, label # branch less than
  SLT r1, rA, rB # r1 = 1 if R[rA] < R[rB]; o.w. r1 = 0
  BNE r1, r0, label # go to address label if r1!=r0; i.t. rA < rB
Notes: BLT rA, rB, label
becomes
SLT r1, rA, rB
BNE r1, r0, label

## Slide 34: Program Layout
Programs consist of segments used for different purposes
  Text: holds instructions
  Data: holds statically allocated program data such as variables, strings, etc.
add r1,r2,r3
ori r2, r4, 3
...
“cornell cs”
13
25
data
text

## Slide 35: Assembling Programs
Assembly files consist of a mix of
+ instructions
+ pseudo-instructions
+ assembler (data/layout) directives
(Assembler lays out binary values
in memory based on directives)
Assembled to an Object File
  Header
  Text Segment
  Data Segment
  Relocation Information
  Symbol Table
  Debugging Information
.text
.ent main
main: la $4, Larray
li $5, 15
...
li $4, 0
jal exit
.end main
.data
Larray:
.long 51, 491, 3991
Notes: A program is made up by code and data from several object files
Each object file is generated independently
Assembler starts at some PC address, e.g. 0, in each object file, generates code as if the program were laid out starting out at location 0x0
It also generates a symbol table, and a relocation table
In case the segments need to be moved

## Slide 36: Assembling Programs
Assembly with a but using (modified) Harvard architecture
  Need segments since data and program stored together in memory
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 37: Takeaway
Assembly is a low-level task
  Need to assemble assembly language into machine code binary. Requires
  Assembly language instructions
  pseudo-instructions
  And Specify layout and data using assembler directives
  Since we use a modified Harvard Architecture (Von Neumann architecture) that mixes data and instructions in memory
  … but best kept in separate segments

## Slide 38: Next time
How do we coordinate use of registers?
Calling Conventions!
PA1 due Monday

## Slide 39: Administrivia
Prelim1: Today, Tuesday, February 26th in evening
  Location: GSHG76: Goldwin Smith Hall room G76
  Time: We will start at 7:30pm sharp, so come early
  Closed Book: NO NOTES, BOOK, CALCULATOR, CELL PHONE
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of last week
    Appendix C (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, HW2, Lab0, Lab1, Lab2

## Slide 40: Administrivia
Project1 (PA1) due next Monday, March 4th
  Continue working diligently. Use design doc momentum
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab