## Slide 1: Calling Conventions
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
See P&H 2.8 and 2.12

## Slide 2: Administrivia
Prelim1 results
  Mean 78.5 (median 79), standard deviation 10
  Prelims available in 305 Upson
  Regrade requires written request
    Whole test is regraded

## Slide 3: Administrivia
Some Survey Results
  Lecture speed
    59% think lecture pace is a little to way too fast
    28% think just about right
    13% variable
    < 1% think lecture is too slow (2 people)
  Read the book
    Over 50% never read the book at all!
    10% read before class
  Need to meet halfway!
    Slow lecture down a bit, but need to read!

## Slide 4: Administrivia
Some Survey Results
  Taking notes
    40% paper/notebook
    22% computer/tables
    7% printed copy of lecture slides
    29% don’t take notes at all
  Comments
    Some people’s computer use is distracting (playing games, facebook, email, youtube, etc)
    Peer pressure: kindly ask neighbor not to distract with computer

## Slide 5: Goals for Today
Review: Calling Conventions
  call a routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register
  Today
  More on Calling Conventions
  globals vs local accessible data
  callee vs caller saved registers
  Calling Convention examples and debugging

## Slide 6: Goals for Today
Review: Calling Conventions
  call a routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register
  Today
  More on Calling Conventions
  globals vs local accessible data
  callee vs caller saved registers
  Calling Convention examples and debugging
Warning: There is no one true MIPS calling convention.
lecture != book != gcc != spim != web

## Slide 7: Recap: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains $fp
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    (i.e. argument “spilling)
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Bottom of
current
stack frame
Top of
the stack
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 8: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 9: Globals and Locals
Global variables in data segment
  Exist for all time, accessible to all routines
Dynamic variables in heap segment
  Exist between malloc() and free()
Local variables in stack frame
  Exist solely for the duration of the stack frame
Dangling pointers into freed heap mem are bad
Dangling pointers into old stack frames are bad
  C lets you create these, Java does not
  int *foo() { int a; return &a; }

## Slide 10: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
Caller-save registers are responsibility of the caller
  Caller-save register values saved only if used after call/return
  The callee function can use caller-saved registers
Callee-save register are the responsibility of the callee
  Values must be saved by callee before they can be used
  Caller can assume that these registers will be restored
Save if want to
use after a call
Save before use

## Slide 11: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
MIPS ($t0-$t9), x86 (eax, ecx, and edx) are caller-save…
  … a function can freely modify these registers
  … but must assume that their contents have been destroyed if it in turns calls a function.
MIPS ($s0 - $s7), x86 (ebx, esi, edi, ebp, esp) are callee-save
  A function may call another function and know that the callee-save registers have not been modified
  However, if it modifies these registers itself, it must restore them to their original values before returning.

## Slide 12: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
A caller-save register must be saved and restored around any call to a subroutine.
In contrast, for a callee-save register, a caller need do no extra work at a call site (the callee saves and restores the register if it is used).

## Slide 13: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
CALLER SAVED: MIPS calls these temporary registers, $t0-t9
  the calling routine saves the registers that it does not want a called procedure to overwrite
  register values are NOT preserved across procedure calls
CALLEE SAVED: MIPS calls these saved registers, $s0-s8
  register values are preserved across procedure calls
  the called procedure saves register values in its Activation Record (AR), uses the registers for local variables, restores register values before it returns.

## Slide 14: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
Registers $t0-$t9 are caller-saved registers
  … that are used to hold temporary quantities
  … that need not be preserved across calls
Registers $s0-s8 are callee-saved registers
  … that hold long-lived values
  … that should be preserved across calls

## Slide 15: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1

## Slide 16: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prolog
Epilog

## Slide 17: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prolog
Epilog
How many bytes do we
need to allocate for the
stack frame?
24
32
40
44
48

## Slide 18: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
saved ra
saved fp
saved regs ($s0 and $s1)
locals
($t0)
outgoing args
space for a0 - a3
and 5th and 6th arg
$fp 
$sp 
Prolog
Epilog

## Slide 19: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
saved ra
saved fp
$fp 
$sp 
Prolog
Epilog
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40

## Slide 20: Activity #2: Calling Convention Example: Prolog, Epilog
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
test:
saved ra
saved fp
$fp 
$sp 
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40

## Slide 21: Activity #2: Calling Convention Example: Prolog, Epilog
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
test:
ADDIU $sp, $sp, -44
SW $ra, 40($sp)
SW $fp, 36($sp)
SW $s1, 32($sp)
SW $s0, 28($sp)
ADDIU $fp, $sp, 40
LW $s0, 28($sp)
LW $s1, 32($sp)
LW $fp, 36($sp)
LW $ra, 40($sp)
ADDIU $sp, $sp, 44
JR $ra
NOP
Body
(previous slide, Activity #1)
saved ra
saved fp
$fp 
$sp 
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40
Space for $t0
and six args
to pass to
subroutine

## Slide 22: Next Goal
Can we optimize the assembly code at all?

## Slide 23: Activity #3: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prolog
Epilog
How can we optimize
the assembly code?
Notes: Optimize by removing the NOPs. That is, putting a independent instruction in the delay slot

## Slide 24: Activity #3: Calling Convention Example: Prolog, Epilog
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
test:
ADDIU $sp, $sp, -44
SW $ra, 40($sp)
SW $fp, 36($sp)
SW $s1, 32($sp)
SW $s0, 28($sp)
ADDIU $fp, $sp, 40
LW $s0, 28($sp)
LW $s1, 32($sp)
LW $fp, 36($sp)
LW $ra, 40($sp)
ADDIU $sp, $sp, 44
JR $ra
NOP
Body

## Slide 25: Minimum stack size for a standard function?
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 26: Minimum stack size for a standard function?
24 bytes = 6x 4 bytes ($ra + $fp + 4 args)
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 27: Leaf Functions
Leaf function does not invoke any other functions
int f(int x, int y) { return (x+y); }
Optimizations?
No saved regs (or locals)
No outgoing args
Don’t push $ra
No frame at all?
Maybe.
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 

## Slide 28: Administrivia
Upcoming agenda
  Schedule PA2 Design Doc Mtg for next Monday, Mar 11th
  HW3 due next Wednesday, March 13th
  PA2 Work-in-Progress circuit due before spring break
  Spring break: Saturday, March 16th to Sunday, March 24th
  Prelim2 Thursday, March 28th, right after spring break
  PA2 due Thursday, April 4th

## Slide 29: Recap
  How to write and Debug a MIPS program using calling convention
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains $fp
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    (i.e. argument “spilling)
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?