## Slide 1: Caches (Writing)
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
P & H Chapter 5.2-3, 5.5

## Slide 2: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)

## Slide 3: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
Stack, Data, Code
Stored in Memory

## Slide 4: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Memory: big & slow vs Caches: small & fast
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
Stack, Data, Code
Stored in Memory
$$
$$

## Slide 5: Big Picture
How do we make the processor fast,
Given that memory is VEEERRRYYYY SLLOOOWWW!!

## Slide 6: Big Picture
How do we make the processor fast,
Given that memory is VEEERRRYYYY SLLOOOWWW!!
But, insight for Caches
If Mem[x] was accessed recently...
… then Mem[x] is likely to be accessed soon
  Exploit temporal locality:
    Put recently accessed Mem[x] higher in memory hierarchy
    since it will likely be accessed again soon
… then Mem[x ± ε] is likely to be accessed soon
  Exploit spatial locality:
    Put entire block containing Mem[x] and surrounding addresses higher in memory hierarchy since nearby address will likely be accessed

## Slide 7: Goals for Today: caches
Comparison of cache architectures:
  Direct Mapped
  Fully Associative
  N-way set associative
Writing to the Cache
  Write-through vs Write-back
Caching Questions
  How does a cache work?
  How effective is the cache (hit rate/miss rate)?
  How large is the cache?
  How fast is the cache (AMAT=average memory access time)
Notes: Caches vs memory vs tertiary storage
- Tradeoffs: big & slow vs small & fast
- working set: 90/10 rule
- How to predict future: temporal & spacial locality

## Slide 8: Next Goal
How do the different cache architectures compare?
  Cache Architecture Tradeoffs?
  Cache Size?
  Cache Hit rate/Performance?

## Slide 9: Cache Tradeoffs
A given data block can be placed…
  … in any cache line  Fully Associative
  … in exactly one cache line  Direct Mapped
  … in a small set of cache lines  Set Associative

## Slide 10: Cache Tradeoffs
Direct Mapped
+ Smaller
+ Less
+ Less
+ Faster
+ Less
+ Very
– Lots
– Low
– Common
Fully Associative
Larger –
More –
More –
Slower –
More –
Not Very –
Zero +
High +
?
Tag Size
SRAM Overhead
Controller Logic
Speed
Price
Scalability
# of conflict misses
Hit rate
Pathological Cases?

## Slide 11: Cache Tradeoffs
Compromise: Set-associative cache
Like a direct-mapped cache
  Index into a location
  Fast
Like a fully-associative cache
  Can store multiple entries
    decreases thrashing in cache
  Search in each element

## Slide 12: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
=
hit?
data
word select
32bits
0…001000
offset
index
tag
word
selector
Byte offset
in word

## Slide 13: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
n bit index, m bit offset
Q: How big is cache (data only)?

## Slide 14: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
n bit index, m bit offset
Q: How much SRAM is needed (data + overhead)?

## Slide 15: Fully Associative Cache (Reading)
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 16: Fully Associative Cache (Reading)
V
Tag
Block
Tag Offset
m bit offset
Q: How big is cache (data only)?
, 2n blocks (cache lines)
Notes: “way” = line

## Slide 17: Fully Associative Cache (Reading)
V
Tag
Block
Tag Offset
m bit offset
Q: How much SRAM needed (data + overhead)?
, 2n blocks (cache lines)
Notes: “way” = line

## Slide 18: 3-Way Set Associative Cache (Reading)
word select
hit?
data
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 19: 3-Way Set Associative Cache (Reading)
Tag Index Offset
n bit index, m bit offset, N-way Set Associative
Q: How big is cache (data only)?

## Slide 20: 3-Way Set Associative Cache (Reading)
Tag Index Offset
n bit index, m bit offset, N-way Set Associative
Q: How much SRAM is needed (data + overhead)?

## Slide 21: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 22: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 23: Comparison: 2 Way Set Assoc
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Using byte addresses in this example! Addr Bus = 5 bits
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 24: Misses
Cache misses: classification
The line is being referenced for the first time
  Cold (aka Compulsory) Miss
  The line was in the cache, but has been evicted…
  … because some other access with the same index
  Conflict Miss
… because the cache is too small
  i.e. the working set of program is larger than the cache
  Capacity Miss
Notes: Q: What causes a cache miss?
conflict: collisions, competition

## Slide 25: Misses
Cache misses: classification
Cold (aka Compulsory)
  The line is being referenced for the first time
Capacity
  The line was evicted because the cache was too small
  i.e. the working set of program is larger than the cache
Conflict
  The line was evicted because of another access whose index conflicted
Notes: conflict can’t happen with fully associative
block size influences cold misses

## Slide 26: Cache Performance
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle per word, plus 3 cycle per consecutive word
Performance depends on:
Access time for hit, miss penalty, hit rate
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 27: Takeway
Direct Mapped  simpler, low hit rate
Fully Associative  higher hit cost, higher hit rate
N-way Set Associative  middleground

## Slide 28
Writing with Caches

## Slide 29: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    random: select one of the lines at random
    round-robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 30: Cached Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 31: What about Stores?
Where should you write the result of a store?
  If that memory location is in the cache?
    Send it to the cache
    Should we also send it to memory right away?
    (write-through policy)
    Wait until we kick the block out (write-back policy)
  If it is not in the cache?
    Allocate the line (put it in the cache)?
    (write allocate policy)
    Write it directly to memory without allocation?
    (no write allocate policy)

## Slide 32: Write Allocation Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is not in the cache…
Write-Allocate
  allocate a cache line for new data (and maybe write-through)
No-Write-Allocate
  ignore cache, just go to main memory

## Slide 33: Handling Stores (Write-Through)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
Assume write-allocate
policy
Using byte addresses in this example! Addr Bus = 4 bits
Fully Associative Cache
2 cache lines
2 word block
3 bit tag field
1 bit block offset field

## Slide 34: How Many Memory References?
Write-through performance

## Slide 35: Write-Through vs. Write-Back
Can we also design the cache NOT to write all stores immediately to memory?
  Keep the most current copy in cache, and update memory when that data is evicted (write-back policy)
  Do we need to write-back all evicted lines?
  No, only blocks that have been stored into (written)

## Slide 36: Write-Back Meta-Data
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 37: Handling Stores (Write-Back)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Using byte addresses in this example! Addr Bus = 4 bits
Assume write-allocate
policy
Fully Associative Cache
2 cache lines
2 word block
3 bit tag field
1 bit block offset field

## Slide 38: Write-Back (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]

## Slide 39: How Many Memory References?
Write-back performance

## Slide 40: Write-through vs. Write-back
Write-through is slower
  But cleaner (memory always consistent)
Write-back is faster
  But complicated when multi cores sharing memory

## Slide 41: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 42: Performance Tradeoffs
Q: Hit time: write-through vs. write-back?
Q: Miss penalty: write-through vs. write-back?

## Slide 43: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: What does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 44: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 45: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
May need to snoop on other CPU’s cache activity
Invalidate cache line when other CPU writes
Flush write-back caches before other CPU reads
Or the reverse: Before writing/reading…
Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net

## Slide 46: Administrivia
Prelim1: Thursday, March 28th in evening
  Time: We will start at 7:30pm sharp, so come early
  Two Location: PHL101 and UPSB17
    If NetID ends with even number, then go to PHL101 (Phillips Hall rm 101)
    If NetID ends with odd number, then go to UPSB17 (Upson Hall rm B17)
  Prelim Review: Yesterday, Mon, at 7pm and today, Tue, at 5:00pm.
  Both in Upson Hall rm B17
  Closed Book: NO NOTES, BOOK, ELECTRONICS, CALCULATOR, CELL PHONE
  Practice prelims are online in CMS
  Material covered everything up to end of week before spring break
    Lecture: Lectures 9 to 16 (new since last prelim)
    Chapter 4: Chapters 4.7 (Data Hazards) and 4.8 (Control Hazards)
    Chapter 2: Chapter 2.8 and 2.12 (Calling Convention and Linkers), 2.16 and 2.17 (RISC and CISC)
    Appendix B: B.1 and B.2 (Assemblers), B.3 and B.4 (linkers and loaders), and B.5 and B.6 (Calling Convention and process memory layout)
    Chapter 5: 5.1 and 5.2 (Caches)
    HW3, Project1 and Project2
Notes: Appendix C (logic, gates, FSMs, memory, ALUs)
Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
Chapter 1 (Performance)
HW1, HW2, Lab0, Lab1, Lab2

## Slide 47: Administrivia
Next six weeks
  Week 9 (May 25): Prelim2
  Week 10 (Apr 1): Project2 due and Lab3 handout
  Week 11 (Apr 8): Lab3 due and Project3/HW4 handout
  Week 12 (Apr 15): Project3 design doc due and HW4 due
  Week 13 (Apr 22): Project3 due and Prelim3
  Week 14 (Apr 29): Project4 handout
Final Project for class
  Week 15 (May 6): Project4 design doc due
  Week 16 (May 13): Project4 due

## Slide 48: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  (big & fast) built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate

## Slide 49: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
Multi-core / Multi-Processor is complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right